## Slide 1: UAE Digital TV Switchover Plan
By: TRA, UAE at the ITU Regional Workshop on
Efficiency of the Frequency Spectrum Use in the Arab Region;
Amman-Jordan, 5-7 Dec. 2011

## Slide 2: Introduction
GE-06 agreement for Band III: 174‑230 MHz, Band IV: 470‑582 MHz and Band V: 582-862 MHz
WRC-07 made MOBILE co-primary in 790-862 MHz for Region 1
Administrations part of GE-06 have digital broadcasting allotment / assignments in the Digital Dividends bands
These Allotments & Assignments are coordinated and have full protection rights from interference as per GE-06.
To use the digital dividend, the digital switch over has to be completed which has associated challenges.
UAE TRA started with the DSO planning and this presentation provides an overview of the steps in the experience

## Slide 3: GCC-GENEVA 06 ASSIGNMENTS/ALLOTMENTS IN UHF
Chart: 
| Assign | Allot | Assign | Allot | Assign | Allot | Assign | Allot | Assign | Allot | Assign | Allot | UAE | Oman | KSA | Qatar | Bahrain | Kuwait
470-694 MHz | 94 | 2 | 324 | 16 | 662 | 0 | 17 | 0 | 12 | 0 | 14 | 0
694-790 MHz | 48 | 2 | 187 | 7 | 226 | 0 | 16 | 0 | 24 | 0 | 10 | 0
790-862 MHz | 18 | 0 | 104 | 3 | 127 | 0 | 5 | 0 | 9 | 0 | 9 | 0

## Slide 4: Policy Questions
What is the market situation (Assessment of TV services, channels usage and stakeholder consultation)?
How the DTT re-planning can be done to make contiguous spectrum available as digital dividend?
How the Frequency assignment and licensing of DTT should be done?
What are the Technological aspects of DTT?
What business models will be feasible for DTT operators (impact of MUX operator, content provider relation)?
Approval and issuance of the DSO Plan

## Slide 5: Assessment of UAE TV services
Only 3% of all UAE TV households rely solely on analogue TV
GDP (billion USD) | Adult population (millions) | GDP per capita (USD) | Households (000s) | TV households (000s) | TV penetration (%) | DSO start date | ASO
178 | 3.9 | 27 385 | 1327 | 1294 | 97.5 | 2011 | 2013
Salient features of the UAE TV market
Approximately 70% of the population of UAE are foreign workers
UAE has a strong pay-TV (cable and IPTV) market led by telecoms operators Etisalat and du
The total number of free-to-air (FTA) satellite channels reached 487 in 2010 due to diversity in population
The increasing market shares of cable and IPTV show the growing network expansion by Etisalat and du
The number of households relying solely on terrestrial TV has halved in the past four years to reach 3% by end of 2009 as more choice is available to consumers from cable or IPTV platforms

## Slide 6: Assessment and benchmarking
Stakeholders identification (Telcos, Broadcasters, Media Zones, NMC)
TV holds a small share of the total advertising market in the UAE, as all ads are aired on a pan-Arab basis. Local ads through print media
Key learnings from international experiences were considered in development of the switchover plan
Six benchmark countries were shortlisted from over 30 countries, following a set of filtering criteria;
    similar TV platform structure to UAE, i.e. high cable and/or satellite penetration
    Improving terrestrial and/or DTT competitiveness, measured as platform market share or alternative use for DTT
    preferably ASO completed as full learnings (before & after) from DSO process can be captured
  Benchmarked countries are USA, UK, Germany, Singapore, Finland, and Netherlands

## Slide 7: Stakeholders DTT Plans
Stakeholders’ DTT plans are based on a mix of strategic and commercial decisions, HD capacity is a key success factor
Dubai TV
Introduction of DTT is a strategic decision (to maintain control of public information)
Improved quality of analogue programming on a national basis
Purely a commercial decision to deploy DTT
Potential advantage in creating a national TV market which could re-distribute print advertising revenues to TV for national advertisers
Strategic decision (to maintain control of public information and for emergency services)
DTT may provide universal service benefits in providing access to services to the public, but there is very little commercial future for DTT in a satellite-dominated market
Abu Dhabi TV
Sharjah TV
twofour54
General plans for using DTT
Key success factors
Availability of HD capacity to provide a competitive alternative to satellite and cable
Could create a national market, with local programming feeds, which could attract local advertisers
Gives broadcasters opportunity to purchase affordable local content rights for sport events, documentaries, movies, etc.
Enables interaction with audience & mobility in reception

## Slide 8: Overall assessment
Broadcasters intend to air current terrestrial channels on the DTT
All three broadcasters aim to broadcast current channels – a total of 12 channels
Sharjah TV would consider launching an education-themed channel
All broadcasters see a combination of FTA programming and pay-TV as a model for DTT
EPG is deemed to be a must-have service for the DTT platform, together with the possibility to offer interactive services
Enablement of subscription video-on-demand (SVOD) services
Built-in PVR capabilities (in the STB)
Sharjah TV would prefer to hold both transmission and broadcasting licences to allow control of network, and the possibility of a network-sharing arrangement for national transmission
Dubai TV would prefer centralised operations. Implicitly it would want to own the broadcasting licence itself but leave the transmission licence to a third party
Standards & technical aspects
All broadcasters prefer all reception capabilities: fixed, portable and mobile – to maximise reach
DVB-T2, is the preferred choice, if it does not impede coverage and successful in other markets
MPEG-4 coding / 64QAM is the preferred mode of operation and seen as a robust solution
All broadcasters linked to the respective local governments and receive funding for their operations
Advertising revenues cover only a proportion of total costs
A large proportion (60–70%) of all programming is produced locally. An equally large share of total revenues are related to programming costs
Channels use
EPG & other services
Licensing Model
Financial information

## Slide 9: Frequency Planning
Study showed that multi-frequency network (MFN) configuration would reduce the total capacity available, and therefore single-frequency network (SFN) configuration was selected
DTT planning undertaken for UHF Bands IV/V initially, with VHF Band III reserved either for future expansion of DTT (e.g. more MUX or more regional services) or for T-DAB (if market demand)
UHF Blocks 60 and 69 reserved for mobile services (DVB-H)
Analysis showed national coverage using three SFN national MUXs (provisionally named A, B and C) using UHF blocks 21 (474MHz), 27 (522MHz) and 60 (786MHz)
Creation of three DTT MUX will allow existing broadcasters to transmit existing analogue programmes digitally (and in HD if desired), with some space for additional services
Plan was then modified to cater for the vacation of 698-806 MHz for Mobile. Block 60 replaced by blocks 31 (554MHz) and 37 (602MHz) for MUX C

## Slide 10: Coverage Planning
Study on coverage through existing sites showed 70-80% of total pop. coverage is achievable using available main sites with the selected frequencies
Coverage is less in some Emirates (primarily Abu Dhabi, Sharjah and Fujairah) due to insufficient main sites having an assignment for the selected frequencies within the GE-06 Plan
However other frequencies are available at sites within those Emirates, and these could be used to complete coverage
Alternatively, broadcasters can in-fill coverage using repeater sites (not included in our analysis)

## Slide 11: Approaches to licensing
There are three levels of licensing that can be considered for DTT:
  Digital channels (i.e. bits in a MUX)
  MUX (i.e. spectrum)
  Transmission (i.e. transmission sites)
International experience suggests there are two approaches that can be used:
  Combined licensing – broadcasters are licensed to provide programme services and to establish and operate the MUXs to deliver those services. Under this option, broadcast and transmission licences are assigned to individual broadcasters
  Separate licensing – one or more MUX operators are established and licensed to operate the DTT network, leasing capacity to broadcasters. Under this option, DTT frequencies would be assigned to the MUX operator(s), and broadcasters would be allocated a broadcasting licence

## Slide 12: Pros & Cons to the Approaches to licensing
Approach | Pros | Cons
Separate licensing | A MUX operator would be independent from existing broadcasters and would allocate capacity on commercial terms | Independent operator might fail to agree commercial terms with broadcasters for carriage of existing programmes, hampering development of the platform and requiring regulatory intervention
Combined licensing | Existing broadcasters are best placed to define infrastructure roll-out requirements based on their own business case | Possible risk of duplication of infrastructure (unless broadcasters enter into commercial sharing arrangements) and/or over-investment in infrastructure, hampering content investment

## Slide 13: Technology issues
Issues: DVB-T versus DVB-T2 and MPEG-2 versus MPEG-4
Use of MPEG-4 with DVB-T2 increases the number of programmes per MUX
Choice of MPEG-4 also offers better picture quality
Typical net bit rate of a DVB-T MUX is around 24 Mbit/s, DVB-T2 gives around 35 Mbit/s
  Typical data requirements per channel: SD needs 3Mbps, HD needs 8Mbps
 | DVB-T | DVB-T | DVB-T2 | DVB-T2
 | SD | HD | SD | HD
MPEG-2 | 6 | 2 | 10 | 2
MPEG-4 | 16 | 3 | 20 | 4
Number of Digital channels per MUX for DVB-T and DVB-T2

## Slide 14: DVB-T2 is the choice
  A number of regulators have mandated use of MPEG-4 for national DTT implementations
  Countries implementing DVB-T2: UK, Finland, Sweden, Italy, South Africa and Sri Lanka
Benefits of deploying DVB-T2 compared to DVB-T include:
    an estimated 30% higher transmission capacity (using 256-QAM), offering more channel space (e.g. at least 4 HD channels per MUX)
    improved SFN performance
    greater transmission robustness
    improved transmission for portable reception
UAE therefore decided to mandate DVB-T2 with MPEG-4
Harmonization of receiver specification is also important
Receiver standard should also include requirements for conditional access, to enable both paid and free-to-air content to be provided over the platform
Notes: Technology mandate is required so that national MUX can be planned and same receivers can be used

## Slide 15: Technology developments
  Mobile TV: DVB-H is not successful. Mobile reception is possible with DVB-T and DVB-T2
  Hybrid TV: Hybrid TV is an extension of IPTV, bringing IPTV and broadcast TV together in the same device, enabling internet TV and other Internet services to be available via a TV set (typically using a hybrid box)
  3D TV: Developing and might become successful for certain content, e.g. sports or films
  Interactive TV: requires a return path for full interactivity, which is not specified in the DVB-T standard

## Slide 16: Model & Scenario Building
One independent MUX operator will operate three MUXes in an efficient manner
Channel capacity will be sold to broadcasters on a commercial basis
Each of the three broadcasters will operate one MUX
Existing analogue terrestrial channels will be aired, new channels either created, licensed or re-sold
Separate advertising streams will be sent on the DTT platform to allow for localised messages
MODEL 1
MODEL 2
SCENARIO BUILDING:
Different scenarios were created for only Free to Air (FTA), combination of FTA and Pay TV, SD only, SD+HD, growth of IPTV, changes in satellite TV, cable TV, etc and the impact on business model and spectrum

## Slide 17: Business forecasts under different scenarios
  IPTV platform will become the dominant form of reception by 2020, reaching 37% market share of all TV households
  Market share of satellite declines from 61% in 2010 to 47% by the end of 2020 due to competition from other platforms
  DTT market is expected grow from 34,000 households today to 162,000 households, corresponding to a 10% market share by 2020
  Portable users (both FTA and pay TV) to reach 24,000 by 2020
  DTT will enable broadcasters to create a national UAE TV market for advertisers to air, targeted adverts to the UAE population increasing advertising revenues for broadcasters
  The MUX operator will generate revenues from broadcasters and programme producers who buy channel capacity from the MUX
  The MUX operator may get 30% premium based on benchmarking
  Forecasts for OPEX, programming costs, NPV and FCF was also generated

## Slide 18: Licensing approach
  Transmission Service Licenses be awarded either to broadcasters (if a combined licensing approach is followed) or to a separate MUX operator (if a separate licensing approach is followed)
  Time limited licence e.g. 10 year duration
  Must carry obligations
  Coverage obligations
  Use it or Loose it clause
  Minimum standard to start is DVB-T2 with MPEG-4
  Number of programmes that each MUX should carry be left to the industry (MUX operator and broadcaster) to define

## Slide 19: Digital Switch Over Plan
  UAE issued the DSO Plan in Dec 2009
  The Plan provides general guidelines and time frame for digital TV switchover process
  Plan consists of 4 main phases and proposes dates for the major milestones
  All the dates are tentative and depend on:
    Switchover plans adopted by other GCC Administrations (interference issues).
    Availability of sufficient budgets with the existing operators to switchover.
    Readiness of the general public for adopting digital TV.
  The GCC Ministerial Committee agreed on DSO date as Dec 2013 except Oman which is Dec 2015
Ref: www.tra.gov.ae/spectrum-policies-regulations.php

## Slide 20: Thank you
My Contact:
Hasan Sharif
Senior Manager Spectrum Strategy
E-mail: hasan.sharif@tra.gov.ae
Broadcasting Section:
Muhammad Imran Gill
Senior Engineer Broadcasting
E-mail: imran.gill@tra.gov.ae
Broadcasting Section:
Mohamed Saad Al Marzouqi
Senior Engineer Broadcasting
E-mail: mohamed.saad@tra.gov.ae
Address:
Spectrum & International Affairs
TRA, PO Box 26662, Abu Dhabi, UAE
Web: www.tra.gov.ae