FASCICLE 1

NEW TECHNOLOGIES SUPPORTING

NEW NETWORKS

The mention of specific companies or products does not imply any endorsement or recommendation by the ITU.

TABLE OF CONTENTS

## Chapter

- INTRODUCTION		23

1.1	General			23

1.2	Structure of Fascicle 1		23

2.	NEW TRANSPORT MEDIA TECHNOLOGIES		25

2.1	Optical fibres		25

2.1.1 	Transmission Properties		25

2.1.1.1	Attenuation		26

2.1.1.2	Chromatic Dispersion		26

2.1.1.3	Cut-off Wavelength		26

2.1.1.4	Polarisation Mode Dispersion		27

2.1.2	Fibre Types		28

2.1.3	Optical Fibre Implementation		29

2.1.3.1	Fibre Protection		30

2.1.3.2	Installation Procedures		31

2.1.3.3	Splicing		31

2.1.4	Protection of Optical Fibre Rings		32

2.1.4.1	Introduction		32

2.1.4.2	Network Survivability		32

2.1.4.2.1  SNC-P/I (Sub-network Connection Protection with
				           Inherent monitoring)		32

        - SNC-P/N (Sub-network Connection Protection with
Non instrusive Monitoring)		33

        - MS Linear Trail Protection		33

        - MS-SPRING (Multiplex Section Shared Protected
Ring)		33

        - Restoration		34

2.1.4.3	Selection Criteria to Chose Restoration or Protection		34

2.1.4.4	Conclusions		35

2.1.4.5	ITU-T References		35

2.1.5	Abbreviations		36

2.2	DIGITAL RADIO-RELAY SYSTEMS		36

### 2.2.1	General		36

2.2.2	New Digital Microwave (Point-to Point) Radio Technologies		38

2.2.3	A Modern SDH System Utilising New Technologies		44

2.2.4	Multiple Access Radio Systems		45

2.2.4.1	System Architecture		46

2.2.5	Digital Radio Networks		55

2.2.6	ITU Publications 		56

2.2.7	Abbreviations		57

2.3	MOBILE COMMUNICATION SYSTEMS		59

2.3.1	Introduction		59

2.3.2	Spectrum		60

2.3.3	Terrestrial Systems		61

2.3.3.1	Analogue cellular technologies		62

2.3.3.2	Second Generation Systems		64

2.3.3.2.1  Digital Cellular Mobile Networks		68

2.3.3.2.1.1 Global System for Mobile Communications/
						                  Digital Cellular System 1800 
						                   (GSM/DCS1800)		68

2.3.3.2.1.2 Interim Standard (IS-54)		69

2.3.3.2.1.3 Interim Standard IS-95		70

2.3.3.2.1.4 Personal Digital Cellular (PDC)		73

2.3.3.3	Cordless Telephony (CT)		74

2.3.3.4	Private Mobile Radiocommunications (PMR)		75

2.3.3.5	Third Generation IMT – 2000		78

2.3.3.6	The Use of Satellite Systems		78

2.3.4	Abbreviations		79

2.4	SATELLITE SYSTEMS 		82

2.4.1	GSO Satellites 		83

2.4.1.1	Fixed GSO Satellite Systems		84

2.4.1.2	Digital Circuit Multiplication Equipment		85

2.4.1.3	High-capacity International Satellite Telephony and
Data Systems		88

      - Low to Medium-capacity Regional and DOMSAT Systems		91

2.4.1.5	VSAT Systems		99

2.4.1.6	Transportable DSNG TV Earth Station Transmission System		101

2.4.2	Technology for Mobile GSO Satellite System		103

2.4.3	Non-GSO Satellite Systems		103

2.4.3.1	Systems Description		105

2.4.4	Global Mobile Personal Communications by satellite		105

2.4.5	Global Satellite Positioning Systems		106

2.4.6	ITU-R Publications		106

2.4.7	Abbreviations		106

Annexes	A – VSAT System		109

B – The Inmarsat System		113

C – The Globalstar System		116

D – The ICO System		123

E – SkyBridge - Global Multimedia Access		132

F – The Teledesic System		140

G – The Final Analysis System		144

3.	DIGITAL SWITCHING SYSTEMS 		146

3.1	Introduction		146

3.1.1	Concepts		146

3.1.2	Switching Principles		148

3.1.3	References		149

3.2	Channel switching		149

3.2.1	Connection phases		150

3.2.2	Structure of a switching system		151

3.2.3	Task requirements of the function unit ‘switching’
		of a switching system		152

3.2.4	Switching matrix		153

3.2.5	Control of switching devices		161

3.2.6	References		162

3.3	Message switching		162

3.3.1	Packet switching		163

3.3.2	Message switching		165

3.3.3	ATM switching		165

3.3.4	Virtual connections		166

3.3.5	Switching and routing		168

3.3.6	References		168

3.4	Telephone switching technology		169

3.4.1	Local network		170

3.4.2	Long haul network		170

3.5	Connectionless messages transfer		171

3.5.1	Principles		171

3.5.2	Individual techniques		172

3.6	Abbreviations		173

4.	NEW SIGNALLING SYSTEMS AND SS NO. 7		174

4.1	Introduction		174

4.2	Signalling System No7 (SS7)		174

4.2.1	Message Transfer Part (MTP)		175

4.2.1.1	Introduction		175

4.2.1.2	Description		175

4.2.1.3	Future developments		178

4.2.2	Signalling Connection Control Part (SCCP)		178

4.2.2.1	Introduction		178

4.2.2.2	Description		178

4.2.2.3	Future developments		181

4.2.3	Transaction Capabilities (TC)		181

4.2.3.1	Introduction		181

4.2.3.2	Description		181

4.2.3.3	Future developments		182

4.2.3.4	Road map		183

4.2.4	ISDN User Part (ISUP)		183

4.2.4.1	Introduction		183

4.2.4.2	Description		183

4.2.4.2.1  Call identification and routing		183

4.2.4.2.2  ISUP syntax		184

4.2.4.2.3  ISUP features		184

4.2.4.2.3.1 Basic services		184

4.2.4.2.3.2 Simple segmentation		184

4.2.4.2.3.3 Compatibility		184

4.2.4.2.3.4 Application transport mechanism (APM)	185

4.2.4.2.3.5 Supplementary services		185

4.2.4.3	Future developments		185

4.2.4.4	Road-map (Q.761 to Q.764 and Q.730 series)		186

4.2.5	Intelligent Network Application Part (INAP)		186

4.2.5.1	Introduction		186

4.2.5.2	Description		186

4.2.5.3	Future developments		188

4.2.5.4	Road-Map		188

4.3	Digital Subscriber Signalling System 1 (DSS1)		188

4.3.1	Introduction		188

4.3.2	Description		189

4.3.2.1	Call control		189

4.3.2.1.1  Protocol design		189

4.3.2.1.2  Control of circuit-switched calls		190

4.3.2.1.3  Control of packet-switched calls		190

4.3.2.2	Control of supplementary services		190

4.3.2.3	Future developments		191

4.4.	Broadband Signalling		191

4.4.1	Low layers supporting B-ISDN signalling		191

4.4.2	Broadband ISDN User Part (B-ISUP)		193

4.4.2.1	Introduction		193

4.4.2.2	B-ISUP signalling protocols		193

4.4.2.2.1  Point-to-point Switched Virtual Channels		193

4.4.2.2.2  Signalling of the ATM Transfer Capabilities and
					  associated traffic parameters		194

4.4.2.3	Negotiation of traffic parameters		194

4.4.2.4.	Modification of traffic parameters		195

4.4.2.5	QoS class indication and support of individual
				QoS parameters		195

4.4.2.6	Point-to-multipoint SVCs		195

4.4.2.7	Supplementary services		196

4.4.2.8	ITU-T Recommendations		197

4.4.3	Digital Signalling System Number Two (DSS2)		198

4.4.3.1	Introduction		198

4.4.3.2	DSS2 signalling protocols		198

4.4.3.2.1  Point-to-point ATM switched virtual channels
					  (Rec. Q.2931)		198

4.4.3.2.2  Point-to-point ATM switched virtual paths
					  (Rec. Q.2934)		199

4.4.3.2.3  Signalling of ATM traffic capabilities (Rec. Q.2961)	199

4.4.3.2.4  Negotiation of ATM traffic parameters 
					  (Rec. Q.2962)		199

4.4.3.2.5  Modification of ATM traffic parameters
					  (Rec. Q.2963)		199

4.4.3.2.6  Signalling of Quality of Service (QoS)
					  characteristics (Rec. Q.2965)		199

4.4.3.2.7	  Point-to-multipoint Switched Virtual Channels
					  (Rec. Q.2971)		200

4.4.3.2.8  Generic identifier transport (Rec. Q.2941)		200

4.4.3.2.9	  Supplementary services (Q.295x series)		200

4.4.3.2.10 Generic functional protocol (Rec. Q.2932.1)		201

4.4.3.3	ITU-T Recommendations		202

4.5	Abbreviations		203

Annex A:	Other ATM Signalling Protocols		206

Annex B:	DSS2 and the ATM Forum UNI Signalling Specification		207

# 5.	SYNCRONIZATION TECHNIQUES AND METHODS		209

## 5.1	Introduction		209

- Synchronization of the transmission systems		210

5.2.1	The clock signal extraction from binary data stream		210

5.2.2	Point-to-point synchronization		212

- PLL based technique		214

5.3.1	Slave clock disciplining in discrete time		214

5.3.2	Oscillator disciplining in continuous time		215

5.4	Timing correction		215

5.4.1	Error correction in discrete time domain		216

5.4.2	Error correction in frequency domain		216

5.4.3	Error correction in both time and frequency domains		217

- Networks synchronization		218

5.5.1	Synchronization of telephone exchanges in PSTN		218

5.5.2	Dynamics of the ITU-T activity in synchronization aspects of 
	communication		220

  - Synchronization in ATM		225

  - References		226

  - Abbreviations		227

6.	PLESIOCHRONOUS DIGITAL HIERARCHY (PHD)		228

- DIGITAL TRANSMISSIONS		228

6.1.1	Principles		228

6.1.2	Standards		228

6.1.3	Implementation		229

6.2	Synchronous Digital Hierarchy (SDH)		230

6.2.1	Principles		230

6.2.2	Standards		231

6.2.3	Implementation		234

# Dense Wavelength Division Multiplex (WDM)		237

6.3.1	Principles		237

6.3.2	Standards		238

6.3.3	Implementation		240

  - Digital Subscriber Lines (xDSL)		243

6.4.1	Subscriber Loops		243

6.4.2	Subscriber Line Systems		245

6.4.3	ADSL		247

6.4.4	HDSL		251

6.4.5	VDSL		253

6.4.6	Network Examples		255

6.4.7	ITU-T Recommendations		257

6.4.8	Outlook		258

6.4.9	Literature		258

6.5	Abbreviations		259

7.	ATM TECHNOLOGY		261

## 7.1	Introduction		261

## Virtual Connections – Virtual Channel and Virtual Path		266

## 7.3	ATM Transport Network Layering – General Concept		267

## 7.4	ATM Switching of VPs and VCs		269

## 7.5	ATM Cell Format		270

## 7.6	The B-ISDN Protocol Reference Model		273

### 7.6.1	Functions of the individual layers of the B-ISDN PRM		274

### 7.6.2	Physical Layer		275

### 7.6.3	The ATM Layer		275

### 7.6.4	The ATM Adaptation Layer		276

## 7.7	Operation and maintenance		280

7.7.1	OAM principles		280

7.7.2	Oam levels in the B-ISDN		281

7.7.3	F4(F5) flow mechanism		281

7.8	Signalling in the ATM Network		282

7.8.1	Capabilities to control ATM virtual channel connections and virtual path
connections for information transfer		282

7.8.2	Capability to support multiparty and multiconnection calls		283

7.8.3	Others		283

7.8.4	Signalling transport function		284

7.8.5	Signalling Protocols		284

7.9	Traffic management		284

7.9.1	ATM transfer capabilities (ATC)		287

7.9.2	ATM Forum service categories		289

7.10	References			291

7.11	Abbreviations		292

CHAPTER 1

1.	INTRODUCTION

1.1 	GENERAL

Extensive demand for voice and data communication is offering a major opportunity for telecommunication operators. Demand for broadband services, Internet access with the need for high speed data transmission, Video on Demand etc. require significantly increasing capacities in the network, challenging operators of fixed and mobile networks to deploy enhancements to their infrastructures quickly enough to respond for those demands. In addition, operators of narrowband wireless local loop and cellular networks require cost-effective transmission feeders to connect their base stations. A powerful infrastructure with appropriate transmission media will enable operators to be prepared for emerging new trends in networks and services. In many cases, the telecommunication infrastructure consists of a mix of different technologies for the successful realization of physical and logical networks.

Optical fibre is recognized as the superior transmission media and consequently has already been in use for a number of years. It supports the development of a new digital hierarchy e.g. the Synchronous Digital Hierarchy, SDH. The global demand for optical fibre cables is expected to grow at between 15 to 20% per year over the coming years. Thirty six million fibre/ kilometres were installed in 1997.  Optical fibre deployment started in long distance networks, but the market for optical cables in the local telephone, cable TV and data communication applications continues to grow, more and more rapidly. Optical fibre cables are installed by either burial (directly in underground ducts) or on poles. The new developments in the field of the Wavelength Division Multiplexing - WDM, have emphasized the role of using optical fibres over long time periods, and demonstrate the possibility of further exploiting the existing fibre optical networks. Thanks to the new techniques, such as optical amplifiers and Dense Wavelength Division Multiplexing – DWDM, the cost of the network infrastructure is significantly cheaper than in the past.

New optoelectronic devices, studied in this Fascicle, will make it possible to build optical networks with high traffic capacities operating at high bit rates (several hundred Gbit/s to Terabit/s).

However, great progress has also been made in the development of radio technologies, specially, in satellite and cellular technologies, changing dramatically the fields of telecommunication development, universal access and user mobility. In order to facilitate implementation of these different telecommunication technologies the ITU has issued different publications elaborating these matters. This Fascicle, which is a part of the Handbook “New Technologies and New Services” has such a role.

1.2 	Structure of Fascicle 1

Fascicle 1 is divided in 7 Chapters with this Introduction as Chapter 1.

Each Chapter is self-contained (apart from Chapter 2 where each sub-chapter is self-contained) in order to simplify the updating of the text.

Chapter 2, New transport media technologies, is divided in four Subchapters: Optical Fibres, Radio-Relay Systems, Mobile Communication Systems, and Satellite Systems.

The first Subchapter, Optical Fibres, deals with the main considerations when deploying optical fibres, discussing transmission properties (e.g. Attenuation, Chromatic dispersion, and polarization), fibre types, optical fibre implementation, and protection of optical fibre rings.

Digital Radio-relay Systems, as Subchapter 2, deals with developments in digital microwave technologies, multiple access radio systems, and digital radio networks.

The third Subchapter addresses Mobile Communications Systems including spectrum allocation, existing analogue cellular systems, and the various digital cellular systems.  Also discussed are cordless telephony, and the use of satellite systems. The subject of third generation mobile systems is primarily addressed in Fascicle 2.

The fourth and final  Subchapter, Satellite Systems, discusses the satellite technologies as a special case of radio technology. Satellite systems are similar to radio systems, the only real difference being that the intermediate link station is in orbit. Satellites used for telecommunications purposes are placed in geostationary, medium earth and low earth orbits. The development of global satellite based personal communication systems -  GMPCS, is addressing a new market, which has not been exploited by costly conventional mobile satellite systems. The new satellite techniques, such as VSAT, DAMA, TDMA, DCME, are discussed also. As examples, Annexes introduce global satellite systems such as  Globstar, ICO, SkyBridge, Teledesic and Final Analysis.

Chapter 3, Digital Switching Systems, deals with technologies for circuit and packet switching, and with SPC switching system organization. The development of SPC technology has made it possible to design nodes with extensive functionality to carry different services. These capabilities are called “network intelligence” and are the subject of this subchapter. New switching procedures, such as ATM and optical switching, are discussed here also.

Chapter 4 studies New signalling Systems and SS No 7 and is composed of four Subchapters. The Introduction highlights the importance of new signalling systems for network evolution and new services.

Subchapter 2 deals with Signalling System No 7 with details on the Message Transfer Part (MTP), Signalling Connection Control Part (SCCP), Transaction Capabilities (TC), ISDN User Part (ISUP), and the Intelligent Network Application Part (INAP).

Subchapter 3 deals with Digital Subscriber Signalling System 1 (DSS1).

Subchapter 4 evaluates Broadband signalling explaining User Network Interface (UNI), Broadband ISDN user Part (B-ISDN), Digital Signalling System Number 2 (DSS2) and relevant ITU-T Recommendations. Annexes deal with Signalling functions, Other ATM Signalling Protocols, and DSS2 and the ATM Forum UNI signalling specifications.

Chapter 5 deals with Synchronization Techniques and Methods with Synchronization of the transmission systems, Phased Locked Loop, Timing correction, Network synchronization, and Synchronization in ATM are elaborated in separate Subchapters.

Chapter 6 deals with transmission technology PDH, SDH, DWDM and xDSL. The Chapter introduces Synchronous Digital Hierarchy, SDH, explaining a SDH frame structure, multiplexing scheme, and SDH management. DWDM, as a new technology offers high transmission rates on fibres and capacity can be increased without laying new cables. In addition Chapter 6  also deals with the new transmission technology for upgrading cooper wire using - Digital Subscriber Line transmission techniques. A number of new technologies, classed as –‘xDSL’ technologies, offer new approaches to use the existing local networks for higher bit rate services.

Chapter 7 deals with ATM technology. ATM frame structure, multiplexing, protocols and management are addressed in detail.

The references listed in the chapters should enable readers  to get more information on the subjects.

The mention of specific companies or products in this Fascicle does not imply any endorsement or recommendation by the ITU.

# Comments

I would like to delete this paragraph.