| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On Next Generation Networks |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2001-2004 | FGNGN-ID-000102R1 |
|  | Original: English |
|  |  | Geneva, 19 - 23 July 2004 |
| INPUT DOCUMENT |
| Source: | WG7 Technical Leaders |
| Title: | Draft Problem Statement |

# Introduction

This Problem Statement  and Issues document is the first deliverable from WG7 on  “Future Packet Based Bearer Network”.  Subsequent documents will further identify the requirements for architectures (and protocols), which will fill the gaps, if any, which are identified with current architectures and systems.

# Some problems with current Packet Based Networks (PBNs)

Network operators are now facing a major turning point in the evolution of their many and various service-dedicated network platforms (such as PSTN, ATM, FR, Internet backbone, IP VPN, etc.) towards a simpler, more converged “Connectionless” and “Connection-Oriented” common service networks.  Such a network must be robust, carrier-scale, and flexible, while at the same time optimizing both Capital Expenditures (CAPEX) and Operational Expenditures (OPEX).

Definitions

- cl-ps   -- connectionless packet switched (e.g., the IP transport network)

- co-ps  -- connection oriented packet switched (e.g., MPLS as a server)

- co-cs – connection oriented circuit switched (e.g., the traditional TDM network)

- Network Mode -- One of cl-ps, co-ps, or co-cs

Issues Facing Network Operators

## 1. Support for different traffic types

Network operators require a scalable QoS architecture that provides for different traffic types and their associated service differentiation.  Further, in order to provide such QoS based services, a network must provide a mechanism (virtual or otherwise), which provides for the logical separation of different traffic classes associated with different traffic.

2.  Protecting the control and management planes from user-plane traffic

Network operators require that their control and management infrastructure be protected from user traffic. Thus, a network architecture must provide the capability to separate the various planes in a particular mode (e.g., cl-ps, co-ps, or co-cs).  An example is the separation of data plane from control plane in the SS7 architecture.  Any solution should also provide the capability to separate network modes.

## 3.	Guaranteeing and charging for QoS

As broadband access penetration increases and new applications emerge, the question of how to deliver QoS based services, along with the mechanisms for charging these services has become increasingly important.  To this end (and at the very least), network operators will want to:

- Control load distribution to avoid focused overload in the core.

- Support hard guarantees to customers.

- Support pricing of different classes.

Hence any QoS architecture must provide for these functions. It is important to note that in general, the QoS functions described above are characterized by their end-to-end behaviour.  However, while QoS architectures such as the IETF’s Differentiated Services (DS) architecture [RFC2475] define an end-to-end QoS model, the model itself is described in terms of Per-Hop Behaviours (PHBs).  As a result, network operators may feel that the DS model is insufficient to provide the required end-to-end QoS guarantees.

## Example: The need to ensure emergency calls get through

Network operators are required to ensure that emergency (e.g., 112) calls are not dropped under congestion conditions.  As a result, many operators feel that classification of QoS at the packet level such as provided by the Differential Services Architecture is insufficient (see the above discussion on PHP). The main concerns here related the lack of direct support in the DS architecture to distinguish based on ‘urgency’ (defined as how fast a packet must get processed in the up-state to meet the applications QoS requirements) or ‘importance’ (defined as the survivability of a given packet compared to all other packets when the network has insufficient resources to service all the traffic, irrespective of QoS classifications).

## 5. Provide adequate security

Network operators require that their infrastructures are as secure as possible. However, architectures that carry control and management plane information in-band (i.e., over the user-plane network, such as the IP network) can offer greater potential for attacks against an operator’s network infrastructures. Such attacks include classical security attacks (hijacking, privacy, non-repudiation, etc), as well as attacks on network availability (e.g., DoS attacks).

## 6.  Identification, location, and remediation of faults (OAM)

Clearly, network operators will require the ability to rapidly detect, locate, and remediate network faults (preferably proactively, i.e., before the customer notices).  However, certain architectural choices can make such rapid fault remediation difficult or impossible. For example, consider the case of IP networks, where management information is carried in-band. In this case, it can be difficult or impossible to rapidly locate, diagnose, and repair certain classes of faults (in particular, those faults which have the property that the fault itself prevents fault detection, location, or repair).

References

[RFC2475]      Blake, S., Black, D., Carlson, M., Davies, E., Wang, Z.

and W. Weiss, "An Architecture for Differentiated

Services", RFC 2475, December 1998.

# Footnotes

Please see FGNGN-ID-000AB.doc (tbd) for a discussion of traffic types.

See section 5 additional discussion of security.