| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On Next Generation Networks |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2001-2004 | FGNGN-OD-00025 |
|  | English only |
| WG(s): | WG3 | 27 September - 01 October 2004 |
| OUTPUT DOCUMENT |
| Source: | WG3 Editor |
| Title: | Revised version of Draft TR-NGN.NHNperf. |

This document contains the revised version of TR-NGN.NHNperf. as the result of the 3rd FG NGN meeting.

Followings are the main revisions;

- Addition of new section 12.2 for the mapping between Y.1541 QoS classes and TS 23-107 (3GPP UMTS) QoS classes.

- Addition of new section 11 to describe generic approach of performance measurement.

------------------

TR-NGN.NHNperf.

< Network performance of non-homogeneous networks in NGN >

_______________________________________

CONTENTS

Page

1	Scope	3

2	References	3

3	Abbreviations	4

4	NGN Transport Network components	5

5	Measurement points and measurable sections	6

6.	Vertical layered model of the NGN transport network	8

7.	Horizontal reference configuration of the NGN transport network	9

8	Reference events	10

9	Performance objectives	10

10	Allocation principles	10

11	Performance measurement	10

11.1 Intrusive performance measurement	10

11.2 Non-intrusive performance measurement	11

12	Relationships between the homogeneous network performance classes	12

12.1 ATM network performance support of IP QoS	12

12.2 IP-based network to UMTS	12

12.3 Frame Relay network performance and ATM network performance	13

12.4 ATM network performance and STM network performance	13

12.5 IP QoS and MPLS QoS	13

12.6 Ethernet network performance and IP QoS	13

13. 	NGN network performance classes	14

< Network performance of non-homogeneous networks in NGN >

Summary

<Mandatory material>

Keywords

<Optional>

Introduction

<Optional – This clause should appear only if it contains information different from Scope and Summary>

# 1	Scope

This Draft has been developed to:

- describe performance aspects of the transport layer on Next Generation Network (NGN)

- identify general performance principles and frameworks that can be applied to the development of specific performance descriptions supporting evolution of the NGN (e.g., methods and methodologies for performance specification, allocation, and validation);

- define the relationship among individual networks’ performance which may be observed at physical interfaces between a specific network and associated terminal equipment, and at physical interfaces between specific networks.

# 2	References

The following ITU-T Recommendations contain provisions which, through reference in this text, constitute provisions of this Draft. At the time of publication, the editions indicated were valid. All Recommendations are subject to revision; all users of this Draft are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations listed below. A list of the currently valid ITU-T Recommendations is regularly published.

[1]	Rec. E.800	Terms and definitions related to quality of service and network performance including dependability

[2]	Rec. I.350		General aspects of quality of service and network performance in digital networks, including ISDNs

[3]	Rec. I.356		B-ISDN ATM layer cell transfer performance

[4]	Rec. I.610		B-ISDN operation and maintenance principles and functions

[5]	Rec. O.181	Equipment to assess error performance on STM-N interfaces

[6]	Rec. O.191	Equipment to measure the cell transfer performance of ATM connections

[7]	Rec. O.211	Test and measurement equipment to perform tests at the IP layer

[8]	Rec. X.200	Information technology - Open Systems Interconnection - Basic Reference Model: The basic model

[9]	Rec.Y.1540	Internet protocol data communication service - IP packet transfer and availability performance parameters

[10]	Rec.Y.1541	Network performance objectives for IP-based services

[11]	Rec. Y.1560	Parameters for TCP connection performance in the presence of middleboxes

[12]	Rec. Y.1561	Performance and Availability Parameters for MPLS Networks

[13]	Rec. Y.1711	Operation & Maintenance mechanism for MPLS networks

[14]	Rec. Y.1730 	Requirements for OAM functions in Ethernet-based networks and Ethernet services

[15]	Draft Rec. Y.NGN-GRM	General Reference Model for NGN

[15]	Rec. Y.2011	General principles and general reference Model for NGNs

[16]	Draft TR-NGN.QoS	General Aspects of QoS/NP on NGN

[17]	IETF RFC 2011	SNMPv2 Management Information Base for the Internet Protocol using SMIv2

# 3	Abbreviations

This Draft uses the following abbreviations:

ATM		Asynchronous Transfer Mode

B-ISDN	Broadband Integrated Services Digital Network

BRM		Basic Reference Model

CER		Cell Error Ratio

CMR		Cell Misinsertion Rate

CLR		Cell Loss Ratio

IETF		Internet Engineering Task Force

IP		Internet Protocol

IPDV		IP Packet Delay Variation

IPER		IP Packet Error Ratio

IPLR		IP Packet Loss Ratio

IPTD		IP Packet Transfer Delay

MIB		Management Information Base

MP              Measurement Point

MPE	Measurement Point E

MPN	Measurement Point N

MPLS		Multi-Protocol Label Switching

NG		Network Group

NGN		Next Generation Network

NP		Network Performance

OAM		Operation, Administration and Maintenance

OSI		Open System Interconnection

PDU		Protocol Data Unit

QoS		Quality of Service

SDH		Synchronous Digital Hierarchy

SDU		Service Data Unit

SMI		Structure of Management Information

SNMP		Simple Network Management Protocol

SPR		Spurious Packet Rate

TCP		Transmission Control Protocol

TE		Terminal Equipment

UDP		User Datagram Protocol

UMTS		Universal Mobile Telecommunication System

3GPP		Third Generation Partnership Project

# 4	NGN Transport Network components

4.1 NGN Transport Network: NGN is a packet-based network able to provide services including Telecommunication Services and able to make use of multiple broadband, QoS-enabled transport technologies and in which service-related functions are independent from underlying transport-related technologies. It offers unrestricted access by users to different service providers. It supports generalized mobility which will allow consistent and ubiquitous provision of services to users.

In this Draft, NGN transport network is defined as a segment that connects together terminal equipments and allows service functions that are mounted on different terminal equipments to communicate with each other. It consists of various networks to support the transport layer functions of NGN layered model and has user data transport functions, control functions and management functions.

4.2 Terminal Equipment (TE): Equipment which allows users to gain access to the NGN through networks, used to describe the terminal device employed by the service application.

4.3 Network: A segment that has their own specific protocols, which provides communication between two or more defined points to facilitate NGN service between them. Each can be operated by different providers and generally interconnected as described in Figure 4.

4.4 Interface: A shared boundary between networks and between TE and network. An interface supports various characteristics pertaining to the functions, physical interconnections, signal exchanges and other characteristics as appropriate.

Figure 1/TR-NGN.NHNperf. - NGN Transport Network Components

# 5	Measurement points and measurable sections

The end points of interest for the end-to-end network performance of NGN transport network segment will be located between the TEs. For the purpose of practical measurement, the physical interface which is connected to transport function of the TE may be used as the measurement point (MP) for network performance. The ideal measurement point is an issue for further study.

Measurement point (MP): The boundary between a TE and a network or between networks at which performance reference events can be observed and measured. A network or a set of networks is measurable if it is bounded by a set of measurement points.

There are two types of MPs. MPEs are measurement points near network interface and thus are at terminal equipment. MPNs are measurement points established at the network node before and after the link crosses the network.

Measurement point E (MPE): A measurement point E is located at an interface that separates a TE from an attached network component.

Measurement point N (MPN): A measurement point N is located at an interface between networks. The exact location of the MPN depends on the network type and is specified, for each network type, in the associated Recommendation (for example, I.356 for ATM, I.353 for ISDN, Y.1540 for IP, Y.1561 for MPLS, etc.)

Figure 2/TR-NGN.NHNperf. – Measurement Point E and N

In this Draft, the following sections are measurable.

Basic network portion: Either a TE or a network, which is delimited by two MPs.

The performance of any network is measurable relative to any given unidirectional transfer of a protocol data units (PDU). A PDU is corresponding to a specific protocol format, i.e., the cell for ATM, the packet for IP, the frame for Frame Relay or Ethernet, etc.

The ingress MP is the set of MPs crossed by PDUs from that service as they enter that basic network portion. The egress MP is the set of MPs crossed by PDUs from that service as they leave that basic network portion.

End-to-end NGN transport network: The set of networks that provides the transport of PDUs transmitted between TEs. The MPs that bound the end-to-end NGN transport network are the MPs at the TEs.

The end-to-end NGN transport network performance is measurable relative to any given unidirectional transfer of PDUs. The ingress MP is the set of MPs crossed by PDUs from that service as they enter the end-to-end NGN transport network at the TE (source). The egress MP is the set of MPs crossed by PDUs from that service as they leave the end-to-end NGN transport network at the TE (destination).

Network group (NG): A NG refers to any concatenated subset of NGs together with the entire interface that interconnect them.

The performance of any given NG is measurable relative to any given unidirectional transfer of PDUs. The ingress MP is the set of MPs crossed by PDUs from that service as they enter that NG. The egress MP is the set of MPs crossed by PDUs from that service as they leave that NG.

Figure 3/TR-NGN.NHNperf. – Relationships among measurable sections

Note 1. : The performance of Interworking System is for further study.

Figure 4/TR-NGN.NHNperf. – Pracical measurement points in a NG

# 6.	Vertical layered model of the NGN transport network

Figure 5 shows a relationship between OSI BRM (ITU-T Recommendation X.200) and the layered protocol stack of NGN general reference model (ITU-T Recommendation Y.2011). The NGN transport network consists of many protocols to support a set of transport layer stratum functions of NGN layered model.

In this figure the end of the transport layer stratum protocol stack is denoted by the datum at layer 3 and the beginning of the service layer stratum protocol stack by the datum at layer 4. So, for example, in an IP-based transport network, layer 3 would be the IP layer, and layer 4 would be the TCP or UDP layer. A variety of underlying layers, layer 1 and 2, will exist depending on the underlying technologies used to support IP (e.g. ATM over SDH over Optical, Ethernet over Optical or SDH over Optical, etc.).

(OSI BRM’s view)		   (NGN strata’s view)

Figure 5/TR-NGN.NHNperf. – Generic layered protocol stack architecture

# 7.	Horizontal reference configuration of the NGN transport network

Scenario 1 - Homogeneous protocol on two MPs

The same protocol is used at each end. Network performance between MPs can be evaluated by a protocol-specific performance criterion that has an end-to-end significance, even when different network types are included.

If there isn’t an end-to-end significant protocol between two MPs, scenario 2 on behalf of scenario 1 should be considered.

Figure 6/TR-NGN.NHNperf. - General configuration of homogeneous protocol in MPs

Note – Performance for homogeneous protocols will be outside of the scope of Draft TR-NGN.NHNperf. A main target for this Draft will be cases where heterogeneous protocols are used at the two MPs.

Scenario 2 - Heterogeneous protocols on two MPs

Different protocols are used at each end. These different protocols may interwork by protocol mapping, translation, conversion or encapsulation.

Figure 7/Y.NGN-NHNperf. - General configuration of heterogeneous protocols in MPs

# 8	Reference events

Reference events must be defined for the transfer of user information or control information across the measurement points. The dominant PDU of the NGN are expected to be IP packets, but each network’s unique PDUs create reference events at their MPs.

Two classes of reference events are distinguished: exit events and entry events.

Exit event: An exit event occurs when a unit of user or control information crosses the MP exiting the network component or TE into the attached network component.

Entry event: An entry event occurs when a unit of user or control information crosses the MP entering the network component or TE from the attached network component.

# 9	Performance objectives

Scenario 1 - Homogeneous protocols

The performance objectives and parameters that are specified for a homogeneous network may be applied to support a specific network performance.

Scenario 2 - Heterogeneous protocols

Though performance at each interface is described its own specific parameters, service requirements should be met by some additional functions (for example, performance parameter mapping such like cell loss ratio in ATM network to frame loss ratio in Frame Relay network. One such description is introduced in X.144).

# 10	Allocation principles

This is for further study, but homogeneous portions and the portions entirely within the jurisdiction of a single network provider may be considered.

# 11	Performance measurement

There are two basic approaches to performance measurement defined in ITU-T Recommendation M2301 (for IP performance measurement). These are "intrusive" and "non-intrusive" which equate to the terms "active" and "passive" used by the IETF (formerly, “out-of-service” and “in-service” by ITU-T Recommendation O.181, O.191, etc.).

## 11.1 Intrusive performance measurement

Intrusive performance measurements are made by inserting test PDUs (IP test packet of Recommendation O.211, ATM test cells of Recommendation O.191, STM test signal structure of Recommendation O.181, etc.) interleaved with the normal traffic flows/connections between two MPs. This kind of measurement allows more detailed investigation of specific performance parameters e.g. one-way delay using time stamped PDUs, effect of PDU size and number of PDUs on performance.

It should be noted that intrusive performance measurement causes additional traffic through the network so care must be taken to ensure that the use of this test does not cause congestion and the subsequent loss of customer's PDUs (IP packet, ATM cell, Ethernet Frame, etc.). It is also important that the test is not carried out when customer traffic is so low that the results of the test are invalid.

The test PDU stream and the measurement period should be appropriate to the application service to be supported. The test PDU length and characteristics, and the intervals between measurement periods are separately specified in other Recommendations as follows:

- For IP performance measurement, ITU-T Recommendation O.211 “Test and measurement equipment to perform tests at the IP layer”

- For ATM performance measurement, ITU-T Recommendation O.191 “Equipment to measure the cell transfer performance of ATM connections”

- For STM performance measurement, ITU-T Recommendation O.181 “Equipment to assess error performance on STM-N interfaces”

## 11.2 Non-intrusive performance measurement

The performance can be assessed by interrogating all the network nodes (IP router, ATM switch, and Ethernet switch, etc.) for performance statistics and thus obtaining a real time view of the effect of the network on the traffic passing through that network.

It can also be used for maintenance purposes and/or to check the OAM procedures or MIB monitoring by SNMP applications. This kind of measurement has the advantages of minimizing impact on customer's traffic and testing every route/connection through the network.

Problems on links or network nodes can also be quickly identified. It should be noted, however, that non-intrusive measurements can realistically be done only within one domain or one network that has its own specific protocol since it may be undesirable or impossible for one domain/network to access the network node in another's domain or network.

The details of OAM PDU format, functions and monitoring methods are separately specified in other Recommendations as follows:

- For ATM OAM, ITU-T Recommendation I.610 “B-ISDN operation and maintenance principles and functions”

- For MPLS OAM, ITU-T Recommendation Y.1711 “Operation & Maintenance mechanism for MPLS networks”

- For Ethernet OAM, ITU-T Recommendation Y.1730 “Requirements for OAM functions in Ethernet-based networks and Ethernet services”

- For IP MIB monitoring, IETF RFC 2011 “SNMPv2 Management Information Base for the Internet Protocol using SMIv2”

# 12	Relationships between the homogeneous network performance classes

## 12.1 ATM network performance support of IP QoS

This cluase presents an analysis of mapping IP performance parameters on top of the ATM QoS Class objectives as specified in ITU-T Rec. I.356. The purpose of this analysis is to estimate IP level performance obtained when ATM is used as the underlying transport. Because there are no routers considered in this analysis, the IP performance numbers shown here are the best that can be expected. In scenarios where intermediate routers exist, the IP performance will be worse.

Table 1/TR-NGN.NHNperf. – IP Packet Loss Ratio (IPLR) values corresponding to ATM QoS service classes 1 and 2 (IP packet size 40 bytes; all errored packets are assumed lost)

| ATM QoS Class | Delivered ATM CER | Delivered ATM CLR | Resulting IPLR |
| --- | --- | --- | --- |
| 1 | 4.00 E-06 | 3.00 E-07 | 4.30 E-06 |
| 2 |  | 1.00 E-05 | 1.40 E-05 |

Table 2/TR-NGN.NHNperf. – IP Packet Transfer Delay (IPTD) values for a flow 
over a national portion and an end-to-end flow

| Network Portion | IPTD resulting from ATM QoS Class 1 (no delay from IP routers) |
| --- | --- |
| National Portion | ~27.4 ms |
| End-to-End | 400 ms |

Note that Class 0 and Class 2 mean IPTD cannot be met on the 27 500 km reference connection of I.356.

The value of the Cell Error Ratio (CER) in the ATM classes is 4 × 10(6. If IP packets are long (1500 bytes) and errored cells cause errored IP packets, the value of IP packet error ratio will be about 10(4.

Cell Misinsertion Ratio (CMR) is currently specified as 1/day. The implications of CMR on SPR requires more study.

## 12.2 IP-based network to UMTS

The QoS translator would map Y.1541 class 0 to the UMTS conversational class, selecting the 10-4 value for the SDU error ratio attribute. The UMTS SDU transfer delay value (100 ms maximum) might or might not meet the example objective for the UMTS network portion (50 ms mean), depending on the SDU transfer delay distribution. The UMTS SDU error ratio value (10-4) would meet the Y.1541 IPLR and IPER objectives assumed for the UMTS network portion (5x10-4, 5x10-5), since the former parameter definition combines the Y.1541 packet loss and packet error outcomes. The UMTS conversational class requirement to “preserve time relation (variation) between information entities of the stream” would relate qualitatively to the Y.1541 IPDV objective, but the end-to-end objective would not be assured since the UMTS specification does not currently limit IPDV.

Y.1541 class 1 would be mapped to the UMTS streaming class, again selecting the 10-4 SDU error ratio value. The UMTS SDU transfer delay value (280 ms maximum) might or might not meet the example objective for the UMTS network portion (200 ms mean), depending on the delay distribution. The UMTS SDU error ratio value would meet the example Y.1541 IPLR and IPER objectives as described for class 0 above. The Y.1541 IPDV objective would be addressed qualitatively but without end-to-end assurance as noted above.

Y.1541 classes 2-4 could be mapped to the UMTS interactive class with a 10-4 SDU error ratio. The three Y.1541 classes could be mapped to different UMTS interactive class priority levels to reflect their different IPTD objectives; but these relative priorities would not provide assured quality levels. If more assured IPTD values were required, Y.1541 classes 2-4 could be mapped to the UMTS conversational or streaming class. The SDU transfer delay limit of the UMTS conversational class (100 ms maximum) might or might not meet the example IPTD objective of class 2 (50 ms mean); it would definitely meet the assumed IPTD objectives of classes 3 and 4 (200 ms and 500 ms mean, respectively). Similarly, the SDU transfer delay limit of the UMTS streaming class (280 ms maximum) might or might not meet the assumed IPTD objectives of classes 2 and 3 (50 ms and 200 ms mean respectively), but would definitely meet the assumed IPTD objective of class 4 (500 ms mean).

Y.1541 class 5 would be mapped to the UMTS background class.

The mappings suggested above are probably the most reasonable ones for the stated example, and they could meet the postulated IPLR and IPER requirements for all of theY.1541 classes. The suggested mappings would not meet the end-to-end delay requirements for some classes, and as noted, would place no quantitative bounds on end-to-end IPDV.

For comparability between Y.1541 and TS 23-107 (3GPP), the SDU should be defined to correspond to an IP packet in 3GPP specifications of QoS requirements for IP-based services. An evaluation interval of 1 minute should be used in assessing both mean delay and delay variation. Payload sizes of 160 and 1500 octets should be used in specifying and evaluating performance values.

## 12.3 Frame Relay network performance and ATM network performance

Editor’s Note: Relationship between ITU-T Rec. X.144 and Rec. I.356 will be described.

## 12.4 ATM network performance and STM network performance

Editor’s Note: Relationship between ITU-T Rec. I.356 and Rec. G.829 will be described.

## 12.5 IP QoS and MPLS QoS

This is for further study

## 12.6 Ethernet network performance and IP QoS

This is for further study

# 13. 	NGN network performance classes

This is for further study and will be derived from the performance matrix that is specified in Draft TR-NGN.QoS.

Editor’s Note: There is an opinion that NGN work simply use the Y.1541 classes until a need for a new set of performance objectives/new class is identified, and at that time we can determine where to add the new class.

____________

# Text boxes

TE

Network

Network

Network

Network

Network

Network

Network

TE

TE

TE

TE

: Terminal Equipment

Network

: Network

: Interface

TE

TE

Network

Network

Network

MPE

MPE

MPN

MPN

MPN

MPN

MPE

MPE

Network

TE

Network

Network

TE

The end-to-end NGN transport network

Network Group

Network Group

TE

MPE

ATM Network

IP Network

TE

Higher Layer

ATM

SDH

SDH

ATM

ETH

IP

SDH

ATM

Higher Layer

ETH

IP

ETH

IP

Higher Layer

SDH

ATM

SDH

ATM

Higher Layer

ATM Switch

ATM System

IP router

Interworking System

MPE

MPN

ATM Network Performance

IP Network Performance

TE

TE

(4.a) Conceptual MPs and basic network portions

(4.b) Practical MPs and basic network portions

ATM Network Performance

IP Network Performance

Note 1

Layer 3

Layer 2

Layer 1

Layer 4

Layer 5

Transport layer stratum

Service layer stratum

Layer 6

Layer 7