| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On Next Generation Networks |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2001-2004 | FGNGN-OD-00029 |
|  | Original: English |
| WG(s): | WG 7 | Ottawa, 27 September - 1 October 2004 |
| OUTPUT DOCUMENT |
| Source: | Editors |
| Title: | Draft Requirements Document |

# Introduction

This document specifies high-level requirements of a Future Packet Based Network (FPBN). The document specifies data plan, control plan and management plan requirements.

# Scope

The scope of this document is requirements for architecture of FPBN comprised of transport stratum packet based path layer networks (refer to G.805, G.809 and Y.2011).

# References

# Terms and Definitions

Urgency

Importance

OOB

# Abbreviations

# Requirements

## General requirements

The FPBN:

- Shall provide both connectionless and connection-oriented services for multiple client types. Shall efficiently support p-t-p, mp-t-mp and p-t-mp services.

- Shall support a range of QoS including best effort and guaranteed services

- Should allow smooth migration from current packet networks

- Shall interwork and co-exist with current packet networks

- Shall support arbitrary network topologies and be able to expand bandwidth, topology, number-of-customers and number-of-services incrementally.

- Shall secure, protect and transport customer traffic as appropriate to the requirements of the service.

- Shall detect, and recover from facility and equipment failures and performance degradation.

- Shall offer comprehensive OAM functions for each plane.

- Shall completely secure control and management plane traffic from attack and shall ensure that it remains secure and stable under situations of extreme stress.

- Shall be ‘designed for uncertainty’ and therefore it shall be able to accommodate unforeseen traffic types/vectors.

- Shall offer a strong degree of performance and behavior isolation between different traffic sources and traffic types.

- Shall allow statistical multiplexing for efficiency.

- Shall support Lawful intercept as required.

- Shall be able to monitor the traffic conditions and bill for the service delivered.

- Shall provide the ability to distinguish between Urgency and Importance

- Shall support services that require in-order delivery of packets.

- Shall support out-of-band Control and Management planes.