| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On Next Generation Networks |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2001-2004 | FGNGN-OD-00045 |
|  | English only |
| Group(s): | WG3 | 27 September - 01 October 2004 |
| OUTPUT DOCUMENT |
| Source: | WG3 Editor |
| Title: | Revised version of Draft TR-NGN.QoS |

This document contains the revised version of TR-NGN.QoS as the result of the 3rd FG-NGN meeting.

Followings are the main revisions;

- Addition of some abbreviations in section 3.

- Deletion of Editor’s note in section 4.

- Replacement of definitions for the layered model in section 7.

- Addition of new section 8 to explain the applicability of Application QoS classes.

------------------

TR-NGN.QoS

< General Aspects of Quality of Service and Network Performance in the Next Generation Networks >

_______________________________________

Contents

Page

1	Scope	3

2	References	3

3	Abbreviations	4

4	Description of Quality of Service (QoS), Network Performance (NP) and Quality of Experience (QoE)	5

5	Distinction among QoS, NP and QoE	6

6	Measurability of QoS, NP and QoE parameters values	6

7	Layered Model of QoS and NP for NGN	6

8	Application QoS classes	8

8.1	Classification of Application QoS	8

8.2	Relationship between Application QoS classes and Network QoS classes	9

9	Performance Parameters	9

Appendix I	10

The impact of QoE to clarify NGN QoS	10

I.1. User acceptability for NGN service	10

I.2. Network/service provider’s viewpoint for user acceptability	10

<General Aspects of Quality of Service and Network Performance in the Next Generation Networks>

Summary

<Mandatory material>

Keywords

<Optional>

Introduction

<Optional – This clause should appear only if it contains information different from Scope and Summary>

# 1	Scope

This Draft has been developed to:

- provide descriptions of NGN Quality of Service, Network Performance and Quality of Experience;

- illustrate how the Quality of Service, the Network Performance, and Quality of Experience concepts are applied in NGN environment;

- describe performance aspects of the Next Generation Network (NGN) including performance of service and transport stratum;

- provide a basis for common understanding of performance concepts useful to users and to the industries that compose the NGN (e.g., Fixed & mobile telecommunications, broadcasting, etc.).

- define the application QoS classes of the NGN

# 2	References

The following ITU-T Recommendations contain provisions which, through reference in this text, constitute provisions of this Draft. At the time of publication, the editions indicated were valid. All Recommendations are subject to revision; all users of this Draft are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations listed below. A list of the currently valid ITU-T Recommendations is regularly published.

- Rec. E.800	Terms and definitions related to quality of service and network performance including dependability

- Rec. G.1000	Communications quality of service: A framework and definitions

- Rec. G.1010	End-user multimedia QoS categories

- Rec. I.350		General aspects of quality of service and network performance in digital networks, including ISDNs

- Rec. I.356	B-ISDN ATM layer cell transfer performance

- Rec. X.800	Security Architecture for Open Systems Interconnection for CCITT applications

- Rec. X.805	Security Architecture for systems providing end-to-end communications

- Rec.Y.1540	Internet protocol data communication service - IP packet transfer and availability performance parameters

- Rec.Y.1541	Network performance objectives for IP-based services

- Rec. Y.1560	Parameters for TCP connection performance in the presence of middleboxes

- Rec. Y.1561	Performance and Availability Parameters for MPLS Networks

- Rec. Y.2011	General principles and general reference model for NGNs

# 3	Abbreviations

This Draft uses the following abbreviations:

AN		Access Network

ATM		Asynchronous Transfer Mode

B-ISDN	Broadband Integrated Services Digital Network

CN		Core Network

CPN		Customer Premise Network

FTP		File Transfer Protocol

HTTP		Hyper Text Transfer Protocol

IP		Internet Protocol

ISDN		Integrated Services Digital Network

MP		Measurement Point

MPLS		Multi-Protocol Label Switching

NGN		Next Generation Network

NP		Network Performance

PDH		Plesiochronous Digital Hierarchy

QoE		Quality of Experience

QoS		Quality of Service

RTP		Real-time Transport Protocol

SDH		Synchronous Digital Hierarchy

TCP		Transmission Control Protocol

TE		Terminal Equipment

UDP		User Datagram Protocol

# 4	Description of Quality of Service (QoS), Network Performance (NP) and Quality of Experience (QoE)

QoS is defined in Recommendation E.800 as follows: “Collective effect of service performance which determine the degree of satisfaction of a user of the service”.

The definition of QoS in Recommendation E.800 is a wide one encompassing many areas of work, including subjective user satisfaction. However, within this Draft the aspects of QoS that are covered are restricted to the identification of parameters that can be directly observed and measured at the point at which the service is accessed by the user.

Recommendation I.350 defines Network Performance as the “NP is measured in terms of parameters which are meaningful to the network provider and are used for the purpose of system design, configuration, operation and maintenance. NP is defined independently of terminal performance and user actions”.

QoE is defined as the overall acceptability of an application or service, as perceived subjectively by the end-user. Quality of Experience includes the complete end-to-end system effects (client, terminal, network, services infrastructure, etc). Overall acceptability may be influenced by user expectations and context.

Figure 1 illustrates how the concepts of QoS, NP and QoE are applied in the NGN environment.

- CN : Core Network	- TE : Terminal Equipment

- AN : Access Network 	- CPN : Customer Premise Network

Note: The definitions of each network are based on existing telecommunication terminologies. In order to include the functions for radio communication and broadcasting, those definitions may be changed. This is FFS.

Editor’s Note: User-to-user communication is the basic consideration in this figure. In order to cover the broader view of NGN, Machine-Network interface will be added on the next revision.

Figure 1/ Draft TR-NGN.QoS

General reference configuration for NGN QoS, NP and QoE

# 5	Distinction among QoS, NP and QoE

QoS provides a valuable framework for network provider, but it is not necessarily usable in specifying performance requirements for particular network technologies (i.e. ATM, IP, MPLS, etc.). Similarly, NP ultimately determines the (user observed) QoS, but it does not necessarily describe that quality in a way that is meaningful to users.

QoE is subjective in nature, i.e. depend upon user actions and subjective opinions.

The definition of QoS, NP and QoE should make mapping clear in cases where there is not a simple one-to-one relationship among them.

Table 1 shows some of the characteristics which distinguish QoS, NP and QoE.

Table 1/ Draft TR-NGN.QoS

Distinction between quality of experience, quality of service and network performance

| Quality of Experience | Quality of Service | Network Performance |
| --- | --- | --- |
| User oriented | Provider oriented |
| User behavior attribute | Service attribute | Connection/Flow element attribute |
| Focus on user-expected effects | Focus on user-observable effects | Focus on planning, development (design), operations and maintenance |
| User subject | Between (at) service access points | End-to-end or network elements capabilities |

# 6	Measurability of QoS, NP and QoE parameters values

Due to separating QoS, NP and QoE, a number of general points should be noted when considering the development of parameters;

- the definition of QoS parameters should be clearly based on events and states observable at service access points and independent of the network processes and events which support the service;

- the definition of NP parameters should be clearly based on events and states observable at network element boundaries, e.g. protocol specific interface;

- the definition of QoE parameters are for further study.

# 7	Layered Model of QoS and NP for NGN

Figure 2 illustrates the layered nature of QoS and NP of NGN.

Recommendation Y.2011 describes the layered model of NGN as follows:

NGN service stratum:  That part of the NGN which provides the user functions that transfer service-related data and the functions that control and manage service resources and network services to enable user services and applications. User services may be implemented by a recursion of multiple service layers within the service stratum. The NGN service stratum is concerned with the application and its services to be operated between peer entities. For example, services may be related to voice, data or video applications, arranged separately or in some combination in the case of multimedia applications. From an architectural perspective, each layer in the service stratum is considered to have its own user, control and management planes.

NGN transport stratum:  That part of the NGN which provides the user functions that transfer data and the functions that control and manage transport resources to carry such data between terminating entities. The data so carried may itself be user, control and/or management information. Dynamic or static associations may be established to control and/or manage the information transfer between such entities. An NGN transport stratum is implemented by a recursion of multiple layer networks as described in Recommendations G.805 and G.809. From an architectural perspective, each layer in the transport stratum is considered to have its own user, control and management planes.

Figure 2/ Draft TR-NGN-QoS – Layered model of QoS and NP for NGN

- The transport stratum that provide connection-oriented or connectionless transport supporting the service stratum. This stratum may involve different types of technologies, for example, IP, ATM, Frame Relay, SDH, PDH, ISDN, and leased lines. There may be several layers of protocols and services below the IP layer that is dominant protocol in NGN.

- The service stratum, supported by the transport stratum, that may include, for example, TCP, UDP, FTP, RTP, and HTTP. The service stratum will modify and may enhance the end-to-end performance provided at the transport stratum.

In the case of service stratum, the interface between the user and the service provider may be a man-machine interface. In the case of transport stratum, this interface corresponds to the network interface card of terminal equipment (TE). As a result, some of parameters for describing the QoS of the service stratum will be different from those that describe the QoS of a transport stratum.

The parameters and objectives for the performance of service stratum are specified in other Recommendations, i.e. G.1000 and G.1010. For the transport stratum, Draft TR-NGN.NHNperf. specifies the performance of non-homogeneous networks environment.

# 8	Application QoS classes

(Note : This section is still active discussion item)

ITU-T has developed well-defined Network QoS classes based on the specific technology and network, which are ITU-T Recommendation Y.1541 for IP performance, I.356 for ATM performance, etc. The coverage of those Recommendations focuses on UNI-to-UNI (Y.1541) and S/T reference points (I.356). It is important to note that, specifications for CPN (Customer Premise Network), user’s terminal and user-to-user connection are beyond the scope of these Recommendations.

In ITU-T Recommendation Y.2011, NGN service should be supported by user-to-user connectivity and CPE is encompassing into the portion of interest for this purpose.

From this sense, the scope of the end-to-end NGN QoS should encompass CPN and TE and describes in the figure 1 of this Draft.

NGN has to support different types of access networks. The harmonization of these specifications is needed to be able to manage end-to-end QoS in a non-homogeneous network. But different network and various Network QoS classes make a complex to the mapping when those networks are interconnected.

Application QoS provides guidance on the key factors that user-to-user connectivity from the perspective of the end-user. By considering the performance requirement of applications involving the media of voice, video, image and text, and the parameters that govern end-user satisfaction for these applications, Application QoS is determined.

Application QoS classes will be categorized by a user’s QoS requirement range and may insist of performance parameters (as in the Network QoS Classes of ITU-T Rec. Y.1540 for IP service offers).

## 8.1	Classification of Application QoS

A typical user is not concerned with how a particular application is supported. However, the user is interested in comparing the same service offered by different quality in terms of various ranges. This implies that Application QoS should be classified as follows;

- Based on end-to-end user expectation of impairments and is therefore not dependent on any specific technology (network as well as application) for its validity. But the classification should be easily applied to the Network QoS classes for the purpose of implementation and operation.

- Provides an indication of the upper and lower boundaries for applications to be perceived as essentially acceptable to the user.

- Shows how the performance parameters (delay, delay variation, loss, etc.) and their objectives can be grouped appropriately, with implying that one class may "better" than another.

## 8.2	Relationship between Application QoS classes and Network QoS classes

Application QoS classes are used as the basis for deriving Network QoS classes and associated QoS control mechanisms/signaling for the underlying transport networks. (More details of cooperation with control and signaling functions are for further study).

The below table shows some of the characteristics, which distinguish Application QoS classes and Network QoS classes.

Table 2/ Draft TR-NGN.QoS

Distinction between Application QoS classes and Network QoS classes

| Application QoS classes | Network QoS classes |
| --- | --- |
| Service acceptability | Network capability |
| Network technology independent | Network technology dependent |
| NGN service stratum | NGN transport stratum |
| Requested/selected by user: the end-to-end service | Supported by service/network provider: the end-to-end network |
| User-required performance | Network-supporting performance |

# 9	Performance Parameters

The 3x3 performance matrix may be extended to address QoS and NP of the NGN. The performance criterion: speed, accuracy, and dependability might be supplemented with criteria such as ease-of-use. The communications functions: access, user information transfer, and disengagement might be supplemented with information storage, information translation, and brokerage functions.

Editor’s Note: Figure1/G.1000 shows the extended matrix between criteria and function to facilitate identification of communications QoS criteria.

Draft NGN-MAN introduces Manageable Network concept.

Addition of billing for functions as well as reliability and security for criteria on the matrix may be considered, but those functions should be quantifiable.

# Appendix I

# The impact of QoE to clarify NGN QoS

## I.1. User acceptability for NGN service

A service acceptability that is experienced by a user depends on the expected value from the service. When this user is using the service to take a high value and perceives the high QoS, this service can be classified as the acceptable level.

Case 1. E-mail service

Recommendation G.1010 introduces a well-defined QoS requirement for the specific service itself as follows;

“E-mail is generally thought to be a store and forward service which, in principle, can tolerate delays of several minutes or even hours”

For the user who is trying to let someone know how he is, delays of hours may be acceptable. But, when this user should be required urgent information for the business purpose, the acceptable delay will be less than several seconds.

Case 2. Voice service

An acceptable target value for conversational voice prefers delays of less 150 ms in Table (.1/G.1010. Also Table 2/Y.1541 gives some guidance for the applicability and engineering of IP-based network QoS classes, and voice service (VoIP) is aligned for QoS class 0 and 1. These two classes specify delays of 100 ms and 400 ms respectively.

Voice has been traditionally considered one of the high quality-required services. But, when the user communicates a very long distance international call by Internet telephony for free, delay of 150 ms is not expected and delays of 1 second may be acceptable.

## I.2. Network/service provider’s viewpoint for user acceptability

QoS target value is supported by a provider should depend on the user acceptability. When the user requests the service to give a high value and expects the high QoS value, this service should be supported by the acceptable level.

For the purpose to meet user acceptability, a provider should transfer e-mail in several seconds when there is a requirement for the fast and reliable service of e-mail from a user.

The user who doesn’t pay for voice service like Internet telephony, the provider doesn’t need to support a high quality for that voice service. It may be dealt with the lowest quality service from provider’s viewpoint.

______________

# Text boxes

Network Interface

Man-Machine Interface

Man-Machine Interface

QoE

QoE

Quality of Service for NGN

Network Performance for NGN

User

User

TE

TE

CPN

CPN

AN

AN

CN

Network Interface

Transport

Service

Transport

Transport

Service

QoS for NGN (G.1010)

NP for NGN (Y.HYBperf.)

I.356 for ATM connection

Y.1541 for IP flow

Y.1561 for MPLS LSP