QUESTION 21/2

Calculation of frequency fees

RESOLUTION 9 (Rev. Istanbul, 2002)

Participation of countries, particularly developing countries, in frequency spectrum management

ITU-D	STUDY GROUP 2	3rd STUDY PERIOD (2002-2006)

Report on Resolution 9
(Rev. Istanbul, 2002)
and Question 21/2

DISCLAIMER This report has been prepared by many volunteers from different Administrations and companies. The mention of specific companies or products does not imply any endorsement or recommendation by the ITU.

TABLE  OF  CONTENTS

Page

ACKNOWLEDGEMENTS		vii

PREFACE		ix

REPORT ON RESOLUTION 9 (REV. ISTANBUL, 2002) AND QUESTION 21/2 – PARTS I AND II		1

1	Introduction		1

1.1	ITU-D and ITU-R Joint Group for Resolution 9 (2002-2003)		1

1.2	Work programme		2

1.3	Structure of the report		2

1.3.1	Part I: National use of spectrum 960-3 000 MHz		2

1.3.2	Part II: National spectrum management practices		3

1.3.3	Part III: Calculation of frequency fees		4

1.4	Proposals for future work		4

PART  I		7

2	Analysis of the submissions to Part I of the questionnaires		7

2.1	Overview		7

2.2	Some examples of national allocation tables		7

2.3	Further sources of information on national strategies for spectrum management		8

PART  II		9

3	Analysis of the submissions to Part II of the questionnaire		9

3.1	General structure of Part II of the questionnaire		9

3.2	Legal and regulatory aspects: Questions 1, 2, 4 and 5		9

3.2.1	Question 1: Legal and regulatory texts		9

3.2.2	Question 2: Regulations and procedures		10

3.2.3	Question 4: Equipment – technical requirements and standards		11

3.2.4	Question 5: Spectrum redeployment		17

3.3	Updating the database: Questions 3 and 10		19

3.3.1	Question 3: National frequency allocation table		19

3.3.2	Question 10: Policy and planning functions		20

3.4	Assignments (generic): Questions 7, 8, 9 and 11		21

3.5	Spectrum management: Questions 6, 15 and 16		28

3.6	Spectrum monitoring: Questions 12, 13 and 14		37

3.6.1	Fixed monitoring stations		39

3.6.2	Mobile monitoring stations		41

3.6.3	Transportable monitoring stations		43

3.6.4	Space monitoring stations		45

3.7	Handbooks and reports		53

3.8	Problems		54

Page

ANNEX 1-A – Index of submitters and designated focal points		56

ANNEX 1-B – Table 1 – Extract from the submission of Albania		96

ANNEX 1-C – Table 2 – Extract from the submission of the United Kingdom		98

ANNEX 1-D – Table 3 – Extract from the submission of the US Federal Government		99

ANNEX 1-E – Table 4 – Extract from the submission of the Czech Republic		101

ANNEX 2-A – Question 1: Regulatory texts		102

ANNEX 2-B – Question 2: Are regulations and procedures publicly available?		108

ANNEX 2-C – Question 4: Compliance procedures		109

ANNEX 2-D – Question 5: Spectrum redeployment		114

ANNEX 2-E – Responses concerning Questions 3 et 10		121

ANNEX 2-F – Responses concerning Question 6		124

ANNEX 2-G – SECTION 1 – Use of computers for national spectrum management		130

ANNEX 2-G – SECTION 2 – Adminitrative management		132

ANNEX 2-H – Responses concerning responsibilities of spectrum management (Question 16 b) and c))		136

ANNEX 2-I – Responses concerning human resources (Question 16 e) and f))		148

ANNEX 2-J – List of fixed, mobile and transportable radio monitoring stations by Member State		151

ANNEX 2-K – Radio monitoring stations		159

ANNEX 2-L – Responses concerning cooperation between spectrum management and monitoring (Question 12 r), s), t) and u))		165

ANNEX 2-M – Responses concerning inspection of radio stations (Question 13)		167

ANNEX 2-N – Responses concerning handbooks and reports (Question 17) – SECTION 1 - Response by country		171

ANNEX 2-N – SECTION 2 – Breakdown of answers		174

ANNEX 2-O – Responses concerning the identification of problems experienced in national spectrum management (Question 18)		175

Page

REPORT ON RESOLUTION 9 (REV. ISTANBUL, 2002) AND QUESTION 21/2 – PART III		185

1	Introduction		185

2	Questionnaire responses		185

3	Analysis of responses		190

3.1	General Questions (Q.1 to Q.5)		190

3.2	Exemption from payment of frequency fees		194

3.3	The application of frequency fees		198

3.3.1	Methods used by administrations		198

3.3.2	Explanations, grounds and objectives		198

3.3.3	Recourse to market mechanisms		199

4	Updating the report and database		201

4.1	Updating the report		201

4.2	Updating the database		202

5	Analysis of results		202

5.1	Variables used to determine fees		202

5.1.1	Variables and applications identified in the questionnaire		202

5.1.2	Processing of responses from administrations		203

5.1.3	Analysis of variables used		203

5.2	Fee size		206

5.3	Recourse to market mechanisms		206

5.4	Advantages and disadvantages of each approach		206

6	Database		209

7	Using the database		209

ANNEX 1 – Definition of Question 21/2		211

1	Statement of the situation or problem		211

2	Question or issue proposed for study		211

3	Expected outputs		212

4	Required timing of the expected output		212

5	Proposers/sponsors		212

6	Source of required inputs		212

7	Target audience for the output		213

8	Proposed method of handling this Question		213

9	Coordination requirements for the study		213

ANNEX 2 – Spectrum fees database statistics for all countries		214

LIST  OF  FIGURES

Page

Chart 1: Fixed measurement stations		160

Chart 2: Fixed direction-finding stations		161

Chart 3: Mobile measurement stations		162

Chart 4: Mobile direction-finding stations		163

Chart 5: Transportable measurement stations		164

Chart 6: Transportable direction-finding stations		164

LIST  OF  TABLES

Page

Table 1 – Extract from the submission of Albania		96

Table 2 – Extract from the submission of the United Kingdom		98

Table 3 – Extract from the submission of the US Federal Government		99

Table 4 – Extract from the submission of the Czech Republic		101

General rate of response to Part II (reply to at least one part of the Questionnaire)		130

Rate of response for Questions 6, 15 and 16 by region		130

Rate of response for Questions 6, 15 and 16 by development status		131

Wireless local loop		199

2G mobile systems		200

3G mobile systems		200

Analogue terrestrial radio		200

Digital terrestrial radio		201

Digital terrestrial television broadcasting		201

Fixed service		204

Mobile service		204

Satellite service		204

Terrestrial broadcasting service		204

Other applications		204

Radio-relays		205

2G mobile systems		205

REPORT  ON  RESOLUTION  9  (REV.  ISTANBUL,  2002)
AND  QUESTION  21/2

ACKNOWLEDGEMENTS

The following contributors are thanked for their continuous support in preparing this report:

	For Part I:

Mr Terry Jeacock (United Kingdom)
Mr Norbert Schroeder (United States)
Mr Zoltan Zsuffa (Hungary)

	For Part II:

Mr Terry Jeacock (United Kingdom) 	Overall work 
Mr Howard Del Monte (United Kingdom)	Legal and regulatory aspects
Mr Lopez Vanegas (Nicaragua)	Updating the database
The late Mr Simplice Zanga Yene (Cameroon)	Assignments (generic)
Mr Michel-René Lemaitre/Ms Durand (France)	Spectrum management
Mr Sherif Guinena (Egypt)	Spectrum monitoring
Mr Makhtar Fall (Senegal)	Handbooks and Reports
Mr Jan Verduijn (Netherlands)	Problems
Mr Philippe Mège (Thales)	Overall statistics

	For Part III:

Mr Jesús González Vidal (Cuba)
Mr Norbert Schroeder (United States)
Mr Sherif Guinena (Egypt)
Mr Makhtar Fall (Senegal)
Ms Ilham Ghazi (Morocco)
Mr Jean-Pierre Huynh (France)

	For specific needs in spectrum management needs for developing countries:

The late Mr Simplice Zanga Yene (Cameroon)
Ms Béatrice Durand (France)
Mr Makhtar Fall (Senegal)

	For overall work:

Mr Terry Jeacock (United Kingdom, representing ITU-D)
The late Mr Simplice Zanga Yene (Cameroon, representing ITU-R) and 
Mr Nabil Kisrawi (Syria, Chairman of ITU-D Study Group 2)

REPORT  ON  RESOLUTION  9  (REV.  ISTANBUL,  2002)
AND  QUESTION  21/2

PREFACE

The active participation of countries, particularly developing countries, in frequency spectrum management is one of the important concerns of every administration throughout the world. The extraordinary growth rate of mobile telecommunications is just one indicator that the use of radiocommunications is essential to the social and economic welfare of any nation. Additionally, the calculation of fees for the use of the spectrum is another issue for which some administrations are seeking guidance from ITU, because there is no universal solution that can balance the need to promote telecommunications, determine an economic value for the spectrum and take into account national circumstances and policies. This report, the result of the fruitful collaboration between ITU-R Study Group 1 and ITU-D Study Group 2, is intended to assist the administrations and telecommunication operators to reach acceptable solutions for a wide variety of radiocommunication questions.

At the completion of this stage of the work, I would like to commend Mr Terry Jeacock (UK) and Mr Simplice Zanga Yene (Cameroon), the two Co-Chairmen of the Joint ITU-R/ITU-D Group on Resolution 9 (Rev. Istanbul, 2002), dealing with “Participation of countries, particularly developing countries, in frequency spectrum management”, and on Question 21/2 (“Calculation of frequency fees”), for the valuable results achieved.

Unfortunately, it is with deep regret that I have to inform you that Mr Simplice Zanga Yene passed away, suddenly, earlier in 2005. Special recognition must be given for his valuable contribution to identify the specific needs of developing countries in spectrum management that he prepared as an attachment to the proposal for revision of Resolution 9 (Rev. Istanbul, 2002). In addition, it was expected that he would take over both co-chairmanships of the Joint Group until the World Telecommunication Development Conference to be held in 2006 in Doha, Qatar.

Mr Terry Jeacock has now retired from his Administration and has therefore resigned as Co-Chairman of the Joint Group as he is no longer involved in ITU work. On behalf of all those involved in the Resolution 9 activities, I would like to express my sincere thanks and appreciation to him and to wish him every success for the future.

Finally, it is my sincere wish and expectation that this report will become a useful tool for both those working with respect to spectrum management and radio monitoring as well as for those facing the problems of the calculation of spectrum fees.

Hamadoun I. Touré
Director, BDT

REPORT  ON  RESOLUTION  9  (Rev.  ISTANBUL,  2002)
AND  QUESTION  21/2

PARTS  I  AND  II

# 1	Introduction

Resolution 9, first adopted in 1998 by the World Telecommunication Development Conference (WTDC-98) and revised in 2002 by WTDC-02, requires the Directors of ITU-D and ITU-R to develop a report, in several stages, on current and foreseen national uses of the radio-frequency spectrum. This Resolution also requires the Directors of the Telecommunication Development and Radiocommunication Sectors to consider and implement effective means to encourage and facilitate the active participation of both developing and least developed countries in the preparation of this report.

A Joint Group between the Telecommunications Development Sector and the Radiocommunication Sector was established in 1999 to develop the reports required by Resolution 9. A Report on the first stage was completed in 2000. This current document contains the Report on the second stage.

In addition to the work programme to develop the second stage of the report on national spectrum management, WTDC-02 requested that the Joint Group should include in its scope the provision of assistance to the BDT in Programmes 2 and 4 of the Istanbul Action Plan, with respect to “Spectrum management and radio monitoring” and the preparation of a report in answer to Question 21/2 “Calculation of frequency fees”.

## 1.1	ITU-D and ITU-R Joint Group for Resolution 9 (2002-2003)

The Joint Group is co-chaired by Mr Simplice Zanga-Yene (Cameroon) representing ITU-R Study Group 1 and Mr Terry Jeacock (United Kingdom) representing ITU-D. The group held six meetings: 1) July 2002; 2) September 2002 (during the ITU-D Study Group 2 meeting); 3) December 2002; 4) April 2003; 5) October 2003; 6) April 2004.

The first meeting agreed the basic structure of the Report and methodology. A three-part Questionnaire was developed, Part I: National use of the spectrum 960-3 000 MHz; Part II: National spectrum management; Part III: Question 21/2. At the second meeting a presentation was given to the members of Study Group 2 to explain the purpose of the Questionnaires and advise how they should be completed. At the third meeting, the initial responses were reviewed and the method for analyzing the results agreed. Rapporteurs were appointed to manage the development of the various parts of the Report. At the fourth meeting, the progress on the analysis was reviewed and final time-scales agreed for completion of the Report. The fifth meeting agreed to finalize all parts of the Report for 2004 and decided to invite the Members to provide their comments on the usability of the “Spectrum Fees” database (created by the BDT Secretariat) and to consider any possible refinement. The fifth meeting also decided to complete the Report with case studies to demonstrate practical examples of using the database, and with the requirements of developing countries for assistance in spectrum management activities.

The sixth meeting continued studying the requirements for assistance from developing countries, proposed a revision of the Resolution 9 for consideration by WTDC-06 and finalized the Report to be submitted to ITU-D Study Group 2 meeting in September 2004.

## 1.2	Work Programme

After the presentation at the September Study Group 2 meeting in 2002, the three-part Questionnaire was circulated to members of the Radiocommunication Sector and Telecommunication Development Sector via joint Administrative Circular CA/12 (ITU-D) and CA/120 (ITU-R), dated 11 September 2002. A deadline for receipt of responses was set for 1 November 2002. At the December meeting of the Joint Group, it was noted that 56 responses had been received. BDT produced, for each delegate, a CD-ROM containing an electronic version of these responses. It was also noted that during the period available for administrations to complete the Questionnaire, several important ITU meetings were in progress (including PP-02 and ITU-R CPM) and administrations may have found difficulty in finding the necessary resources to undertake this task. Further, it was recognized that some parts of the Questionnaire were complex and administrations might have needed assistance. Therefore, the meeting decided to extend the deadline for the replies to 14 February 2003. The BDT Secretariat therefore sent another Circular letter to extend the deadline to 14 February 2003. As BDT was receiving responses after this date, it was agreed to take into account all responses received by 28 February. Responses received after this date were placed on the web for information only.

The responses have been analysed according to the three-part Report structure and methodology agreed at the third meeting (see Section 1.4 below).

With respect to providing assistance on Programmes 2 (Technologies and Telecommunication Network Development) and 4 (Economics and Finance, including Cost and Tariffs) of the Istanbul Action Plan, the Joint Group was able to provide advice on the needs of developing countries in the preparation of Recommendation SM.1604: “Guidelines for an UPGRADED Spectrum Management System for developing countries”. The sixth meeting of the Group decided to first identify the needs for assistance on the basis of a sample of three African countries. On the basis of needs identified, a small group, including BDT and BR, will be able to review the specification of requirements and make an estimate of the cost and, thereafter, advise on the advantages and disadvantages of the options for upgrading the WinBASMSs software.

## 1.3	Structure of the Report

### 1.3.1	Part I – National use of spectrum 960-3 000 MHz

Part I of the Questionnaire deals with national spectrum use. Member States were requested to provide information on their national use of the spectrum in the frequency range 960-3 000 MHz. This range was identified by developing countries as being of particular interest to them.

For convenience in responding to these questions, an extract of Article 5 of the Radio Regulations (Allocation Table for the frequency bands from 960 MHz to 3 000 MHz) was provided in both paper and electronic forms of the Questionnaire. Administrations were encouraged to submit the requested information in electronic form to facilitate analysis by the Joint Group. An example extract from a national table was given to show the typical information requested. The information on national spectrum use will be made available for several key purposes: firstly, it demonstrates that a large number of administrations have recognized the benefits of making this information available publicly to inform users about the frequency availability for their particular communication requirement and to guide manufacturers in the design and construction of equipment. Secondly, it is intended to facilitate the coordination requirements of use of the spectrum, either nationally or with neighbouring countries, or with other countries at an international level. Thirdly, by giving examples to show the variety of formats and depth of information provided, it encourages and guides administrations currently in the decision-making process of how to publish their Tables.

It will not be possible to include all the national frequency tables in the final Report because the quantity of the information is too large. Also, although administrations follow the international table at service allocation level, there are considerable differences on a national, regional and worldwide basis in the detailed arrangements for specific applications, channel and band-plans, etc. It could be misleading to summarize or attempt to show commonality. Further, the information collected through the Questionnaire can be considered as only a “snapshot” of the situation at that particular point in time. It is necessary to revise national tables from time to time to accommodate new applications and requirements and changes resulting from World Radiocommunication Conferences.

The Joint Group therefore considered how best to present this information in a useful format. The “raw” information as supplied in the responses to the Questionnaire is available on the ITU-D website and on CD-ROM. Also, many administrations include their Tables on their websites. Therefore, the Report includes a list of website addresses of those administrations that gave this information. In addition, the Joint Group is considering the possibility of developing a PC-based computer tool that will facilitate comparison of use between different regions or administrations.

Finally, Part I also provides a list of points of contact for each administration. The Questionnaire invited administrations to identify the person responsible for responding and able to answer queries on the information. This list may provide a useful reference for informal contact and cooperation between administrations.

### 1.3.2	Part II – National spectrum management practices

Part II of the Questionnaire dealt with general questions on national spectrum management. The Joint Group made a thorough review of the questionnaire used for the first stage of the (1998) Report. The results and replies from the first stage were taken into account to revise some of the questions to improve clarity and add new questions to obtain information to assist the related studies in ITU-R Study Group 1.

In order to provide clarity and ensure helpful comparisons are made in the statistical analysis, the questions were grouped into topics and the responses were grouped according to the regional and development categories of the responding administration.

The following topics were used for question grouping:

•	Legal and Regulatory

•	Spectrum management and engineering

•	Monitoring, enforcement, interference

•	Database management and computer assistance

•	Economic aspects (to be considered in association with Q.21/2)

•	Use of the ITU-R Handbooks and Reports

•	Identification of problems experienced in national spectrum management.

The regional and development categories were obtained from lists supplied by the UN and the BDT.

An example of the format for presenting the statistical analysis is given in the table below. This example deals with a question on national requirements for compliance with equipment standards.

| Region | Number of responses received | Yes, technical characteristics specified | Total “Yes” per cent for region |
| --- | --- | --- | --- |
|  |  | Developed | Developing | Least developed | Total “ Yes” responses |  |
| Africa | 19 | – | 5 | 14 | 19 | 100% |
| Americas | 15 | 1 | 13 | – | 14 | 93% |
| Arab States | 8 | – | 8 | – | 8 | 100% |
| Asia-Pacific | 9 | – | 7 | 2 | 9 | 100% |
| Europe and CIS | 29 | 9 | 18 | – | 27 | 93% |
| TOTALS | 80 | 10 | 51 | 16 | 77 | 96%* |
| * Percentage of total response |

### 1.3.3	Part III: Calculation of frequency fees

The elaboration of a national frequency fee calculation model is a very complex matter and is the source of major difficulties for numerous developing countries and particularly LDCs for which the need is extremely urgent. Question 21/2 requested the establishment, in electronic format, of a document structure bringing together the calculation formulas and frequency fee amounts applied by different countries for different radiocommunication uses in the various frequency bands. The Question also requests a report on the various frequency fee calculation formulas currently applied in different countries.

Comprehensive information from administrations for this part of the report was obtained through Part III of the Questionnaire included in Circular letters CA/12 and CA/120. In order to store the results in electronic format, as requested by Q.21/2, the BDT secretariat has arranged for a suitable database to be designed and implemented and for the data from Part III to be entered into the database during 2003.

## 1.4	Proposals for future work

Resolution 9 was conceived as an ongoing task, to be undertaken in stages. The two stages completed so far have followed the same procedure, that is, the circulation of a multipart questionnaire dealing with (I) National spectrum use and (II) National spectrum management practices. Part I of the first stage dealt with national spectrum use in the range 30-960 MHz, the second in the frequency range 960-3 000 MHz. One proposal for future work could therefore consider analysing national frequency use in a third frequency range, for example 3 000 MHz to 30 GHz. Also, the analysis of the responses of the first and second Questionnaires for Part II, national spectrum management practices, has given an opportunity for comparisons of progress on a national and regional basis, especially for developing countries. Further, this analysis has enabled the identification of where developing countries would benefit from assistance in their spectrum management. The first stage of the Report required the full study period (1998-2002) to complete, while the Report of the second stage will be available after 2003 and included the additional work for

Q.21/2. In consideration of the future work plan for the remainder of the current study period (until 2006), the Joint Group proposes not to re-issue a third questionnaire until the next study period. Considerable resources are required by administrations to respond to these detailed questionnaires and the results that would be obtained from a questionnaire issued too soon after the second stage report would not be helpful. There is a wealth of information contained in the responses to the first and second Questionnaires that could be extracted by further analysis and presented in the form of supplementary reports.

The following work plan is therefore proposed for the remainder of the study period:

•	Re-examine the responses to Stage 1 and Stage 2, with a view to preparing supplementary reports, e.g. on the requirements of developing countries for assistance in spectrum management activities, typical spectrum use in the ranges covered and changes foreseen, etc.

•	Continuation of development on web-based access to national frequency allocation tables.

•	Review the Resolution 9 website and consider how it could be improved to better distribute to developing countries information to assist them with national spectrum management.

•	Review the use of the “Spectrum fees” database and the need for keeping it up to date.

•	Prepare a revision of Resolution 9 for consideration by WTDC-06 with a view to continue to the third stage.

•	Consider further cooperative projects between ITU-D study groups and ITU-R Study Group 1.

PART  I

# 2	Analysis of the Submissions to Part I of the Questionnaires

## 2.1	Overview

In Part I of both questionnaires (ITU-D CA/08 and ITU-R CA/71 for Phase 1; and ITU-D CA/12 and ITU-R CA/120 for Phase 2) information was sought on the national strategies being followed by Member States for the allocation and use of the radio-frequency spectrum. To facilitate the preparation of responses, respective portions of the International Table of Frequency Allocations that appears in Article 5 of the International Telecommunication Union Radio Regulations were included in these questionnaires (27.5 to 960 MHz for Phase 1 and 960 MHz to 3 000 MHz for Phase 2). Member States were requested, in preparing their responses to these questionnaires, to identify the radiocommunication services allocated spectrum in the respective frequency bands and to provide information regarding the application of these radiocommunication services for satisfying spectrum requirements in given bands. These questionnaires also requested the Member States to designate individuals who would serve as focal points for addressing matters related to these questionnaires.

Annex 1-A presents an index of the submissions received in response to the questionnaires and a listing of the individuals who have been designated to serve as focal points. This index indicates that 117 Member States, one regional telecommunication organization (CEPT) and one national telecommunication operator (Korea Telecom) have submitted responses to these two questionnaires, that sixty-three submissions contain national allocation tables for the bands 27.5-960 MHz, that eighty-four submissions contain national allocation tables for the bands 960-3 000 MHz, and that thirty-six submissions contain national allocation tables for the entire spectrum from 27.5 to 3 000 MHz.

As is stated in the National Spectrum Management Handbook1 “a national table of frequency allocations provides a foundation for an effective spectrum management process”. Consequently, the objective of the working group was to promote the establishment of national allocation tables, where they do not yet exist. The approach pursued by the working group toward achieving this objective was to first obtain a broad range of existing national allocation tables and then make them readily available as examples that could be used by an administration in the development of both its own national table of frequency allocations table and an effective national strategy for radio-frequency spectrum management.

The responses submitted to these two questionnaires contain a wealth of highly useful information. All of this information is posted on the ITU-D Sector web page and is readily available to spectrum managers worldwide. The web page addresses for accessing this information are provided in the annexes.

## 2.2	Some examples of national allocation tables

In reviewing the national allocation tables submitted by the various administrations, some notable differences are evident in their scope, content, and format. While some administrations focused on national allocations, other administrations also presented their spectrum allocations in context with the provisions of the Radio Regulations and with strategies for spectrum use throughout their geographic region. While some administrations focused on current spectrum allocations, other administrations also presented strategies for planned changes in spectrum allocations and planned applications.

The submission from Albania, given in Annex 1-B Table 1, is an example of how national spectrum allocations and uses can be presented in context with the strategies for spectrum use throughout an administration's geographic region.

The submission from the United Kingdom, given in Annex 1-B Table 2, is an example of how strategies for planned changes in spectrum use to satisfy anticipated requirements can be presented along with existing allocations and current spectrum uses.

The submission from the United States, given in Annex 1-B Table 3 is an example of how various applications of given allocated radiocommunication services are currently used, or planned for future use, to satisfy specified spectrum requirements.

The submission from the Czech Republic, given in Annex 1-B Table 4 is an example of how specified responsibilities can also be identified as an element of the national table of frequency allocations.

## 2.3	Further sources of information on national strategies for spectrum management

In addition to the information available from the administrations submission as is noted in the annexes, additional information can be obtained from a number of WebPages maintained by administrations. Some of these sources are the following:

A)	Canada:	http://strategis.ic.gc.ca/SSG/sf01608e.html

B)	CEPT:	http://www.ero.dk/documentation/docs/doc98/official/pdf/REPO25.PDF

C)	Finland:	http://www.ficora.fi/englanti/radio/Taulukko3.htm

D)	United Kingdom:	http://www.ofcom.org.uk/static/archive/ra/rahome.htm

E)	United States:	http://www.ntia.doc.gov
	http:/www.fcc.gov

F)	Venezuela: http://www.conatel.gov.ve/ns/downloads/macro_legal/CUNABAF%20Extraordinaria.zip

PART  II

# 3	Analysis of the submissions to Part II of the questionnaire

## 3.1	General structure of Part II of the questionnaire

For Part II of the questionnaire the questions were grouped into key aspects of national spectrum management and are dealt with in the following Sections:

3.2	Legal and regulatory aspects in questions 1, 2, 4 and 5

3.3	Updating the database in questions 3 and 10

3.4	Assignments (generic) in questions 7, 8, 9 and 11

3.5	Spectrum management in questions 6, 15 and 16

3.6	Spectrum monitoring in question 12, 13 and 14

3.7	Handbooks and reports in question 17

3.8	Problems in question 18

Each of these Sections are structured to give:

•	a statement of the questions asked;

•	a brief explanatory review to place the particular aspect in context;

•	identification of any obvious misunderstanding of the questions;

•	a tabular presentation of the analysis of the responses grouped into region and country category (developed, developing or least developed);

•	preliminary summary per question.

For each of the categories, a tabular “country-by-country” presentation is given in the Annex 2 part of the Report.

## 3.2	Legal and regulatory aspects: questions 1, 2, 4 and 5

### 3.2.1	Question 1: Legal and regulatory texts

Background

National spectrum management consists of the structures, capabilities, procedures, and regulations whereby each administration controls the use of the radio spectrum within its geographical boundaries. By international agreement, each national government has flexibility and autonomy in the regulation of its radio use. Each administration must develop its laws, and organization to carry out the duties of spectrum management. The spectrum management system will grow in direct relationship to the level of radio use within a country and the laws may be changed to enable development of the spectrum.

Q.1: What legal or regulatory texts govern your national spectrum management processes?

The responders referred to national telecommunications acts and radio regulations. Only one administration did not provide details of a relevant text, although answering other Part II questions. The complete list of texts is given in Annex 2-A.

Q.1 subsidiary: Are any actions planned to change these legal texts or regulations? (YES/NO)

A total of 58 Administrations replied that they were planning changes and some added explanations about the changes. Several expected changes as part of the establishment of a new regulatory authority. Detailed comments are listed in Annex 2-A.

| Region | Responses received | Yes, changes are planned | Changes planned as a percentage of region response |
| --- | --- | --- | --- |
|  |  | Developed | Developing | Least developed | Total changes planned in region |  |
| Africa | 19 | – | 2 | 10 | 12 | 63% |
| Americas | 15 | 1 | 11 | – | 12 | 80% |
| Arab States | 8 | – | 5 | – | 5 | 63% |
| Asia-Pacific | 9 | – | 5 | 1 | 6 | 67% |
| Europe and CIS | 29 | 8 | 15 | – | 23 | 79% |
| TOTALS | 80 | 9 | 38 | 11 | 58 | 73%* |
| * Percentage of total response |

### 3.2.2	Question 2: Regulations and procedures

Background

Effective management of the spectrum resource depends on a number of fundamental processes. These fundamentals encompass the goals and objectives of the spectrum management system, the major directives that establish the responsibility of the national spectrum management authority and regulate spectrum use, the national spectrum management structure and related processes, and the specific functional responsibilities that must be carried out by the spectrum management authority. Although no two administrations will manage the spectrum in exactly the same manner, these fundamental elements are essential to all approaches. Without them, the implementation of radio services will be delayed or not available. With these elements in place, an administration can begin to carry out more detailed spectrum management functions and daily activities, and maximize the benefits derived from use of the radio spectrum resource.

Q.2: Have you publicly available regulations and procedures for national spectrum management (e.g. radio services, licence requirements, etc.)? (YES/NO)

84% of the responders do make their regulations and procedures available. The following table breaks down the responses into region and development status. The full response is given in Annex 2-B.

| Region |  | Yes, R&Ps are publicly available | Total “Yes” per cent for region |
| --- | --- | --- | --- |
|  | Responses received | Developed | Developing | Least developed | Total “Yes” response |  |
| Africa | 19 | – | 3 | 10 | 13 | 68% |
| Americas | 15 | 1 | 12 | – | 13 | 87% |
| Arab States | 8 | – | 6 | – | 6 | 75% |
| Asia-Pacific | 9 | – | 7 | 2 | 9 | 100% |
| Europe and CIS | 29 | 10 | 16 | – | 26 | 90% |
| TOTALS | 80 | 11 | 44 | 12 | 67 | 84% |

### 3.2.3	Question 4: Equipment – technical requirements and standards

Background

Article 3 of the Radio Regulations concerns the requirements for the technical characteristics of stations with the objective to avoid interference. Appendices 2 and 3 respectively of the Radio Regulations give maximum values for frequency tolerance and spurious emissions. Administrations have the responsibility to ensure that equipment authorized for use in their territory conforms to these Regulations. This is achieved through the use of “equipment standards” (documents which specify the minimum performance standards required for radio transmitters and receivers and other equipment) and the associated procedures to ensure conformity with these standards.

Q.4: Do you specify that the technical characteristics of radiocommunications equipment must comply with certain requirements (often referred to as “equipment standards”), for example to avoid interference to other services and users? (YES/NO)

A total of 96% of the responders do specify compliance. The table below breaks down the response for each region. Refer to Annex 2-C for the full listing.

| Region | Number of responses received | Yes, technical characteristics specified | Total “Yes” per cent for region |
| --- | --- | --- | --- |
|  |  | Developed | Developing | Least developed | Total “Yes” response |  |
| Africa | 19 | – | 5 | 14 | 19 | 100% |
| Americas | 15 | 1 | 13 | – | 14 | 93% |
| Arab States | 8 | – | 8 | – | 8 | 100% |
| Asia-Pacific | 9 | – | 7 | 2 | 9 | 100% |
| Europe and CIS | 29 | 9 | 18 | – | 27 | 93% |
| TOTALS | 80 | 10 | 51 | 16 | 77 | 96%* |
| * Percentage of total response |

Q.4a): Do you develop these technical requirements or equipment standards on a national basis or use those developed by other administrations or international/regional standards organizations? (National/Other)

In addition to answering “national” or “other” some responders answered both. Generally the basis was less “national” than “other”; in two regions there is a greater choice of a national basis. The table below breaks down the results into region and development status. The full list of replies is given in Annex 2-C.

The range of answers received were:		National
		Other
		National and Other

| Region | Basis of technical requirements and equipment standards? |
| --- | --- |
|  | Answer | By development status | Regional total |
|  |  | Developed | Developing | Least developed |  |
| Africa | National: | – | 1 | 3 | 4 |
|  | Other: | – | 4 | 10 | 14 |
|  | Nat. and other: | – | – | 1 | 1 |
| Americas | National: | 1 | 2 | – | 3 |
|  | Other: | – | 11 | – | 11 |
|  | Nat. and other: | – | 1 | – | 1 |
| Arab States | National: | – | 4 | – | 4 |
|  | Other: | – | 3 | – | 3 |
|  | Nat. and other: | – | 1 | – | 1 |
| Asia-Pacific | National: | – | 3 | 2 | 5 |
|  | Other: | – | 3 | – | 3 |
|  | Nat. and other: | – | 1 | – | 1 |
| Europe and CIS | National: | – | 4 | – | 4 |
|  | Other: | 9 | 9 | – | 18 |
|  | Nat. and other: | 2 | 5 | – | 7 |
| TOTALS |  |  |  |  | 80 |

Q.4b): Do you have a procedure to ensure that radiocommunications equipment complies with the technical requirements, for example: Type Approval/Manufacturer’s Declaration of Compliance/ Other?

Responders replied with one or more of the options in the questions and some gave other examples, e.g. RTTE2. To simplify the presentation of the results they are divided into several tables according to the type of answer, i.e. type approval, manufacturer's declaration or other.

The tables show the regional and development breakdown. The “% of total response” figure is based on the 80 replies received. The “% of development category” shows the percentage for each development status category, i.e. based on the 12, 52, and 16 responses received as tabulated in section 1, i.e. 50% of responses from developed countries refer to type approval  Finally there is a summary table showing all answers with a regional breakdown. The full response is listed in Annex 2-C.

| Region | Responses received | Procedure: 1. Type approval |
| --- | --- | --- |
|  |  | By development status | Regional total |
|  |  | Developed | Developing | Least developed |  |
| Africa | 19 | – | 5 | 4 | 9 |
| Americas | 15 | 1 | 10 | – | 11 |
| Arab States | 8 | – | 6 | – | 6 |
| Asia-Pacific | 9 | – | 6 | 1 | 7 |
| Europe and CIS | 29 | 5 | 11 | – | 16 |
| TOTALS | 80 | 6 | 38 | 5 | 49 |
| % of total response | 100 | 8 | 48 | 6 | 61 |
| % of development category |  | 50 | 73 | 31 |  |

|  |  | Procedure: 2. Manufacturer’s declaration |
| --- | --- | --- |
| Africa | 19 | – | 3 | 8 | 11 |
| Americas | 15 | – | 5 | – | 5 |
| Arab States | 8 | – | 4 | – | 4 |
| Asia-Pacific | 9 | – | 1 | 2 | 3 |
| Europe and CIS | 29 | 10 | 12 |  | 22 |
| TOTALS | 80 | 10 | 25 | 10 | 47 |
| % of total response | 100 | 13 | 31 | 13 | 59 |
| % of development category |  | 83 | 48.08 | 63 |  |

|  |  | Procedure: 3. Other |
| --- | --- | --- |
| Africa | 19 | – | 1 | 4 | 5 |
| Americas | 15 | – | 1 | – | 1 |
| Arab States | 8 | – | 2 | – | 2 |
| Asia-Pacific | 9 | – | 1 | – | 1 |
| Europe and CIS | 29 | 2 | 7 | – | 9 |
| TOTALS | 80 | 2 | 12 | 4 | 21 |
| % of total response | 100 | 3 | 15 | 5 | 26 |
| % of development category |  | 17 | 23.08 | 25 |  |

Q.4c): (Summary of types of compliance procedures): Do you have a procedure to ensure that radiocommunications equipment complies with the technical requirements, for example: Type Approval/Manufacturer’s Declaration of Compliance/Other?

The following table combines and summarizes the results of the previous three tables. Type approval (TA) and manufacturer’s declaration (MD) are the main procedures used.

| Region | Responses received | Only type approval | TA and MD | Only manufacturer’s declaration | Only Other | Type approval and other | TA, MD and other | MD and other | No Response | TOTAL |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Africa | 19 | 5 | 4 | 6 | 3 | – | – | 1 | – | 19 |
| Americas | 15 | 8 | 2 | 3 | – | 1 | – | – | 1 | 15 |
| Arab States | 8 | 3 | 2 | 1 | 1 | – | 1 | – | – | 8 |
| Asia-Pacific | 9 | 5 | 1 | 2 | – | 1 | – | – | – | 9 |
| Europe and CIS | 29 | 3 | 8 | 7 | 4 | – | 5 | 2 | – | 29 |
| TOTAL | 80 | 24 | 17 | 19 | 8 | 2 | 6 | 3 | 1 | 80 |
| % of total response | 100% | 30.00% | 21.25% | 23.75% | 10.00% | 2.50% | 7.50% | 3.75% | 1.25% | 100% |

The total for each type of answer is determined by adding all the segments that include that answer. For example the percentage of responders who use type approval is 29 + 21 + 3 + 8  61% and the percentage who use procedures other than type approval and manufacturer's declaration is 10 + 3 + 8 + 4  25%. Individual percentages are rounded to the nearest integer.

### 3.2.4	Question 5: Spectrum Redeployment

Background

Spectrum redeployment uses a collection of various tools to assist the spectrum manager in releasing valuable frequencies from existing users for new or more efficient use to provide greater economic benefit from the radio spectrum.

Q.5a): Has there been any spectrum redeployment in your country or has a need for spectrum redeployment been identified? (YES/NO)

A total of 50 responders have used or have a need for spectrum redeployment. In regional terms this ranged from 38% in Arab States to 86% in Europe & CIS. The full response is shown in Annex 2-D.

| Region | Responses received | Yes, spectrum redeployment is used or needed |
| --- | --- | --- |
|  |  | By development status | Regional total |
|  |  | Developed | Developing | Least developed | Total “Yes” response | Total “Yes” percentage for region |
| Africa | 19 | – | 4 | 5 | 9 | 47% |
| Americas | 15 | 1 | 8 | – | 9 | 60% |
| Arab States | 8 | – | 3 | – | 3 | 38% |
| Asia-Pacific | 9 | – | 5 | 1 | 6 | 67% |
| Europe and CIS | 29 | 10 | 15 | – | 25 | 86% |
| TOTALS | 80 | 11 | 35 | 6 | 52 |  |

Q.5b): If so, do you have a method for achieving this redeployment in respective frequency bands and for given radiocommunication services? (YES/NO)

The regional percentages in the table below relate to whether there is a redeployment method used by the responders who answered YES in Question 5a above. This figure ranged from 67% to 89%. The full response is listed in Annex 2-D.

| Region | Total “Yes” response from Q.5a) above | Yes, a method exists |
| --- | --- | --- |
|  |  | By development status | Regional total |
|  |  | Developed | Developing | Least developed | Total “Yes” response | Total “Yes” percentage for region |
| Africa | 9 | – | 3 | 3 | 6 | 67% |
| Americas | 9 | 1 | 7 | – | 8 | 89% |
| Arab States | 3 | – | 2 | – | 2 | 67% |
| Asia-Pacific | 6 | – | 4 | 1 | 5 | 83% |
| Europe and CIS | 25 | 8 | 10 | – | 18 | 72% |
| TOTALS | 52 | 9 | 26 | 4 | 39 |  |

Q.5c): Please define the established method and describe the nature of the consultation, if any, with users regarding the potential costs resulting from the planned redeployment.

Q.5c): Please define the established method and describe the nature of the consultation, if any, with users regarding the potential costs resulting from the planned redeployment.

The long-term approach involves forward planning with a long period of time before the frequencies are required. This allows advance notification of assignments and allows users to release frequencies at a routine system change, e.g. end of equipment life or expiration of licence. Geographical (space diversity) is another option. Six administrations, mainly from the European region, use at least one of the passive methods.

However, when the need for redeployment is more urgent a pro-active approach is required and the short-term options used range from incentives to licence revocation. Incentives can be used to persuade existing users to volunteer to release assignments. Spectrum pricing has also been identified as a method that can simplify the spectrum redeployment process.

Consultation with public and other affected users is often included in the preliminary procedures.

Redeployment can incur expenditure to the existing user for new equipment and infrastructure and many responders referred to the basis for compensation. Compensation payments can be derived from state funds or, more commonly, from the new user of the released frequencies.  The state and the new user could also jointly fund compensation. The actual compensation amount can also be negotiated and can take account of expenditure that would have been expected even without redeployment, for example, end of life equipment replacement costs.

Apart from the use of passive methods there was no clear regional pattern of methods of redeployment or compensation.

Annex 2-D lists all the comments.

## 3.3	Updating the database: Questions 3 and 10

### 3.3.1	Question 3: National Frequency Allocation Table

Background

A national table of frequency allocations is a basic tool for an effective spectrum management process. It provides a general plan for spectrum use and the basic structure to ensure efficient use of the spectrum and the prevention of RF interference between services. Through use of the table, manufacturers will have a guide to where in the spectrum to design and build equipment and users will know where to operate. As described in the National Spectrum Management Handbook, the International Table of Frequency Allocations, Article 5 of the Radio Regulations forms the basis for national tables and in some countries this may be used as the national table. However, other countries have included additional information on national use varying in detail from showing which service operates when the Radio Regulations offer a choice, to spectrum available for government and non-government use, and, for specific sub-bands, channel arrangements and equipment specifications in use. Example extracts of national allocation tables are given in Part I of this Report.

Q.3: Do you have a national radio-frequency spectrum allocation table?

Statistical results

The country-by-country analysis of the responses to Question 3 is given in Annex 2-E.

A summary analysis by region and development category is given below and based on 73 responses.

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | – | Y  4 N  2 | Y  8 N  3 | Y  12 N  5 | Y  71% N  29% |
| Americas | Y  1 | Y  11 N  2 | – | Y  12 N  2 | Y  86% N  14% |
| Asia-Pacific | – | Y  4 N  1 | Y  2 N  0 | Y  6 N  1 | Y  86% N  14% |
| Europe and CIS | Y  9 | Y  17 N  1 | – | Y  26 N  1 | Y  96% N  4% |
| Arab States | – | Y  6 N  2 | – | Y  6 N  2 | Y  75% N  25% |
| TOTAL | Y  10 | Y  42 N  8 | Y  10 N  3 | Y  62 N  11 | Y  85% N  15% |
| % of response | Y  100% | Y  84% N  16% | Y  77% N  23% |  |  |

It is worthwhile to note that 85% of the responses indicate that there is a national allocation table. In case of the developed countries, there is a 100% score.

### 3.3.2	Question 10: Policy and planning functions

Background

The primary purpose of policy making and planning in national spectrum management is to ensure that the radio spectrum is allocated to meet, both in the short and longer term, the often-competing requirements from different users and services. This must take account of international obligations and technical constraints as well as the national social, economic and political realities. Establishment of a national allocation table provides a basis for current and near-future needs; however, spectrum requirements and uses will change considerably over time especially due to economic growth and advances in technology. A national strategy for future use of the spectrum is developed from the national table, incorporating time-scales for foreseen changes, showing plans for phasing out old systems and introducing replacement technology. This enables these changes to be accommodated more easily, for different options to be considered and an opportunity for consultation with key players representing the radiocommunication industry, operators and users.

Q.10: Do you have a policy and planning function for national spectrum management (i.e. a national strategy for future use of the spectrum)?

Statistical Results

The country by country analysis to Question 10 is given in Annex 2-E. A summary analysis by region and development category is given below and based on 73 responses.

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | – | Y  4 N  2 | Y  9 N  2 | Y  13 N  4 | Y  76% N  24% |
| Americas | Y  1 | Y  13 | – | Y  14 | Y  100% |
| Asia-Pacific | – | Y  5 | Y  2 | Y  7 | Y  100% |
| Europe and CIS | Y  9 | Y  15 N  4 | – | Y  24 N  4 | Y  86% N  14% |
| Arab States | – | Y  6 N  1 | – | Y  6 N  1 | Y  86% N  14% |
| TOTAL | Y  10 | Y  43 N  7 | Y  11 N  2 | Y  64 N  9 | Y  88% N  12% |
| % of response | Y  100% | Y  86% N  14% | Y  85% N  15% |  |  |

88% of the Administrations have a policy and planning department concerning the future use of the frequencies. The value can be linked with the 85% of administrations which have an allocation table because an allocation table allows the planning of future use of frequencies.

## 3.4	Assignments (generic): Questions 7, 8, 9 and 11

Background

A national process of assigning frequencies should be implemented to ensure that new frequency use does not cause unacceptable interference to existing users on a national and, sometimes, international basis.

The assignment process includes the analysis of requirements for proposed radio services together with any relevant studies, and the assignment of frequencies in accordance with the national frequency allocation plan. This plan should also include references to related actions necessary to co-ordinate the national radiocommunication systems with those of other countries in order to provide mutual protection from potential interference.

After successful completion of  the frequency assignment process,  a licence is issued that requires the collection of relevant licence fees and other possible charges. It provides the basis both for technical and administrative planning. Administratively, this procedure will account for the majority of the work and staffing in many frequency management organizations. Therefore, careful planning is required to develop an operational version of this procedure when establishing a (new) frequency management organization.. This procedure should also be the subject of regular review with adjustments made based on practical experience.

To apply for frequency assignment, a user typically will prepare and submit an application form (which may be different for each radio service or groups of services). The application for a frequency assignment will usually be included as a part of the more general Radio Licence Application, although this need not always be the case. In those cases where only a permit or authorization is required (as may be the case when a government agency is requesting a frequency assignment) the information required for a frequency assignment will be much the same as for a licence application but without much of the administrative and business related information.

Question 7a): Does your administration have a system (manual or computerized) to keep and maintain records of national frequency assignments and spectrum use (usually known as a Data Base Management System (DBMS))?

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response | % of response by region |
| --- | --- | --- | --- | --- | --- | --- |
| Africa | – | Y  6 | Y  14 N  1 | Y  20 N  1 | Y = 25 N  2 | Y  95% N  5% |
| Americas | Y  1 | Y  13 | – | Y  14 | Y  18 | Y  100% |
| Asia-Pacific | – | Y  8 | Y  2 | Y  10 | Y  13 | Y  100% |
| Europe and CIS | Y  10 | Y  16 | – | Y  26 | Y  33 | Y  100% |
| Arab States | – | Y  7 | – | Y  7 | Y  9 | Y  100% |
| TOTAL | Y  11% | Y  50% | Y  16% N  1% | Y  77% N  1% |  |  |

Virtually all the Member States (99%) have a system for keeping and maintaining records of frequency assignments. One LDC does not have such a system. This demonstrates its importance for managing frequency assignments.

Question 7b): Is there a single national DBMS or separate DBMS(s) for different users (for example a DBMS for assignments to government users and separate DBMS for assignments to non-government users)?

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | Si  0 Se  0 | Si  4 Se  2 | Si  12 Se  2 | Si  16 Se  4 | Si  20.78% Se  5.19% |
| Americas | Si  1 Se  0 | Si  12 Se  1 | Si  0 Se  0 | Si  13 Se  1 | Si  16.88% Se  1.30% |
| Asia-Pacific | Si  0 Se  0 | Si  6 Se  2 | Si  2 Se  0 | Si  8 Se  2 | Si  10.39% Se  2.60% |
| Europe and CIS | Si  4 Se  6 | Si  7 Se  9 | Si  0 Se  0 | Si  11 Se  15 | Si  14.29% Se  19.48% |
| Arab States | Si  0 Se  0 | Si  7 Se  0 | Si  0 Se  0 | Si  7 Se  0 | Si  9.09% Se  0.00% |
| TOTAL | Si  5 Se  6 | Si  36 Se  14 | Si  14 Se  2 | Si  55 Se  22 |  |  |
| % of response | Si  6% Se  8% | Si  47% Se  18% | Si  18% Se  3% | Si  71% Se  29% |  |  |
| Si: single; Se: separate |  |  |

Most Member States (71%) use a single database for all assignments. This preference is particularly pronounced in Africa, where deregulation is recent. The opposite tendency is observed in Europe (by 58% approximately).

Question 7c): What is the approximate size (at 2002) of your DBMS (number of frequency assignments)?

| Region | No response | < 1 000 | 1 000 < X < 10 000 | > 10 000 | Total |
| --- | --- | --- | --- | --- | --- |
| Africa | 3 | 9 | 7 | 2 | 21 |
| Americas | 2 | 2 | 4 | 6 | 14 |
| Asia-Pacific | 2 | 1 | 2 | 5 | 10 |
| Arab States | 2 | 1 | 2 | 2 | 7 |
| Europe and CIS | 2 | 1 | 6 | 18 | 27 |
| TOTAL | 11 | 14 | 21 | 33 | 79 |
| % of response | 14% | 18% | 27% | 42% |  |

A very considerable proportion of the returns (14%) gave no response. This may be due to difficulties understanding the question. For subsequent stages it should be re-worded. Several Member States still have less than one thousand frequency assignments, by contrast with the 72% of European countries having more than ten thousand.

Question 7d): What is the approximate size (at 2002) of your DBMS (number of licences)?

| Region | No response | < 1 000 | 1 000 < X < 10 000 | > 10 000 | Total |
| --- | --- | --- | --- | --- | --- |
| Africa | 5 | 11 | 3 | 2 | 21 |
| Americas | 3 | 3 | 4 | 4 | 14 |
| Asia-Pacific | 3 | 0 | 3 | 4 | 10 |
| Arab States | 2 | 1 | 2 | 2 | 7 |
| Europe and CIS | 1 | 6 | 4 | 16 | 27 |
| TOTAL | 14 | 21 | 16 | 28 | 79 |
| % of response | 18% | 27% | 20% | 35% |  |

Sixty-five administrations responded to this question. A very considerable proportion of the returns (18%) gave no response. Most of the latter are Least Developed Countries in Africa or in the Asia and Pacific region. The difficulty may be due to insufficiently clear wording in the question, allowing for some confusion between the number of networks per band and the number of licences. In the event, 27% of administrations have issued less than one thousand licences.

Question 7e): Are these frequency assignment records made available to public?

Seventy-seven Member States responded to this question. It emerged that 82% of administrations do not make their records available to the public. Presumably, privacy and security are the reasons. Nonetheless, some administrations are in the process of opening up. This may be a result of improved capabilities in protecting assigned frequencies and information contained.

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | Y  0 N  0 | Y  0 N  6 | Y  3 N  11 | Y  3 N  17 | Y  4% N  22% |
| Americas | Y  1 N  0 | Y  4 N  9 | Y  0 N  0 | Y  5 N  9 | Y  6% N  12% |
| Asia-Pacific | Y  0 N  0 | Y  0 N  8 | Y  1 N  1 | Y  1 N  9 | Y  1% N  12% |
| Europe and CIS | Y  2 N  8 | Y  3 N  13 | Y  0 N  0 | Y  5 N  21 | Y  6% N  27% |
| Arab States | Y  0 N  0 | Y  0 N  7 | Y  0 N  0 | Y  0 N  7 | Y  0.00% N  9% |
| TOTAL | Y  3 N  8 | Y  7 N  43 | Y  4 N  12 | Y  14 N  63 |  |  |
| % of response | Y  4% N  10% | Y  9% N  56% | Y  5% N  16% | Y  18% N  82% |  |  |

Question 7f): Is the DBMS computerized?

Seventy-seven response were received to this question. The trend is towards computerization (81%). 35% of responding African states had no computerized DBMS.

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | Y  0 N  0 | Y  4 N  2 | Y  9 N  5 | Y  13 N  7 | Y  17% N  9% |
| Americas | Y  1 N  0 | Y  12 N  1 | Y  0 N  0 | Y  13 N  1 | Y  17% N  1% |
| Asia-Pacific | Y  0 N  0 | Y  7 N  1 | Y  1 N  1 | Y  8 N  2 | Y  10% N  3% |
| Europe and CIS | Y  9 N  1 | Y  12 N  4 | Y  0 N  0 | Y  21 N  5 | Y  27% N  6% |
| Arab States | Y  0 N  0 | Y  7 N  0 | Y  0 N  0 | Y  7 N  0 | Y  9% N  0% |
| TOTAL | Y  10 N  1 | Y  42 N  8 | Y  10 N  6 | Y  62 N  15 |  |  |
| % of response | Y  13% N  1% | Y  55% N  10% | Y  13% N  8% | Y  81% N  19% |  |  |

Question 7g): What computerized DBMS do you use?

| Region | No response | Manual | Auto | Total |
| --- | --- | --- | --- | --- |
| Africa | 8 | 1 | 12 | 21 |
| Americas | 3 | 0 | 11 | 14 |
| Asia-Pacific | 2 | 0 | 8 | 10 |
| Europe and CIS | 6 | 0 | 21 | 27 |
| Arab States | 2 | 0 | 5 | 7 |
| TOTAL | 21 | 1 | 57 | 79 |
| % of response | 27% | 1% | 72% |  |

Details on the responses received are annexed to this document. Only one administration uses a manual database. However, it must be pointed out that a total of 21 Member States skipped this question in their responses to the questionnaire, whether because of the way the question was worded or because this information was considered too confidential. Several administrations use proprietary software running under Oracle or Unix. Others operate with lists drawn up in Excel or Access. WinBASMS in its current form is not being used on an exclusive basis by any administration. It would be useful to know the degree of advancement of the DMBS products used (BASMS, ASMS and so on).

Question 8: Coordination of frequency assignments with other countries

Background

Coordination of frequency assignments is essential for efficient sharing between radio stations within a given zone, or between different administrations or services. The procedures for coordination are clearly laid out in the relevant parts of the Radio Regulations. The Radiocommunication Bureau plays a crucial role, the ultimate purpose of which is to protect national radio systems against interference.

Question 8.1: Do you coordinate assignments to terrestrial stations?

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | 0 N  0 | Y  5 N  0 | Y  10 N  4 | Y  15 N  4 | Y  19% N  5% |
| Americas | 1 N  0 | Y  7 N  6 | Y  0 N  0 | Y  8 N  6 | Y  10% N  8% |
| Asia-Pacific | 0 N  0 | Y  6 N  2 | Y  1 N  1 | Y  7 N  3 | Y  9% N  4% |
| Europe and CIS | 11 N  0 | 1 Y  4 N  2 | Y  0 N  0 | 2 Y  5 N  2 | Y  32% N  3% |
| Arab States | 0 N  0 | Y  7 N  0 | Y  0 N  0 | Y  7 N  0 | Y  9% N  0% |
| TOTAL | 12 N  0 | Y  39 N  10 | Y  11 N  5 | Y  62 N  15 |  |  |
| % of response | Y  16% N  0% | Y  51% N  13% | Y  14% N  6% | Y  81% N  19% |  |  |

For this question there were 77 valid responses. The tendency is increasingly to practice coordination for frequency assignments to terrestrial stations. However, 21% of African administrations and 30% of administrations in the Asia-Pacific region do not yet do so.

Question 8.2: Do you coordinate assignments to space stations?

For this question there were 78 valid responses. The tendency is increasingly to practice coordination for frequency assignments to space stations, frequently with the involvement of the Radiocommunication Bureau. In the African and American regions one half of all states do not practice coordination.

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | Y  0 N  0 | Y  3 N  3 | Y  7 N  7 | Y  10 N  10 | Y  13% N  13% |
| Americas | Y  1 N  0 | Y  6 N  7 | Y  0 N  0 | Y  7 N  7 | Y  9% N  9% |
| Asia-Pacific | Y  0 N  0 | Y  7 N  1 | Y  1 N  1 | Y  8 N  2 | Y  10% N  3% |
| Europe and CIS | Y  11 N  0 | Y  14 N  2 | Y  0 N  0 | Y  25 N  2 | Y  32% N  3% |
| Arab States | Y  0 N  0 | Y  7 N  0 | Y  0 N  0 | Y  7 N  0 | Y  9% N  0% |
| TOTAL | Y  12 N  0 | Y  37 N  13 | Y  8 N  8 | Y  57 N  21 |  |  |
| % of response | Y  15% N  0% | Y  47% N  17% | Y  10% N  10% | Y  73% N  27% |  |  |

Question 9: Do you notify to the ITU those frequency assignments that are required to be notified by the Radio Regulations?

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | Y  0 N  0 | Y  4 N  2 | Y  10 N  5 | Y  14 N  7 | Y  18% N  9% |
| Americas | Y  1 N  0 | Y  6 N  6 | Y  0 N  0 | Y  7 N  6 | Y  9% N  8% |
| Asia-Pacific | Y  0 N  0 | Y  8 N  0 | Y  2 N  0 | Y  10 N  0 | Y  13% N  0% |
| Europe and CIS | Y  10 N  1 | Y  15 N  1 | Y  0 N  0 | Y  25 N  2 | Y  32% N  3% |
| Arab States | Y  0 N  0 | Y  7 N  0 | Y  0 N  0 | Y  7 N  0 | Y  9% N  0% |
| TOTAL | Y  11 N  1 | Y  40 N  9 | Y  12 N  5 | Y  63 N  15 |  |  |
| % of response | Y  14% N  1% | Y  51% N  12% | Y  15% N  6% | Y  81% N  19% |  |  |

Virtually all Member States (81%) notify their frequency assignments in accordance with the Radio Regulations. A point of interest that remains unexplored is the extent to which bilateral or multilateral agreements with neighbouring countries are used in the process of notifying and coordinating frequency assignments.

Question 11: Do you perform technical analyses of frequency assignment requests?

| Region | Developed countries | Developing countries | Least developed countries | Total | % of response |
| --- | --- | --- | --- | --- | --- |
| Africa | Y  0 N  0 | Y  6 N  0 | Y  13 N  2 | Y  19 N  2 | Y  24% N  3% |
| Americas | Y  1 N  0 | Y  12 N  1 | Y  0 N  0 | Y  13 N  1 | Y  17% N  1% |
| Asia-Pacific | Y  0 N  0 | Y  8 N  0 | Y  2 N  0 | Y  10 N  0 | Y  13% N  0% |
| Europe and CIS | Y  10 N  1 | Y  14 N  2 | Y  0 N  0 | Y  24 N  3 | Y  31% N  4% |
| Arab States | Y  0 N  0 | Y  5 N  1 | Y  0 N  0 | Y  5 N  1 | Y  6% N  1% |
| TOTAL | Y  11 N  1 | Y  45 N  4 | Y  15 N  2 | Y  71 N  7 |  |  |
| % of response | Y  14% N  1% | Y  58% N  5% | Y  19% N  3% | Y  91% N  9% |  |  |

A total of 78 responses from Member States were received to this question. Technical analyses for frequency assignment requests are conducted in 91% of the responding countries. It should be noted that analysis is essential to determine electromagnetic compatibility in frequency utilization and ensure that the new assignment does not cause harmful interference against existing services. Technical analysis considers such aspects as frequency, time and geographical separation between stations, and operates with technical parameters that include protection criteria, radiated power, propagation modes and bandwidth.

## 3.5	Spectrum management: Questions 6, 15 and 16

Q.6: Spectrum management costs

Radio spectrum management bears a cost for the administration. This cost is made of staff wages and by the amount of investment made, for computers and for monitoring equipment. To know this cost can be very useful for the administrations. It can help to fix the amount of spectrum usage fees.

The extensive text of responses from administrations is given in Annex 2-F.

Q.6a): What is the cost of providing national spectrum management functions in your country (if there is more than one organization or agency responsible for spectrum management please give the total costs if this information is available)? (Swiss Francs)

More than half of administrations did not fill this line. The spectrum management process can be very complex and it then becomes difficult to ensure the costs, in particular general overhead costs, are apportioned fairly between the licences for different types of radio use. The costs and charges of many administrations are open to public scrutiny (for example by a national audit office) and the mechanisms for raising revenue to pay for spectrum management must be seen to ensure that fees charged to one type of licence use is not (accidentally) subsidising the costs of another type of use. The situation is complicated further if more than one organisation has responsibility for spectrum management or if the organisation has responsibility for additional (e.g. non-radio) functions.

A future Questionnaire should take care to specify what has to be taken into account to evaluate the cost of spectrum management. Do we consider only the central organization or service in charge of planning and monitoring, or do we take into account the budget used for frequency management of all the organizations managing spectrum for themselves (administrations) or for third parties (operators)?

| Region | Developed | Developing | Least developed | Rate* |
| --- | --- | --- | --- | --- |
| Swiss francs (Hundreds) | Min. | Max. | Number of responses | Min. | Max. | Number of responses | Min. | Max. | Number of responses |  |
| Africa | – | – | – | nd. | nd. | 0 | 0.450 | 250 | 5 | 26% |
| Americas | – | 55 000 | 1 | 55.2 | 3 017 | 5 | – | – | – | 40% |
| Asia-Pacific | – | – | – | 250 | 2 500 | 3 | – | – | 0 | 37% |
| Arab States | – | – | – | 200 | 330 | 2 | – | – | – | 22% |
| Europe and CIS | 14 500 | 116 000 | 5 | 98 | 36 800 | 10 | – | – | – | 52% |
| Responses | 14 500 | 116 000 | 6 | 55.2 | 36 800 | 20 | 0.450 | 250 | 5 | 39% |
| * this rate corresponds to the number of responses per region on this question 6a) in comparison with the responses in Part II per region. |

Some form of cost and resource management information system must be put in place to enable the full costs to be determined with accuracy.

The responses are split between two extremes, 116 million SF and 450 SF.

Q.6b): What is the source of the funding required to accomplish these spectrum management functions?

Administrations may obtain their funds for spectrum management, usually from spectrum usage fees. These fees can be given directly to the organization in charge of spectrum management or paid to the Treasury, the spectrum management organizations being then funded by subventions from the general Budget.

Responses to the Questionnaire can be grouped in three main groups depending on how the spectrum management function is funded:

–	by a subvention from the general State Budget;

–	by the budget of the organization in charge of this function, regulatory authority or an agency of a ministry (either the financing comes from the general Budget, or from the fees directly affected to this organization) or in some cases, by the budget of the incumbent telecommunication operator (when the telecommunication sector reform is not fully achieved);

–	and in a limited number of Least Developed Countries, by donations from World Bank or UNDP.

Responses indicating a mixture of two of these groups are under column title “mixed”.

| Region | Developed (10) | Developing (45) | Least developed countries (14) | A |
| --- | --- | --- | --- | --- |
|  | General budget | Organization budget (fees) | Mixed | General budget | Organization budget (fees) | Mixed | General budget | Organization budget (fees) | Mixed |  |
| Africa | – | – | – | – | 4 | 1 | 2 | 7 | 3 | 17 |
| Americas | 1 | – | – | 6 | 6 | – | – | – | – | 13 |
| Asia-Pacific | – | – | – | 3 | 3 | – | 2 | – | – | 8 |
| Arab States | – | – | – | 2 | 2 | 1 | – | – | – | 5 |
| Europe and CIS | 2 | 5 | 2 | 5 | 10 | 1 | – | – | – | 25 |
| TOTAL | 3 | 5 | 2 | 16 | 25 | 3 | 4 | 7 | 3 | 68 |

More than half the administrations which answered to the Questionnaire use fees to directly fund spectrum management (were included responses showing a financing by the telecommunication which receives frequency usage fees). In developing countries, it is the main source of financing.

| Region | General budget | Fees or budget of the organization responsible for spectrum management | Mixed | Number of responses |
| --- | --- | --- | --- | --- |
| Africa | 2 | 11 | 4 | 17 |
| Americas | 7 | 6 | – | 13 |
| Asia-Pacific | 5 | 3 | – | 8 |
| Arab States | 2 | 2 | 1 | 5 |
| Europe and CIS | 7 | 15 | 3 | 25 |
| TOTAL | 23 | 37 | 8 | 68 |
| % of responses | 34% | 54% | 12% | 100% |

Q.15: Use of computers for national spectrum management

Seventy-eight exploitable responses (on one response, the corresponding page was missing) were received. This shows that the Questionnaire was perhaps a little too complex. More useful information would have been obtained if the responses had included an explanatory note, especially in the case of the Least Developed Countries.

An administration answered too late and its response could not be taken into account in this Questionnaire.

Of the 78 responses received, 30 asked for the updating of WinBASMS.

For Q.15m) to q), there are too few responses to draw any conclusions.

The full responses by administrations are listed in Annex 2-G.

Q.15a): Do you use computers for national spectrum management?

Q.15b): Type of computers

Q.15c): How many workstations and/or personal computers (PCs)?

Q.15d): Operating system(s)

Q.15e): Does your spectrum management system operate within a Local Area Network (LAN)?

Q.15a), c) and e)

Administrations using PCs or workstations and use of Local Area Network (LAN)

| Region | Developed (12) | Developing (50) | Least developed (15) | Total (77) |
| --- | --- | --- | --- | --- |
|  | PC and/or stations | LAN | PC and/or stations | LAN | PC and/or stations | LAN | PC and/or stations | LAN |
| Africa | – | – | 5 | 1 | 12 | 3 | 17 | 4 |
| Americas | 1 | 1 | 12 | 11 | – | – | 13 | 12 |
| Asia-Pacific | – | – | 6 | 6 | 2 | 0 | 8 | 6 |
| Arab States | – | – | 5 | 5 | – | – | 5 | 5 |
| Europe and CIS | 11 | 10 | 17 | 15 | – | – | 28 | 25 |
| TOTAL | 12 | 11 | 45 | 38 | 14 | 3 | 71 | 52 |
| % of responses | 100% | 92% | 90% | 76% | 93% | 20% | 92% | 68% |
| (Between brackets, the number of administrations having answered to this question) |

This question was perhaps not enough specific. In many responses, workstations and availability of PCs were mixed, resulting in figures ranging from 0.5 to 3 000 PC available.

Moreover,  some responses, listed only those PCs used for spectrum management (frequency allocations and files maintenance), while other responses included the entire PC equipment of the organization.

It should be noted that PC availability does not always mean that spectrum management is computerized. Six administrations (1 in Africa, 2 in Americas, 1in Arab States and 2 in Europe and CIS) do not have at their disposal PC for spectrum management.

Q.15f): Do you have access to the internet?

Q.15g): Does your administration provide a website on the internet to disseminate spectrum management information? If yes, please provide the address (URL) of the website:

Administrations having access to the internet and/or having a website:

| Region | Developed (11) | Developing (50) | Least developed (15) | Total (76) |
| --- | --- | --- | --- | --- |
|  | Internet access | WWW site | Internet access | WWW site | Internet access | WWW site | Internet access | WWW site |
| Africa | – | – | 5 | 2 | 11 | 8 | 16 | 10 |
| Americas | 1 | 1 | 13 | 9 | – | – | 14 | 10 |
| Asia-Pacific | – | – | 7 | 7 | 2 | 0 | 6 | 2 |
| Arab States | – | – | 6 | 2 | – | – | 9 | 7 |
| Europe and CIS | 10 | 8 | 17 | 11 | – | – | 27 | 19 |
| TOTAL | 11 | 9 | 48 | 31 | 13 | 8 | 72 | 48 |
| % of responses | 100% | 82% | 96% | 62% | 87% | 53% | 95% | 63% |
| (Between brackets, the number of administrations having answered to this question) |

Internet access is widely available. Construction of websites and their use for spectrum management are in progress, especially in developing countries.

Questions on Windows Basic Spectrum Management System (WinBASMS)

Q.15h): Are you aware that a Windows Basic Spectrum Management System is available from the ITU at no cost?

Q.15i): Has your administration used WinBASMS?

Q.15j): Has your administration had problems using WinBASMS?

Q.15k): Please list all problems that were encountered using WinBASMS.

Q.15l): Would you recommend using WinBASMS if the problems identified in (d) have been corrected?

| Region | Developed (10) | Developing (52) | Least developed (15) | Total WinBASMS (77) |
| --- | --- | --- | --- | --- |
|  | known/ used | difficulties/ recommended | known/ used | difficulties/ recommended | known/ used | difficulties/ recommended | known/ used | difficulties/ recommended |
| Africa | – | – | 4/2 | 2/4 | 12/5 | 10/11 | 16/7 | 12/15 |
| Americas | 1/0 | –/1 | 7/1 | 1/3 | – | – | 8/1 | 1/4 |
| Asia-Pacific | – | – | 5/1 | 1/1 | 1/1 | 0/1 | 6/2 | 1/2 |
| Arab States | – | – | 5/2 | 2/1 | – | – | 5/2 | 2/1 |
| Europe and CIS | 7/1 | 1/1 | 13/1 | 3/2 | – | – | 20/2 | 4/3 |
| TOTAL | 8/1 | 1/1 | 34/7 | 7/11 | 13/6 | 10/11 | 55/14 | 18/25 |
| % of responses | 80/10 | 10/10 | 65/13 | 13/61 | 87/40 | 67/73 | 71/18 | 23/32 |

Fifty-five administrations are aware of BASMS, i.e. 71% of responses, but 14, i.e. 18% use it, and 18, i.e. nearly one quarter indicate difficulties, either because they use it, or having given up the use of it because of these difficulties.

Almost one third of administrations of which some do not use it at present, would consider using WinBASMS if it was updated.

Q.15m): Do you need an enhanced spectrum management system if you answered no in (e)?

| Administrations having answered they need an enhanced system | Developed (10) | Developing (52) | Least developed (15) | Total | In % of responses of regions to Q.15 |
| --- | --- | --- | --- | --- | --- |
| Africa | – | 4 | 6 | 9 | 50% |
| Americas | – | 3 |  | 4 | 27% |
| Asia-Pacific | – | 2 | 1 | 4 | 57% |
| Arab States | – | 4 | – | 3 | 33% |
| Europe and CIS | 2 | 2 | – | 4 | 14% |
| TOTAL | 2 | 15 | 7 | 24 | 31% |
| % of responses | 20% | 29% | 47% |  |  |

Almost one third of administrations declared their need for an enhanced system, mostly in Africa and in Arab States. Nearly one half of the Least Developed Countries that responded to the questionnaire, declared their need for such a system.

Questions on Advanced Automated Spectrum Management Systems (AASMS)

Q.15n): Does your administration use an Automated Spectrum Management Systems (AASMS) ?

Q.15o): Has your administration had problems using your AASMS?

Q.15p): Please list all problems that were encountered using your AASMS

Q.15q): How would you propose to change the AASMS to correct or overcome these problems (please describe)?

| Region | Developed (10) | Developing (52) | Least developed (15) | Total AASMS (77) |
| --- | --- | --- | --- | --- |
|  | used | difficulties | used | difficulties | used | difficulties | used | difficulties |
| Africa | – | – | 0 | 1 | 2 | 1 | 2 | 2 |
| Americas | 1 | 1 | 4 | 2 | – | – | 5 | 3 |
| Asia-Pacific | – | – | 1 | 1 | – | 0 | 1 | 1 |
| Arab States | – | – | 3 | 0 | 0 | 0 | 3 | 0 |
| Europe and CIS | 3 | 0 | 0 | 0 | – | – | 3 | 0 |
| TOTAL | 4 | 1 | 8 | 4 | 2 | 1 | 14 | 6 |
| % of responses | 40% | 10% | 15% | 8% | 13% | 6% | 18% | 8% |

Q.16: Organization of spectrum management

There was a variety of responses from administrations on how they organized their national spectrum management. This variety of responses proved very difficult to analyze statistically.

One third of the 72 administrations that responded to all or some parts of Q.16 sent an organization chart for their administration. Responses were grouped as followed:

Organizational structure of spectrum management and recent or planned changes to this structure.

Q.16a): Please describe your country’s spectrum management structure and enclose a copy of the organization chart. The following aspects are of particular interest:

Q.16d): Have there been recent changes in this organizational structure or are changes planned (for example to take account of any changes in your government’s policy for telecommunications)?

One third of responses stated there had been recent or that changes were planned changes in the near future.

Responsibility of spectrum management, at the Ministry level or not, and responsibility given to a unique organization or shared between several organizations.

Q.16b): Is the spectrum management organization a separate ministry, department or agency reporting directly to the government or is it part of a larger government department (for example, a department responsible for all telecommunications)?

Q.16c): Is the responsibility for spectrum management contained within a single organization or is it shared between separate organizations (for example, some administrations have separate organizations for regulatory matters and policy matters, other administrations have separate organizations for government users and non-government users)?

The full text of responses is listed in Annex 2-H.

|  | Developed (10) | Developing (44) | Least developed (13) | Total (67) |
| --- | --- | --- | --- | --- |
| Level of responsibility for spectrum management | Ministry | Agency | Operator | Ministry | Agency | Operator | Ministry | Agency | Operator |  |
| Africa | – | – | – | 2 | 1 | 1 | 9 | 2 | 1 | 16 |
| Americas | 1 | – | – | 8 | 1 | 1 |  | – | – | 11 |
| Asia-Pacific | – | – | – | 5 | 1 |  | 1 | – | – | 7 |
| Arab States | – | – | – | 3 | 1 | 2 | – | – | – | 6 |
| Europe and CIS | 6 | 3 | – | 12 | 6 | 0 | – | – | – | 27 |
| TOTAL | 7 | 3 | – | 30 | 10 | 4 | 10 | 2 | 1 | 67 |
| % of responses | 70 | 30 | – | 68 | 23 | 9 | 77 | 15 | 8 | 100 |
| Total Ministry | 47 | % of total responses | 70% |  |  |  |  |  |
| Total Agency | 15 | % of total responses | 22% |  |  |  |  |  |
| Total Operator | 5 | % of total responses | 7% |  |  |  |  |  |

In 80% of responses, the responsibility for spectrum management is given to a unique organization.

| Unique organization or several organizations | Developed (10) | Developing (38) | Least developed (14) | Total (67 responses to Q.16) |
| --- | --- | --- | --- | --- |
| Organization | Unique | Several | Unique | Several | Unique | Several | Unique | Several |
| Africa | – | – | 3 | 1 | 13 | – | 16 | 1 |
| Americas | 1 | – | 8 | 2 | – | – | 9 | 2 |
| Asia-Pacific | – | – | 6 | 1 | 1 | – | 7 | 1 |
| Arab States | – | – | 4 | 1 | – | – | 4 | 1 |
| Europe and CIS | 7 | 2 | 12 | – | – | – | 19 | 2 |
| TOTAL | 8 | 2 | 33 | 5 | 14 | – | 55 | 7 |
| % of responses | 80% | 20% | 87% | 13% | 100% | – | 82% | 10% |

Human resources

Q.16e): Number of specialist staff in national spectrum management?

Q.16f): Number of support staff in national spectrum management?

The number of specialist or support staff varies considerably according to the responses from the administrations. However, the responses did not always make a distinction between specialist staff and support staff.

The full text of responses is given in Annex 2-I.

| Region | Developed | Developing | Least developed | Total |
| --- | --- | --- | --- | --- |
| Staff | ( 100 | 99-10 | < 10 | ( 100 | 99-10 | < 10 | ( 100 | 99-10 | < 10 | ( 100 | 99-10 | < 10 |
| Africa | – | – | – | 0 | 2 | 1 | 0 | 2 | 12 |  | 4 | 13 |
| Americas | 1 | – | – | 1 | 5 | 7 | – | – | – | 2 | 5 | 7 |
| Asia-Pacific | – | – | – | 2 | 3 | 0 | – | – | 2 | 2 | 3 | 2 |
| Arab States | – | – | – | 0 | 5 | 2 | – | – | – | 0 | 5 | 2 |
| Europe and CIS | 5 | 2 | 3 | 4 | 12 | 2 | – | – | – | 9 | 14 | 5 |
| TOTAL | 6 | 2 | 3 | 7 | 27 | 12 | 0 | 2 | 14 | 13 | 31 | 29 |
|  | 11 | 46 | 16 | 73 |
| in % |  |  |  |  |  |  |  |  |  | 18% | 42% | 40% |

## 3.6	Spectrum monitoring: Questions 12, 13 and 14

Question 12 concerns technical monitoring facilities set up by administrations (fixed, mobile and transportable stations) for different parts of the radio spectrum.

It must be borne in mind that the purpose of technical monitoring with specialized stations is to assist administrations throughout the radio spectrum management process, including frequency assignment and planning. Thus, monitoring stations provide compliance information with respect to the technical requirements in the transmission licences, within the overall framework of radio spectrum management. Thus technical monitoring programmes are used to obtain precise data on currently valid assignments. Technical monitoring is an essential part of the spectrum management process, and the monitoring stations are an indispensable resource for effective technical monitoring of the spectrum at the national level.

Question 12: Do you perform radio monitoring of terrestrial radio services?

Sixty-five administrations responded to this portion of the questionnaire’s Part II (see Annex 2-J). A synopsis is provided in the following.

| Region | Developed Countries | Developing Countries | Least Developed Countries | Total | % of answers |
| --- | --- | --- | --- | --- | --- |
| Africa | – | 6 | 11 | 17 | 26% |
| Americas | 1 | 9 | – | 10 | 15% |
| Asia-Pacific | – | 5 | 1 | 6 | 9% |
| Europe and CIS | 8 | 16 | – | 24 | 38% |
| Arab States | – | 8 | – | 8 | 12% |
| TOTALS | 9 | 44 | 12 | 65 | 100% |

At the time of the previous questionnaire for Resolution 9, in 2001, responses were received from 71 administrations. The 9% drop results from different factors:

•	32 of the administrations which had responded in 2001 did not give a reply this time around.

•	29 new administrations which had not responded in 2001 did so in 2003 (mainly from Africa and Arab States).

If the responses received are tabulated on the basis of the ITU's membership of 189 States, the results by region are as follows:

| Region | Questionnaire | Change 2003-2001 |
| --- | --- | --- |
|  | 2003 | 2001 |  |
| Africa | 35% | 30% | +5% |
| Americas | 28% | 34% | –6% |
| Asia-Pacific | 16% | 37% | –11% |
| Europe and CIS | 43% | 49% | –6% |
| Arab States | 42% | 21% | +21% |

Among the 65 responses submitted by ITU Member States, several merely indicate that the State in question either does not possess any radio spectrum monitoring system or that transmission monitoring stations were at the acquisition or installation stage. They break down as follows:

| Region | No monitoring | Monitoring planned | Extension monitoring |
| --- | --- | --- | --- |
| Africa | 4 Least Developed Countries | – | 3 |
| Americas | 2 Developing countries | – | – |
| Asia-Pacific | 1 Least Developed Country | – | – |
| Europe and CIS | – | – | 1 |
| Arab States | 1 Developing Country | 2 | – |

As a result, the statistics presented in the following are based on the responses received from 55 Member States that actually possess and operate radio monitoring stations, which break down as follows:

| Region | Developed countries | Developing countries | Least developed countries | Total | % of answers |
| --- | --- | --- | --- | --- | --- |
| Africa | – | 5 | 8 | 13 | 24% |
| Americas | 1 | 7 | – | 8 | 15% |
| Asia-Pacific | – | 5 | – | 5 | 9% |
| Europe and CIS | 8 | 16 | – | 24 | 43% |
| Arab States | – | 5 | – | 5 | 9% |
| TOTALS | 9 | 38 | 8 | 55 | 100% |

### 3.6.1	Fixed monitoring stations

a)	How many fixed monitoring stations do you have?

b)	Please provide a brief list of the facilities available at your fixed monitoring stations (for example: receivers, spectrum analysers, direction finding equipment)

c)	What is the upper frequency limit of your fixed monitoring stations? ----- MHz

d)	What is the upper frequency limit of your fixed direction finding stations? ---- MHz

The results for fixed monitoring stations are broken down in Annex 2-K:

•	Chart 1: Fixed measurement stations

•	Chart 2: Fixed direction finding stations

The results may be summarized as follows:

| Region | Measurement stations (MS) | Direction finding Stations | Ratio MS/DF |
| --- | --- | --- | --- |
|  | Quantity | % of total | Quantity | % of total |  |
| Africa | 11 | 2% | 4 | 1% | 2.75 |
| Americas | 100 | 14% | 101 | 15% | ≈ 1 |
| Asia-Pacific | 237 | 33% | 237 | 35% | 1 |
| Europe and CIS | 352 | 49% | 326 | 48% | 1.08 |
| Arab States | 12 | 2% | 13 | 1% | 0.92 |
| TOTALS | 712 | 100% | 681 | 100% | 1.05 |

Closer examination shows that, on the basis of the responses sent in by administrations, 520 fixed stations for radio spectrum monitoring are accounted for by only six administrations:

| Region | Fixed stations | % of total | Administrations |
| --- | --- | --- | --- |
| Americas | 85 | 84% | 1 developed country |
| Asia-Pacific | 206 | 87% | 3 developed +1 developing countries |
| Europe and CIS | 229 | 65% | 1 developing country |

This means that six Member States are responsible for 520 monitoring stations, or 73% of all declared fixed monitoring stations.

#### 3.6.1.1	HF monitoring stations

In the 2003 questionnaire, for frequency bands between 960 MHz and 3 GHz including VHF and UHF, only two administrations in the Europe and CIS region reported fixed DF stations, for a total of two stations.

#### 3.6.1.2	VHF/UHF monitoring stations

Taking charts 1 and 2 from Annex 2-K, the responses may be meaningfully broken down into three categories on the basis of frequency bands.

|  | Fixed stations/Region |
| --- | --- |
| Frequency bands | Africa | Americas | Asia & Pacific | Europe &CIS | Arab States | Total |
| 1 GHz-2 GHz | 6 (1%) | 102 (15%) | 228 (33%) | 346 (50%) | 5 (1%) | 687 (100%) |
| 2 GHz-3 GHz | 4 (1%) | 98 (17%) | 207 (36%) | 266 (45%) | 5 (1%) | 580 (100%) |
| 20 MHz-1 GHz | 11 (2%) | 106 (15%) | 237 (33%) | 346 (48%) | 12 (2%) | 712 (100%) |

In summary, it may be noted that the Europe and CIS region accounts for some 50% of all declared fixed stations throughout the spectrum.

#### 3.6.1.3	Stations SHF

The results of the analysis of the number of fixed SHF (> 3 GHz) stations declared under the 2003 questionnaire may be compared with those declared under the 2001 questionnaire.

| Region | 2003 Questionnaire | 2001 Questionnaire |
| --- | --- | --- |
| Africa | – | – |
| Americas | – | 2 developed + 15-1 developing countries |
| Asia-Pacific | – | 10-1 developing countries |
| Europe and CIS | 3 (developed countries) + 137 3 (developing countries) | 8-1 (developed countries) |
| Arab States | – | – |
| TOTALS | • 137 stations • 19% of 712 declared stations • 6 countries • 9% of 65 countries | • 33 stations • 6% of 568 declared stations • 5 countries • 8% of 71 countries |

The above table shows:

•	a major increase of 315% in the number of fixed SHF stations, from 33 to 137; and

•	only the Europe & CIS region has declared fixed SHF stations, with a single administration possessing measurement and DF stations (a total of 14).

### 3.6.2	Mobile monitoring stations

e)	How many mobile monitoring stations do you have?

f)	Please provide a brief list of the facilities available in your mobile monitoring stations (for example: receivers, spectrum analysers, direction finding equipment)

g)	What is the upper frequency limit of your mobile monitoring stations? --- MHz

h)	What is the upper frequency limit of your mobile direction finding stations? --- MHz

The main function of mobile monitoring stations is to carry out all monitoring of emission characteristics that cannot be undertaken (easily) by fixed centres, either on account of the magnitude of the measurement in question, or of difficulties resulting from spectrum congestion or to locate the exact position of a transmission. This is particularly true for all monitoring carried out on frequencies above 30 MHz, where the low transmitter power, higher antenna directivity and, in particular, propagation characteristics make effective measurements from fixed positions impossible.

A detailed analysis of the number of mobile stations declared by the 60 administrations is given in Annex 2-K:

•	Chart 3 (mobile measurement stations)

•	Chart 4 (mobile radio direction-finding stations)

The results of the analysis are as follows:

| Region | Mobile measurement stations (MS) | Mobile direction-finding stations | Ratio Mobile MS /Mobile DF |
| --- | --- | --- | --- |
|  | Qty | % of total | Qty | % of total |  |
| Africa | 5 | 2% | 7 | 2% | 0.71 |
| America | 16 | 5% | 15 | 5% | 1.07 |
| Asia-Pacific | 86 | 28% | 85 | 28% | 1.01 |
| Europe and CIS | 194 | 63% | 185 | 62% | 1.05 |
| Arab States | 8 | 2% | 8 | 3% | 1 |
| TOTALS | 309 | 100% | 300 | 100% | 1.03 |

It may be noted that virtually all (97%) mobile stations have both measurement and DF capabilities.

In addition, the results show that four administrations (or 6%) have declared 192 stations between them, i.e. 62% of all declared mobile stations.

| Region | Stations | % total | Administrations |
| --- | --- | --- | --- |
| Asia-Pacific | 71 | 83 | 2 developing countries |
| Europe and CIS | 121 | 62 | 2 developing countries 2 developed countries |

#### 3.6.2.1	HF stations

For the 2003 questionnaire, Part I, frequency bands between 960 MHz and 3 GHz, only three administrations declared mobile HF stations with exclusive DF functionality, for a total of 59 stations.

#### 3.6.2.2	VHF/UHF stations

For VHF/UHF (20 MHz-3 GHz) mobile stations, three groups of stations may be distinguished, depending on the frequency bands.

| Frequency band | Mobile Measurement Stations per Region |
| --- | --- |
|  | Africa | Americas | Asia & Pacific | Europe & CIS | Arab States | Total |
| 20 MHz-1 GHz | 5 (1%) | 16 (5%) | 86 (28%) | 194 (63%) | 8 (3%) | 309 (100%) |
| 1 GHz-2 GHz | 3 (2%) | 16 (8%) | 13 (6%) | 165 (82%) | 4 (1%) | 201 (100%) |
| 2 GHz-3 GHz | 1 (1%) | 16 (8%) | 8 (4%) | 162 (85%) | 4 (2%) | 191 (100%) |

In conclusion, it should be noted that the Europe and CIS region represents some 70% of all mobile stations declared, in all frequency bands.

#### 3.6.2.3	SHF stations

The results of the analysis of the number of mobile SHF (> 3 GHz) stations declared under the 2003 questionnaire may be compared with those declared under the 2001 questionnaire.

| Region | 2003 Questionnaire | 2001 Questionnaire |
| --- | --- | --- |
| Africa | – | – |
| Americas | 8 stations (up to 4 GHz) | 9 stations (up to 40 GHz) |
| Asia-Pacific | – | – |
| Arab States | 1 station (up to 18 GHz) | – |
| Europe and CIS | 84 stations (up to 50 GHz) | 55 stations (up to 105 GHz) |
| TOTALS | • 93 stations • 30% of 309 mobile stations | • 64 stations • 11% of 600 mobile stations |

The data gathered leads to the following observations:

•	Growth in the number of mobile SHF stations from 64 to 93, i.e. +145%.

•	SHF mobile stations increased by 173%.

•	Only two administrations (Europe and CIS) have mobile stations for measurement and DF: three in the range 20 MHz to 50 GHz and seven in the range 20 MHz to 20 GHz.

### 3.6.3	Transportable monitoring stations

i)	How many transportable monitoring stations do you have?

j)	Please provide a brief list of the facilities available in your transportable monitoring stations (for example: receivers, spectrum analysers, direction finding equipment)

k)	What is the upper frequency limit of your transportable monitoring stations?

l)	What is the upper frequency limit of your transportable direction finding stations?

This question concerns specifically transportable monitoring station systems, and was not present in the report on the 2001 questionnaire.

The results of the responses to the 2003 questionnaire that were received from the various administrations are presented in Annex 2-K.

Transportable monitoring stations are increasingly employed by administrations responsible for frequencies. They are used primarily for inspecting radio stations (licence compliance) and tracking down unauthorized or illegal transmitters. The results from the data received are presented in the table below.

| Region | Transportable Measurement Stations (MS) | Transportable Direction-Finding Stations (DF) | Ratio Transportable MS/DF |
| --- | --- | --- | --- |
|  | Quantity | % of Total | Quantity | % of Total |  |
| Africa | 8 | 2% | 1 | – | 8 |
| Americas | 5 | 1% | 6 | 1% | 0.83 |
| Asia-Pacific | 306 | 79% | 311 | 80% | 0.98 |
| Europe and CIS | 67 | 17% | 73 | 19% | 0.92 |
| Arab States | 2 | 1% | – | – | – |
| TOTAL | 388 | 100% | 391 | 100% | 0.99 |

Closer study shows that only two administrations declared 345 transportable monitoring stations.

| Region | Transportable stations | % of total | Administrations |
| --- | --- | --- | --- |
| Asia-Pacific | 300 | 0.98% | 1 developing country |
| Europe and CIS | 45 | 0.67% | 1 developed country |

These two administrations account for 89% of the overall market in transportable stations.

General observations

The responses which administrations provided to the 2003 questionnaire show an increase in the utilization of fixed monitoring stations by comparison with mobile monitoring stations:

N.B.: The ratio in 2001 was as follows:

0.94

It should be noted that the results from the 2001 questionnaire showed a total of 600 mobile stations, so that the ratio of mobile stations is:

This difference may be due to the fact that 32 of the administrations which participated in the 2001 questionnaire did not do so by 1 January 2003.

For the SHF band, the results give the following ratio:

N.B.: The ratio in 2001 was 2.24.

### 3.6.4	Space monitoring stations

m)	Do you perform space monitoring?

n)	Please provide a brief list of the facilities available at your space monitoring stations.

o)	What tasks does your space monitoring station perform for GSO satellite monitoring?

p)	What tasks does your space monitoring station perform for non-GSO satellite monitoring?

As with section 6.2 above, this is a new question not present in the 2001 questionnaire.

A total of three administrations responded to this question: China, Croatia and France. The responses are summarized below:

Space Monitoring

| China |
| --- |
| Facilities | Automatic measurement and analysis of signals (broadband receiver, vectorial signal analyser and C/Ku band antenna), location of interference sources (SATID) by means of fixed stations monitoring space emissions. |
| Tasks for GSO | – |
| Tasks for non-GSO | – |
| Croatia |
| Facilities | Monitoring of technical parameters and content |
| Tasks for GSO | – |
| Tasks for non-GSO | – |
| France |
| Facilities | The agency does not have its own resources for monitoring space transmissions. Since 2001 it has worked by agreement with the German Leeheim station, with which a cooperation MOU has just been signed for several years, covering the monitoring of satellites within the CEPT jurisdiction. The Leeheim station consists primarily of three receiving antennas covering the range 130 MHz-12.75 GHz and a control room housing the measuring and computing systems. |
|  | Main activites conducted at Leeheim | % of workload |
|  | Assistance with satellite network | 20% |
|  | Dealing with interference | 20% |
|  | Monitoring | 60% |
|  | The centre conducts observations of existing satellite systems. It also deals with requests for compatibility testing prior to satellite launches. |
| Tasks for GSO | The Leeheim station conducts the following basic operations for the agency • scanning an orbit or frequency band • creating identity files for satellites • monitoring satellite position |
| Tasks for non-GSO | For non-GSO satellites the agency’s work involves mainly: • measuring pfd • calculating trajectories • signal demodulation |

Radio monitoring requires hardware (e.g. earth stations) associated with a very high cost and advanced component technology, completely different from that used for HF, VHF or UHF.

Further to the response provided by France, various CEPT countries are working towards a Memorandum of Understanding (MOU) with the German Administration for joint use of the Leeheim station.

q)	Participation of administrations in the International Monitoring Programme of ITU

Fifty-nine administrations responded to this question (see Annex 5.2). From the responses, only 50 provided useful information, which is summarized below:

| Region | RESPONSES (International Monitoring Programme) |
| --- | --- |
|  | Total | Positive | Negative |
|  |  | Quantity | % of total | Quantity | % of total |
| Africa | 11 | 1 | 9% | 10 | 91% |
| Americas | 7 | 3 | 43% | 4 | 57% |
| Asia-Pacific | 6 | 1 | 17% | 5 | 83% |
| Europe and CIS | 21 | 8 | 38% | 13 | 62% |
| Arab States | 5 | – | – | 5 | 100% |
| TOTAL | 50 | 13 | 22% | 37 | 78% |

By way of a conclusion, it may be observed that only 28% of responding administrations stated that they participate in the International Monitoring Programme, representing 29% of all ITU Member States.

The results for the various administrations analysed by development region and category are given below.

| Region | Developed | Developing | Least developed | Total | % of responses |
| --- | --- | --- | --- | --- | --- |
| Africa | – | Y  0 N  4 | Y  1 N  6 | Y  1 N  10 | Y  9% N  91% |
| Americas | Y  1 | Y  2 N  4 | – | Y  3 N  4 | Y  43% N  57% |
| Asia-Pacific | – | Y  1 N  3 | N  2 | Y  1 N  5 | Y  17% N  83% |
| Europe and CIS | Y  4 N  2 | Y  4 N  11 | – | Y  7 N  13 | Y  38% N  62% |
| Arab States | – | N  5 | – | N  100 | N  100% |
| TOTAL | Y  5 N  2 | Y  7 N  27 | Y  1 N  8 |  |  |
| % of responses | Y  77% N  23% | Y  21% N  79% | Y  13% N  87% |  |  |

r)	Cooperation between spectrum management and monitoring

Please indicate the amount of work (in percentages) performed by the monitoring service for:

s)	frequency management department

t)	enforcement department

u)	licence department

The results of the analysis of the responses sent in by the different administrations (a total of 40 usable answers were received) are given in Annex 2-L.

| Region | Countries | Average score, by department |
| --- | --- | --- |
|  |  | Frequency management | Enforcement | Licence |
| Africa | 8 | 28.62% | 40.75% | 30.63% |
| Americas | 6 | 33.33% | 39.17% | 27.50% |
| Aisa-Pacific | 4 | 37.50% | 37.50% | 25.00% |
| Europe and CIS | 19 | 36.95% | 35.58% | 27.47% |
| Arab States | 3 | 33.33% | 21.67% | 45% |
| TOTAL | 40 | 34% | 35% | 31% |

These results lead to the conclusion that, overall, the monitoring service provides support on a roughly equal basis of one third each to the frequency management, enforcement and licence department.

Inspection of radio stations

Q.13: Do you perform Inspections on Radio Stations?

The purpose of inspecting radio stations is to verify that radio stations, whether new or existing, comply fully with the technical requirements stipulated in their licences, in particular, that any new station does not cause unacceptable interference to existing stations in operations.

Result statistics

Annex 2-M gives the results country by country, for 71 administrations.

A synopsis of the results by region and by category of economic development is given in the table below.

| Region | Developed | Developing | Least developed | Total | % of responses |
| --- | --- | --- | --- | --- | --- |
| Africa | – | Y  6 | Y  6 N  4 | Y  12 N  4 | Y  75% N  25% |
| Americas | N  1 | Y  11 N  2 | – | Y  11 N  3 | Y  79% N  21% |
| Asia-Pacific | – | Y  5 | Y  2 | Y  7 | Y  100% |
| Europe and CIS | Y  9 | Y  20 | – | Y  29 | Y  100% |
| Arab States | – | Y  5 | – | Y  5 | Y  100% |
| TOTAL | Y  9 N  1 | Y  47 N  2 | Y  8 N  4 | Y  64 N  7 | Y = 90% N = 10% |
| % of responses | 14% | 69% | 17% |  |  |

The results in the above table show that 90% of administrations conduct inspections of radio station sites.

Question 13 was expanded into subsidiary questions a) to e) to discover the exact administrative, legal and technical resources which administrations have at their disposal to ensure radio station inspections are carried out in the best possible manner.

a)	What inspection techniques are used by your administration to determine that users of the spectrum are complying with national or international requirements?

From the 64 administrations which responded positively to the question on radio station inspection, we received 71 responses to point a), of which 60 could be used, due to certain administrations (8) which did not reply to point a) and three others which replied in the negative were all LDCs.

From an examination of the responses listed in Annex 2-L for item a), the following conclusions may be drawn. All the administrations that conduct radio station inspections do so in accordance with national legislation and regulations, using the technical means at their disposal to verify that station facilities are in full compliance with the technical requirements stipulated in their transmission licences.

b)	What are the administrative procedures that determine your inspection policy (for example the number of inspections, type of notification provided prior to inspection, rules and regulations)?

From the responses sent in by 77 administrations, only 49 could be used (71%) for this item, for the following reasons:

•	18 administrations did not reply:

| Region | Developed | Developing | Least developed |
| --- | --- | --- | --- |
| Africa | – | 2 | 7 |
| Americas | – | 1 | – |
| Asia-Pacific | – | 1 | 1 |
| Europe and CIS3 | 1 | 3 | – |
| Arab States | – | 2 | – |
| TOTAL | 1 | 9 | 8 |

•	5 administrations replied in the negative: 1 developed country and one developing from Americas, 1 Least Developed Country and one developing country from Africa, 1 developing country from Europe

From the analysis of the responses given in Annex 2-M, the following conclusion may be reached.

The vast majority of administrations bases its inspection policy for radio stations on the laws and regulations that are applicable on the national territory, using technical monitoring of stations with the means at their disposal with respect to licensing.

c)	What measurement equipment does your administration use to perform technical measurements at an inspection?

To carry out technical measures relating to radio station inspections, administrations require suitable technical equipment. Positive replies were received from 54 administrations, while:

•	fourteen administrations did not reply

| Region | Developed | Developing | Least developed |
| --- | --- | --- | --- |
| Africa |  |  | 5 |
| Americas |  | 2 | 1 |
| Asia-Pacific |  |  |  |
| Europe and CIS | 1 | 3 | – |
| Arab States | – | 2 | – |
| TOTAL | 1 | 7 | 6 |

•	two administrations (one developed from Americas and one least developed from Africa) stated that a) did not apply to them

•	one least developed administration from Africa stated that it lacked the technical equipment

It may be noted that the positive responses show that a great variety of measuring equipment is in use by administrations, but the most popular are spectrum analyzers, frequency meters and wattmeters, in addition to portable receivers or DF units, occasionally. Naturally, administrations also use mobile monitoring stations.

d)	What technical parameters does your administration measure when inspecting a radio system?

The responses sent in by administrations included 58 which could be used, compared to:

•	twelve administrations which did not reply, and

| Region | Developed | Developing | Least developed |
| --- | --- | --- | --- |
| Africa | – | – | 4 |
| Americas | – | 1 | – |
| Asia-Pacific | – | – | – |
| Europe and CIS | 1 | 3 | – |
| Arab States | – | 2 | – |
| TOTAL | 1 | 6 | 5 |

•	one administration (a developing country from the Americas) which replied in the negative.

The positive responses are given in Annex 2-M. They show a great variety in the technical parameters that are measured when inspecting radio systems, but in general they fall under the inspection parameters recommended by ITU-R. The vast majority of administrations state that the parameters verified as a priority are frequency, power and bandwidth (80%).

e)	What station records does your administration review when inspecting a radio station?

Out of the 71 administrations which replied to the general question about radio station inspection, only 50 valid replies were received for question e), because

•	seventeen administrations did not reply

| Region | Developed | Developing | Least developed |
| --- | --- | --- | --- |
| Africa | – | 2 | 4 |
| Americas | – | 2 | – |
| Asia-Pacific | – | 1 | 1 |
| Europe and CIS | 2 | 3 | – |
| Arab States | – | 2 | – |
| TOTAL | 2 | 10 | 5 |

•	four administrations replied in the negative:

•	1 developed from Europe (deregulation)

•	1 least developed from Africa (lack of resources)

•	2 developing from Americas

Without exception, the 50 administrations which provided a positive response stated that they use the technical and administrative information contained in the licences or frequency assignment databases and compare them to technical parameters measured in the field.

Q.14.1: Do you perform technical analyses of radio frequency interference complaints?

The response to this question makes it possible to assess how administrations handle interference complaints: administratively only or technically as well.

Result statistics

Annex 14 gives the responses received from a total of 69 administrations.

A synopsis of the results by region and by economic status is given below.

| Region | Developed | Developing | Least developed | Total | % of responses |
| --- | --- | --- | --- | --- | --- |
| Africa | – | Y  6 | Y  7 N  1 | Y  13 N  1 | Y  93% N  7% |
| Americas | Y  1 | Y  11 N  1 | – | Y  13 N  1 | Y  33% N  7% |
| Asia-Pacific | – | Y  5 | Y  2 | Y  7 | Y  100% |
| Europe and CIS | Y  9 | Y  17 N  1 | – | Y  26 N  1 | Y  96% N  4% |
| Arab States | – | Y  7 | – | Y  7 | Y  100% |
| TOTAL | Y  10 | Y  47 N  2 | Y  9 N  1 | Y  66 N  3 | Y  96% N  4% |
| % of responses | 14% | 72% | 14% |  |  |

96% of administrations carry out technical studies in response to interference complaints.

Another question was raised under item 14 of the questionnaire:

Q.14.2: Do you have an established consultation process, involving Government and non-government organization, for resolving these complaints?

The reply statistics are given in Annex 14 by administration (total of 68). A synopsis of the results by region and by economic status is given below.

| Region | Developed | Developing | Least developed | Total | % of responses |
| --- | --- | --- | --- | --- | --- |
| Africa | – | Y  4 N  2 | Y  1 N  7 | Y  5 N  9 | Y  36% N  64% |
| Americas | Y  1 | Y  6 N  6 | – | Y  7 N  6 | Y  54% N  46% |
| Asia-Pacific | – | Y  3 N  2 | Y  1 N  1 | Y  4 N  3 | Y  57% N  43% |
| Europe and CIS | Y  6 N  3 | Y  11 N  7 | – | Y  17 N  10 | Y  63% N  37% |
| Arab States | – | Y  4 N  3 | – | Y  4 N  3 | Y  57% N  43% |
| TOTAL | Y  7 N  3 | Y  28 N  20 | Y  2 N  8 | Y  37 N  31 | Y  54% N  46% |
| % of responses | 14% | 72% | 14% |  |  |

It is observed that only 54% of administrations responded in the affirmative.

## 3.7	Handbooks and reports

Question 17 is worded as follows: Do you use the ITU-R Handbooks and Reports on:

a)	National Spectrum Management, version 1995?

b)	Spectrum Monitoring, version 2002?

c)	Computer-aided Techniques for Spectrum Management, version 1999?

d)	Report SM.2012-1, Economic Aspects of Spectrum Management, version 2000?

ITU-R handbooks and reports are published to help frequency managers in the performance of their duties. The objective of this question is to determine to what extent, and at what level, these documents are used by administrations.

Eighty countries replied, i.e. some 42% of ITU Member States. Not all of those replies addressed the question adequately, unfortunately. Useful results (those that are sufficiently detailed and unambiguous) are available on:

•	Question a): 64 replies

•	Question b): 59 replies

•	Question c): 60 replies

•	Question d): 60 replies

A breakdown of responses by country, with distribution, is given in Annex 2-N, section 1 and 2.

ANALYSIS OF RESPONSES

Analysis of the responses allows the following conclusions to be drawn:

i)	With respect to question a), 78% of the responding countries stated that they used the National Spectrum Management handbook (1995 version). This indicates a good level of utilization. This is the most widely used of all the handbooks.

ii)	The Spectrum Monitoring handbook (2002 version) is little used. Almost 56% of responding countries are not using it at the moment. It should be pointed out that the French-language version of the document has not yet been published by ITU. Only five francophone countries were among those that stated they were using this handbook. In the future, it should be verified that a document is available in the appropriate versions, to avoid obtaining distorted results in response to such a question.

iii)	Utilization of the handbook “Computer-aided Techniques for Spectrum Management” (1999 version) remains weak, at some 42%. This is the handbook which is used least widely.

iv)	Report SM.2012-1 (“Economic Aspects of Spectrum Management”) (2000 version) meets a current need, but also a need that was expressed by developing countries in general. Against this background, its level of utilization, at merely 52%, is disappointing.

A number of countries stated that they had taken steps to acquire handbooks which they did not have in their possession.

## 3.8	Problems

Question 18: Identification of problems experienced in national spectrum management.

Please use the following table to describe problems experienced by your administration in national spectrum management. This information will be used by the ITU, in particular ITU-R Study Group 1, to identify future areas of work, within the normal study programme, so that effort may be focused on the development of recommendations and reports for subjects where assistance is most needed.

This question is a summary of the problems as identified by the responses for all questions.

A detailed overview of all responses to this question is in Annex 2-O.

In analysing the responses to this question it can be noted that there is a variety of topics indicated.

The responses can be divided in a number of categories:

•	Sometimes remarks are given to improve some situations;

•	In other cases one can find real questions for explanation or requests for information on experiences by other administrations;

•	In many cases it is indicated that a certain activity cannot or hardly not performed because of:

–	the lack of experienced staff;

–	even the lack of staff;

–	lack of sufficient equipment (both hard- and software).

It is for this latter part of responses that many times the assistance of the ITU is asked for.

In the case of legislation one can find responses varying from not having a telecom law, the modification of the telecom law due to the development of new technology to the difficulties in the development of secondary legislation in telecommunications.

In case of planning functions many of the responses indicated that, due to the lack of sufficient hard- and software for a computerized frequency management system, this is a difficult problem for administrations.

Regarding AASMS (Advanced Automated Spectrum Management System) and WinBASMS one can find requests to improve WinBASMS and questions for more explanation for the first system.

To perform monitoring it is in many cases indicated that a substantial improvement of the facilities are needed. In many cases, the lack of monitoring equipment is hampering the overall process of good spectrum management.

Administrations also remarked that they were having difficulties in solving national interference problems and how to overcome interferences from stations in neighbouring countries.

There were recommendations to organize regional seminars on the various topics.

Last but not least there were requests for training courses for specialists on various spectrum management topics.

ANNEX  1-A

Index of submitters and designated focal points

(last revised July 9, 2003)

NOTE 1 – The individuals listed are designated focal points only for information relevant to the two WTDC Resolution 9 questionnaires that have been issued (ITU-D CA/08 and ITU-R CA/71 for Phase 1; ITU-D CA-12 and ITU-R CA-120 for Phase 2); requests for other information should be directed to the official ITU contact for Member States that is listed in the ITU Global Directory.

NOTE 2 – All of the information submitted in response the questionnaires can be found for Phase 1 (27.5-960 MHz) at:

http://www.itu.int/ITU-D/study_groups/SGP_1998-2002/JGRES09/Res9_Index.html

and for Phase 2 (960-3 000 MHz) at:

http://www.itu.int/ITU-D/study_groups/SGP_2002-2006/JGRES09/Res9_Index.html

| SUBMITTING ADMINISTRATION or ORGANIZATION ITU Code/Region | PHASE 1 RESPONSES INCLUDE Parts I/II | PHASE 2 RESPONSES INCLUDE Parts I/II/III | FOCAL POINTS DESIGNATED BY THE SUBMITTERS | Formats used: Word-- *.doc Spreadsheet-- *.xls Scanned-- *.pdf Power Point-- *.ppt Image-- *.gif Publisher-- *.pub Compressed-- *.zip | Language of submission Phone # Fax # Email address Link to Webpage |
| --- | --- | --- | --- | --- | --- |
| Albania ALB/1 | – | I/II/III | Loreta Andoni Radiocommunication Specialist Ministry of Transport and Telecommunication Scanderbeg Square, Tirana, Albania | *.doc | Submission in English Ph: +355 682 220903 Fx: +355 423 3772 loandoni@hotmail.com |
| Algeria ALG/1 | I/II | – | Houria Khenchelaoui Sous-Directeur de la Reglementation des Services Radio Ministere des P et T L1, Bol Krim Belkacem, Alger, Algeria | *.pdf | Submission in French Ph: 271 1220 Fx: 272 4957 |

| Angola AGL/1 | – | I/II/III | Domingos Pedro António Directeur Général Adjoint INACOM – Institut Angolais des Communications Av de Portugal, 92 –7° andar, Luanda, Angola | *.doc | Submission in French Ph: 002 44 2 338352 Fx: 002 44 2 339356 incom.dg@netangola.com |
| --- | --- | --- | --- | --- | --- |
| Antigua-and-Barbuda ATG/2 | – | I/II/III | Eustace Phillip Telecommunications Officer Ministry of Public Works and Communications St. John’s Street, St. John’s, Antigua and Barbuda | *.doc | Submission in English Ph: 268 562 1868 Fx: 268 562 1872 phillipe@candw.ag |
| Argentina ARG/2 | I | – | Roberto Eduardo Perez Director Ejecutiveo de Relaciones Externas e Iniciativas Estrategicas Compania de Radiocomunicaciones Moviles S.A. Tucuman 744 Piso 2 – (1049) Buenos Aires, Argentina | *.pdf | Submission in Spanish Ph: 54 11 4321 5006 Fx: 54 11 4978 7373 rree@movi.com.ar |
| Armenia ARM/1 | I/II |  | Phase 1 Arthur Andreassyan Administrative Director Armenia/Republican Center of Telecommunications SCJSC Ministry of Posts and Telecommunications 2, Mkhitar Heratsi Str. Yerevan 375025 Republic of Armenia | *.doc | Submission in English Ph: 3742 52 79 22 Fx: 3742 52 60 32 |

|  |  | I/II/III | Phase 2 Ashot Verdyan Director Republican Centre of Telecommunications – closed stock company 29, Tbilisian Highway Yerevan, 3750941 Republic of Armenia | *.doc | Submission in English Ph: 374 1 28 87 17 Fx: 374 1 28 86 83 ether@web.am |
| --- | --- | --- | --- | --- | --- |
| Austria AUT/1 | I/II | – | Gerd Lettner Federal Ministry for Science and Transport P.O. Box 127, A-1103 Vienna, Austria | *.pdf | Submission mostly in English and partly in German Ph: 43 17 9731 4200 Fx: 43 17 9731 4209 Gerd.lettner@bmv.gv.ost |
| Bahamas BAH/2 | – | I/II/III | John Halkitis Senior Telecommunications Engineer Public Utilities Commission Fourth Terrace, East, Collins Avenue P.O. Box N-4860 Nassau, Bahamas | *.doc | Submission in English Ph: 1 242 322 4437 Fx: 1 242 323 7288 ahalkitis@PUCBahamas.gov.bs Note: Bahamas uses the ITU Region 2 and the United States Spectrum Allocation Tables |
| Bahrain BHR/1 | – | I/II/III | Abdulla Al-Thawadi Director Directorate of Wireless Licensing Frequency and Monitoring P.O. Box 26627 Manama Kingdom of Bahrain |  | Submission in English Ph: 973 715111 Fx: 973 715030 dlmf@batelco.com.bh |

| Bangladesh BGD/3 | I/II | – | S.M. Zabed Robbani Divisional Engineer (Frequency and Wireless) Ministry of Post and Telecommunication/ Frequency and Wireless Board Telecommunication Training Center Tejgaon, Dhaka 1208 Bangladesh | *.doc | Submission in English Ph: 880 2 9883181 Fx: 880 2 988 4299 zrobbani@hotmail.com |
| --- | --- | --- | --- | --- | --- |
| Belarus BLR/1 | II | – | Anatoly Budai First Deputy Minister Ministry of Posts and Telecommunications 10 Skoryna Ave. 220050 Minsk, Republic of Belarus | *.pdf | Submission in English Ph: 375 172 272 526 Fx: 375 172 260 848 SRFC@mpt.gov.by |
| Belgium BEL/1 | II | – | Michael Vanroogenbroek Ingenieur – Conseiller IBPT Ave. de l'Astronomie 14 Bte 21 B-1210 Bruxelles, Belgique | *.pdf | Submission is in French Ph: +32 2 226 8800 Fx: +32 2 226 8882 michael.vandroogenbroek@ibpt.be |
| Belize BLZ/2 | I/II | – | Clifford M. Slusher Director Office of Telecommunication P.O. Box 310 Belize City, Belize | *.pdf | Submission in English Ph: 501 2 24938 Fx: 501 2 24939 |
| Bhutan BTN/3 | – | I/II/III |  |  |  |

| Bolivia BOL/2 | I/II | – | Jose Alfredo Arce Jofre Director General de Comunicaciones Direccion General de Comunicaciones Avenida Mariscal Santa Cruz, Esquina Oruro, Edificio Palacio de Comunicaciones, Piso 4 Bolivia | *.doc | Submission in Spanish Ph: 591 2 378129 Fx: 591 2 371360 mtccom@caoba.entelnet.bo |
| --- | --- | --- | --- | --- | --- |
| Bosnia and Herzegovina BIH/1 | – | I/II | Ms. Krivosic Amina Expert in Spectrum Division of CRA Communication Regulatory Agency 10, Vilsonovo setaliste 71000 Sarajevo Bosnia and Herzegovina | *.doc | Submission in English Ph: 387 33 250600 Fx: 387 33 713 080 akrivosic@cra.ba |
| Botswana BOT/1 | – | I/II/III | Tshoganetso Kepaletswe Chief Engineer, Radio Services Botswana Telecommunication Authority Plot 206 & 207 Independence Avenue Private Bag 00495 Gaborone, Botswana |  | Submission in English Ph: 267 395 7755 Fx: 267 395 7976 kepaletswe@bta.org.bw |
| Brazil B/2 | I/II | – | Haroldo Motta Engineer Agencia Nacional de Telecomunicações – ANATEL SAS – Quadra 6 Bloco H, 60 Andar Brazilia – DF, Brazil 70 313-900 | *.zip *.doc | Submission partly in Spanish (Part 1) and partly in English (Focal point and Part 2) Ph: 55 61 312 2373 Fx: 55 61 312 2328 haroldo@anatel.gov.br |

| Bulgaria BUL/1 | I/II | – | Nikola Mantchev Committee of Posts and Telecommunications 6 Gourko St. Sofia 1000, Bulgaria ------------ Grigor Grigorov Director of Frequency Management_Directorate State Telecommunications Commission 6 Gourko St Sofia 1000, Bulgaria | *.doc | Submission in English Ph: 359 2 949 2606 Fx: 359 2 987 9540 nmanchev@cpt.bg Ph: 9492327 Fx: 9492198 spectrum@acpt.bg |
| --- | --- | --- | --- | --- | --- |
| Burkino Faso BFA/1 | I/II | I/II/III | Phase 1 and Phase 2 Pousbilo Ouedrraogo Directeur de la Gestion du Spectre (DGS) Authorité nationale de régulation des télécommunications (ARTEL) 01 BP 6437 Ouagadougou 01 Burkina Faso | *.pdf-Phase 1 *.doc-Phase 2 | Submission in French Ph: (226) 33 41 98/99 33 51 87 Fx: (226) 33 50 39 pousbil@artel.bf |
| Burundi BDI/1 | I/II | I/II/III | Phase 1 Constaque Hakizimana Chef de Service Technique A.R.C.T Bujumbino Avenue Bururi No. 5 BP 6702 Burundi | *.pdf-Phase 1 *.doc-Phase 2 | Submission in French and provides some specific assignments Ph: 257 210276 Fx: 257 210269 |

|  |  |  | Phase 2 Deogratias Bizindavyi Chef chargé de la gestion du spectre des fréquences Agence de régulation et de contrôle des télécommunications (ARCT) Avenue Patrice Lumumba Burundi |  | Submission in French Ph: + 257 210 276 Fx: + 257 242 832 deobizi@caramail.com |
| --- | --- | --- | --- | --- | --- |
| Cameroon CME/1 | I/II | I/II/III | Phase 1 and Phase 2 Simplice Zanga Yene Chef de la cellule des études et de la planification du spectre à l'agence de régulation des télécommunication du Cameroun BP 6132 ART Yaoundé République du Cameroun | *.pdf-Phase 1 | Submission in French Ph: (237) 230 380 Fx: (237) 233 748 simplice.zanga@camnet.cm |
| Canada CAN/2 | I/II | I/II/III | Phase 1 Thomas Racine Director, Automated Spectrum Management Systems Industry Canada 300 Slater Street, Rm B1240 Ottawa, Ontario Canada K1A0C8 | *.doc | Submission in English Ph: +1 613 990 4767 Fx: +1 613 990 7287 racine.thomas@ic.gc.ca |

|  |  |  | Phase 2 Barry Isherwood International Regulations Officer Industry Canada 300 Slater Street, Rm 1538B Ottawa, Ontario Canada K1A0C8 | *.doc | Further information can be found at http://strategis.ic.gc.ca/SSG/sf01608e.html Submission in English Ph: +1 (513) 998 3778 Fx: +1 (613) 952 9871 isherwood.barry@ic.gc.ca |
| --- | --- | --- | --- | --- | --- |
| Central Africa, Republic of CAF/1 | – | I/II/III | Josue Yongoro Chargé de Mission Ministère des postes et télécommunications Rue Gallieni, Bangui République Centrafricaine | *.doc | Submission in French Ph: +236 615 622 Fx: +236 612 313 yongoro@intnet.cf |
| CEPT/ERC | I | I | Phase 1 and Phase 2 Reiner Liebler Chairman ECC WG FM Regulatory Authority for Telecommunications and Posts P.O. Box 80 01 D – 55003 Mainz Germany | *.pdf *.doc | The submission is an extract of ERC Report 25 that can be found in its entirety at http://www.ero.dk/documentation/docs/doc98/official/pdf/REP025.PDF Ph: +49 6131 18 3110 Fx: +49 6131 18 5604 reiner.liebler@regtp.de |
| Chad TCD/1 | II | – | Guirdonan Mogalbaye Office national des postes et télécommunications | *.pdf | Submission in French |

| Chile CHL/2 | – | I/II/III | Pezoa Lizama Claudio Jefe Departmento Ingeniería y Adminstración del Espectro Radioeléctrico Subsecretaria de Telecomunicaciones Amunategui 139 Santiago, Chile | *.doc | Submission in Spanish Ph: 56 2 421 3665 Fx: 56 2 421 3549 cpezoa@subtle.cl |
| --- | --- | --- | --- | --- | --- |
| China CHN/3 | I/II | I/II/III | Phase 1 Yuansheng Xie Director Radio Regulatory Department 13 West Chang An Ave. Beijing 100804 Peoples Republic of China | *.pdf | Submission in English Ph: 86 10 6834 7623 Fx: 86-10-6836 6494 xieysh@srrc.gov.cn |
|  |  |  | Phase 2 Zhou Xingguo Deputy Director Ministry of Industry No, 80, BeiLiShi Road Beijing, China | *.doc | Submission in English Ph: +86 10 883 85038 Fx: +86 10 683 66494 zhouxg@srrc.gov.cn |

| Columbia CLM/2 | I/II | I/II/III | Phase 1 Néstor Alonso Jiménez Estrada Profesional Especializado Ministerio de Comunicaciones Carreras 7 y 8 Calles 12.a y 13.a, Edificio Murillo Toro, piso 4 Columbia | *.doc | Submission in Spanish Ph: 571 344 2357 Fx: 571 344 2206 intermin@mincomunicaciones.gov.co |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Phase 2 Gustavo Osorio Morales Profesional Universitario 3020-13 Ministerio de Comunicaciones Edificio Murillo Toro, Calle 13 carrera 8 Bogota D.C. Columbia | *.doc | Submission in Spanish Ph: 344 2357 Fx: 344 3445 ofinter3@mincomunicationes.gov.co |
| Comoros COM/1 | – | I/II/III | Mahamoud Abiamri Directeur des télécommunications Société nationale des postes et télécommunications (SNPT) B.P. 5000 Moroni Union des Comores | *.doc | Submission in French Ph: +269 74 43 20 Fx: +269 73 03 02 abiamri@snpt.km |
| Costa Rica CTR/2 | – | I/II/III | Guillermo Rivero Gonzales Proceso Transmisión, UEN DEP. Instituto Costarricense de Electricidad y Telecomunicaciones (ICE) Piso 10, Oficinas Centrales del ICE San Jose, Costa Rica | *.doc | Submission in Spanish Ph: (506) 220 6969 Fx: (506) 220 6961 grivero@ice.go.cr |

| Côte d'Ivoire CTI/1 | I/II | I/II/III | Phase 1 Ebou Kouatchi Le Directeur General Agence des télécommunications de Côte d'Ivoire Immeuble Postel 2001 Rue Lecoeur- Plateur 18 BP 2203 Abidjan 18 Côte d'Ivoire | *.pdf | Submission in French Ph: 34 42 56 or 34 42 55 Fx: 34 42 58 |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Phase 2 Kouakou JB Yao Direcreur ATCI 18 BP 2203 Abidjan 18 Côte d'Ivoire | *.doc | Submission in French Ph: 225 203 44973 Fx: 225 203 44965 yao.kouakou@ties.iitu.int |
| Croatia HRV/1 | I/II | I/II/III | Phase 1 DOMINIK FILIPOVIĆ Director Croatian Institute of Telecommunications Prisavlje 14, HR-10000 Zagreb Croatia | *.doc | Submission in English Ph: + 385 1 616 91 10 Fx: + 385 1 619 66 62 dominik.filipovic@telekom.hr |
|  |  |  | Phase 2 Ante Dodig Director Croatian Institute for Telecommunications Jurisiceva 13 HR-10000 Zagreb Croatia | *.doc | Submission in English Ph: 381 148 96000 Fx: 385 149 20227 info@telekom.hr |

| Cuba CUB/2 | – | I/II | Jesús Antonio Gonzalez Vidal Ingeniero Especialista Superior Ministerio de la Informatica y las Comunicaciones MIC Plaza de la Revolucion Ave. Rancho Boyeros y 19 de Mayo La Habana, Cuba | *.doc | Submission in Spanish Ph: +537 668 039 Fx: +537 335 193 jesus@mic.cu |
| --- | --- | --- | --- | --- | --- |
| Cyprus CYP/1 | II | I/II | Phase 1 Andronicos Kakkouras Telecommunications Officer Ministry of Communications and Works Directorate of Telecommunications CY-1424 Lefkosia (Nicosia), Cyprus | *.pdf | Submission in English Ph: +357 2 800206 Fx: +357 2 776254 kakkouras@mcw.gov.cy |
|  |  |  | Phase 2 Anatasios Elia Telecommunications Officer Ministry of Communications and Works 28 Achaion, CY-1101 Nicosia, Cyprus | *.doc | Submission in English Ph: 357 22 800 209 Fx: 357 22 776 254 a.elia@mcw.gov.cy |
| Czech Republic CZE/1 | I/II | I/II/III | Phase 1 Ludmila HALOUSKOVÁ Department of Frequency Spectrum Management Ministry of Transport and Communications – Czech Telecommunication Office Klimentská 27, CZ-225 02 Praha 1, Czech Republic | *.doc | Submission in English Ph: +420 2 24006 666 Fx: +420 2 2491 1658 halouskoval@ctu.cz |

|  |  |  | Phase 2 Petr Zeman Ing. Czech Telecommunication Office Post Box 02 225 02 Praha 025 Czech Republic |  | Submission in English Ph: 420 224 004 736 Fx: 420 224 004 817 zemanp@ctu.cz |
| --- | --- | --- | --- | --- | --- |
| Denmark DNK/1 | I/II | – | Claus B. Mortensen Master of Law/Economics Officer The National Telecom Agency Holsteinsgade 63, DK-2100 Copenhagen, DENMARK | *.doc | Submission in English Ph: +45 35 45 02 31 Fx: +45 35 45 00 16 cbm@tst.dk |
| Egypt EGY/1 | II | I/II/III |  | *.pdf | Submission in English |
| El Salvador SLV/2 | – | I/II/III | Víctor Manuel Artiga Gerente de Telecomunicaciones SIGET 6.a 10.a Calle Poniente Y 37 Avenida Sur N.° 2001 Colonia Flor Blanca San Salvador | *.doc | Submission in Spanish Ph: 503 257 4438 Fx: 503 257 4495 vartiga@siget.gob.sv |

| Eritrea ERI/1 | I/II | I/II/III | Phase 1 and Phase 2 Teklehaimanot Mogos Zerai Director, Standards and Regulatory Division Ministry of Transport and Communications Department of Communications Harnet Street P.O. Box 4918 Asmara, Eritrea | *.pdf-Phase 1 *.doc-Phase 2 | Submission in English Ph: 29 11 126 965 29 11 120 555 29 11 123 692 Fx: 29 11 126 966 zerait@eol.com.er |
| --- | --- | --- | --- | --- | --- |
| Estonia EST/1 | I | I/II/III | Phase 1 Julia Arold Head of Radiocommunication Development Office Technical Planning Department Estonian National Communications Board Adala 4d Estonia | *.pdf-Phase 1 | Submission in English Ph: +372 693 1163 Fx: +372 693 1155 arold@sa.ee |
|  |  |  | Phase 2 Jaak Joesoo Estonian National Communications Board 10614 Adala 2 Tallinn, Estonia | *.doc-Phase 2 | Submission in English Ph: 372 693 1154 Fx: 372 693 1155 postbox@sa.ee |

| Ethiopia ETH/1 | I/II | I/II/III | Phase 1 Getachew Kebede Head of Frequency Management Division Ethiopian Telecommunications Agency P.O. Box 9991 Addis Ababa, Ethiopia | *.pdf-Phase 1 | Submission in English Ph: 251 1 515 766 Fx: 251 1 551 253 tele.agency@telecom.net.et |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Phase 2 Samson Tadesse Engineer, Frequency Management Ethiopian Telecommunication Agency Debrezeit Rd. Tegene Bldg. P.O. Box 9991 Addis Ababa, Ethiopia | *.doc-Phase 2 | Submission in English Ph: 251 1 668 282 Fx: 251 1 655 763 tele.agency@telecom.net.et |
| Finland FIN/1 | I/II | I/II/III | Phase 1 and Phase 2 Margit Huhtala Head of Frequency Division Finnish Communications Regulatory Authority P.O. Box 313 00181 Helsinki Finland | *.pdf-Phase 1 *.doc-Phase 2 | Submission in English Refers to CEPT/ERC/WGFM submission which includes European Allocation Table (ERC Report 25) that can be found in its entirety at http://www.ero.dk/documentation/docs/doc98/official/pdf/REP025.PDF Ph: +358 9 6966 425 Fx: +358 9 6966 410 margit.huhtala@ficora.fi http://www.thk.fi |

| France F/1,2,3 | II | I/II/III | Phase 1 and Phase 2 Ms. Béatrice Durand Direction de la planification du spectre et des affaires internationales, Département Affaires UIT Agence nationale des fréquences BP 400 F- 94704 Maisons Alfort Cedex France | *.pdf-Phase 1 *.doc-Phase 2 | Submissions in French Ph: +33 1 45 18 72 15 Ph: +33 1 45 18 73 13 durand@anfr.fr |
| --- | --- | --- | --- | --- | --- |
| Gabon GAB/1 | I/II | I | Louis Nkogiie Ndong Chef de Division des Relations Techniques Internationales Office des Postes et Telecommunications B.P. 20 000 Libreville Gabon | *.pdf-Phase 1 *.doc-Phase 2 | Submission in French Ph: 241 78 71 21 Fx: 241 78 71 17 2nl@opt.ga |
| Georgia GEO/1 | I/II | – | Alexander Tsivtsivadze Director Ministry of Post and Communications, Post and Communication Supervision Service 46, Tevdore Mghvdeli St., Tbilisi, 380054, Georgia | *.doc | Submission in French Ph: 241 78 71 21 Fx: 241 78 71 17 2nl@opt.ga |

| Germany D/1 | I/II | – | Bernd-Dieter Wolko Administrative Officer Regulatory Authority for Telecommunications and Posts (RegTP) Canisiusstrasse 21 D-55122 Mainz Germany | *.pdf *.doc | Submission in English Refers to CEPT/ERC/WGFM submission which includes European Allocation Table (ERC Report 25) that can be found in its entirety at http://www.ero.dk/documentation/docs/doc98/official/pdf/REP025.PDF Ph: 00 49 6131 18 3111 Fx: 00 49 6131 18 5604 Bernd-dieter.Wolko@regtp.de |
| --- | --- | --- | --- | --- | --- |
| Greece GRC/1 | I/II | I/II/III | Phase 1 Nissim Benmayior Head of Department Minstry of Transport and Communications 2, Anastaseos Str. GR-101 91 Athens Greece | *.pdf-Phase 1 | Submission in English Ph: +301 650 8571 Fx: +301 650 8570 ymegde@hol.gr |
|  |  |  | Phase 2 George Drossos Engineer Ministry of Transport and Communications 2 Anastaseos Str. Papagou 101 91 Athens Greece | *.doc-Phase 2 | Submission in English Ph: 30 201 650 8568 Fx: 30 201 650 8570 g.drossos@yme.gov.gr |

| Guatemala GTM/2 | – | I/II/III | Godofredo Mendez Subcoordinado de Asuntos Internacionales 14 Calle 3-51, Zona 10 Edificio Murano Center Nivel 16 Ciudad de Guatemala 01010 Guatemala | *.doc | Submission in Spanish Ph: 502 366 5880 Fx: 502 366 5892 godomen@sit.gob.gt |
| --- | --- | --- | --- | --- | --- |
| Guyana GUY/2 | I/II | – | Valmikki Singh Engineer-Spectrum Planning /International Relations National Frequency Management Unit 68 Hadfield Street D'Urban Park Georgetown, Guyana | *.pdf *.doc | Submission in English Ph: 592 2 63976 Fx: 592 2 67661 nfmu@guyana.net.gy |
| Hungary HNG/1 | I | I/II/III | Dr. Gyoray Demendi Deputy Head of Frequency Management Office Ministry of Transport, Communications and Water Manaagement P.O. Box 87 Budapest H-1h00 Hungary | *.pdf *.Zip *.doc | Submission in English Ph: +36 1 461 3334 Fx: +36 1 461 3392 demendi@cms.khvm.hu |
| Indonesia INS/3 | I | – | Denny Setiawan Director, Spectrum Policy and Planning Directorate General of Posts and Telecommunications Gedung Sapta Pesona 7th Floor JL. Medan Merdeka Barat 17 Jakarta 10110 Indonesia | *.doc et *.pdf | Submission in English Ph: +62 21 383 8363 Fx: +62 21 386 7500 denny.setiawan@ties.itu.int |

| Iran IRN/3 | II | I/II | Phase 1 Ali Asghar Dolatabadi Director General of Telecommunications Islamic Republic of Iran | *.pdf *.doc | Submission in English Fx: +98 21 867-999 hamed@radtel.or.ir |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Phase 2 Javad Hamed Rouhbakhsh Director General of Telecommunications Ministry of PTT Directorate General of Telecommunications P. O. Box 15875-4415 Tehran Islamic Republic of Iran |  | Submission in English Ph: +98 21 840 36 12 Fx: +98 21 867-999 hamed@radtel.or.ir |
| Ireland IRL/1 | – | I/II | Samuel Ritchie Manager: Spectrum Management Office of the Director of Telecommunications Regulation Abbey Court, Irish Life Centre Lower Abbey Street Dublin 1, Ireland | *.doc | Submission in English Ph: +353 1 804 9619 Fx: +353 1 804 9671 Ritchies@odtr.ie |
| Italy I/1 | I | – | Emanuele D'Andria Head of Space Segment and Regulatory Affairs Telespazio S.p.A. Via Tiburtina, 965 00156 Roma, Italy | *.pdf | Submission in English Ph: +39 06 4079 3370 Fx: +39 06 4079 3722 emanuele_dandria@telepzio.it |

| Japan J/3 | I/II | – | Masahiko Tominaga Director of International Frequency Policy Office Telecommunications Bureau Ministry of Posts and Telecommunications 1-3-2 Kasumigaseki, Chiyoda-Ku Tokyo 100-8798, Japan | *.pdf *.doc | Submission in English Ph: +81 3 3504 4884 Fx: +81 3 5251 7650 sat-fpd@mpt.go.jp |
| --- | --- | --- | --- | --- | --- |
| Jordan JOR/1 | – | I/II/III | Rima Ayyoub Chief, Frequency Management Section Jordan Telecom P. O. Box 1689 Amman 11118, Jordan | *.pdf | Submission in English Ph: 962 6 460 6183 Fx: 962 6 460 6330 yayoubi@jt.com.jo |
| Korea, Democratic People’s Republic KRE/3 | I/II | – | Pak Kwang Sik Manager, Department of Radio Regulation Ministry of Posts and Telecommunications Oesong-dong, Central District Democratic People’s Republic of Korea | *.pdf | Submission in English Provides exceptions to international table Ph: +850 2 3813180 Fx: +850 2 3814418 |

| Korea, Republic of KOR/3 | I/II | – | Jeong Yeol Park Director, Frequency Division, Radio and Broadcasting Bureau Ministry of Information and Communication 100, Sejongno, Chongno-gu Seoul 110-777, Republic of Korea | *.pdf | Submission in English Ph: +82 2 750 2440 Fx: +82 2 750 2449 jypark@mic.go.kr |
| --- | --- | --- | --- | --- | --- |
| Korea Telecom | I | – | Jong-Tae Kim Korea Telcom 206 Jungja-Dong Pundang-Gu Songnam-SI Kyonggi-Do 463-711 Republic of Korea | *.pdf | Submission in English Ph: +82 342 727 2473 Fx: +82 342 727 2189 kjtae@kt.co.kr |
| Laos LAO/3 | I/II | – | Phanoulangsy Phimmachanh Head, Frequency Management Division Department of Posts and Telecommunications, Jawaharlal Nehru Street, 0100 Vientiane Lao PDR | *.pdf | Submission in English Ph: (856-21) 412299 Fx: (856-21) 412279 laofreqm@laotel.com depostel@laotel.com |
| Latvia LVA/1 | II | I/II/III | Karlis Bogens Director, Latvia Telecommunication State Inspection 41/43 Str. Elizabetes Riga LV-1010, Latvia | *.pdf-Phase 1 *.doc-Phase 2 | Submission in English Ph: +371 733 3034 Fx: +371 782 1275 |

| Lebanon LBN/3 | – | I/II/III | Aref Mansour Technical Advisor to the Minister Ministry of Telecommunication Ryad El Soloh Street Beirut, Lebanon | *.pdf | Submission in English Ph: 961 161 1975 Fx: 961 161 1964 amansour@sodetel.net.lb |
| --- | --- | --- | --- | --- | --- |
| Lesotho (Lesotho Telecommunications Corporation) LSO/1 | I/II | I/II/III | Phase 1 and Phase 2 Tennyson Saoana Manager, Frequency Management and Monitoring Lesotho Telecommunications Authority P.O. Box 15896 Moposo House Maseru 100, Lesotho | *.pdf-Phase 1 *.doc-Phase 2 | Submission in English Ph: +266 22 325 595 Fx: +266 22 310 984 lta@lta.org.ls |
| Liberia LBR/1 | I/II | – | Gabriel Pannoh Director of Technical Services Ministry of Posts and Telecommunications Post Office Box GPO Monrovia, Liberia | *.pdf | Submission in English Ph: + 71 821 60565 Fx: + 360 4102 |
| Libya LBY/1 | I/II | – | Mohamed Saleh Alsabey Head, International Relations Department General Directorate of Posts and Telecommunications P.O. Box 81686 Tripoli, Libya | *.pdf | Submission in English Ph: + 71 821 60565 Fx: + 360 4102 |

| Liechtenstein LIE/1 | – | I/II/III | Markus Laesser Frequency Manager Office for Communications Kirchstrasse 10, 9490 Vaduz Liechtenstein | *.doc | Submission in English Ph: +423 236 6484 Fx: +423 236 6489 markus.laesser@ak.llv.li |
| --- | --- | --- | --- | --- | --- |
| Lithuania LTU/1 | I/II | I/II/III | Phase 1 Arturas Medeisis Head of Section, Strategic Planning Lithuanian State Radio Frequency Service SRFS, Algirdo Str. 27 LT-2006 Vilnius, Lithuania | *.pdf-Phase 1 *.doc-Phase 2 | Submission in English Ph: + 370 2 33 0825 Fx: + 370 2 26 1564 medeisis@radio.lt http://www.radio.lt/table.htm |
|  |  |  | Phase 2 Mindaugas Zilinskas Communications Regulatory Authority Algirdo 27, LT-2006 Vilnius, Lithuania |  | Submission in English Ph: +370 52 161 407 Fx: +370 52 161 564 mzilinsk@rrt.lt |
| Madagascar MDG/1 | I/II | I/II/III | Phase 1 and Phase 2 Devarieux Aubertin Rasendramiadana Directeur de la gestion des fréquences Office malgache d'études et de régulation des télécommunications (OMERT) B. P. 99991Antananarivo -101- République de Madagascar | *.pdf | Submission in French Ph: +261 20 22 421 19 Fx: +261 20 22 215 16 omert@dts.mg |

| Maldives MLD/3 | I/II | – | Abdulla Rasheed Director of Engineering Post and Telecommunication Section Ministry of Communication, Science and Technology Telecom Building Husnuheena Magu Male’ 20-04 Republic of Maldives | *.pdf | Submission in English Ph: +960 32 33 44/323 444 Fx: +960 32 0000 telecom@dhivehinet.net.mv |
| --- | --- | --- | --- | --- | --- |
| Mali (SOTELMA) MLI/1 | I/II | I/II/III | Phase 1 and Phase 2 Cheick Oumar Traore Chef, Section Radio Décametrique et Gestion des Fréquences SOTELMA BP 740 Bamako Mali | *.pdf | Submission in French Ph: 223 223 1691 Fx: 223 223 1491 cotraore@sotelma.ml |
| Malta MLT/1 | I/II | I/II/III | Phase 1 and Phase 2 Adrian Galea Henry Mifsud Consultant Ministry for Transport and Communications, Wireless Telegraphy Department Evans Building Merchants Street, Valletta CMR 02, MALTA | *.doc | Submission in English Ph: +356 2124 7224-8 Fx: +356 2124 7229 wtd.info@gov.net |

| Mauritius MAU/1 | – | I/II/III | Mukund Krishna Oown Director of Engineering/Licensing Information and Commnication Technology Authority 1st Floor Jade House CNR Jummah Mosque 2 Remy Ower Street Port Louis, Mauritius | *.doc | Submission in English Ph: 230 217 2222 Fx: 230 217 7777 icta@intnet.mu |
| --- | --- | --- | --- | --- | --- |
| Mauritania MTN/1 | – | I/II/III | Mohamed Vadel Ould Taabou Responsable chargé du contrôle et de la gestion du spectre des fréquences 14 Ilot z, Nouakchott, Mauritanie | *.doc | Submission in French Ph: +222 529 1270 529 4038 Fx: +222 529 1279 tabouv@yahoo.fr |
| Mexico MEX/2 | I/II | I/II | Phase 1 González Bustamante Director General de Planeación y Administración del Espectro Comisión Federal de Telecomunicaciones Bosque de Radiatas N.° 44, 1.er Piso, Col. Bosques de Las Lomas México | *.doc *.pdf | Submission in Spanish Ph: (52) 5 2614005 Fx: (52) 5 2614041 rglezbus@cft.gob.mx |

|  |  |  | Phase 2 Fernando Carrillo Valderrábano Director General de Organismos de Regulación Internacional Comisión Federal de Telecomunicaciones Bosque de Radiatas #42, 4to, Piso, Col. Bosques de las Lomas, México D. F. C. P. 05120 | *.pdf | Submission in Spanish Ph: 5255 52 61 41 87 Fx: 5255 52 61 40 55 carrillo@cft.gob.mx |
| --- | --- | --- | --- | --- | --- |
| Moldova MDA/1 | – | I/II/III | Evghenii Sestacov Head, Spectrum Management Department State Communication Inspection 28/2 Drumul Viilor MD-2021 Chisinau Moldova | *.doc | Submission in English Ph: +373 2 733 934 Fx: +373 2 733 941 esestacov@isc.net.md |
| Monaco MCO/1 | – | I/II/III | Roul Viora Directeur Direction du contrôle des concessions et des télécommunications 23, Avenue Prince Héréditaire Albert MC 98000 Monaco | *.doc | Submission in French Ph: +377 93 15 88 00 Fx: +377 97 98 56 57 |

| Morocco MRC/1 | – | I/II/III | Ilham Ghazi Chef du service de la planification Division de la gestion du spectre des fréquences Direction technique Agence national de réglementation des télécommunications (ANRT) Avenue Ennakhil Centre d'Affaires BP 2939 Hay Ryad Rabat 10.100 Maroc | *.doc | Submission in French Ph: +212 0 3771 8512 ou 16 Fx: +212 0 3771 8547 ghazi@anrt.net.ma |
| --- | --- | --- | --- | --- | --- |
| Myanmar BRM/3 | I/II | – | Kyi Than Director General, Posts and Telecommunications Department Ministry of Communications, Posts, and Telegraphs 125 Ground Floor, Pansodan St. Yangon (RGN) Myanmar (BRN) | *.pdf | Submission in English Ph: +95 1 280 024 Fx: +95 1 286 365 DG.PTD@mtpt400.stems.com |
| Namibia NMB/1 | II | – | Jan Kryger Deputy General Namibian Communications Commission Private Bag 13309 Winohoer Namibia | *.pdf | Submission in English Ph: 222 666 + 264 61 Fx: 222 790 janhk@ncc.org.na |
| Netherlands HOL/1 | – | I/II/III | Jan Ter Horst Radiocommunications Agency of NL Emmasingel 1, Postbus 450 9700AL Groningen The Netherlands | *.doc | Submission in English Ph: 0031 50 587 7261 Fx: 0031 50 587 76400 jan.thorst@ast-ez.nl |

| Nicaragua NCG/2 | II | I/II/III | Phase 1 Hjalmar Ruiz Tuckler Director DAER Administracion del Espectro Radioelectrico DAER-TELCOR Edificio INSS V-VI-Piso Apartado 2664 Managua, Nicaragua | *.pdf | Submission in Spanish Ph: 222 7348 Fx: 222 7644 jvado@telcor.gob.ni |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Phase 2 Richard López Vanegas Chief, Engineering Department Instituto Nicaragüense de Telecomunicaciones y Correos Telcor Telcor Building 3rd Floor Managua, Nicaragua | *.doc | Submission in English Ph: +505 222 7350 Fx: +505 222 7327 rlopez@telcor.gob.ni |
| Norway NOR/1 | I/II | – | Stein Gudbjorgsrud Head of Frequency Planning Norwegian Post and Telecommunication Authority P.O. Box 447 Sentrum N-0104 OSLO Norway | *.pdf | Submission in English Ph: +47 22 824 802 Fx: +47 22 824 790 stein.gudbjorgsrud@npt.no |
| Niger NGR/1 | – | II/III | Soumaila Abdoulkarim Chef, Département des politiques et de la tutelle des exploitants Direction de la réglementation des postes et télécommunications Ministère des transports et des communications BP 452 Niamey, Niger | *.doc | Submission in French Ph: 227 733 097 Fx: 227 725 028 drpt@intent.ne |

| Pakistan PAK/3 | I/II | – | Mahboob Ali Vice Chairman, Frequency Allocation Board Ministry of Communications 19 Mauve Area, G-8/1 Islamabad, Pakistan | *.pdf *.doc | Submission in English Ph: 92 51 926 0183 Fx: 92 51 926 0185 vcfab@paknet2.ptc.pk |
| --- | --- | --- | --- | --- | --- |
| Panama PNR/2 | – | I/II |  | *.pdf |  |
| Papua New Guinea PNG/3 | – | I/II/III | Gari Arua Taravatu Executive Manager Radiocommunication Papua New Guinea Radiocommunication and Telecommunication Technical Authority P.O Box 8227 Boroko 111 Papua New Guinea | *.doc | Submission in English Ph: 675 325 8633 Fx: 675 325 6868 agt@tiare.net.pg |
| Peru PRU/2 | I/II | I/II/III | Phase 1 Edgard Alvarado Barreto Subdirector de Sistemas de Radiocomunicaciones Ministerio de Transportes, Comunicaciones Vivienda y Construcción Av. 28 de Julio N.° 800 Lima, Perú | *.pdf | Submission in Spanish Ph: 511 423 0998 Fx: 511 433 1450 Ealvarado@mtc.gob.pe |

|  |  |  | Phase 2 Claudio Palomares Sartor Asesor Tecnico, Secretary de Communicaciones Ministerio de Transportes y Communicaciones Av 28 de Julio N( 800 Lima 1, Peru | *.doc | Submission in Spanish Ph: 511 332 4079 Fx: 511 332 4084 cpalomares@mtc.gob.pe |
| --- | --- | --- | --- | --- | --- |
| Philippines PHL/3 | – | I/II/III | Armi Jane Borje Commissioner National Telecommunications Commission NTC Bldg. BIR/Agham Road East Triangle, Diliman Quezon City, Philipines | *.doc | Submission in English Ph: 632 924 4042 Fx: 632 921 7128 commissioner@ntc.gov.ph |
| Poland POL/1 | – | I/II |  | *.pdf |  |
| Portugal POR/1 | I/II | I/II/III | Phase 1 Maria Luísa Mendes Head of Spectrum Management and Engineering Directorate ICP – Instituto das Comunicações de Portugal Ava José Malhoa , n° 12 1099-017 Lisboa Portugal | *.doc | Submission in English Ph: +351 721 1000 Fx: +351 721 1006 luisa.mendes@icp.pt |

|  |  |  | Phase 2 Fernanda Girao Deputy Director ANACOM Autoridade Nacional das Comunicacoes Av. Jose Malhoa12 1099-017 Lisboa Portugal | *.doc | Submission in English Ph: +351 217 122 220 Fx: +351 217 211 006 girao@anacom.pt |
| --- | --- | --- | --- | --- | --- |
| Qatar QAT/1 | – | I/II | Abdulwahed Fakhroo Divisional Manager, Radio Regulatory and International Affairs Qatar Telecomm 14th Floor, Q-tel Tower West Bay, Post Box 217 Doha, Qatar | *.doc | Submission in English Ph: +974 440 0789 Fx: +974 483 0630 |
| Romania ROU/1 | – | I |  | *.doc |  |
| Rwanda RRW/1 | – | II | Felicien Riikihza Hinitraco B.P. 24 Kigali, Rwanda | *.pdf | Submission in French Ph: 250 82574 Fx: 250 72971 250 82570 Mintraco@Rwanda.t.com |
| Samoa SMO/3 | I/II | I/II | Phase 1 Fong David Assistant Director Monitoring/Spectrum Private Bag Chan Mow Plaza Apia, Samoa | *.pdf | Submission in English Ph: 0685 26117 Fx: 0685 24671 mpt@somoa.ws |

|  |  |  | Phase 2 Tu'aimalo Asamu Ah Sam Director Ministry of Posts and Telecommunications Private Bag Apia CA & CJ Chan Mow Plaza Savalalo, Samoa | *.doc | Submission in English Ph: 0685 26117 Fx: 0685 24671 a.ahsam@samoa.ws mpt@samoa.ws |
| --- | --- | --- | --- | --- | --- |
| Saudi Arabia ARS/1 | – | I |  | *.doc |  |
| Senegal SEN/1 | – | I/II/III | Makhtar Fall Responsable des radiocommunications Agence de régulation des télécommunications Rue 3 X F Fann Résidence BP: 14 130 Dekar Peytavin Senegal | *.doc | Submission in French Ph: 221 869 0369 Fx: 221 864 3934 makhtar.fall@art.sn |
| Seychelles, Republic of SEY/1 | I/II | – | Dr. G. Ah-Thew Telecom Division Ministry of Information Technology and Communications P.O. Box 1389 Oceangate House Victoria, Republic of Seycelles | *.pdf | Submission in English Ph: 248 382 039 Fx: 248 225 325 telecoms@seychelles.net |

| Slovak Republic SVK/1 | I | – | Mária Alakšová Ing. Ministry of Transport, Posts and Telecommunications of The Slovak Republic Námestie slobody 6, 821 05 Bratislava, Slovak Republic | *.doc | Submission in English Ph: +421 7 52731434 Fx: +421 7 52731437 maria.alaksova@telecom.gov.sk |
| --- | --- | --- | --- | --- | --- |
| Slovenia SVN/1 | – | I/II | Trdin Marjan Head of Radiocommunications Sector Telecommunications, Broadcasting and Post Agency of the Republic of Slovenia Kotnikova 19a SI-1000 Ljubljana, Slovenia | *.pdf | Submission in English Ph: +386 1 4734 900 Fx: +386 1 4328 036 info.box@atrp.si |
| Spain E/1 | I/II | I/II/III | Juan Canas Santos Consejero Técnico Secretaria General de Comunicaciones Palacio de Comunicaciones Pza. Cibeles s/n 28071 Madrid, España (Spain) | *.pdf | Submission in Spanish Ph: 34 91 346 1500 Fx: 34 91 396 2229 juan.canas@sgc.mjom.es |
| Sri Lanka CLN/3 | – | I/II/III | Helasiri Ranatunga Deputy Director/Spectrum Management Telecommunications Regulatory Commission of Sri Lanka 276, Elvitigala Mawatha Colombo 08, Sri Lanka | *.doc | Submission in English Ph: +94 1 683 841 Fx: +94 1 671 444 hela@sltnet.lk spectrc@sltnet.lk |
| Sudan SDN/1 | – | II/III |  | *.doc |  |

| Suriname SUR/2 |  | I/II/III | Soenildath Boeddha Head Radio Frequency Control Division Telecommunicatiebedrijf Surinam, TELESUR Letitia, Vriesdelaan Suriname | *.pdf | Submission in English Ph: 597 545 022 Fx: 597 546 157 telesur_brc@sr.net |
| --- | --- | --- | --- | --- | --- |
| Swaziland SWZ/1 | – | I/II/III | Seth Dlamini Manager Frequency Management Swaziland Posts and Telecomms Corporation P.O. Box 125, Mbabane. H100 Swaziland | *.doc | Submission in English Ph: 268 405 2315 Fx: 268 405 2020 stdlamini@sptc.co.sz |
| Sweden S/1 | I/II | – | Hedlund Jan Spectrum Engineer National Post and Telecom Agency P.O. Box 5398 S-102 49 Stockholm, Sweden | *.doc | Submission in English Ph: +46 8 678 5565 Fx: +46 8 678 5505 jan.hedlund@pts.se |
| Switzerland SUI/1 | I | I/II/III | Phase 1 and Phase 2 Ivan Franic El. Ing. HTL OFCOM 44, Rue de L'Avenir 2501 Biel-Bienne Suisse | *.pdf | Submission in English Ph: +41 (0) 32 / 327 5703 Fx: +41 (0) 32 / 327 5666 Ivan.franic@bakom.admin.ch |
| Syria SYR/1 | – | I/II/III | Moustafa Ajeneh Director of Radio Frequencies Directorate Syrian Telecommunications Establishment (STE) Mazeh Autostrade Damascus, Syria | *.doc | Submission in English Ph: +963 11 612 2291 Fx: +963 11 612 1291 frq-dir@net.sy |

| Tajikistan TJK/1 | – | I/II/III | Mahmadaly Azizov Head The State Inspectorate of Communication at the Ministry of Communication Rudaki Avenue 57 734025 Dushanbe Tajikistan | *.doc | Submission in English Ph: +992 372 21 71 83 21 54 21 Fx: +992 372 21 77 08 gis@netrt.org |
| --- | --- | --- | --- | --- | --- |
| Thailand THA/3 | I/II | I/II/III | Auraphan Suwanrat Deputy Director General Post and Telegraph Department 87 Phaholyothin 8 Road Bangkok 10400 Thailand | *.pdf | Submission in English includes national allocation table from 9 kHz to 1 350 MHz Ph: 662 27 10 15160 Fx: 662 27 13514 or 13512 http://www.ptd.go.th |
| Turkey TUR/1 | I/II | I/II/III | Phase 1 Abdullah Karakas Head of Frequency Management Department Republic of Turkey Ministry of Transportation General Directorate of Radiocommunications Telsiz Genel Müdürlüğü-TGM Ulaştırma Bakanlığı Sitesi Emek 06510 Ankara Turkey | *.doc | Submission in English Ph: 2126010/210 Fx: 2213226 akarakas@tgm.gov.tr |

|  |  |  | Phase 2 N. Funda Demirci Telecommunication Expert Assistant Telecommunications Authority Yesilirmak Sokak N0=16 06430 Demirtepe Ankara, Turkey | *.doc | Submission in English Ph: 550 5321 Fx: 550 5316 nfdemirci@tk.gov.tr |
| --- | --- | --- | --- | --- | --- |
| Uganda UGA/1 | – | I/II/III | Jonas Muhoozi Bantulakl Assistant Technical Manager, Spectrum Management Uganda Communications Commission Communications House 12 Floor, Plot 1, Colville Street P.O. Box 7376 Kampala, Uganda | *.doc | Réponse présentée en anglais Tél.: 256 41 348831 Fax: 256 41 348832 jobantu@ucc.co.ug |
| Ukraine UKR/1 | – | I/II/ |  | *.doc |  |
| United Arab Emirates UAE/1 | I/II | I/II/III | Phase 1 Sultan Ali Hassan Al Marzouki A/Director, Department of Telecommunication Ministry of Communication P.O. Box 900 Abu Dhabi, United Arab Emirates | *.pdf | Submission in English Ph: 00 97 12 662 909 Fx: 00 97 12 668 180 |

|  |  |  | Phase 2 Mohamed Mohamed Abd Allah A/D Telecommunication Department Ministry of Communications P.O. Box 900 Abu Dhabl, United Arab Emirates | *.doc | Submission in English Ph: 00 97 1269 111 22 Fx: 00 97 1266 681 80 engrhassan@moc.uae.gov.ae |
| --- | --- | --- | --- | --- | --- |
| United Kingdom G/1 | I/II | I/II/III | Phase 1 Terry Jeacock Office of Communications (Ofcom) Riverside House 2A Southwark Bridge Road London SE1 9SX United Kingdom | *.zip *.doc *.gif | Submission in English Ph: +44 (0)207 7834294 terence.jeacock@ties.itu.int |
|  |  |  | Phase 2 Howard Del Monte Contact T. G. Jeacock using the details given above | *.doc | Submission in English |

| United States USA/2 | I/II | I/II | Phase 1 and Phase 2 William Luther (non-Federal Government issues) Chief, Radiocommunication Policy Federal Communications Commission Washington, DC USA Norbert Schroeder (Federal Government issues) Chief, Strategic Spectrum Planning and Policy Reform Division National Telecommunications and Information Administration Department of Commerce Washington, DC, 20230 USA | *.doc | Submission in English Ph: 202 418 0729 Fx: 202 418 7270 wluther@fcc.gov Ph: +202 482 6207 Fx: +202 501 6198 nschroeder@ntia.doc.gov |
| --- | --- | --- | --- | --- | --- |
| Uzbekistan UZB/1 | – | I/II/III | Mayram Khalmuratova Deputy Chairman State Committee for Radio Frequencies of the Republic of Uzbekistan 700000 Tashkent Alexsey Tolstoy Street 1 Uzbekistan | *.doc | Submission in English Ph: 998 71 137 45 16 Fx: 998 71 133 16 95 scr@uzpak.uz |

| Venezuela VEN/2 | – | I/II/III | Rita C. Hermosa M Ingeniero CONATEL Ave. Veracruz c/c Cali, Edificio CONATEL Las Mercedes Caracas, Venezuela | *.doc | Réponse présentée en espagnol Tél.: +58 212 9090 527 Fax: +58 212 9935 389 rhermoso@conotel.gov.ve http://www.conatel.gov.ve/ns/downloads/marco_legal/CUNABAF%20Extraordinaria.zip |
| --- | --- | --- | --- | --- | --- |
| Viet Nam VTN/2 | I/II | I/II/III | Phase 1 Luu Van Luong Director General Radio Frequency Department (DGPT) 18 Nguyen Du Street Hanoi, Vietnam | *.pdf | Submission in English Ph: 84 4 822 6732 Fx: 84 4 822 6930 |
|  |  |  | Phase 2 Quan Hoan Doan Deputy Director General Radio Frequency Department 18 Nguyen Du Street Hanoi, Viet Nam |  | Submission in English Ph: 84 44 43 4704 Fx: 84 48 22 6910 |

ANNEX  1-B

Table 1 – Extract from the submission of Albania

| Frequency Band | RR Region 1 Allocation and Relevant Footnotes | European Common Allocation | Major Utilization | Notes | Albanian Allocation | Utilization, Users in Albania |
| --- | --- | --- | --- | --- | --- | --- |
| 942-960 MHz | FIXED MOBILE except aeronautical mobile BROADCASTING S5.322 S5.323 | MOBILE S5.323 | GSM Existing cellular networks | EU13 ERC Decision ERC/DEC/(94)01, FB paired with 897-915 MHz | MOBILE S5.323 | GSM CIVIL/TRE |
| 960-1 215 MHz | AERONAUTICAL RADIONAVIGATION S5.328 | AERONAUTICAL RADIONAVIGATION S5.328 | Flight, Safety, Navigation and Information Distribution Systems (for example, DME, TACAN, SSR, MIDS) |  | AERONAUTICAL RADIONAVIGATION S5.328 | Flight, Safety, Navigation and Information Distribution Systems (for example, DME, TACAN, SSR, MIDS) CIVIL/TRE A37: Fixed service should be terminated prior to 2003. |

| Frequency Band | RR Region 1 Allocation and Relevant Footnotes | European Common Allocation | Major Utilization | Notes | Albanian Allocation | Utilization, Users in Albania |
| --- | --- | --- | --- | --- | --- | --- |
| 1 215-1 240 MHz | EARTH EXPLORATION SATELLITE (active) RADIOLOCATION RADIONAVIGATION-SATELLITE (space to Earth) S5.329 SPACE RESEARCH (active) S5.330 S5.331 5.332 | RADIOLOCATION RADIONAVIGATION-SATELLITE (space to Earth) S5.329 EARTH EXPLORATION SATELLITE (active) SPACE RESEARCH (active) RADIONAVIGATION S5.331 S5.332 | Radar and Navigation Systems and Active Sensors; GNSS |  | RADIOLOCATION RADIONAVIGATION-SATELLITE (space to Earth) S5.329 EARTH EXPLORATION SATELLITE (active) SPACE RESEARCH (active) RADIONAVIGATION S5.331 S5.332 | Radar and Navigation Systems and Active Sensors; GNSS CIVIL/TRE A38: The operation of governmental users should be terminated prior to 2004. A39: Fixed services should be terminated prior to 2003. |

ANNEX  1-C

Table 2 – Extract from the submission of the United Kingdom

| International Region 1 Allocation | European Common Allocation Table Report 25 | UK Allocations | Current Use | Strategy |
| --- | --- | --- | --- | --- |
| 1 240-1 260 MHz EARTH EXPLORATION-SATELLITE (active) RADIOLOCATION RADIONAVIGATION-SATELLITE (sE) (ss) SPACE RESEARCH (active) RADIONAVIGATION-SATELLITE (sE) (ss) S5.329, S5.329A Amateur S5.330, S5.331, S5.332, S5.334, S5.335 | 1 240-1 260 MHz RADIOLOCATION RADIONAVIGATION-SATELLITE (sE) EARTH EXPLORATION SATELLITE (active) SPACE RESEARCH (active) RADIONAVIGATION Amateur S5.329, S5.331, S5.332 | 1 240-1 260 MHz EARTH EXPLORATION-SATELLITE (active) RADIOLOCATION RADIONAVIGATION-SATELLITE S5.329 SPACE RESEARCH (active) Amateur S5.332 | AMATEUR Amateur secondary at powers of up to 26 dBW PEP (into the antenna) for many modes including packet, TV, Morse, etc. Amateur services are permitted on a non-interference basis. AERONAUTICAL/MoD 1 215-1 365 MHz – Naval and air defence radars. 1 164-1 300 MHz – RNSS allocation identified at WRC-2000. Civil and military radar, video radar data and security devices. WRC-97 accepted wind profiler radars on site protection basis. Spaceborne radiolocation for Earth exploration. | The Agency is currently looking into the possibility of permitting the use of spread spectrum techniques in the amateur service. Protection of existing services and aircraft systems from interference effects. Possible use by the European Galileo initiative. Monitor ICAO and European developments. Introduction of wind profiler radars to be monitored. |

ANNEX  1-D

Table 3 – Extract from the submission of the US Federal Government

| Band MHz | Government Allocation(s) | Government Allocations by Footnote | Government Usage | Planned Usage |
| --- | --- | --- | --- | --- |
| 1 215-1 240 | RADIOLOCATION RADIONAVIGATION-SATELLITE(space-to-Earth) EARTH EXPLORATION-SATELLITE (active) SPACE RESEARCH (active) S5.332 G56 | None | Surveillance Radars. This band is jointly used by the FAA and DOD for radiolocation performing long-range air surveillance and safety-of-flight enroute air traffic control under Joint Surveillance System agreements. The military services make use of the band for high-power long-range surveillance radars on land and ships in support of national defense missions. The DOD and FAA recently deployed a modernized Air-Route Surveillance Radar Model 4 (ARSR-4) in this band for air-defense, drug interdiction and air-traffic control. GPS. The frequency 1 227.6 MHz 12 MHz is designated for the Global Positioning System (GPS) as part of the radionavigation satellite service. This is a 24B satellite constellation system with large numbers of U.S. and international users. Drug Interdiction. In this application, radar equipment is mounted on tethered balloons along the southern border of the U.S. to detect low-flying aircraft entering U.S. airspace. | Use expected to increase. Awaiting IRAC approval of AH 206 recommended implementation of WRC-2000 allocation changes: 1) to add ITU footnotes (S5.330 and S5.331); and 2) to add RADIONAVIGATION-SATELLITE (space-to-space). |

| Band MHz | Government Allocation(s) | Government Allocations by Footnote | Government Usage | Planned Usage |
| --- | --- | --- | --- | --- |
|  |  |  | NASA. Space research and Earth exploration-satellite activities for active microwave sensor measurements of geological surfaces and ocean wave structure are performed by NASA. |  |
| 1 240-1 260 | RADIOLOCATION EARTH EXPLORATION-SATELLITE (active) SPACE RESEARCH (active) S5.332 S5.334 S5.335 G56 | AERONAUTICAL RADIONAVIGATION S5.334 | Surveillance Radars. This band is jointly used by the FAA and DOD for radiolocation performing long-range air surveillance and safety-of-flight enroute air traffic control under Joint Surveillance System agreements. The military services make use of the band for high-power long-range surveillance radars on land and ships in support of national defense missions. The DOD and FAA recently deployed a modernized Air-Route Surveillance Radar Model 4 (ARSR-4) in this band for air-defense, drug interdiction and air-traffic control. NASA Research. Space research and Earth exploration-satellite studies of geological surfaces and ocean wave structures are done by NASA using active microwave sensor systems. | Use expected to increase. Awaiting IRAC approval of AH 206 recommended implementation of WRC-2000 allocation changes: 1) to add ITU footnotes (S5.330 and S5.331); and 2) to add RADIONAVIGATION-SATELLITE (space-to-Earth) (space-to-space). |

ANNEX  1-E

Table 4 – Extract from the submission of the Czech Republic

| (CZE) 960-1 215 MHz |
| --- |
| Frequency band | According to RR | National allocation | Responsible entity | Remarks |
| 960-1 145 | AERONAUTICAL RADIONAVIGATION 5.328 | AERONAUTICAL RADIONAVIGATION 5.328 [2] [6] | [2] TA [6] MD | Navigation system TACAN. DME equipment linked with the portion 108-118 MHz (ILS-LLZ and VOR) and 328.6-335.4 MHz (ILS-GP). |
| 1 145-1 215 | 5.328A | AERONAUTICAL RADIONAVIGATION 5.328 [2] [6] Fixed [7] CZ12 5.328A | [2] TA [6] MD [7] pol | Navigation system TACAN. DME equipment, linked with the portion 108-118 MHz (ILS-LLZ and VOR) and 328.6-335.4 MHz (ILS-GP). |

ANNEX  2-A

Question 1: Regulatory texts

| Administration | Region | Development Status | Q.1 Reg Texts | Q.1 Changes | Q.1 Change Comment |
| --- | --- | --- | --- | --- | --- |
| Botswana | Africa | Developping | Telecommunication Act, 1996 [No.15 of 1996] | No | – |
| Burundi | Africa | Least Developed | Ministerial directive n° 520/730/540/231 of 9 April 1999 sets forth the conditions for conducting operations in the telecommunications sector. An act of the legislature n° 1/011 of 04/09/1997 makes formal provisions regarding telecommunication | Yes | – |
| Burkina Faso | Africa | Least Developed | Law n° 0051/98/AN of 04/12/1998 and the associated decision n° 001/MC/MEF of 28/09/2000 Burkina Faso | Yes | – |
| Cameroon | Africa | Developping | Law n° 67/LF/of 12 June 1967 regulating private radio and establishing an associated system of rates – Law n° 98/014 of 14 July 1998 governing telecommunications in Cameroon – Associated decision n° 00080/MINEFI/MINPT of 20 February 2002 concerning rights, rates, contributions and fees received by the “Agence de Régulation des Télécommunications” | No | – |
| Central African Republic | Africa | Least Developed | Decision N° 011/Mtacpt.Cab.Sg.Dgsocatel | Yes | – |
| Comoros | Africa | Least Developed | There are as yet no legal or regulatory provisions governing spectrum management in our country. Regulatory texts (a presidential decree and ministerial decisions) have been elaborated since July 2002 but have not yet adopted by the political decision makers. | No | – |
| Côte d'Ivoire | Africa | Developping | Law n° 95-526 of 07-07-1995; directive n° 97-173 of 18 March 97 and decree n° 97-391 | Yes | – |
| Eritrea | Africa | Least Developed | Proclamation no.102/08 on National Telecom policy | Yes | – |
| Ethiopia | Africa | Least Developed | Telecommunication Services, Council of Ministers, Regulation No. 47/1999 | No | – |
| Lesotho | Africa | Least Developed | Lesotho Telecommunications Authority Act of 2000. | No | – |
| Madagascar | Africa | Least Developed | Law 96-034 and the associated decree 99-228. | Yes |  |
| Mali | Africa | Least Developed | Directive No. 99-043/P-RM of 30/9/99. | Yes | – |
| Mauritania | Africa | Least Developed | Law N° 99-019 of 11/07/1999 concerning telecommunications, and the associated decisions on its application (decision N° R134/MIPT of 28/02/2001 and R138/MIPT of 04/03/2001) | Yes | – |

| Administration | Region | Development Status | Q.1 Reg Texts | Q.1 Changes | Q.1 Change Comment |
| --- | --- | --- | --- | --- | --- |
| Mauritius | Africa | Developing | Information and Communication Technologies Authority | No |  |
| Niger | Africa | Least Developed | Decision N° 99-045 , decree N°2000-370/PRN/MC, decision N° 0006/MC/DRP | Yes | – |
| Rwanda | Africa | Least Developed | Regulatory agency | Yes | – |
| Senegal | Africa | Least Developed | Telecommunication code, decree on frequency management | Yes | – |
| Swaziland | Africa | Developing | ITU Radio Regulations; Swaziland National Radio Regulations and SADC Regional Frequency Allocation Plan. | Yes | Update of the National Radio Regulations when the Regulatory Authority comes to force. Update of the SADC Regional Plan from 3-100GHZ Band. |
| Uganda | Africa | Least Developed | Uganda Communications Act -1997 and UCC Radiocommunication Regulations. On many occasions, we make reference to ITU Radio Regulations. | No | Not in the next five years. |
| Antigua and Barbuda | Americas | Developing | Government of Antigua, Telecommunications Act 1951, Cap 423 | Yes | – |
| Bahamas | Americas | Developing | The Telecommunications Act, 1999 and the Telecom Sector Policy, July 2001 revised October 2002. | Yes | To produce New Regulations. |
| Canada | Americas | Developed | Legislation, Regulations and Treaties http://strategis.ic.gc.ca/SSG/sf01360e.html | Yes | – |
| Chile | Americas | Developing | The General Plan on Use of the Radio Spectrum, approved by Ministry of Transport and Telecommunications Decree No. 15 of 1983 and its modifications. | Yes | – |
| Columbia | Americas | Developing | Decree 1900/90 y Decree 555/98 | Yes | – |
| Costa Rica | Americas | Developing | Act 1758 15 | Yes | – |
| Cuba | Americas | Developing | Decrees, ministerial resolutions, instructions | Yes | – |
| El Salvador | Americas | Developing | Telecommunications Act and its implementing Regulations | Yes | – |
| Guatemala | Americas | Developing | General Telecommunications Act Regulations on the Operation of Satellite Systems Regulations on the Provision of International Telephony | No | – |
| Mexico | Americas | Developing | Federal Act on Telecommunications – Mexican National Table of Frequency Allocations | Yes |  |
| Nicaragua | Americas | Developing | 1. Regulations on Use of the Radio Spectrum and Communication Systems 2. National Table of Frequency Allocations | No | – |
| Panama | Americas | Developing | JD-107 of 30/9/97 | Yes | – |

| Administration | Region | Development Status | Q.1 Reg Texts | Q.1 Changes | Q.1 Change Comment |
| --- | --- | --- | --- | --- | --- |
| Peru | Americas | Developing | Consolidated and Amended Text of the Telecommunications Act, its General Regulations, Standards for Use of the Radio Spectrum for Public Telecommunication Services, National Frequency Allocation Plan | Yes | – |
| Suriname | Americas | Developing | The Telegraph and Telephone Act, 1945 | Yes | – |
| Venezuela | Americas | Developing | Organizational Act on Telecommunications (LOTEL) and regulations and resolutions in force | No | – |
| Bahrain | Arab States | Developing | None | Yes | – |
| Egypt | Arab States | Developing | Law 66 at 1979 governs our national spectrum management processes | Yes | – |
| Jordan | Arab States | Developing | The Telecommunications Law No. 13 and its amendments | No | To be answered by Telecommunication Regulatory Commission (TRC) |
| Lebanon | Arab States | Developing | New Law of Telecommunications N 431 dated 22/7/2002. | Yes | – |
| Morocco | Arab States | Developing | Law 24-96, concerning the post and telecommunication Decision 310-98 fixes fees for frequency assignments Decisions ANRT/DG/N°27, N°11/02, N°25, N°28, N°03/02 by the director of the “Agence Nationale de Réglementation des Télécommunications” | Yes | Some provisions will be modified. |
| Qatar | Arab States | Developing | Law No. 13 (of 1987 and Law No. 21 (of 1998) of the state of Qatar. | No | – |
| Syria | Arab States | Developing | Law No. 451 dated 1957. | Yes | – |
| United Arab Emirates | Arab States | Developing | Federal Law 1973 | No | – |
| Bhutan | Asia & Pacific | Least Developed | National Radio Regulations 1999 | No | – |
| China | Asia & Pacific | Developing | Radio Regulations Of The People's Republic Of China | No | – |
| Iran | Asia & Pacific | Developing | Rules and regulations approved by Islamic republic of Iran's Majlis | Yes | – |
| Papua New Guinea | Asia & Pacific | Developing | The Radio Spectrum Act 1996 and Radio Spectrum Regulation 1997. | Yes | – |
| Philippines | Asia & Pacific | Developing | Legislative Acts (Republic Act 7325, Act 3846) Memorandum Circular issued by this Commission (National Telecommunication Commission (M.C.: 8-5-95, M.C.: 3-3-96, etc.) | Yes | As deemed necessary |
| Samoa | Asia & Pacific | Least Developed | New Radio Regulation 2000, Posts and Telecommunications Act 1999. | Yes | – |

| Administration | Region | Development Status | Q.1 Reg Texts | Q.1 Changes | Q.1 Change Comment |
| --- | --- | --- | --- | --- | --- |
| Sri Lanka | Asia & Pacific | Developing | Sri Lanka Telecommunications Act No. 25 of 1991 as amended Act No. 27 of 1996 and Gazette Notifications (629/16 of 28.09.1990, 929/10 of 25.06.1996.1104/4 of 01.11.1999, 986/18 of 31.07.1997, 1084/14 of 16.06 and ITU regulatory publications. | Yes | – |
| Thailand | Asia & Pacific | Developing | The Act, Ministerial Relations and PTD announcements. | Yes | Yes, when the new independent organization, name NTC, is established, the Master Plan and new regulations for spectrum management should be published. |
| Vietnam | Asia & Pacific | Developing | Post and Telecommunications Act | No |  |
| Albania | Europe & CIS | Developing | Law No 8618, dated 14.6.2000, “On Telecommunication in the Republic of Albania” and National Frequency Allocation Plan. | No | – |
| Armenia | Europe & CIS | Developing | Article 13, Law of Armenian Republic “On Telecommunications”(17 February 2002; N614 (20 November 1999) Decree of Armenian Government “On Regulation of use of radio electronic equipment and high-frequency facilities, distribution of radio frequencies in Armenian Republic”; National Table of Frequency Allocations | Yes | – |
| Bosnia & Herzegovina | Europe & CIS | Developing | Communication Law Of Bosnia And Herzegovina | Yes | – |
| Croatia | Europe & CIS | Developing | The Telecommunication Law, The RF Spectrum Assignment Rule | Yes | – |
| Cyprus | Europe & CIS | Developing | The Radiocommunications Law of 2002 (Law 146(I) of 2002) | Yes | The above new Law has been in force since July 2002. New regulations are expected to be voted by the Parliament by the end of this year. |
| Czech Republic | Europe & CIS | Developing | Act No. 151/2000 Coll. on Telecommunications and on Amendments to Other Acts – Number of Governmental Decrees – Set of General Licences Detailed list of all regulatory texts is published of web pages http://www.ctu.cz – Act No. 151/2000 Coll. on Telecommunications and on Amendments to Other Acts – Number of Governmental Decrees – Set of General Licences Detailed list of all regulatory texts is published of web pages http://www.ctu.cz | Yes | – |
| Estonia | Europe & CIS | Developing | Telecommunication Act | Yes | – |
| Finland | Europe & CIS | Developed | Radio Act (1015/2001), Act on Communications Administration (625/2001 and 493/2002). | No | – |

| Administration | Region | Development Status | Q.1 Reg Texts | Q.1 Changes | Q.1 Change Comment |
| --- | --- | --- | --- | --- | --- |
| France | Europe & CIS | Developed | The management of the radio spectrum as concerns the allocation of frequency bands is governed by: – the post and telecommunication code (which includes laws and decrees governing telecommunications, in particular the “loi de réglementation des télécommunications” (LRT) L. n°96-659 of 26 July 1996, creating the French national frequency agency (“Agence nationale des fréquences” or ANFR) and decree D. n°96-1178 of 27 December 1996 establishing the objectives and functioning of ANFR – Law n° 86-1067 of 30 September 1986 concerning freedom of communication; – the national frequency distribution table, adopted by a decision of the prime minister (article 21 of Law n° 86-1067 of 30 September 1986) | No | These documents are undergoing change, and it is anticipated that the LRT will be revised in five years, taking into account the fact that internal law must be brought into line with the EU telecom package by July 2003 at the latest. |
| Greece | Europe & CIS | Developed | TELECOMMUNICATION LAW 2867/00, LAW 2801/00 National Telecommunications and Post Commission (EETT) DECISIONS 210/2, 210/3, 254/72 | Yes | to conform with the new EU framework |
| Hungary | Europe & CIS | Developing | Act on Communications (2001) Government Decree on the organization of the Authority dealing with non-civil frequency management and on the rules of non-civil frequency management (2001) Government Decree on the organization of the Communications Authority of Hungary (2001) | Yes |  |
| Ireland | Europe & CIS | Developed | Wireless Telegraphy Acts 1926 - 1988, Telecommunications (Misc. Provisions) Act 1996, ITU Radio Regulations 2001, CEPT Decisions and Recommendations, EU Directives and Decisions. | Yes | – |
| Latvia | Europe & CIS | Developing | General legal instruments on utilization of radio frequencies in Latvia: – Law on Telecommunications adopted 1 November 2001; – Law on the Constitution of the International Telecommunication Union, Convention of the International Telecommunication Union and Optional Protocol on the Compulsory Settlement of Disputes Relating to the Constitution of the International Telecommunication Union, to the Convention of the International Telecommunication Union and to the Administrative Regulations and Other Legal Instruments adopted 21 March 2001; – Law on Radio and Television adopted 24 August 1995; – Latvian Administrative Offence Code (Articles 146-147 and 235); – Cabinet of Ministers Regulations No. 348 dated 7 October 1997 Regulations On The Licensing Of Several Types Of Commercial Activities; – Cabinet of Ministers Regulations No. 171 dated 30 April 2002 Radio Equipment Conformity Assessment Regulations entering into force .1 January 2003; – Cabinet of Ministers Regulations No. 188 dated 30 May 2000 Equipment Electromagnetic Compatibility Regulations; – Cabinet of Ministers Regulations No. 187 dated 30 May 2000 Equipment Electrical Safety Regulations; – Cabinet of Ministers Regulations No. 283 dated 22 August 2000 Telecommunication Terminal Equipment Conformity Assessment Regulations; – Cabinet of Ministers Regulations No. 395 dated 2 December 1997 Special Regulations On The Construction Of Telecommunication Networks And Equipment; – Other legal instruments, e.g. Standards Law, Law on Public Services Regulators, etc | Yes | – |

| Administration | Region | Development Status | Q.1 Reg Texts | Q.1 Changes | Q.1 Change Comment |
| --- | --- | --- | --- | --- | --- |
| Liechtenstein | Europe & CIS | Developed | Legal Act of 20 June 1996 on Telecommunications (TelG), Liechtenstein Legal Gazette 1996 No. 132 (http://www.ak.li/rechtsgrundlagen/gesetze.asp) Ordinance of 13 August 2002 on frequency management and usage (FVNV), Liechtenstein Legal Gazette 2002 No. 105 (http://www.ak.li/rechtsgrundlagen/verordnungen.asp) | Yes | – |
| Lithuania | Europe & CIS | Developing | Law on Telecommunications, 9 June, 1998 No. VIII-774 (in effect till 31.12.2002) | Yes | Law on Amending of the Low of the Republic of Lithuania on Telecommunications, 5 July, 2002 No. IX-1053 (with effect from 01.01.2003) |
| Malta | Europe & CIS | Developing | Wireless Telegraphy Ordinance (Chapter 49) | Yes |  |
| Moldova | Europe & CIS | Developing | Telecommunication Law | No | – |
| Monaco | Europe & CIS | Developed | Law 928 of 8 December 1972 concerning non-public radio stations | Yes | – |
| Netherlands | Europe & CIS | Developed | On a national level: Telecommunication Act and the Frequency Decree. On an international level: the ITU Regulations, CEPT/ECC Decisions and EU directives. | Yes | – |
| Poland | Europe & CIS | Developing | Telecommunications Law 2000 | Yes | – |
| Portugal | Europe & CIS | Developing | Telecommunications Law, Decree Laws and ANACOM Statutes. Can be found in ANACOM´s site in the address (http://www.anacom.pt/template16.jsp?categoryId=4654). | Yes | – |
| Slovenia | Europe & CIS | Developing | Telecommunications Law (Ztel-1) (Off.gaz. RS, 30/2001). | Yes | – |
| Spain | Europe & CIS | Developed | Act 11/1998 “General Telecommunications Act” and subsequent developments thereof | Yes |  |
| Switzerland | Europe & CIS | Developed | Federal law of 30 April 1997 on telecommunication (LTC) Decision of the “Conseil fédéral” of 6 October 1997 on frequency management and radio concessions (OGC). | No | – |
| Tajikistan | Europe & CIS | Developing | Law “On Telecommunications” dated 22 May 2002, Radio Regulations. | No | – |
| Turkey | Europe & CIS | Developing | Wireless Law numbered 2813 and Implementing Regulations numbered 18183. | Yes |  |
| Ukraine | Europe & CIS | Developed | The laws of Ukraine “On communications”, “On a radio frequency resource ”, Resolution No 112 of 7 February 2001 of the Cabinet of Ministers of Ukraine “On the order of issuing of the licences on use of the radio frequency resource”, “Rule on the allocation of radio frequencies”. | Yes | – |
| United Kingdom | Europe & CIS | Developed | Wireless Telegraphy Act, last modified 1998 | Yes | A new draft Communications Bill is currently being considered. |
| Uzbekistan | Europe & CIS | Developin On a national level: Telecommunication Act and the Frequency Decree. On an international level: the ITU Regulations, CEPT/ECC Decisions and EU directives.g | Radiofrequency Spectrum Law and National Radio Regulations. | Yes | – |

ANNEX  2-B

Question 2: Are regulations and procedures publicly available?

| Administration | Region | Development Status | Q.2 Public Availability |
| --- | --- | --- | --- |
| Albania | Europe & CIS | Developing | Yes |
| Antigua and Barbuda | Americas | Developing | No |
| Armenia | Europe & CIS | Developing | Yes |
| Bahamas | Americas | Developing | Yes |
| Bahrain | Arab States | Developing | Yes |
| Bhutan | Asia & Pacific | Least Developed | Yes |
| Bosnia & Herzegovina | Europe & CIS | Developing | Yes |
| Botswana | Africa | Developing | Yes |
| Burundi | Africa | Least Developed | Yes |
| Burkina Faso | Africa | Least Developed | No |
| Cameroon | Africa | Developing | No |
| Canada | Americas | Developed | Yes |
| Central African Republic | Africa | Least Developed | Yes |
| Chile | Americas | Developing | Yes |
| China | Asia & Pacific | Developing | Yes |
| Columbia | Americas | Developing | Yes |
| Comoros | Africa | Least Developed | Yes |
| Costa Rica | Americas | Developing | Yes |
| Côte D'Ivoire | Africa | Developing | Yes |
| Croatia | Europe & CIS | Developing | Yes |
| Cuba | Americas | Developing | Yes |
| Cyprus | Europe & CIS | Developing | No |
| Czech Republic | Europe & CIS | Developing | Yes |
| Egypt | Arab States | Developing | Yes |
| El Salvador | Americas | Developing | Yes |
| Eritrea | Africa | Least Developed | Yes |
| Estonia | Europe & CIS | Developing | Yes |
| Ethiopia | Africa | Least Developed | No |
| Finland | Europe & CIS | Developed | Yes |
| France | Europe & CIS | Developed | Yes |
| Greece | Europe & CIS | Developed | Yes |
| Guatemala | Americas | Developing | Yes |
| Hungary | Europe & CIS | Developing | Yes |
| Iran | Asia & Pacific | Developing | Yes |
| Ireland | Europe & CIS | Developed | Yes |
| Jordan | Arab States | Developing | Yes |
| Latvia | Europe & CIS | Developing | Yes |
| Lebanon | Arab States | Developing | Yes |
| Lesotho | Africa | Least Developed | Yes |
| Liechtenstein | Europe & CIS | Developed | No |
| Lithuania | Europe & CIS | Developing | Yes |
| Madagascar | Africa | Least Developed | Yes |
| Mali | Africa | east Developed | No |
| Malta | Europe & CIS | Developing | No |
| Mauritania | Africa | Least Developed | Yes |
| Mauritius | Africa | Developing | Yes |
| Mexico | Americas | Developing | Yes |
| Moldova | Europe & CIS | Developing | Yes |
| Monaco | Europe & CIS | Developed | Yes |
| Morocoo | Arab States | Developing | Yes |
| Netherlands | Europe & CIS | Developed | Yes |
| Nicaragua | Americas | Developing | Yes |
| Niger | Africa | Least Developed | No |
| Panama | Americas | Developing | Yes |
| Papua New Guinea | Asia & Pacific | Developing | Yes |
| Peru | Americas | Developing | Yes |
| Philippines | Asia & Pacific | Developing | Yes |
| Poland | Europe & CIS | Developing | Yes |
| Portugal | Europe & CIS | Developing | Yes |
| Qatar | Arab States | Developing | No |
| Rwanda | Africa | Least Developed | Yes |
| Samoa | Asia & Pacific | Least Developed | Yes |
| Senegal | Africa | Least Developed | Yes |
| Slovenia | Europe & CIS | Developing | Yes |
| Spain | Europe & CIS | Developed | Yes |
| Sri Lanka | Asia & Pacific | Developing | Yes |
| Suriname | Americas | Developing | No |
| Swaziland | Africa | Developing | No |
| Switzerland | Europe & CIS | Developed | Yes |
| Syria | Arab States | Developing | Yes |
| Tajikistan | Europe & CIS | Developing | Yes |
| Thailand | Asia & Pacific | Developing | Yes |
| Turkey | Europe & CIS | Developing | Yes |
| Uganda | Africa | Least Developed | Yes |
| Ukraine | Europe & CIS | Developed | Yes |
| United Arab Emirates | Arab States | Developing | No |
| United Kingdom | Europe & CIS | Developed | Yes |
| Uzbekistan | Europe & CIS | Developing | Yes |
| Venezuela | Americas | Developing | Yes |
| Viet Nam | Asia & Pacific | Developing | Yes |

ANNEX  2-C

Question 4: Compliance Procedures

| Administration | Region | Development Status | Q.4 Specify Compliance | Q.4a) Development | Q.4a) Develop Source | Q.4b) Procedure | Q.4b) Procedure Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Albania | Europe & CIS | Developing | Yes | Other | – | Manufacturer's Declaration | – |
| Antigua and Barbuda | Americas | Developing | Yes | Other | – | Manufacturer's Declaration | – |
| Armenia | Europe & CIS | Developing | Yes | National & Other | – | Other | National declaration of compliance |
| Bahamas | Americas | Developing | Yes | Other | – | Type Approval & Declaration | – |
| Bahrain | Arab States | Developing | Yes | Other | – | Type Approval | – |
| Bhutan | Asia & Pacific | Least Developed | Yes | National | – | Manufacturer's Declaration | – |
| Bosnia & Herzegovina | Europe & CIS | Developing | Yes | Other | – | Other | Preparing regulations |
| Botswana | Africa | Developing | Yes | Other | – | Type Approval | – |
| Burundi | Africa | Least Developed | Yes | Other | – | Manufacturer's Declaration | – |
| Burkina Faso | Africa | Least Developed | Yes | Other | – | Type Approval |  |
| Cameroon | Africa | Developing | Yes | Other | (However, national standards are under development) | Type Approval | – |
| Canada | Americas | Developed | Yes | National | – | Type Approval | – |
| Central African Republic | Africa | Least Developed | Yes | Other | – | Manufacturer's Declaration | – |
| Chile | Americas | Developing | Yes | Other | – | Type Approval | and Other |
| China | Asia & Pacific | Developing | Yes | National | – | Type Approval | – |
| Columbia | Americas | Developing | Yes | Other | – | Manufacturer's Declaration | – |
| Comoros | Africa | Least Developed | Yes | Other | – | Manufacturer's Declaration | – |
| Costa Rica | Americas | Developing | Yes | Other | – | Type Approval | – |
| Côte d'Ivoire | Africa | Developing | Yes | National | – | Type Approval & Declaration | – |

| Administration | Region | Development Status | Q.4 Specify Compliance | Q.4a) Development | Q.4a) Develop Source | Q.4b) Procedure | Q.4b) Procedure Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Croatia | Europe & CIS | Developing | Yes | National & Other | – | Type Approval & Declaration | – |
| Cuba | Americas | Developing | Yes | National | – | Type Approval | – |
| Cyprus | Europe & CIS | Developing | Yes | Other | – | Type Approval & Declaration | – |
| Czech Republic | Europe & CIS | Developing | Yes | National & Other | ETSI | Type Approval & Declaration | and Other |
| Egypt | Arab States | Developing | Yes | National | – | Type Approval | Calibration and standardization institute |
| El Salvador | Americas | Developing | Yes | Other | – | Type Approval | – |
| Eritrea | Africa | Least Developed | Yes | Other | – | Manufacturer's Declaration | – |
| Estonia | Europe & CIS | Developing | Yes | National | Etsi | Manufacturer's Declaration | – |
| Ethiopia | Africa | Least Developed | Yes | National | – | Other | – |
| Finland | Europe & CIS | Developed | No | Other |  | Type Approval & Declaration | Also market surveillance. Note TA for only aeronautical and maritime equipment. Technical characteristics for radio equipment are defined in terms of essential requirements in the R&TTE directive. These are interpreted by Harmonized Standards drafted by standardization organizations recognized by the European Commission and on a mandate given by the European Commission. However these standards are not compulsory and a manufacturer can also use other technical basis for complying with the essential requirements but in that process a notified body, which has a consultative role, has to be used. Harmonized Standards do not contain all technical conditions needed to be defined for the use of the radio frequencies and such details, called Radio Interface Specifications, must be incorporated in the National Frequency Allocation Tables or defined separately. The borderline between Harmonized Standards and Radio Interface Specifications is not fixed but there is the principle that matters already coved in the relevant Harmonized Standards must not be redefined as part of the Radio Interface Specification. Compliance is based on Manufacturer's Declaration of Conformity as an a priori legal instrument but there is also Market Surveillance performed by the Competent Authority. For conformity assessment the R&TTE directive is the general framework with Manufacturer's Declaration of Conformity only, but for marine radio equipment (for compulsory use in ships) and for aeronautical radio equipment there is a separate EU legal framework based on type approval. |

| Administration | Region | Development Status | Q.4 Specify Compliance | Q.4a) Development | Q.4a) Develop Source | Q.4b) Procedure | Q.4b) Procedure Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
| France | Europe & CIS | Developed | Yes | National & Other | The technical regulations needed for the minimum necessary level of compliance (health and safety, EM compatibility, efficient spectrum utilization, etc.) are laid down in decisions of the minister responsible for telecommunications following consultation with the telecommunication regulatory authority. Standards for the equipment used include, in particular, ETSI standards. | Manufacturer's Declaration | Radio equipment is subject to an assessment for compliance with essential requirements (art. L.34-9). |
| Greece | Europe & CIS | Developed | Yes | Other | – | Manufacturer's Declaration | – |
| Guatemala | Americas | Developing | No | Other | – | – | – |
| Hungary | Europe & CIS | Developing | Yes | National & Other | Mostly based on international (European) standards | Other | R&TTE |
| Iran | Asia & Pacific | Developing | Yes | National | – | Type Approval | – |
| Ireland | Europe & CIS | Developed | Yes | Other | – | Type Approval & Declaration | – |
| Jordan | Arab States | Developing | Yes | Other | International standard equipment used. | Other | – |
| Latvia | Europe & CIS | Developing | Yes | National & Other | – | Type Approval & Declaration | – |
| Lebanon | Arab States | Developing | Yes | Other | – | Manufacturer's Declaration | – |
| Lesotho | Africa | Least Developed | Yes | Other | – | Other | – |
| Liechtenstein | Europe & CIS | Developed | Yes | Other | – | Type Approval & Declaration | – |
| Lithuania | Europe & CIS | Developing | Yes | National | We establish these on a basis of those developed by international standards organizations. | Type Approval & Declaration | TA is an option. |
| Madagascar | Africa | Least Developed | Yes | National | – | Type Approval & Declaration | – |
| Mali | Africa | Least Developed | Yes | Other | – | Manufacturer's Declaration | and other |
| Malta | Europe & CIS | Developing | Yes | Other | – | Type Approval & Declaration | – |

| Administration | Region | Development Status | Q.4 Specify Compliance | Q.4a) Development | Q.4a) Develop Source | Q.4b) Procedure | Q.4b) Procedure Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Mauritania | Africa | Least Developed | Yes | Other | – | Type Approval | – |
| Mauritius | Africa | Developing | Yes | Other | – | Type Approval & Declaration | – |
| Mexico | Americas | Developing | Yes | National | – | Type Approval | – |
| Moldova | Europe & CIS | Developing | Yes | Other | – | Type Approval | – |
| Monaco | Europe & CIS | Developed | Yes | Other | – | Type Approval | – |
| Morocco | Arab States | Developing | Yes | National | Nationals regulations are elaborated on the basis of, in particular, norms adopted by regional or international standardization bodies and taking into account national requirements. | Type Approval | A study is under way on the current process for certifying equipment. This could lead to a revision of the system currently in use. |
| Netherlands | Europe & CIS | Developed | Yes | Other | – | Manufacturer's Declaration | – |
| Nicaragua | Americas | Developing | Yes | Other | – | Type Approval | – |
| Niger | Africa | Least Developed | Yes | Other | – | Manufacturer's Declaration | – |
| Panama | Americas | Developing | Yes | Other | – | Manufacturer's Declaration |  |
| Papua New Guinea | Asia & Pacific | Developing | Yes | National & Other | – | Type Approval | and National Radio Standards and Specifications. |
| Peru | Americas | Developing | Yes | Other | – | Type Approval | – |
| Philippines | Asia & Pacific | Developing | Yes | Other | – | Type Approval | – |
| Poland | Europe & CIS | Developing | Yes | Other | – | Type Approval & Declaration | or Certificate of Conformity of the Equipment. |
| Portugal | Europe & CIS | Developing | Yes | Other | – | Manufacturer's Declaration | – |
| Qatar | Arab States | Developing | Yes | National & Other | – | Type Approval & Declaration | – |
| Rwanda | Africa | Least Developed | Yes | National | – | Type Approval | – |
| Samoa | Asia & Pacific | Least Developed | Yes | National | – | Type Approval & Declaration | – |
| Senegal | Africa | Least Developed | Yes | National & Other | – | Manufacturer's Declaration | – |
| Slovenia | Europe & CIS | Developing | Yes | Other | CEPT, ETSI | Type Approval | – |
| Spain | Europe & CIS | Developed | No | Other | – | Manufacturer's Declaration | – |
| Sri Lanka | Asia & Pacific | Developing | Yes | Other | – | Manufacturer's Declaration | – |

| Administration | Region | Development Status | Q.4) Specify Compliance | Q.4a) Development | Q.4a) Develop Source | Q.4b) Procedure | Q.4b) Procedure Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Suriname | Americas | Developing | Yes | Other | – | Type Approval & Declaration | – |
| Swaziland | Africa | Developing | Yes | Other | – | Type Approval & Declaration | We accept equipment Type Approved in South Africa and sometimes equipment that is (CE) compliant depending on the service to be used for. |
| Switzerland | Europe & CIS | Developed | Yes | Other | – | Manufacturer's Declaration | National or CE marking on equipment. Equipment Class Identifier. Notification to Administration of the fact that equipment is put on the market. |
| Syria | Arab States | Developing | Yes | National | – | Type Approval & Declaration | – |
| Tajikistan | Europe & CIS | Developing | Yes | Other | – | Other | – |
| Thailand | Asia & Pacific | Developing | Yes | Other | – | Type Approval | – |
| Turkey | Europe & CIS | Developing | Yes | National | – | Type Approval & Declaration | and R&TTE |
| Uganda | Africa | Least Developed | Yes | Other | – | Other | – |
| Ukraine | Europe & CIS | Developed | Yes | National & Other | – | Type Approval & Declaration | – |
| United Arab Emirates | Arab States | Developing | Yes | National | – | Type Approval & Declaration | and Other |
| United Kingdom | Europe & CIS | Developed | Yes | Other | – | Manufacturer's Declaration | R&TTE |
| Uzbekistan | Europe & CIS | Developing | Yes | National | – | Type Approval & Declaration | and Other |
| Venezuela | Americas | Developing | Yes | National & Other | – | Type Approval | – |
| Viet Nam | Asia & Pacific | Developing | Yes | National | – | Type Approval | – |

ANNEX  2-D

Question 5: Spectrum redeployment

| Administration | Region | Development Status | Q.5a) Spectrum Redeployment | Q.5b) Redeployment Method | Q.5c) Define Method | Q.5c) Describe Consultation |
| --- | --- | --- | --- | --- | --- | --- |
| Albania | Europe & CIS | Developing | No | No | – | – |
| Antigua and Barbuda | Americas | Developing | No | Yes | – | – |
| Armenia | Europe & CIS | Developing | Yes | Yes | Limitation of use frequency band for allocation it for new planned systems; temporary licence for operation; bringing in use a new telecommunications system with the functioning systems; closing solitary systems and inappropriate to the standards radio electronic equipment | – |
| Bahamas | Americas | Developing | No | No | – | – |
| Bahrain | Arab States | Developing | No | No | – | – |
| Bhutan | Asia & Pacific | Least Developed | No | No | – | – |
| Bosnia & Herzegovina | Europe & CIS | Developing | No | No | – | – |
| Botswana | Africa | Developing | Yes | Yes | Currently we have waited for the equipment to reach their end of life, not licensing any new system. We are considering in future introducing some incentives for migration like lowering licence fees. |  |
| Burundi | Africa | Least Developed | Yes | No | – | – |
| Burkina Faso | Africa | Least Developed | No | No | – | – |
| Cameroon | Africa | Developing | No | No | – | – |
| Canada | Americas | Developed | Yes | Yes | Public consultation | Extensive public consultation with stake-holders and industry/government strategic partnering to establish the implementation phases and incentives for the Redeployment Plan from 100-500 MHz. |

| Administration | Region | Development Status | Q.5a) Spectrum Redeployment | Q.5b) Redeployment Method | Q.5c) Define Method | Q.5c) Describe Consultation |
| --- | --- | --- | --- | --- | --- | --- |
| Central African Republic | Africa | Least Developed | No | No | – | – |
| Chile | Americas | Developing | Yes | Yes | In a number of specific cases we have implemented the spectrum "redistribution" process referred to in this questionnaire | – |
| China | Asia & Pacific | Developing | Yes | Yes | According to relative international rules | – |
| Columbia | Americas | Developing | Yes | Yes | We have implemented processes to free up spectrum that is required for the introduction of mobile telephony services (e.g. PCS). The Ministry of Communications determines suitable frequencies for migration; the operators bear the costs associated with the changes. | – |
| Comoros | Africa | Least Developed | No | No | Redeployment is likely to become a necessity one day, but nothing has been done in this connection to date. | – |
| Costa Rica | Americas | Developing | Yes | Yes | The Table of Frequency Allocations establishes that, as from 2000, all radiocommunication operators shall use a bandwidth of 12.5 kHz rather than 25 kHz | – |
| Côte d'Ivoire | Africa | Developing | Yes | Yes | Sessions are used to poll users' positions. Upon conclusion of this consultation, the agency makes a redeployment proposal which all of the users concerned adopt at a workshop. | Sessions are used to poll users' positions. Upon conclusion of this consultation, the agency makes a redeployment proposal which all of the users concerned adopt at a workshop. |
| Croatia | Europe & CIS | Developing | Yes | Yes | Two-step procedure is usually applied. In first phase new licences for this spectrum are not issued, and in second step transition to new frequency band upon consultation with interested parties is done. | – |
| Cuba | Americas | Developing | Yes | No | – | – |
| Cyprus | Europe & CIS | Developing | Yes | No | All redeployment is made through the work at CEPT. | – |
| Czech Republic | Europe & CIS | Developing | Yes | Yes | Used methods ranging from persuasion up to change of frequency plans and/or expiration of licences or authorizations, which are not renewed in such cases. | – |
| Egypt | Arab States | Developing | Yes | Yes | Compensation method. | – |
| El Salvador | Americas | Developing | No | No | No application | – |
| Eritrea | Africa | Least Developed | No | No | Not yet. | – |
| Estonia | Europe & CIS | Developing | Yes | No | We don't have the common method for achieving the re-deployment. From legislative point of view the regulator can change technical conditions of licence but the period between the notification of the holder of a technical authorization of the decision to amend the conditions of the technical authorization and the entry into force of the amendments shall be not less than two years. | – |

| Administration | Region | Development Status | Q.5a) Spectrum Redeployment | Q.5b) Redeployment Method | Q.5c) Define Method | Q.5c) Describe Consultation |
| --- | --- | --- | --- | --- | --- | --- |
| Ethiopia | Africa | Least Developed | No | No | – | – |
| Finland | Europe & CIS | Developed | Yes | Yes | The Finnish Radio Act gives FICORA the right to amend, in justified cases, all the licence conditions including the operating frequencies cases. If there is a need to give access for a new radio system operating according to an internationally/European wide adopted frequency usage plan, the relevant regulation by FICORA (On the Use of Radio Frequencies, Regulation 4, http://www.ficora.fi/englanti/document/FICORA04A2002M.pdf) will be revised, as appropriate. In this case moving costs are not compensated. In other cases new spectrum holders should, in general, compensate the moving costs. | – |
| France | Europe & CIS | Developed | Yes | Yes | The term spectrum redeployment is used in the context of long-term planning, while spectrum rearrangement (“réaménagement du spectre”) designates the result of medium or short-term constraints. Spectrum rearrangement is one of the missions of the “Agence nationale des fréquences”. The procedure was set up in 1997. The agency evaluates the cost of the operations, establishes a schedule for implementation, oversees work and manages funding intended for spectrum rearrangement (art. R.52-2-1 9°). As a rule, new entrants must contribute to cover the costs associated with redeployment (installing the previous user in other frequency bands or enabling alternatives to radio). The agency makes a partial contribution to rearrangement expenses from its spectrum rearrangement fund, which acts as an incentive to encourage such operations. Its spending is normally reimbursed by the new entrants once the vacated frequencies have been allocated. | To this end, the agency works through a standing committee which it chairs, in close concertation with administrations and designating authorities, telecommunication operators, and industry and trade union professionals, to prepare and oversee spectrum rearrangement operations. |
| Greece | Europe & CIS | Developed | Yes | Yes | Public consultation | Public consultation. |
| Guatemala | Americas | Developing | No | No | – | – |
| Hungary | Europe & CIS | Developing | Yes | Yes | The Government decides on the communications policy, which includes the introduction of new radiocommunication systems. Such decisions are taken after appropriate consultations with the interested parties. The actual spectrum redeployment process is based on the National Table of Frequency Allocations adopted by the Government after consultations with the interested users and keeping the European harmonization efforts in sight. Such redeployments may be financed from the state budget. | Appropriate consultations with the interested parties. |
| Iran | Asia & Pacific | Developing | Yes | Yes | In case of assigning a part of frequency band to a new service or expanding of frequency band for a service, we can act according to our legal authorities, provided that it isn't previously assigned to another service or user. If it assigned to another service or user, the issue must be solved through mutual negotiation otherwise the new operator shall compensate the loss caused by redeployment. | – |

| Administration | Region | Development Status | Q.5a) Spectrum Redeployment | Q.5b) Redeployment Method | Q.5c) Define Method | Q.5c) Describe Consultation |
| --- | --- | --- | --- | --- | --- | --- |
| Ireland | Europe & CIS | Developed | Yes | No | – | – |
| Jordan | Arab States | Developing | No | No | To be answered by TRC. | – |
| Latvia | Europe & CIS | Developing | Yes | No | Not Yet – the procedure was described in the previous Law on Telecommunications. | – |
| Lebanon | Arab States | Developing | No | No | – | – |
| Lesotho | Africa | Least Developed | Yes | Yes | The redeployed bands have not been used yet. | – |
| Liechtenstein | Europe & CIS | Developed | Yes | Yes | Spectrum Monitoring, degree of usage, density of assignments. | No consultation regarding potential costs. |
| Lithuania | Europe & CIS | Developing | Yes | Yes | The following process describe spectrum redeployment in Republic of Lithuania: In accordance with the Law on Telecommunications one of the functions of the Communications Regulatory Authority shall be are to prepare and submit to the Government for its approval the National Radio Frequency Allocation Table, develop and implement the strategy for the use of radio frequencies in Lithuania; to prepare, together with the Radio and Television Commission, and submit to the Government for its approval the strategy and the strategic plan of allocation of radio frequencies for broadcasting and transmitting radio and television programmes. This plan shall also include the development of telecommunications networks intended for broadcasting of radio and television programmes. | – |
| Madagascar | Africa | Least Developed | Yes | Yes | Division on territorial basis. | – |
| Mali | Africa | Least Developed | Yes | No | – | – |
| Malta | Europe & CIS | Developing | No | No | – | – |
| Mauritania | Africa | Least Developed | No | No | Frequency redeployment has not yet commenced, given the limited number of spectrum users at present. |  |
| Mauritius | Africa | Developing | Yes | Yes | Migration to other frequency band. | – |
| Mexico | Americas | Developing | Yes | No | – | – |
| Moldova | Europe & CIS | Developing | Yes | No | – | – |
| Monaco | Europe & CIS | Developed | Yes | No | – | – |
| Morocco | Arab States | Developing | Yes | Yes | The method is in the process of being finalized and adopted. More information may become available once this has been done. | – |

| Administration | Region | Development Status | Q.5a) Spectrum Redeployment | Q.5b) Redeployment Method | Q.5c) Define Method | Q.5c) Describe Consultation |
| --- | --- | --- | --- | --- | --- | --- |
| Netherlands | Europe & CIS | Developed | Yes | Yes | There is no single method. The method for redeployment depends on the original method of assignment; users are informed well before the date of change. In recent history mostly voluntary withdrawal took place. | – |
| Nicaragua | Americas | Developing | No | No | – | – |
| Niger | Africa | Least Developed | No | No | – | – |
| Panama | Americas | Developing | Yes | Yes | – | Public consultation. |
| Papua New Guinea | Asia & Pacific | Developing | Yes | No | Telikom PNG have decided to avoid usage of bands around 2 GHz. | – |
| Peru | Americas | Developing | Yes | Yes | Políticas sectoriales. | – |
| Philippines | Asia & Pacific | Developing | Yes | Yes | Please refer to the attached copy of M.C. 3-3-96; Previous assignments not in conformity with the approved and current National Frequency Allocation Table shall be recalled. Those affected shall be re-located based on availability of frequency/ies. Special efforts shall be extended by the Commission to assist those affected. 603. TRANSFER OF AFFECTED AUTHORIZED RADIO FREQUENCY USER a. The commission shall allocate available radio frequencies for assignment to those affected by the reallocation as a result of the review of the radio spectrum pursuant to Rule 601. b. The cost of the transfer to new radio frequencies of affected authorized users shall be borne by the new assignees to the radio frequency channel/band where the radio frequencies of the previously authorized users fall within. c. When the transfer to a new set of radio frequencies would require additional radio links, the cost of these links shall also be taken into consideration. d. The manner and the cost of the transfer shall be negotiated in good faith between the affected authorized users and the assignees within 90 days from receipt of notice of relocation. e. The Commission shall extend all the necessary assistance to all affected authorized users and shall mandate settlement if the parties fail to come to an agreement within 90 days from receipt of notice of relocation or when warranted under the circumstances. f. Other means/mode of transmission comparable in quality to the existing facility shall be taken into consideration in the negotiation for the transfer. g. Transfer of radio frequency assignment shall only take effect upon activation of service by relocated party using its newly assigned or relocated frequency as agreed or mandated. | – |

| Administration | Region | Development Status | Q.5a) Spectrum Redeployment | Q.5b) Redeployment Method | Q.5c) Define Method | Q.5c) Describe Consultation |
| --- | --- | --- | --- | --- | --- | --- |
| Poland | Europe & CIS | Developing | Yes | Yes | – | – |
| Portugal | Europe & CIS | Developing | Yes | No | The solutions are applied on a case-by-case basis. | – |
| Qatar | Arab States | Developing | No | No | – | – |
| Rwanda | Africa | Least Developed | Yes | Yes | Contact the regulatory agency. | – |
| Samoa | Asia & Pacific | Least Developed | Yes | Yes | – | – |
| Senegal | Africa | Least Developed | No | No | – | – |
| Slovenia | Europe & CIS | Developing | Yes | Yes | Art. 47 of Telecommunication Law; Revokation, | – |
| Spain | Europe & CIS | Developed | No | No | – | – |
| Sri Lanka | Asia & Pacific | Developing | Yes | Yes | Planned to recover the redeployments cost from the interested parties. | – |
| Suriname | Americas | Developing | No | No | – | – |
| Swaziland | Africa | Developing | Yes | No | This is really a problem except when the re-deployment is not immediate and is envisaged not to incur any costs which might need compensation. Such problems were experienced during the introduction of mobile cell phones as there was a public outcry for the cell phone service which in the region was earmarked at 890 MHz-960 MHz where there were sound broadcasting links We are faced with the same problem with the upcoming of new technologies where there are already existing services. |  |
| Switzerland | Europe & CIS | Developed | Yes | Yes | (1) Waiting for radio licences to expire and (2) revocation of the radio licence (with or without financial compensation of the incumbent licensee). |  |
| Syria | Arab States | Developing | No | No | – | – |
| Tajikistan | Europe & CIS | Developing | Yes | Yes | Conversion and counting the potential costs resulting from the planned redeployment. | Conduct consultation with users working in the band. |
| Thailand | Asia & Pacific | Developing | No | No | None | – |
| Turkey | Europe & CIS | Developing | Yes | Yes | When redeployment is needed, another frequency band is assigned to the user with sufficient time for redeployment. There is no payment due to redeployment. | – |

| Administration | Region | Development Status | Q.5a) Spectrum Redeployment | Q.5b) Redeployment Method | Q.5c) Define Method | Q.5c) Describe Consultation |
| --- | --- | --- | --- | --- | --- | --- |
| Uganda | Africa | Least Developed | No | No | Not applicable. | – |
| Ukraine | Europe & CIS | Developed | Yes | Yes | – | – |
| United Arab Emirates | Arab States | Developing | Yes | No | – | – |
| United Kingdom | Europe & CIS | Developed | Yes | Yes | Spectrum pricing is one method that was introduced partly with the intention of simplifying the spectrum redeployment process. Another method is licence revocation. | Consultation involves user groups and other government organizations depending on the spectrum and services concerned. |
| Uzbekistan | Europe & CIS | Developing | Yes | Yes | Method of compensation of cost for usage other bands. Potential cost is approximately from 2 900 to 9 900 Swiss Francs. | – |
| Venezuela | Americas | Developing | Yes | Yes | Study + inspections, enquiry + auction (beneficiary covers expenses) | – |
| Viet Nam | Asia & Pacific | Developing | No | No | – | – |

ANNEX  2-E

Responses concerning Questions 3 et 10

| Country | Responses concerning Q.3 and Q.10 |
| --- | --- |
|  | Q.3 | Q.10 |
| Albania | – | Yes |
| Angola | Yes | Yes |
| Antigua and Barbuda | No | Yes |
| Armenia | Yes | Yes |
| Bahamas | No | Yes |
| Bahrain | No | Yes |
| Bhutan | Yes | Yes |
| Bosnia | Yes | Yes |
| Botswana | Yes | Yes |
| Burkina Faso | Yes | Yes (in future) |
| Burundi | Yes | No |
| Cameroon | No | Yes |
| Canada | Yes | Yes |
| Central African Rep. | Yes | No |
| Chile | Yes | Yes |
| China | Yes | Yes |
| Colombia | Yes | Yes |
| Comoros | Yes (No use) | Yes in future Agency |
| Costa Rica | Yes | Yes |
| Côte d'Ivoire | Yes | Yes |
| Croatia | Yes | Yes |
| Cuba | Yes | Yes |
| Cyprus | No | No |
| Czech Rep. | Yes | Yes |
| Egypt | Yes | Yes |
| El Salvador | Yes | Yes |
| Eritrea | Yes | Yes |
| Estonia | Yes | No |
| Ethiopia | Yes | No |
| Finland | Yes | Yes |
| France | Yes | Yes |
| Gabon | NR | NR |

| Country | Responses concerning Q.3 and Q.10 |
| --- | --- |
|  | Q.3 | Q.10 |
| Greece | Yes | Yes |
| Guatemala | Yes | Yes |
| Iran | Yes | Yes |
| Ireland | Yes | Yes |
| Jordan | Yes | – |
| Latvia | Yes | Yes |
| Lebanon | Yes | Yes |
| Lesotho | Yes | Yes |
| Liechtenstein | Yes | Yes |
| Lithuania | Yes | Yes |
| Madagascar | No | Yes |
| Mali | – | – |
| Malta | Yes | Yes |
| Mauritania | Yes | Yes |
| Moldova | Yes | Yes |
| Monaco | Yes | No |
| Morocco | Yes | Yes |
| Netherlands | Yes | Yes |
| Nicaragua | Yes | Yes |
| Niger | No | Yes |
| Panama | Yes | Yes |
| Papua New Guinea | Yes | No |
| Peru | Yes | Yes |
| Philippines | NR | NR |
| Poland | Yes | Yes |
| Portugal | Yes | Yes |
| Qatar | Yes | Yes |
| Romania | NR | NR |
| Rwanda | Yes | Yes |
| Samoa | Yes | Yes |
| Saudi Arabia | NR | NR |
| Senegal | Yes | Yes |
| Slovenia | Yes | Yes |
| Spain | Yes | Yes |
| Sri Lanka | Yes | Yes |
| Suriname | Yes | Yes |
| Swaziland | No | No |

| Country | Responses concerning Q.3 and Q.10 |
| --- | --- |
|  | Q.3 | Q.10 |
| Switzerland | Yes | Yes |
| Syria | Yes | Yes |
| Tajikistan | Yes | Yes |
| Thailand | Yes | Yes |
| Turkey | Yes | Yes |
| Uganda | No | Yes |
| Ukraine | Yes | Yes |
| United Arab Emirates | No | No |
| United Kingdom | Yes | Yes |
| Uzbekistan | Yes | Yes |
| Venezuela | Yes | Yes |
| NR = No Response |

ANNEX  2-F

Responses concerning Question 6

| Administration | Region | Status | Q.6a) Spectrum managements costs | Q.6b) What is the source of the funding required to accomplish these spectrum management functions? |
| --- | --- | --- | --- | --- |
| Albania | Europe & CIS | DVG | 98, 000 SF | The fees of licences granted by TRE and NRTC. |
| Antigua and Barbuda | Americas | DVG | Unknown | Local government |
| Armenia | Europe & CIS | DVG | – | Organization's revenue by spectrum regulation |
| Bahamas | Americas | DVG | US $609.000 | From licence fees |
| Bahrain | Arab States | DVG | – | – |
| Bhutan | Asia & Pacific | LDC | – | Royal Government of Bhutan (RGOB funding) Equipments were donated by UNOP and UNDP |
| Bosnia & Herzegovina | Europe & CIS | DVG | Not available | The funding of the Agency shall come from the following sources: a) Recurrent technical licence fees for the regulation and supervision of the telecommunications operators and broadcasters; and b) Grants or donations received by the Agency insofar as they are in conformity with general principles of law. When grants or donations are given for specific tasks or projects in the public interest, they shall be accounted for separately to the approved budget and not be included therein. |
| Botswana | Africa | DVG | Unavailable | Radio licence fees. |
| Burkina Faso | Africa | LDC | – | ARTEL budget and spectrum user fees |
| Burundi | Africa | LDC | – | Fees for spectrum utilization |

| Administration | Region | Status | Q.6a) Spectrum managements costs | Q.6b) What is the source of the funding required to accomplish these spectrum management functions? |
| --- | --- | --- | --- | --- |
| Cameroon | Africa | DVG | Total cost unavailable | Fees for spectrum utilization; otherwise, general budget |
| Canada | Americas | DVD | 55 M SF | The funding is obtained through parliamentary allotment. |
| Central African Republic | Africa | LDC | – | Funding from SOCATEL (fees) |
| Chile | Americas | DVG | – | Fiscal budget assigned to the Subsecretariat for Telecommunications |
| China | Asia & Pacific | DVG | about 2 million per year SF | Mainly from frequency fees |
| Columbia | Americas | DVG | CHF 632 000/year (planning and assignment) CHF 2 385 000/year (control) | National budget, approved with support from the Communications Fund which receives resources by way of compensation, administered by telecommunication service licensees and radio spectrum users |
| Comoros | Africa | LDC | Salary of official assigned to handle spectrum management (450 FS) | These functions are funded by SNPT, which hosts the body responsible for spectrum management within one of its services. |
| Costa Rica | Americas | DVG | Not available | Frequency levies established by the Ministry of Government and Police, the maximum amount being USD 400 per year in the case of television |
| Côte d'Ivoire | Africa | DVG | – | – |
| Croatia | Europe & CIS | DVG | N/A | Frequency Fee |
| Cuba | Americas | DVG | CHF 1.8 million | The income received from radiocommunication service licences, permits, authorizations and concessions |
| Cyprus | Europe & CIS | DVG | 2 000 000 SF | Government budget |
| Czech Republic | Europe & CIS | DVG | Costs are set down case by case, namely if there is intention to award licence to winner of the competitive or comparative selection procedure. | State budget |
| Egypt | Arab States | DVG | 330.000 (Swiss Francs) | The source of funding is self-dependent |
| El Salvador | Americas | DVG | CHF 1.200.000.00 | Own funds (autonomous entity) |
| Eritrea | Africa | LDC | Xxxx | Government budget allocations |
| Estonia | Europe & CIS | DVG | It is responsible for one agency | State budget |

| Administration | Region | Status | Q.6a) Spectrum managements costs | Q.6b) What is the source of the funding required to accomplish these spectrum management functions? |
| --- | --- | --- | --- | --- |
| Ethiopia | Africa | LDC | approx.100.000 SF | Annual budget from the Government of Ethiopia (GoE). |
| Finland | Europe & CIS | DVD | about 14.5 Million CHF (year 2002) (Incl. spectrum management, licensing, radio monitoring, investigation and solving of radio interferences, market surveillance, proficiency examinations, type approvals (aeronautical and maritime radio equipment only), radio equipment standardization. | All the costs of the Radio Administration are covered by the spectrum and licence fees collected from the users and the radio frequencies. |
| France | Europe & CIS | DVD | The cost of the functions of national spectrum management, i.e. for the allocation of frequency bands (planning and international affairs, registration of assignments and sites, monitoring) is equal to the budget of the national frequency agency (some CHF 47.5 million or EUR 32.5 millions in 2002, of which some 15% was for capital spending, including in particular the spectrum monitoring system). | The agency and the independent administrative authorities are funded by public grants from the economics and finance ministry and other concerned ministries. |
| Greece | Europe & CIS | DVD | To be determined | Spectrum fees and licence fee. |
| Guatemala | Americas | DVG | Not calculated | It used to be the case that a percentage was taken of the income received from spectrum auctions, whereas now everything is handled by the central Government |
| Hungary | Europe & CIS | DVG | 36.8 million SF | Frequency reservation and usage fees for civil frequency management State budget for non-civil frequency management |
| Iran | Asia & Pacific | DVG | – | The budget of spectrum management is approved by government budget |
| Ireland | Europe & CIS | DVD | Not available | Licence fees in some cases and a levy (based on revenue) on spectrum users in other cases. |
| Jordan | Arab States | DVG | To be answered by TRC | To be answered by TRC |
| Latvia | Europe & CIS | DVG | – | The fees and charges for the insurance of electromagnetic compatibility, paid by frequency users |
| Lebanon | Arab States | DVG | 200 000 SF | The MPT Public Budget |
| Lesotho | Africa | LDC | 224 265.62 (Swiss Francs) | Annual spectrum fees, Government, Donor Community |
| Liechtenstein | Europe & CIS | DVD | not available | Fees for frequency usage and administrative efforts |
| Lithuania | Europe & CIS | DVG | The total is 7.41 million CHF per year | The fund for the communications management and control under the special program approved by the Government of the Republic of Lithuania Resolution No 1591 of 22 Dec. 2001 Concerning State Budget Allocations Under the Approved Programs. |

| Administration | Region | Status | Q.6a) Spectrum managements costs | Q.6b) What is the source of the funding required to accomplish these spectrum management functions? |
| --- | --- | --- | --- | --- |
| Madagascar | Africa | LDC | SFR 181 585.94 per year | Rights and fees collected from spectrum users |
| Mali | Africa | LDC | – | – |
| Malta | Europe & CIS | DVG | 140.088 (capital) (Swiss Francs) | 70.000 (recurrent) (Swiss Francs) |
| Mauritania | Africa | LDC | Not available | The acquisition of management resources was funded by the state and certain development partners. Ongoing spectrum management will be funded essentially by the regulatory authority. |
| Mauritius | Africa | DVG | spectrum fees: MUR 10.000/100 kHz (approx. 500 FS for 100 kHz) | Licence fees for spectrum usage. |
| Mexico | Americas | DVG | We do not have this information | Government |
| Moldova | Europe & CIS | DVG | – | Fees for frequency usage |
| Monaco | Europe & CIS | DVD | Not identified | State budget |
| Morocco | Arab States | DVG | – | Spectrum user fees |
| Netherlands | Europe & CIS | DVD | 44 million SF | Mostly fees, little contribution from state budget for performing certain legal, non frequency management tasks. |
| Nicaragua | Americas | DVG | – | Operators |
| Niger | Africa | LDC | Figure not available | Spectrum user fees |
| Panama | Americas | DVG | 42.000 $ | Own funds and UNDP funds (World Bank) |
| Papua New Guinea | Asia & Pacific | DVG | 2.5 million SF | Operational Licence fees & Radio Spectrum Fees |
| Peru | Americas | DVG | Not available | Ministry's own resources, generated by the charges levied on telecommunication service operators |
| Philippines | Asia & Pacific | DVG | – | Agency Annual Budget Appropriations. |
| Poland | Europe & CIS | DVG | 23 million SF | State budget |

| Administration | Region | Status | Q.6a) Spectrum managements costs | Q.6b) What is the source of the funding required to accomplish these spectrum management functions? |
| --- | --- | --- | --- | --- |
| Portugal | Europe & CIS | DVG | The value of the ANACOM's costs with management spectrum is not available. It is only available the value of personnel costs, who accounted 4.304.059 Swiss Franc in 2001. This value represented 19.6% of total ANACOM's personnel costs | Financed by fees/charges paid by all licensed operators |
| Qatar | Arab States | DVG | – | Licence fees as well as grant |
| Rwanda | Africa | LDC | Depends on frequency; for more information contact the agency | Operator and state-funded |
| Samoa | Asia & Pacific | LDC | – | The Ministry of Posts and Telecommunication is seeking overseas assistance for funding to accomplish the Spectrum Management Division. (e.g. World Bank) |
| Senegal | Africa | DVG | Information not available | Spectrum user fee income |
| Slovenia | Europe & CIS | DVG | 6.000.000 SF | Frequency fee, numbering fee, licence fee, notifications |
| Spain | Europe & CIS | DVD | – | – |
| Sri Lanka | Asia & Pacific | DVG | 250.000 SF | Telecommunications Regulatory Commission of Sri Lanka |
| Suriname | Americas | DVG | – | – |
| Swaziland | Africa | DVG | – | Swaziland Posts and Telecoms Corporation so far, is responsible for all the funding required to accomplish the spectrum management functions. |
| Switzerland | Europe & CIS | DVD | approx. 18'000'000 SF | Cost-covering administrative fees + General budget of the State |
| Syria | Arab States | DVG | Not available | The functions is funded by the revenues of the licensing |
| Tajikistan | Europe & CIS | DVG | 301 431.801 SF per annum | From frequency fees and any additional charges |
| Thailand | Asia & Pacific | DVG | N/A | Government |
| Turkey | Europe & CIS | DVG | – | Frequency usage fee, licensing fee, contribution fee from 0.3% of endorsement of companies (licensed services only) |
| Uganda | Africa | LDC | There is currently no specific cost for providing spectrum management functions. The frequency fees are paid for frequency usage and these fees cover other Uganda Communications Commission (UCC) functions. | Spectrum Licence Fees |
| Ukraine | Europe & CIS | DVD | – | – |

| Administration | Region | Status | Q.6a) Spectrum managements costs | Q.6b) What is the source of the funding required to accomplish these spectrum management functions? |
| --- | --- | --- | --- | --- |
| United Arab Emirates | Arab States | DVG | – | MOC |
| United Kingdom | Europe & CIS | DVD | 116m SF | Spectrum usage fees |
| Uzbekistan | Europe & CIS | DVG | 793 000 SF | Radiofrequency spectrum fees |
| Venezuela | Americas | DVG | – | State budget + taxes + fees + additional contributions |
| Viet Nam | Asia & Pacific | DVG | – | – |

ANNEX  2-G  –  SECTION  1

Use of computers for national spectrum management

Preliminary remarks

–	which criterion to be used for the purpose of analysis? The development status, the situation in a regional group? The GNP? Besides the diversity of responses given in descriptive texts, statistics can help to give an overall view;

–	spectrum management does not mean exactly the same according to the administrations. It can be understood in a more or less broad meaning, moreover as organizations responsible for spectrum management can vary according the administrations;

–	the large rate of no replies to some questions (up to 60% for question 6 on spectrum management costs) make the use of statistics more perilous.

General rate of response to Part II (reply to at least one part of the Questionnaire)

| Region | Number of administrations in the region (a) | Number of responses (b) | Developed | Developing | Least developed | Rate of response by region (a)/(b) | In % of total responses to Part II |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Africa | 45 | 19 | – | 5 | 14 | 41% | 24% |
| Americas | 34 | 15 | 1 | 14 | – | 44% | 19% |
| Arab States | 19 | 8 | – | 8 | – | 42% | 10% |
| Asia-Pacific | 38 | 9 | – | 7 | 2 | 24% | 11% |
| Europe and CIS | 53 | 27 | 11 | 18 | – | 51% | 34% |
| Total | 189 | 80 | 12 | 52 | 16 |  | 100% |
| As % of all responses Part II |  | 100% | 15% | 67% | 20% |  |  |

Rate of response for questions 6, 15 and 16 by region

| Region | Response to Q.6a) | Response to Q.6b) | Response to Q.15 | Response to Q.16a) to d) | Response to Q.16e) to f) | Response to Part II |
| --- | --- | --- | --- | --- | --- | --- |
| Africa | 5 | 17 | 18 | 17 | 15 | 19 |
| Americas | 6 | 13 | 15 | 11 | 14 | 15 |
| Arab States | 3 | 8 | 7 | 6 | 7 | 8 |
| Asia-Pacific | 2 | 15 | 9 | 8 | 7 | 9 |
| Europe and CIS | 15 | 25 | 29 | 27 | 28 | 27 |
| Total | 31 | 68 | 78 | 69 | 71 | 80 |
| In % of total of responses to Part II | 39% | 85% | 98% | 86% | 89% | 100% |

Rate of response for questions 6, 15 and 16 by development status

| Region | Response to Q.6a) | Response to Q.6b) | Response to Q.15 | Response to Q.16 | Response to Part II |
| --- | --- | --- | --- | --- | --- |
| Developed | 6 | 10 | 12 | 11 | 12 |
| Developing | 20 | 45 | 51 | 46 | 52 |
| Least developed | 5 | 14 | 15 | 15 | 16 |
| Total | 31 | 68 | 78 | 72 | 80 |
| Developed | 50% | 83% | 100% | 92% |  |
| Developing | 38% | 87% | 98% | 88% |  |
| Least developed | 31% | 88% | 94% | 94% |  |
| In % of total responses Part II | 39% | 85% | 98% | 86% | 100% |

ANNEX  2-G  –  SECTION  2

Administrative Management

| COUNTRY | DMBS | No. of assignments | No. of licences | Personnel | IT |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Expert | Techn. | XS | PC | System | LAN | Internet |
| Albania* | Manual | 1 500 | 331 | 14 | 8 | – | 3 DELL | W 2000 | – | X |
| Antigua and Barbuda* | Manual | 800 | 500 | 2 | – | – | – | – | – | X |
| Armenia | Personnel | 1 342 | 673 | 54 | 50 | 1 | 20 IBM | W98/2000/XP | X | X |
| Bahamas* | Access | 1 700 | 2 957 | 3 | 1 | – | 2 | W/2000/XP | X | X |
| Bahrain* | L and S | 3 932 | – | 8 | 16 | – | 11 IBM | W/NT/98 | X | X |
| Bhutan* | Manual | – | – | – | 2 | 1 | 1 | W/98 | – | X |
| Bosnia* | ATDI | 1 100 | 900 | 8+4 | 2 | 15 | 15 IBM | W/2000 | X | X |
| Burkina Faso | – | 1 103 | 1 337 | 2 | 3 | – | 2 COMPAQ | – | – | X |
| Burundi | Access | 689 | – | 2 | 2 | – | 2 DELL | Access | X | X |
| Cameroon | Excel WinBASMS | 3 974 | 183 | – | – | – | 4 | W 58/XP | – | X |
| Canada | Oracle | 587 000 | 869 000 |  | 300 | 50 | 600 | W 2000/NT | X | X |
| China | Oracle | 8 203 | 4 438 | 25 | 100 | 500 | 3 000 | W/2000/NT XP | X | X |
| Colombia | ASMS 710 (TCI) | 13 000 | 78 | 25 | 10 | – | 14 HP | W/NR | W | – |
| Comoros* | Excel (3) | 250 | 6 | 1 | – | – | 1 DELL | World | – | X |
| Costa Rica* | Auto | 8 400 | 12 000 | 11 | 2 | No | No | No | – | X |
| Côte d'Ivoire | Manual | 120 | 50 | 17 | 6 | 15 | 15 | W | X | X |
| Croatia | MS Access | 20 000 | 20 000 | 20 | 30 | – | 20 | W | X | X |

| COUNTRY | DMBS | No. of assignments | No. of licences | Personnel | IT |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Expert | Techn. | XS | PC | System | LAN | Internet |
| Cuba* | MS Access | 422 | 52 705 | – | – | 10 | 7 | W 2000 | X | X |
| Cyprus | Manual (AO) | 2 500 | 2 000 | 7 | 8 | 5 | 8 | W/NT/98 | X | X |
| Czech Rep. | L and S | 50 000 | 20 000 | 30 | 8 | 32 | 6 | W/NT | X | X |
| Egypt | ELLIPSE | 25 000 | 3 800 | 2 | 9 | 1 | 5 | Sun | X | X |
| El Salvador* | SQL | 5 000 | 200 | 2 | 6 | 3 | 3 | W/2000 | X | X |
| Eritrea | Local | 1 000 | 300 | 3 | – | 2 | – | W/95/98 | – | X |
| Estonia | LOIS | 1 168 | 2 260 | 20 | 27 | – | 47 | W/NT/98/2000 | X | X |
| Ethiopia | Excel | 3 000 | – | 2 | 5 | – | 2 | W/XP | – | X |
| Finland | UNIX | 100 000 | 71 000 | 30 | 16 | – | 90 | W/200/XA/NT | X | X |
| France | Auto | 150 000 | 35 000 | 95 | 110 | 10 | 40 | Oracle | X | X |
| Gabon | Pas de | Response |  |  |  |  |  |  |  |  |
| Georgia |  |  |  |  |  |  |  |  |  |  |
| Greece | SQL | > 12 500 | 10 | 12 | 6 | – | 10 | W/2000 | X | X |
| Guatemala* | Auto | 4 824 | 4 824 | 4 | – | – | 37 HP | W/98/NT/XP | X | X |
| Iran | Access | – | – | – | – | 25 | – | W/NT | X | X |
| Ireland* | Infocentre | 19 000 | 14 000 | 3 | 1 | 5 | 100 | W/XP/NT | X | X |
| Jordan* | – | – | – | – | – | – | – | – | – | – |
| Latvia | L and S | 10 500 | 12 800 | 60 | 6 | – | 40 IBM | W/2000 | X | X |
| Lebanon* | ELLIPSE | 500 | 400 | 5 | 5 | – | 10 HP | NT | X | X |
| Lesotho | Excel | 298 | 24 | 14 | 11 | – | 1 | – | – | – |
| Liechtenstein | – | – | – | 1 | 1 | – | 1 | – | – | – |
| Lithuania | Access | 57 000 | 31 000 | 25 | 12 | 100 | 100 | W/95/98 2000/XP | X | X |
| Madagascar | D Base IV | – | – | 8 | 4 | – | 1 | MS/DOS | – | – |
| Mali | Yes | 500 | 155 | 6 | – | 2 | 2 | Windows | – | X |

| COUNTRY | DMBS | No. of assignments | No. of licences | Personnel | IT |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Expert | Techn. | XS | PC | System | LAN | Internet |
| Malta | Manual | – | 15 000 | 4 | 4 | – | – | – | – | X |
| Mauritania* | TCI | 960 | 240 | 3 | 5 | – | 16 DELL | W 2000 | X | X |
| Moldava | FoxPro Access | 14 000 | 1 858 | 6 | 4 | – | 10 | W/98/NT | X | X |
| Monaco | Excel | 800 | 600 | 2 | – | – | 3 | W/NT | X | X |
| Morocco* | Spectrocan (bidding stage) | – | – | 14 | 5 | – | PC | – | – | X |
| Netherlands | Oracle | 5 200 | 10 000 | 150 | 150 | – | 300 | W | X | X |
| Nicaragua | SpectraPlus | 10 000 | – | 2 | – | 12 | – | – | X | X |
| Niger* | No | 315 | 121 | – | – | 1 | 1 | W98 | – | X |
| Norway |  |  |  |  |  |  |  |  |  |  |
| Panama* | Access | – | – | 9 | 2 | – | 10 | W/NT | X | X |
| Papua New Guinea | Oracle | 10 000 | 30 000 | 30 | 30 | 7 | 10 | Oracle | X | X |
| Peru |  |  |  |  |  |  |  |  |  |  |
| Philippines | – | 100 000 | – | 10 | 100 | – | – | – | – | – |
| Poland* | Informix | > 100 000 | > 20 000 | 130 | 70 | – | 120 | W | X | X |
| Portugal | Oracle | 15 512 | 10 524 | 39 | 41 | 1 | 121 | W/2000 | X | X |
| Qatar* | Excel | 7 000 | 2 000 | 11 | 5 | – | DELL | W/98 | X | X |
| Romania | Pas Part II |  |  |  |  |  |  |  |  |  |
| Rwanda* | No | – | – | 3 | 2 | – | – | – | – | – |
| Samoa | Freqman | 849 | 1 843 | 2 | 1 | 1 | – | W/98 | – | X |
| Senegal* | Access | 3 316 | 3 362 | 5 | 3 | – | 5 | W/XP | – | X |
| Slovenia* | Local | 1 500 | 8 | 16 | 7 | – | 50 | W/2000/98 | X | X |
| Spain | Auto | 80 000 | 40 000 | – | – | > 500 | > 500 | W/2000 | X | X |
| Sri Lanka* | Oracle | 7 500 | 1 800 | 10 | 25 | 14 | – | – | W/NT | X |

| COUNTRY | DMBS | No. of assignments | No. of licences | Personnel | IT |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Expert | Techn. | XS | PC | System | LAN | Internet |
| Suriname | Access | 250 | 400 | 1 | 3 | – | 1 | W/NT | – | X |
| Swaziland* | Excel | 1 200 | 400 | 3 | 3 | 1 | 1 DELL | W/98/ 2000 | - | X |
| Switzerland | Oracle | Milliers | Milliers | 90 | 10 | – | X | MS/DOS | X | X |
| Syria* | Auto | – | 13 000 | 15 | 30 | – | – | – | X | X |
| Tajikistan* | Manual | 12 000 | 24 000 | 5 | 17 | 1 | 4 | W/98/ 2000 | - | X |
| Tanzania* | Manual | 500 | 155 | 6 | – | 2 | 2 | W | - | X |
| Thailand | Oracle | 19 742 | 85 058 | 6 | 30 | 2 | 144 | W | X | X |
| Turkey | Oracle | 140 000 | 34 000 | 20 | 5 | – | – | Oracle | X | – |
| Uganda | Excel | 12 000 | 4 000 | 6 | 2 | 6 | – | W/NT | X | X |
| Ukraine* | Local | 100 000 | 2 800 | 300 | 150 | – | 150 | W/2000 | X | X |
| United Arab Emirates | Access | 23 000 | 15 000 | 2 | 3 | 10 | – | W/NT | X | X |
| United Kingdom | Oracle (4) | 200 000 | 212 000 | 245 | 297 | – | – | – | X | X |
| Uzbekistan* | Windows | 71 800 | 26 860 | 136 | 38 | – | 35 | W/95/98/XP | X | X |
| Venezuela | ASMS | 30 000 | 2 300 | 80 | 40 | 80 | 80 | W | X | X |
| * These countries responded for the first time in 2003, having not participated in 2001. |

ANNEX  2-H

Responses concerning responsibilities of spectrum management (Question 16 b) and c))

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Albania | Europe & CIS | DVG | The organizational structure in Albania involved in frequency management process consist on: General Directorate of Posts and Telecommunications (GDPT) is a legal, public, buxhetory person, and works for fulfilment of the objectives of policy on telecommunications. GDPT depends on the Minister of Transport and Telecommunications. GDPT coordinate work for drafting the National Frequencies Allocation Table, as well as for its harmonization with international policies for radio frequencies spectrum development; Telecommunications Regulatory Entity (TRE) is a public legal entity operating in conformity with its regulation approved by the Board of TRE and independent in making its decisions. TRE should supervise the all frequency spectrum, in order to ensure effective, interference-free use of frequencies. TRE manages radio-frequency spectrum for civil purposes and makes regulations for civil spectrum activities. Regulations and activities falling within radio communications must be in conformity with rules and standards of international organizations, conventions and treaties where Republic of Albania is a party. d) No | Organs of Radio Frequency Management: – TRE manages frequency bands designated for civil purposes and public or private use, except broadcasting bands. – National of Radio Television Council manage broadcasting bands – Ministry of Defence, Ministry of Public Order and National Information Service manage frequency bands aimed for national defence use. |  |
| Antigua and Barbuda | Americas | DVG | Telecommunications Officer, Assistant Telecommunications officer and Secretary d) No | Department responsible for all telecommunications | Single organization |
| Armenia | Europe & CIS | DVG | d) Changes are planned in this organizational structure | Ministry of transport and communications | The responsibility for spectrum management is contained within a single organization |
| Bahamas | Americas | DVG | (org.) See Org Chart attached to email d) At present evaluating bids to have section revamped. | Separate. | Single. |
| Bahrain | Arab States | DVG | d) Changes planned | It is a Ministry | A Single organization |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Bhutan | Asia & Pacific | LDC | It is done by a Department called Telecom Authority under Ministry of Communications d) None | A separate Department under the Ministry of Communications | It is totally done by one Department |
| Bosnia & Herzegovina | Europe & CIS | DVG | We have three division in CRA, and CRA is independent regulatory body: Telecom, Broadcast and Spectrum. Total staff is 80. Spectrum is 15. |  | CRA is a regulatory body and policy maker is Council of Minister of BiH. |
| Botswana | Africa | DVG | Under Botswana Telecommunications Authority organization structure spectrum management falls under the Director of Engineering Service. The Chief Engineer, Radio Services heads the sub-section responsible for spectrum planning, monitoring, radio licensing and enforcement. The organization structure can be found at the following website: “http://www.bta.org.bw” d) BTA was established in 1997. Before 1997 The PSTN operator Botswana Telecommunications Corporation was responsible for spectrum management | Spectrum management is the responsibility of the Telecommunication Authority under the Telecommunication Act, 1996. | The Telecommunication Authority, BTA, has the sole mandate of spectrum management under the Telecommunication Act, 1996. |
| Burkina Faso | Africa | LDC | (org.) See organization chart below d) The spectrum management organization was transferred from ONATEL (incumbent operator) to ARTEL (ministerial department) in 2000. | The spectrum management organization is a ministerial department. | Spectrum management is the responsibility of a single organization |
| Burundi | Africa | LDC | Executive – Head of service – Technicians d) Changes are anticipated | An agency attached to a ministry | Single organization |
| Cameroon | Africa | DVG | (org.) | Spectrum management in Cameroon is the responsibility of several organizations, for different sectors. However, they all manage frequencies under the coordination of the ministry of posts and telecommunications. As far as the telecommunications sector is concerned, ART is an administrative public establishment. | No |
| Canada | Americas | DVD | (org.) See attached chart d) No | The spectrum management organization is under a government department called Industry Canada, which reports directly to the Minister. Industry Canada is a large department which includes the Spectrum, Information Technologies & Telecommunications Sector and the Operations Sector. | The responsibility for spectrum management is contained within a single organization. |
| Central African Republic | Africa | LDC | A radiocommunication section with three employees d) The regulatory authority will soon be set up. | PTT ministry | Single organization |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Chile | Americas | DVG | (org.) Spectrum management is the reponsibility of the Subsecretariat for Telecommunications, which comes under the Ministry of Transport and Telecommunications. In accordance with the General Telecommunications Act, the Chilean Navy administers assignments to maritime (mobile and fixed) services, and the General Civil Aeronautics Directorate (DGAC), which comes under the Chilean Air Force, is responsible for administering the aeronautical services bands. d) No | See 16 a) | Ver 16 a). |
| China | Asia & Pacific | DVG | Terrestrial service division, Space service division, Supervision and inspection division, Frequency planning division. d) No, there have not. | It is part of a larger government department. | The responsibility for spectrum management is shared between separate organizations. |
| Columbia | Americas | DVG | Org: – Office for Sectoral Planning, General Services Directorate, General Technical Directorate. – The responsible body is the Ministry of Communications. d) Yes, it is intended to adopt a general telecommunications act that includes a spectrum management policy. | The responsible body is the Ministry of Communications | The responsible body is the Ministry of Communications |
| Comoros | Africa | LDC | (org.) see annexed organization chart d) It is planned to create an independent spectrum management agency. A date for the creation of the agency has not yet been proposed. | The organization responsible for spectrum management is an office of the telecommunication design and planning directorate of the national post and telecommunication company (see annexed organization chart). | Spectrum management is the sole responsibility of the national post and telecommunication company. |
| Costa Rica | Americas | DVG | – | Ministry of Government and Police | The National Radio Control Bureau is the body responsible for spectrum management at the national level. It is, however, assisted in this task by ICE in the case of spectrum that is allocated to ICE for radiocommunication purposes. |
| Côte d'Ivoire | Africa | DVG | Spectrum management is performed by the Radiocommunication directorate of ATCI, broken down into three sub-directorates (spectrum management, spectrum monitoring and licensing), seven services and a monitoring centre. | Agency, organization attached to ministry | Single organization |
| Croatia | Europe & CIS | DVG | d) Yes | Spectrum management is preformed by Administration which is separate institution reporting to Ministry. | All in one institution |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Cuba | Americas | DVG | – | – | – |
| Cyprus | Europe & CIS | DVG | (org.) Figure 1 – Organizational Chart d) Cyprus telecommunications policy is in a changing mode, from a monopoly to a full liberalized market. A new NRA was established, that is responsible for telecommunications – the radio communications are still in the powers of the Ministry. A fixed monitoring station will be established and the two administrations will hire more personnel. | It is a Directorate of Telecommunications which is part of the Ministry of Communications and Works | Single organization-The Directorate of Telecommunications |
| Czech Republic | Europe & CIS | DVG | Main activities are concentrated in the Czech Telecommunication Office (CTO). Ministry of Transport and Communications sets down general strategy of telecommunications, approves drafts of NTFA developed by the CTO. The CTO cooperates with other subjects (Council for Broadcasting and Ministry of Defence) in regulation of specific services. d) This organizational structure has been established two years ago, no significant changes are expected in the near future. | Spectrum management is part of the Czech Telecommunication Office, the independent body of the State Administration, which is responsible for regulatory matters of all telecommunications (taking into account above mentioned detailed specification of the structure). | The separate organizations share the responsibility for spectrum management for government users and broadcasters. |
| Egypt | Arab States | DVG | d) Changes are planned to take places. | It is a department of Telecommunication Regulatory authority. | Within a single organization. |
| El Salvador | Americas | DVG | SIGET d) No changes foreseen | Spectrum management comes under the heading of telecommunications management, which is the responsibility of the General Superintendency for Electricity and Telecommunications (SIGET). SIGET is directly responsible to the Government. | Single organization |
| Eritrea | Africa | LDC | Chart to be supplied by mail if necessary , because it is not practical to draw and send the chart by email attachments d) No Change planned | The last one | Within a single org. |
| Estonia | Europe & CIS | DVG | (org.) There are three departments responsible for frequency management: Technical planning department Licensing Department Supervision Department d) Since 2002 changed our structure was changed and Postal Affairs Department was created. | Estonian National Communication Board is agency under area of responsibility of Minister of Economic Affairs and Communications. | Estonian National Communication Board is a regulator of Telecommunication market (included frequency management) with following exceptions: the coordination of aeronautical frequencies is under responsibility of Estonian Air Navigation Services the use of exclusive military frequencies are under responsibility of Minister of Defence |
| Ethiopia | Africa | LDC | – | – | – |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Finland | Europe & CIS | DVD | (org.) A copy of the organization chart is enclosed at the end of this document. d) Yes | Department of an independent regulatory authority. | Single organization. |
| France | Europe & CIS | DVD | (org.) The responsibilities of the national frequency agency extend over the entire radio spectrum, both civil and military. See the organization block diagram and the organization chart of the agency. d) This system was set up on 1 January 1997. No changes are planned in the immediate future. | The national frequency agency is an administrative public establishment (a specialized administrative body) of the ministry that is responsible for telecommunication (in the current government this is the deputy minister for industry). | The entire domain of spectrum management and public and non-public spectrum utilization is handled by the national frequency agency, which establishes the national table for frequency distribution between the nine different administrations and authorities in question. This table is approved by the prime minister. Overall responsibility for telecommunication policy and regulatory matters lies with the minister responsible for telecommunications. Frequencies are distributed to network or telecommunication service licence-holders by a decision of the telecommunication regulatory authority. Allocation of frequencies for radio and television is by decision of the “conseil supérieur de l'audiovisuel”. |
| Greece | Europe & CIS | DVD | d) Existing framework since 01/01/2001. Changes are going to be made during 2003 to meet the requirements of the new EU Framework. | Spectrum management in Greece is a responsibility of the National Telecommunications and Post Commission (EETT), the National Regulatory Authority, with the exception of the military, broadcasting and aeronautical bands. EETT is also responsible for the maintenance of the National Frequency Register. Ministry of Transport and Communications is responsible for the telecommunications policy guidelines and the Frequency Allocation Table along with the Ministry of Defence. | As above |
| Guatemala | Americas | DVG | d) No | Forms part of the Ministry of Communications, Infrastructure and Housing | Single organization |
| Hungary | Europe & CIS | DVG | (org.) Organizations: – Department in Ministry of Informatics and Communications, – Department in Ministry of Defence, – Directorate in civil Communications Authority of Hungary, – Governmental Frequency Management Agency. d) Ministry of Informatics and Communications was set up in 2002. No changes are planned in the organizational structure in the near future. | The frequency management structure in Hungary has two branches and two levels (see Annex 1). The first branch is responsible for civil, non-government spectrum management. The second one is responsible for the management of frequency issues in state administrations such as police, armed forces, fire authorities. The first higher level (Ministries) is responsible for frequency management policy and legal regulations and the second lower level (Authorities) is responsible for the planning and authorization of spectrum use. | – |

| Administration | Region | Status | Q.16 a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Iran | Asia & Pacific | DVG | d) Yes, our organization have been changed recently | The spectrum management organization is part of the Ministry of PTT | The responsibility of spectrum management is single(Ministry of PTT) |
| Ireland | Europe & CIS | DVD | (org.) d) New legislation expected to be enacted shortly will create a Commission for Communications Regulation which will absorb the current Regulator. | Spectrum management is carried out by the regulator responding to policy received from government. | Responsibility for Spectrum management is carried out by a single organization, the regulator, responding to policy received from government. |
| Jordan | Arab States | DVG | To be answered by TRC | To be answered by TRC | To be answered by TRC |
| Latvia | Europe & CIS | DVG | (org.) d) the potential changes depend on changes in legislation | Latvia Telecommunication State Inspection (LTSI) operates under the supervision of Ministry of Transport. | The responsibility for spectrum management is shared between Ministry of Transport (regulatory and policy matters), Public Utilities Commission (regulatory matters), National Broadcasting Council of Latvia (regulatory matters), LTSI (technical matters) |
| Lebanon | Arab States | DVG | (org.) d) Yes, especially after issuing a new telecom law | According to the new law, the spectrum management organization must be separate ministry organization | One organization (the spectrum management organization) |
| Lesotho | Africa | LDC | The structure of Telecommunications Regulatory Authority as a whole gives a good picture. According to the structure, spectrum management and monitoring falls under the technical division; the licensing and enforcement; licensing and enforcement under telecommunications services; pricing is in the strategic planning division. d) LTA was established in 2000. Before 2000, a parastatal telecommunications network operator performed spectrum management function. | It is part of telecommunications authority reporting to parliament through Communications ministry. | It is contained within the Lesotho Telecommunications Authority (LTA) alone. |
| Liechtenstein | Europe & CIS | DVD | The Liechtenstein regulatory body, the Office for Communications (OfC) consists of the Director, a Vice-Director who is a technical expert, a Frequency Manager a part-time employee for technical administration and a Secretary. Strategic spectrum management matters are dealt with within the OfC while most operational matters are out-sourced. d) No | The spectrum management function is integrated in the OfC which is a autonomous organization reporting to the government, the ministry for traffic and communications. | The OfC has got all spectrum management responsibilities. |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Lithuania | Europe & CIS | DVG | (org.) The organization chart of the Communications Regulatory Authority is given above c). d) The CRA was officially registered on 1 May 2001. The Council of the CRA comprised of 5 members was appointed by a presidential decree on 30 May 2001. According to the Law on Amending of the Low of the Republic of Lithuania on Telecommunications that is in effect from 01.01.2003 the State organizational structure in respect to matters of spectrum management will remain as above mentioned. | In accordance with Law on Telecommunications there are two prescribed Regulatory Bodies of Telecommunications Activities in Republic of Lithuania: the Government or an authority Designated by It. The first of its functions is to develop and implement state policy in the telecommunications sector; the Communications Regulatory Authority (CRA) which shall be an independent institution of the Government regulating communications activities and implementing provisions of in point 1 mentioned Law, acting in accordance with that Law, other laws of the Republic of Lithuania, and its own regulations. It has prescribed appropriate tasks, functions and rights | (note: see Q.16B) |
| Madagascar | Africa | LDC | (org.) see annex 1 | A single organization | – |
| Mali | Africa | LDC | Set up members of the telecoms regulatory committee d) Setting up in progress | A separate organization attached to the government | Single organization |
| Malta | Europe & CIS | DVG | (org.) Following Independence in 1964, the organization responsible for spectrum management and monitoring has been the Wireless Telegraphy Department (WTD). Until 1999 the Director of the WTD reported to the Office of the Prime Minister, but following a Ministerial re-organization, the Department is now responsible, through the Director, to the Permanent Secretary of the Ministry for Transport and Communications. The WTD consists of some 58 staff, including 4 student apprentices, of whom approximately 28% are engineers/technicians, with the remainder being general clerical staff. d) No | The Frequency Management Section falls within the WTD, which forms part of the Ministry for Transport and Communications. | In Malta, the Ministry for Transport and Communications sets the policy. The regulator of all radiocommunication matters, including frequency management and monitoring, is the Wireless Telegraphy Department. |
| Mauritania | Africa | LDC | – | Spectrum management and monitoring is the responsibility of the regulatory body ARE, which reports directly to the prime minister and has the necessary independence to meet its regulatory objectives. | ARE only |
| Mauritius | Africa | DVG | Information and Communications Authority is responsible for spectrum management d) yes | It is a parastatal body responsible for regulating the telecommunications sector. | Single organization |
| Mexico | Americas | DVG | (org.) Organizational diagram attached d) Yes, changes are foreseen | The Directorate-General for Spectrum Planning and Management comes under the Federal Telecommunications Commission, which is the regulatory body responsible to the Ministry of Communications and Transport. | The Federal Telecommunications Commission is responsible for spectrum management, and the Ministry of Telecommunication Policy |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Moldova | Europe & CIS | DVG | (org.) d) No | The Ministry of Transport & Communications is responsible for policy matters. Agency for Regulations in Communications is responsible for regulatory matters in the non-governmental (civil) sector. The radiofrequency management organization in the civil sector is the State Communication Inspection reporting directly to the Ministry of Transport & Communications | The government users are separate from non-government users |
| Monaco | Europe & CIS | DVD | Three workers in the “Direction du Contrôle des Concessions et des Télécommunications” d) No | The “Direction du Contrôle des Concessions et des Télécommunications” is part of the “Département Ministériel des Travaux Publics et Affaires Sociales” | Spectrum management is conducted by a single organization. |
| Morocco | Arab States | DVG | (org.) The organization chart for the directorate charged with spectrum management at the ANRT is attached to the questionnaire. It should be noted that the interconnection division and the terminal equipment certification service, although listed in that organization chart, do not have any spectrum management responsibilities. | It is an independent telecommunication regulatory authority set up in connection with the office of the prime minister. | – |
| Netherlands | Europe & CIS | DVD | see website: http://www.agentschaptelecom.nl/pdf/jaarverslag_eng/rijksdienst_eng.pdf d) Not really, only that the Directorate General of Telecommunications and Postal Services and the RA Netherlands have moved to the Ministry of Economic Affairs. | See Q.4 of part III of the questionnaire and the end of this part II. Organization of spectrum management – Answers to questions 16 a, b, c, and d. The Directorate General for Telecommunication and Postal services (DGTP) and the Radiocommunications Agency are responsible for the national frequency management. Policy issues are the competence of DGTP; product development, putting into effect of decisions, advising on policy issues, inspections and monitoring and of course licensing are the competences of the Radiocommunications Agency Netherlands. Both organizations are within the Ministry of Economic Affairs. DGTP and the Radiocommunications Agency have been moved from the Ministry of Transport to the Ministry of Economic Affairs (22 July 2002). The main reason for this movement is to integrate and strengthen the national ICT policy. | See Q.4 of part III of the questionnaire and the end of this part II. RA Netherlands operates within the policy framework of the Directorate-General for Telecommunications and Post (DGTP). The Directorate General for Telecommunications and Post (DGTP) formulates the government policy in the field of telecommunications (and postal services). RA Netherlands implements that part of the policy which is related to the structuring of the radio spectrum. The distinction between policy and its implementation will lead to productive efficiency: a more effective, flexible and efficient operational performance of the RA Netherlands. |
| Nicaragua | Americas | DVG | d) No | Yes | No |
| Niger | Africa | LDC | Currently attached to the PTT regulatory directorate (“Direction de la Réglementation des postes et Télécommunications”). A radiocommunication department is responsible for spectrum management. | Yes, the directorate responsible for spectrum management is currently attached to the minister responsible for telecommunication. | Single organization |
| Panama | Americas | DVG | – | – | – |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Papua New Guinea | Asia & Pacific | DVG | Spectrum and Broadcasting Planning Department produces frequency plans and assigns frequencies, proposes spectrum usage and pricing policies. The Enforcement Department performs licensing, inspections and monitoring and type approvals. d) Changes are being planned to accommodate in governments policy. | The Spectrum and Broadcasting Planning Department is part of Papua New Guinea Technical Telecommunication Authority and currently it is the only national statutory organization established by the government to regulate radiocommunication policies etc for both private, business and government radio spectrum users in the country. | There is no other organization responsible for spectrum matters. |
| Peru | Americas | DVG | d) There have recently been changes in the organizational structure of the Ministry, as communicated to ITU in letter (M) No. 319-2002-MTC/03 of 27 December 2002 | Forms part of the Ministry of Transport and Communications | Responsibility for spectrum management lies with the Ministry of Transport and Communications |
| Philippines | Asia & Pacific | DVG | org ? d) There might be some changes due to developments brought about by ICT. | The National Telecommunications Commission is an attached Agency to the Dept. of Transportation and Communications | It is contained within a single organization |
| Poland | Europe & CIS | DVG | The URTiP (Office of Telecommunications and Post Regulation) is responsible for the planning and authorization of use over the whole of the civil spectrum with the exception of formal assignments analogue broadcast frequencies. It cooperates on a day-to-day basis with staff from the Ministry of Defence regarding military bands but has no detailed plans of usage within these bands. The URTiP has the status of a statutory body, responsible to the Council of Ministers. The URTiP consists of some 600 staff. Of these 600 staff, some 88 are employed on frequency management at headquarters in Warsaw, with approximately 5 to 8 engineers, in each of the 16 branches. The URTiP has responsibility for the following functions – issuing licences and frequency permits covering the provision of telecommunications services and the use of radio equipment management and monitoring of the frequency spectrum including: Public mobile services, Private mobile services, Aeronautical and marine services, Amateur Radio, Low power devices, Broadcasting services (cooperation with National Broadcasting Council) Public fixed services, Private fixed services, Public satellite services, Private satellite services; Certification of equipment (e.g. terminal equipment); Ensuring compliance with universal service obligations; Management of emergency and disaster recovery plans; Approving wholesale and, in conjunction with the Anti-Monopoly Office, retail tariffs for telecommunications; | Authority reporting directly to the government. | Responsibility for spectrum management is shared between separate organizations. |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Resolving disputes (e.g. inter-connection disputes); Management and assignment of numbers within the nation numbering plan; Fining operations for non-compliance with the law; d) Yes, there have been some changes. |  |  |
| Portugal | Europe & CIS | DVG | (org.) See Appendix 5. d) No | The spectrum management organization is part of “ICP-ANACOM – the Portuguese telecommunications Regulatory Authority. According to point c), n° 1, of article 6° of ICP-ANACOM's Statute, approved by Decree-Law nr. 309/2001, of December the 7th, one of ICP-ANACOM's attributions consists of ensuring the management of radio spectrum namely involving its planning, granting of spectrum resources and its supervision as well as ensuring the coordination between civil, military and semi-military communications. ICP-ANACOM is a public legal entity that has administrative and financial autonomy as well as own patrimony performing its role under the tutelage of Ministry of Economy. ICP-ANACOM is autonomous in its decision making, and needs no “ex ante” or “ex post” approval by the Government.” | The ICP-ANACOM is responsible for the overall management of the spectrum; concerning aeronautical and maritime services there is a coordination procedure with the aeronautical authority and the maritime authority, respectively; there are also some bands whose management is delegated in the military authority. |
| Qatar | Arab States | DVG | (org.) Enclosed d) No | It is a division of Qatar telecom (QSC), empowered by law as sole authority for telecommunication development and providing telecommunication service in the state of Qatar. | Single organization |
| Rwanda | Africa | LDC | d) No change | Ministry (regulatory authority) | Single |
| Samoa | Asia & Pacific | LDC | d) No | No | No |
| Senegal | Africa | DVG | d) Yes | Agency subject to the Presidency | Single organization |
| Slovenia | Europe & CIS | DVG | (org.) Att.3 d) No | Agency reporting directly to the government | Single organization |
| Spain | Europe & CIS | DVD | – | – | – |
| Sri Lanka | Asia & Pacific | DVG | (org.) See Annexure I – A & B d) Yes | A part of a larger government organization | Within a single organization |
| Suriname | Americas | DVG | Is a division of the legal Department of Telecommunicatiebedrijf Suriname (Telesur), a state-owned telecommunication Company, with one (1) Head and 3 other personnel d) Yes, spectrum management will be transferred to a regulatory authority. | Is part of a state-owned telecommunication Company, Telesur. | Single organization |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Swaziland | Africa | DVG | The structure is as follows:- Managing Director(SPTC); General Manager, Telecomms; Senior Manager, Regulatory, Policy and International Affairs; Manager, Frequency Management; Technician, Frequency Management and Monitoring. d) There has been recent changes and more changes are still expected to be made in preparation for the formation of a complete Regulatory unit. The office of Regulatory, Policy and International Affairs has been formed to that effect | The spectrum management organization is part of a larger government department, the Swaziland Posts and Telecomms Corporation. | The responsibility for the spectrum management is contained within a single organization, the Swaziland Posts and Telecomms Corporation with the Regulatory matters and Policy matters shared with the Ministry of Tourism, Environment and Communication while still working towards the formation of an independent Regulatory Authority. |
| Switzerland | Europe & CIS | DVD | (org.) The order in the Frequency Management Division (FM) does not reflect any order of importance. d) No | The Frequency Management Division (FM) is part of the Federal Office for Communications (OFCOM). OFCOM in turn is subordinated to a Ministry the Swiss Federal Department for the Environment, Transport, Energy and Communication (DETEC). The Office prepares the decisions of the Swiss government (the Federal Council) and the Swiss Federal Communications Commission (ComCom). FM is the skills center for regulatory tasks of national authority in the fields of radiocommunications, electromagnetic compatibility (EMC) and environmental electromagnetic compatibility (EECM). The division is subdivided in 4 sections: (1°) Radio Technology (GF), (2°) Frequency Planning (FP), (3°) Frequency Assignment (FZ), and (4°) Radiomonitoring (RM) | In Switzerland, in the civil bands frequency allocation and assignment tasks are shared by two organizations: the Federal Communications Commission (ComCom) and the Federal Office for Communications (OFCOM) - with the exception of assignments in the Aeronautical Service. OFCOM prepares the commercial transactions of the Federal ComCom, makes the necessary applications and implements its decisions. In the radiocommunications sector where ComCom delegated its competencies to OFCOM, the latter grants inter alia those radio licences which do not involve any telecommunications services, e.g. company radio and amateur radio licences. In addition, OFCOM licences all providers of fixed network services (without a tender procedure). ComCom, for its part, awards the basic provision licence and licences for the provision of mobile telephone and other radio services where the licence is awarded on the basis of an invitation to tender. It also approves frequency plans. |
| Syria | Arab States | DVG | d) No | It is part of a larger government department (Syrian Telecommunication Establishment) | It is shared between separate organizations |
| Tajikistan | Europe & CIS | DVG | d) According to the new accepted law “On Telecommunications” dated 22 May 2002, our organization on spectrum management are planed to be agency at the government of the Republic of Tajikistan by December 2003. | Our spectrum management organization is a State Inspectorate of Communication at the Ministry of Communications of the Republic of Tajikistan. | The responsibility for spectrum management is contained within a single organization |
| Thailand | Asia & Pacific | DVG | (org.) see in Attachment d) Thailand has the plan to establish the independent organization (NTC.) | PTD is the part of a larger government department. | Single Organization |

| Administration | Region | Status | Q.16a) Spectrum management organizational structure Q.16d) Have there been recent changes or are changes planned? | Q.6b) Which organization is responsible for spectrum management? | Q.6c) Is the responsibility for spectrum management contained in a single organization or shared between separate organizations? |
| --- | --- | --- | --- | --- | --- |
| Turkey | Europe & CIS | DVG | (org.) d) The organizational structure had been changed in 2001. Before 2001 there wasn't Telecommunication Regulation Authority. | Spectrum Management department is responsible department of Telecommunications Regulatory Authority which is independent authority. Telecommunication Authority was founded as a public judicial entity with a private budget having administrative and financial autonomy on January 27, 2000 in accordance with Article 5 of Law No. 4502 amended by Wireless Law No. 2813 in order to execute the actions envisaged in Wireless Law No. 2813, Law No. 406 on Telegraph and Telephone and other laws, and became effective as from August 15, 2000. The Authority works under the auspices of Ministry of Transportation. | The responsibility for spectrum management contained within only our authority. |
| Uganda | Africa | LDC | a) Refer to 16(c) d) None | It is part of the Uganda Communications Commission Structure. Uganda Communication is a regulatory agency in Uganda. Spectrum Management is part of the technical department of UCC. The section dealing with spectrum Management is six professional technical persons. | The responsibility for spectrum management is contained within UCC, which deals with regulatory, and policy matters on communications in the country. |
| Ukraine | Europe & CIS | DVD | – | – | – |
| United Arab Emirates | Arab States | DVG | – | – | – |
| United Kingdom | Europe & CIS | DVD | (org.) Organization Chart d) Next year the Agency will become part of a new national telecommunications regulator that amalgamates five existing telecommunication organizations | Currently an agency within a government department | Single |
| Uzbekistan | Europe & CIS | DVG | d) Organizational structure of State Committee for Radiofrequencies has been changed: Working group of SCRF has been renamed to Direction, staff has been increased and departments created. |  | Spectrum management organization in our country is a separate organization, named State Committee for Radiofrequencies of the Republic of Uzbekistan (SCRF RU), which complied Communications and Information Agency of Uzbekistan. |
| Venezuela | Americas | DVG | – | An autonomous entity attached to a Ministry | Single organization (CONATEL) |
| Viet Nam | Asia & Pacific | DVG | – | – | Single organization |

ANNEX  2-I

Responses concerning human resources (Question 16 e) and f))

| Administration | Region | Status | Q.16e) Number of specialist staff | Q.16f) Number of support staff |
| --- | --- | --- | --- | --- |
| Albania | Europe & CIS | DVG | app. 14 spec. | app. 8 spec. |
| Antigua and Barbuda | Americas | DVG | none | none |
| Armenia | Europe & CIS | DVG | 54 | 50 |
| Bahamas | Americas | DVG | 3 | 1 |
| Bahrain | Arab States | DVG | 8 | 16 |
| Bhutan | Asia & Pacific | LDC | None | 2 |
| Bosnia & Herzegovina | Europe & CIS | DVG | Experts: 8 planning 4 monitoring | 2 |
| Botswana | Africa | DVG | 8 | 4 |
| Burkina Faso | Africa | LDC | 2 | 3 |
| Burundi | Africa | LDC | 2 | 2 |
| Cameroon | Africa | DVG | – | – |
| Canada | Americas | DVD | 300 (approx) | 50 (approx) |
| Central African Republic | Africa | LDC | 1 | 3 |
| Chile | Americas | DVG | 3 | 6 |
| China | Asia & Pacific | DVG | 25 | about 100 |
| Columbia | Americas | DVG | 25 | 10 |
| Comoros | Africa | LDC | 1 | None |
| Costa Rica | Americas | DVG | 8 CNR, ICE 3 | 2 CNR |
| Côte d'Ivoire | Africa | DVG | – | – |
| Croatia | Europe & CIS | DVG | 20 | 30 |
| Cuba | Americas | DVG | – | – |
| Cyprus | Europe & CIS | DVG | 7 | 8 |
| Czech Republic | Europe & CIS | DVG | 30 | 8 |
| Egypt | Arab States | DVG | 2 | 9 |
| El Salvador | Americas | DVG | 2 | 6 |
| Eritrea | Africa | LDC | 3 | none |
| Estonia | Europe & CIS | DVG | 20 | 27 |
| Ethiopia | Africa | LDC | 2 | 5 |
| Finland | Europe & CIS | DVD | 30 | 16 |

| Administration | Region | Status | Q.16e) Number of specialist staff | Q.16f) Number of support staff |
| --- | --- | --- | --- | --- |
| France | Europe & CIS | DVD | 95 | 110 |
| Greece | Europe & CIS | DVD | 9 EETT 3 Ministry | 6 |
| Guatemala | Americas | DVG | 4 | – |
| Hungary | Europe & CIS | DVG | 135 | 64 |
| Iran | Asia & Pacific | DVG | – | – |
| Ireland | Europe & CIS | DVD | 3 | 1 |
| Jordan | Arab States | DVG | To be answered by TRC | To be answered by TRC |
| Latvia | Europe & CIS | DVG | about 60 specialists | about 6 specialists |
| Lebanon | Arab States | DVG | 5 | 5 |
| Lesotho | Africa | LDC | 14 | 11 |
| Liechtenstein | Europe & CIS | DVD | 1+ outsourcing partner | 1+ outsourcing partner |
| Lithuania | Europe & CIS | DVG | 25 | 12 |
| Madagascar | Africa | LDC | 8 | 4 |
| Mali | Africa | LDC | 6 | – |
| Malta | Europe & CIS | DVG | 4 (part-time) | 4 (part-time) |
| Mauritania | Africa | LDC | 3 | 5 |
| Mauritius | Africa | DVG | – | – |
| Mexico | Americas | DVG | 7 | – |
| Moldova | Europe & CIS | DVG | 6 (only at the State Communication Inspection) | 4 (only at the State Communication Inspection) |
| Monaco | Europe & CIS | DVD | 2 | 0 |
| Morocco | Arab States | DVG | 14 | 5 |
| Netherlands | Europe & CIS | DVD | 150 | 150 |
| Nicaragua | Americas | DVG | 15 | – |
| Niger | Africa | LDC | 2 | – |
| Panama | Americas | DVG | 9 | 2 |
| Papua New Guinea | Asia & Pacific | DVG | About 30 | About 30 |
| Peru | Americas | DVG | 12 | 12 |
| Philippines | Asia & Pacific | DVG | About 10 | About 100 or more |
| Poland | Europe & CIS | DVG | 130 | 70 |
| Portugal | Europe & CIS | DVG | 39 | 41 |
| Qatar | Arab States | DVG | 11 | 5 |
| Rwanda | Africa | LDC | 3 | 2 |
| Samoa | Asia & Pacific | LDC | 2 | 1 |
| Senegal | Africa | DVG | 5 | 3 |
| Slovenia | Europe & CIS | DVG | 16 | 7 |

| Administration | Region | Status | Q.16e) Number of specialist staff | Q.16f) Number of support staff |
| --- | --- | --- | --- | --- |
| Spain | Europe & CIS | DVD | – | – |
| Sri Lanka | Asia & Pacific | DVG | 10 | 25 |
| Suriname | Americas | DVG | 1 | 3 |
| Swaziland | Africa | DVG | 3 | 3 |
| Switzerland | Europe & CIS | DVD | 90 | 10 |
| Syria | Arab States | DVG | 15 | 30 |
| Tajikistan | Europe & CIS | DVG | 5 | 17 |
| Thailand | Asia & Pacific | DVG | 6 | 20 |
| Turkey | Europe & CIS | DVG | 20 | 5 |
| Uganda | Africa | LDC | 6 | 2 |
| Ukraine | Europe & CIS | DVD | About 300 | about 150 |
| United Arab Emirates | Arab States | DVG | 2 | 3 |
| United Kingdom | Europe & CIS | DVD | 245 | 297 |
| Uzbekistan | Europe & CIS | DVG | 136 | 38 |
| Venezuela | Americas | DVG | 80 | 40 |
| Viet Nam | Asia & Pacific | DVG | – | – |

ANNEX  2-J

List of fixed, mobile and transportable radio monitoring stations
by Member State

Legend

| RX | Receiver | TX | Transmitter |
| --- | --- | --- | --- |
| SpA | Spectrum Analyser | Meas | Measuring |
| DF | Direction Finder | R&S | Rohde & Schwarz |
| Ant | Antenna | HP | Hewlett Packard |
| DB | Data Base | Mon | Monitor |
| SW | Software | BC | Broadcast |
| NA | Not Applicable | NR | No Reply |
| – | No Answer to Question |  |  |

| Monitoring Stations |
| --- |
| Country | Fixed | Mobile | Transportable |
|  | Number of stations | Facilities | Mon Fmax MHz | DF Fmax MHz | Number of stations | Facilities | Mon Fmin MHz | DF Fmax MHz | Number of stations | Facilities | Mon Fmin MHz | DF Fmax MHz |
| ALBANIA | 1 | Broadcast only | 3000 | 30 | 1 | RX5,SpA,DF BC only | – | – | 1 | RX,SpA,DF BC only | – | – |
| BAHAMAS | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| ANTIGUA AND BARBUDA | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| BAHRAIN | 4 | RX,SpA,DF | 1000 | 1000 | 1 | RX,DF | 18000 | 1300 | 3 | RX,DF | 1000 | 1000 |
| BHUTAN | 1 | An Argus System, three fixed antenna, Spectrum analyser | 3000 | 3000 | 1 | One miniport spectrum analyser with rotor antenna set | 3000 | 3000 | 1 | Miniport receiver; one ESVN 20 | 3000 | 3000 |
| BOSNIA AND HERZEGOVINA | 0 |  |  |  | 1 | RX,SpA,DF R&S Argus software | 2750 | 2750 | 0 |  |  |  |
| BOTSWANA | 0 | In acquisition |  |  | 0 |  |  |  | 1 | RX, DF | 3000 | 3000 |
| BURKINA FASO | 1 | RX (V/UHF) | 1000 | – | 0 |  |  |  | 1 | RX (V/UHF) | 1000 | – |
| BURUNDI | 0 |  |  |  | 0 |  |  |  | 3 | RX,Watt-Mtr SpA (future) | – | – |
| CAMEROON | 2 | RX 3-30 RX136-470 | 470 | – | 0 | In course of acquisition |  |  | 0 |  |  |  |
| CANADA2 | 2 Centers + 85 Remote | RXs, SPAs, Mod Analyz, Tone Dec., DF, rf switch, Audio matrix | 3000 | 1300 | 7 | RXs, SPAs, modulation analysers, tone decoder, direction finder | 3000 | 1300 | Variable | RXs, SPAs, modulation analysers, tone decoder, direction finder | 3000 | 1300 |

| CHINA | 2006 | HF: RX R/S-ESMB SPA Agilent-8563 DF R/S-DDF01M Ant R/S-ADD011 VHF/UHF: RX R/S-ESMB SpA Agilent-8563 DF R/S-DDF05M Ant R/S-ADD051 | 1000 | 12750 | 56 | RX: R/S-ESVN40 ICOM 8500 DF | 1 | 30 | > 300 | RX R/S-EB200 SpA Agilent-8563E | 30 | 3000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| COLOMBIA | 6 | RX,DF, Vector Signal An, Universal Telegraph Decoder | 3000 | 2700 | 7 | RX,DF,SpA, Vector Signal An, Universal Telegraph Decoder | 4000 | 2700 | 0 |  |  |  |
| COMORES | 1 | RX AR-3000A | 2000 | – | 1 | RX AR-3000A | 2000 | – | 1 | RX AR-3000A | 2000 | – |
| COSTA RICA | 1 | Appropriate | 3000 | 0.009 | 1 | Appropriate | 3000 | 9 | 0 |  |  |  |
| COTE D'IVOIRE | 1 | RX,SpA,DF | 1000 | 0.001 | 2 | RX,SpA,DF | 1000 | 0.001 | 2 | RX,SpA,DF | 1000 | 30 |
| CROATIA | 9 | RX,SpA,DF | 20000 | 20000 | 7 | RX,SpA,DF | 20000 | 20000 | 4 | RX,SpA,DF | 1000 | 1000 |
| CUBA | 4 | RX, SpA, Frq Synth, Automatic monitor System | 2000 | – | 0 |  |  |  | 0 |  |  |  |
| CYPRUS | 0 |  |  |  | 1 | RX,SpA,DF, SW & DB,PC GPS | 3000 | 1000 | 0 |  |  |  |
| CZECH REPUBLIC | 2 | RX: ESVN40, R3261C, SPA: Advantest U3641, Argus IT | 2050 | – | 5 | ESVN40, ESMB, FSEB 30, R3261A, R3371A, Argus IT | 2700 | 2x 1000 1x 1300 | 1 | ICOM 8500, VisualRadio | 2000 | – |
| EGYPT | 4 | RX, SpA, DF | 3000 | 3000 | 2 | RX, SpA, DF | 3000 | 3000 | 2 | RX, SpA | 3000 | – |
| EL SALVADOR | 3 | RX,SpA,DF, automatic monitor of radio parameters, Ant distribut. | 1000 | 1000 | 0 |  |  |  | 2 | RX,SpA,DF, Antenna distribution system | 26500 | 1000 |
| ERITREA | 1 | RX,SpA,DF | 2700 | 2700 | 1 | RX,SpA,DF | 2700 | 2700 | 0 |  |  |  |
| ESTONIA | 5 | RX R&S ESVN20 9kHz – 275 MHz ESVN40 10MHz – 1000MHz SpA R&S FSP 9kHZ – 30GHz HP 9kHz – 23GHz Advatest 9kHz – 26,5GHz) Mong RX R&S EB200 10kHz – 3GHz ESMB 20MHz – 3GHz) DF R&S DDF190 HF,U/VHF | 20000 | 20000 | 8 | RX R&S ESVN20 9kHz – 2750MHz ESVN40 10MHz – 1000MHz SpA R&S FSP 9kHZ – 30GHz HP 9kHz – 23GHz Advatest 9kHz – 26,5GHz), Mon RX R&S EB200 10kHz – 3GHz ESMB 20MHz – 3GHz) DF R&S DDF190 | 20000 | 1000 | 1 | RX R&S ESVN20 9kHz – 2750MHz ESVN40 10MHz – 1000MHz (AM, FM, SSB) SpA (R&S FSP 9kHZ – 30GHz HP 9kHz – 23GHz Advatest 9kHz 26,5GHz) | 1000 | – |

|  |  | Telegon 20MHz – GHz), GSM coverage measurement equipment, GSM interference analyzers system, DAB analyzing system. |  |  |  | HF,U/VHF Telegon 20MHz – 2GHz) |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ETHIOPIA | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| FINLAND | 4 | RX: H/V/UHF DF: HF/VHF | 50000 | 3000 | 3 | RX V/UHF DF VHF | 1300 | 1300 | 3 | RX V/UHF (Hand held Directional Antennas) | 3000 | 3000 |
| FRANCE | 2 16 37 | 6 centers, 52 remote, 7 control | 20-1350 20-3000 9KHz | 20-1350 20-3000 | 27 | Note (1) | 20-1000 30-40000 | 20-1000 | 1 | Note (1) | 3000 | 3000 |
| GABON |  | NR |  |  |  | NR |  |  |  | NR |  |  |
| GREECE | 2 | RX,SpA,DF, Spectrum Monitoring Software | 3000 | 3000 | 1 | RX,SpA,DF | 3000 | 3000 | 1 | 2 SpA | 40000 | – |
| GUATEMALA |  | Uses the transportable |  |  |  | Uses the transportable |  |  | 3 | Directional antennas used both in spectrum analysers and in electric field strength receivers. Also used are global positioning systems and amplifying “pistol” antennas for determining the precise direction and azimuth of the signal detected. | 26500 | 3000 |
| IRAN | 7 | RX,SpA,DF, full range TX6 | 300 | 1000 | 7 | RX,SpA,DF | 1000 | 1000 | 2 | RX,SpA,DF | 1000 | 1000 |

| IRELAND | 1 | Antennas covering from 30 kHz to 1.3 GHz both omni directional and directional. Receivers covering 30 kHz to 3 GHz. Spectrum analysers covering 0 Hz to 40 GHz. | 40000 | 1300 | 1 | Antennas covering from 68 MHz to 1.0 GHz omni directional. Receivers covering 30 kHz to 3 GHz. Spectrum analyzers covering 0 Hz to 40 GHz. | 3000 | 3000 | 2 | Antennas covering from 20 kHz to 3.0 GHz directional. Receivers covering 30 kHz to 3 GHz. | 3000 | 3000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| JORDAN | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| LATVIA | 1 4 | One central station: RX MINILOCK 6910 (Schlumberger), ESVN40 DF ESMC (R&S DDF190 SpA R& S FSP Antenna set R& S AU900A4 Software R&S ARGUS software Four regional stations: RX R&S ESMB ICOM, AoR DF R&S DDF190 Antenna set AU900A5 Software ARGUS software (under implement.) | 3000 | 1300, 3000 | 1 1 1 | Mobile monitoring station with direction finding facility: RX R&S ESVN40 Miniport Receiver EB200 DF R&S DDF190 SpA R&S HP8563E up to 26.5 GHz with set of horn antennas; Antenna pneumatic mast and set of antennas Software ARGUS, Mobile station for GSM measr. and field strength measr. in digital broadcast. RX R&S ESVB, mast and set of antennas coverage measurement system R&S TS9955 Software ARGUS Mobile station adapted for KTV measurement SpA TEKTRONIX 2715, RX R&S ESMB, mast, anten. | 3000 26500 2600 1000 | 2700 | 0 |  |  |  |
| LEBANON | 1 2 | RX, SpA, radio-finder radio-finder | 2700 | 20 | 1 2 | SPA, radio-finder Same but planned | 2700 | 20 | 0 |  |  |  |
| LESOTHO | 1 | RX | 1000 |  | 0 |  |  |  | 1 | RX Portable |  |  |

| LITHUANIA | 5 | RX: EB200, ESVN40, ESMB; SpA: HP8591EM, HE4407B; DF: DDF190 | 1300 | 1300 | 1 | RX: ESMB SpA: HP 8591EM, HP E4407B | 3000 | – | 1 | RX: EB200, ESMB; SpA: HP 8591EM, HP E4407B | 18000 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MADAGASCAR | 1 | RX, SpA | 3000 | – | 0 |  |  |  | 1 | RX, SpA | 3000 | – |
| MALTA | 1 | Radio-monitoring RX Radio-monitoring Software | 3000 | 1000 | 1 1 1 | DF________ Radio-monitoring RX SpA_______ Radio-monitoring RX Radio-monitoring Software | 3000 | 1000 | 0 |  |  |  |
| MAURITANIA | 2 | RX: HF, V/UHF SpA: 9K-26GHz RFI Transceiver equipment Oscilloscope DF: 8067 TCI spectrum analyzer with three DELL workstations | 3000 | 3000 | 2 | RX: R&S ESMB EB200 DF: DF4400 SpA: E4407B 9K-26.5 GHz Antennes: HF,V/UHF, GSM | 26000 | 1300 | 1 | RX: 10K-3GHz SpA: 9K-3GHz | 3000 |  |
| MOLDOVA |  | NR |  |  |  | NR |  |  |  | NR |  |  |
| MONACO | 1 | RX | 2000 |  |  |  |  |  | 1 | RX, SpA, DF | 2000 | – |
| MOROCCO | 1 | RX (measuring), SpA, DF, Antenna System | 1000 | 1000 | 2 | RX (measuring), SpA, DF, Antenna System, Portable RX, GPS Other equipm for spectrum control are in course of acquisition | 1000 | 1000 | 0 |  |  |  |
| NIGER | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| PANAMA | 6 | – | 4000 | 1350 | 1 | – | 4000 | 1300 | – | – | 4000 | 1350 |
| PERU |  | No response |  |  |  |  |  |  |  |  |  |  |
| POLAND | 18 | RX(mon measure), SpA, DF, ANT(meas), PC | 3000 | 1300 | 36 | RX(mon measure), SpA, DF, Ant(meas), PC | 26000 | 1300 |  | Delicated According to task | 26000 | – |
| PORTUGAL | 114 | Manned Remote unmanned RX(com, meas) SpA DF | 2750 | 2750 | 24 | DF Mobile Monitoring units | 50000 | 1000 | 0 |  |  |  |

|  |  | Antenna systems, Decoders, audio Recorders, TV receiver, FM/RDS analyser, modulation analyser. |  |  |  | RX(meas) SpA DF Antenna, Power metr, Counter, TV receiver, RadioCom Monitor. |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| QATAR | 1 | AFMS Project under Implement. RX, SpA, DF EMI/EMC RX | 3000 | 3000 | 2 | AFMS Project under Implement. RX, SpA, DF EMI/EMC RX | 3000 | 3000 | 0 |  |  |  |
| ROUMANIA |  | NR |  |  |  | NR |  |  |  | NR |  |  |
| RWANDA | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| SAMOA | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| SENEGAL | 1 | RX, SpA, DF | 1750 | 1750 | 2 | SpA, DF | 1750 | 1750 | 0 |  |  |  |
| SLOVANIA | 1 | RX, SpA | 2G75 26000 | – |  | RX, SpA, DF (analog/dig). | 3000 | 3000 | 0 |  |  |  |
| SPAIN | 55 | 102 RX 1 SpA 1 DF | 40000 | 3000 | 25 | 1 RX 1 SpA 1 DF | 26000 | 3000 | 45 | RX, SpA | 26000 | 3000 |
| SRI LANKA | 9 | RX, SpA, DF Mon & DF SW. | 3000 | 3000 | 7 | RX, SpA, DF Mon & DF SW. GPS Rec. | 3000 | 3000 | 0 |  |  |  |
| SURINAME | 1 | RX, SpA | 500 | – | 0 |  |  |  | 0 |  |  |  |
| SWAZILAND | 0 |  |  |  | 1 | RX, SpA, DF Sound Recorder |  |  | 0 |  |  |  |
| SWITZERLAND | 55 | – | 26500 | 1300 | – | – | 26500 | 1300 | – | – | 26500 | 1300 |
| SYRIA | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| TAJIKISTAN | 1 | RX AR-5000, AR-3000, STV-402, STV-302-1. SpA SDU-5000 | 2600 | 2600 | 0 |  |  |  | 0 |  |  |  |
| TANZANIA | 0 |  |  |  | 0 |  |  |  | 0 |  |  |  |
| THAILAND | 14 | RX, SpA, DF | 1800 | 1000 | 15 | RX, SpA, DF | 1800 | 1000 | 6 | RX, SpA, DF | 26500 | 1000 |
| TURKEY | 17 8 | Current Under Implement RX, SpA, DF Ant (omni, Log) | 2500 | 2500 | 17 12 | Current Under Implement RX, DF Ant (omni, Log) | 2500 | 2500 | 13 8 | Current Under Implement RX, SpA, DF Ant (omni, Log) | 2500 | 2500 |
| UGANDA | 0 |  |  |  | 1 | Planned AUG 2003 Spectrum Management System | 3000 | 3000 | 1 | FM_RX, SpA, SW | 108.0 |  |
| UKRAINE | 66 | RX,DF | 2600 | 1000 | 33 | RX, SpA, DF | 2600 | 1000 | 5 | RX, DF | 1000 | 1000 |

| UNITED ARAB EMIRATES | 2 | RX 9KHZ -1GHz SpA 10 KHz to 3.5GHz, DF 20-100MHz | 1000 | 1000 | 2 | RX, DF 20 MHz-500MHz RX, DF 20-1000MHz | 1000 | 1-500 2-1000 | 1 | RX 20-1000MHz | 1000 | – |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| UNITED KINGDOM | 20 1 | Fixed Remote DF 9K-30M RX 9K-3G SpA | 3000 | 3000 | 3 | DF RX 9K-50G SpA | 50000 | 50000 | 3 | DF, RX, SpA | 1200 | 1200 |
| UZBEKISTAN | 15 | DF EBD190, RX EB200 | 18000 | 3000 | 15 | DF EBD190, RX ESMB | 3000 | 3000 | 0 |  |  |  |

| Note 1) |
| --- |
| Facilities | Monitoring of technical parameters and content |
| Tasks for GSO | – |
| Tasks for non-GSO | – |
| France |
| Facilities | The agency does not have its own resources for monitoring space transmissions. Since 2001 it has worked by agreement with the German Leeheim station, with which a cooperation MOU has just been signed for several years, covering the monitoring of satellites within the CEPT jurisdiction. The Leeheim station consists primarily of three receiving antennas covering the range 130 MHz – 12.75 GHz and a control room housing the measuring and computing systems. |
|  | Main activities conducted at Leeheim | % of workload |
|  | Assistance with satellite network | 20% |
|  | Dealing with interference | 20% |
|  | Monitoring | 60% |
|  | The centre conducts observations of existing satellite systems. It also deals with requests for compatibility testing prior to satellite launches. |
| Tasks for GSO | The Leeheim station conducts the following basic operations for the agency: • scanning an orbit or frequency band • creating identity files for satellites • monitoring satellite position |
| Tasks for non-GSO | For non-GSO satellites the agency’s work involves mainly: • measuring pfd • calculating trajectories • signal demodulation |

ANNEX  2-K

Radio monitoring stations

•	Chart 1:	Fixed measurement stations

•	Chart 2:	Fixed direction-finding stations

•	Chart 3:	Mobile measurement stations

•	Chart 4:	Mobile radio direction-finding stations

•	Chart 5:	Transportable measurement stations

•	Chart 6:	Transportable radio direction-finding stations

ANNEX  2-L

Responses concerning cooperation between spectrum management
and monitoring (Question 12 r), s), t) and u))

•	Participation of administrations in the International Monitoring Programme of ITU

•	Amount of work (in percentages) performed by the monitoring service for administrative management departments

|  | Country | ITU Mon Prog | Co-op between Spectrum Management and Monitoring Dep. |  | Country | ITU Mon Prog | Co-op between Spectrum Management and Monitoring Dep. |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | % Frequency Management | % Enforcement | % Licence |  |  |  | % Frequency Management | % Enforcement | % Licence |
| 1 | ALBANIA | – | – | – | – | 19 | CYPRUS | NO | 30 | 30 | 40 |
| 2 | BAHAMAS | NA | NA | NA | NA t | 20 | CZECH REPUBLIC | YES | 35 | 65 | – |
| 3 | ANTIGUA AND BARBUDA | NO | 0 | 0 | 0 | 21 | EGYPT | NO | 30 | 15 | 55 |
| 4 | BAHRAIN | NO | 50 | 10 | 40 | 22 | EL SALVADOR | NO | 30 | 60 | 10 |
| 5 | BHUTAN | NO | 60 | – | 80 | 23 | ERITREA | NO | 10 | 70 | 20 |
| 6 | BOSNIA AND HERZEGOVINA | NO | 10 | 5 | 85 | 24 | ESTONIA | NO | 10 | 45 | 45 |
| 7 | BOTSWANA | NO | 35 | 20 | 45 | 25 | ETHIOPIA | NA | NA | NA | NA |
| 8 | BURKINA FASO | YES | 50 | 30 | 20 | 26 | FINLAND | YES | 30 | 30 | 40 |
| 9 | BURUNDI | – | – | – | – | 26 | FRANCE | YES | 20 | 70 | 10 |
| 10 | CAMEROON | NO | 30 | – | – | 28 | GABON | NR | NR | NR | NR |
| 11 | CANADA | YES | 40 | 20 | 40 | 29 | GREECE | Temp | 30 | 60 | 10 |
| 12 | CHINA | YES | 30 | 30 | 30 | 30 | GUATEMALA | NO | 40 | 20 | 40 |
| 13 | COLOMBIA | YES | 5 | 90 | 5 | 31 | IRAN | NO | – | – | – |
| 14 | COMORES | NO | (1) | (1) | (1) | 32 | IRELAND | NO | 56 | 20 | 24 |
| 15 | COSTA RICA | NO | 55 | – | 20 | 33 | JORDAN | NA | NA | NA | NA |

|  | Country | ITU Mon Prog | Co-op between Spetrum Management and Monitoring Dep. |  | Country | ITU Mon Prog | Co-op between Spetrum Management and Monitoring Dep. |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | % Frequency Management | % Enforcement | % Licence |  |  |  | % Frequency Management | % Enforcement | % Licence |
| 16 | COTE D'IVOIRE | NO | 34 | 36 | 30 | 34 | LATVIA | YES FM22 | 70 | 5 | 25 |
| 17 | CROATIA | YES | 35 | 50 | 15 | 35 | LEBANON | NO | 20 | 40 | 40 |
| 18 | CUBA | YES | 30 | 20 | 50 | 36 | LESOTHO | NO | 50 | 30 | 20 |
| 37 | LITHUANIA | YES | 34 | 33 | 33 | 54 | SLOVANIA | NO | 60 | 20 | 20 |
| 38 | MADAGASCAR | NO | 30 | 60 | 10 | 55 | SPAIN | NO | 40 | 20 | 40 |
| 39 | MALTA | NO | 55 | 20 | 25 | 56 | SRI LANKA | NO | 30 | 50 | 20 |
| 40 | MAURITANIA | NO | – | – | – | 57 | SURINAME | NR | 43 | 22 | 43 |
| 41 | MOLDOVA | NR | NR | NR | NR | 58 | SWAZILAND | NO | 80 | 0 | 20 |
| 42 | MONACO | NO | 20 | 10 | 70 | 59 | SWITZERLAND | NO | 70 | 20 | 10 |
| 43 | MOROCCO | NR | 40 | 10 | 50 | 60 | SYRIA | NO | NA | NA | NA |
| 44 | NIGER | NR | NR | NR | NR | 61 | TAJIKISTAN | NO | 72 | 18 | 10 |
| 45 | PANAMA | NO | 50 | 30 | 40 | 62 | TANZANIA | NO | NR | NR | NR |
| 46 | PERU | NR | NR | NR | NR | 63 | THAILAND | YES | 30 | 70 | 0 |
| 47 | POLAND | NO | 15 | 70 | 15 | 64 | TURKEY | NO | NA | NA | NA |
| 48 | PORTUGAL | NO | 5 | 85 | 10 | 65 | UGANDA | NO | 20 | 80 | 80 |
| 49 | QATAR | NO | – | – | – | 66 | UKRAINE | YES | 25 | 30 | 45 |
| 50 | ROMANIA | NR | NR | NR | NR | 67 | UNITED ARAB EMIRATES | NR | NR | NR | NR |
| 51 | RWANDA | NA | NR | NR | NR | 68 | UNITED KINGDOM | YES | 30 | 20 | 0 |
| 52 | SAMOA | NO | 68 | NR | NR | 69 | UZBEKISTAN | NO | 20 | 70 | 10 |
| 53 | SENEGAL | NO | NR | NR | NR |  |  |  |  |  |  |
| NR = No Reponse (1) r) Cooperation between spectrum management and monitoring: Response: One and the same person handles everything: spectrum management, monitoring, licensing, invoicing, correspondence with ITU-R (questionnaires), the ministry that is the beneficiary of spectrum management revenues, and other correspondents, regulatory questions, etc. |

ANNEX  2-M

Responses concerning inspection of radio stations
(Question 13)

Legend:

App.	=	Measuring equipment

T	=	Techniques

Mes	=	Measurements

Monit	=	Monitoring stations

A	=	Antennas

F	=	Frequency

P	=	Power

L	=	Bandwidth

G	=	Gain

M	=	Modulation

I	=	Field intensity

D	=	Frequency deviation

NA	=	Not applicable

NR	=	No response

a)	What inspection techniques are used by your administration to determine that users of the spectrum are complying with national or international requirements?

b)	What are the administrative procedures that determine your inspection policy (for example the number of inspections, type of notification provided prior to inspection, rules and regulations)?

c)	What measurement equipment does your administration use to perform technical measurements at an inspection?

d)	What technical parameters does your administration measure when inspecting a radio system?

e)	What station records does your administration review when inspecting a radio station?

| Country | Station Inspection | a) | b) | c) | d) | e) |
| --- | --- | --- | --- | --- | --- | --- |
| ALBANIA | Yes | Inspection | Law | NA | NA | NA |
| ANGOLA | Yes | NR | NR | App | P,L | NR |
| ANTIGUA AND BARBUDA | No | No | No | No | No | No |
| ARMENIA | Yes | App. | Law | App | App | NR |
| BAHAMAS | Yes | Visual | Inspection | App | F,P,A | Licences |
| BAHRAIN | Yes | App | App | App | App | Technical parameters |
| BHUTAN | Yes | NA | Annual | App | F,P,D | Technical monitoring |
| BOSNIA AND HERZEGOVINA | Yes | NR | NR | NR | NR | NR |
| BOTSWANA | Yes | Licences | Inspection | App | App | Licences |
| BURKINA FASO | Yes | Inspection | Decentralization | App | F,P,L,A | Licences |
| BURUNDI | Yes | Licences | NR | App | F,P | Database |
| CAMEROON | Yes | T parameters | Inspection | App | E,P,PAR,A | Licences |
| Canada | No | T parameters | No | App | Parameters Licences | Licences |
| CENTRAL AFRICAIN REP. | Yes | T parameters | NR | No app | NO | Licences |
| CHILE | Yes | Reception | Type of service | App | P,F, coverage area | Licences |
| CHINA | Yes | Daily monit | NR | Monit | P,L | Licences |
| COLOMBIA | Yes | Inspection | Annual inspection | App | F,M,D,T,P,L | Licences |
| COMOROS | No | App | Annual inspection | App | App | Licences |
| COSTA RICA | Yes | Inspection | Inspection | App | L,F,--- | Privates |
| CÔTE D'IVOIRE | Yes | Inspection | NR | App | T,F,M,-- | Database |
| CROATIA | Yes | Inspection | NR | Monit | P,F,A,--- | Licence |
| CUBA | Yes | T technical parameters | Authorization (Cause for Tx) | App | F,D | Licence |
| CYPRUS | Yes | UIT | Interference complaints | Monit | P,F,.---- | Licences |
| CZECH REP. | Yes | Mes/ Laws | Inspection | App + Monit | F,P,L,D + Parameters | Licences |

| Country | Station Inspection | a) | b) | c) | d) | e) |
| --- | --- | --- | --- | --- | --- | --- |
| EGYPT | Yes | Inspection Database | Laws | App | F,L, place, A interference | Licence |
| EL SALVADOR | Yes | Monit | Inspection | App | F,P,L, Zone | No |
| ERITREA | Yes | Licence | Inspection | App | Tx.out of band | Licence |
| ESTONIA | Yes | Law | Inspection | App | P,L,F | NR |
| ETHIOPIA | No | NR | NR | NR | NR | NR |
| FINLAND | Yes | Inspection | Law | App | P,F,D,A | Licence Database |
| FRANCE | Yes | Inspection | Inspection | Monit Mobile | PAR,F, Spectrum | Licence |
| GREECE | Yes | UIT | Complaints interference | App | P,A, Masques | Licence |
| GUATEMALA | No | No | Complaints | NR | I,L,M | NR |
| IRAN | Yes | Monit | Technical parameters | App | F,L,TX. Place | NR |
| IRELAND | Yes | Parameters | Licences | App | F,L,Tx. | Licence |
| LATVIA | Yes | Inspection | Law | Monit | F,P,L,D,A Place | Licence |
| LEBANON | Yes | Monit | App. | App. | F,D,P,L, ------- | UIT/ Licence |
| LESOTHO | No | NR | NR | NR | NR | NR |
| LIECHTENSTEIN | Yes | Inspection | Inspection | App. | Tx,P | Licence |
| LITHUANIA | Yes | Inspection | Law | App. | P,F,L,D | F,D |
| MADAGASCAR | Yes | Licence | Inspection | App. | P,F,M | Licence |
| MALI | NR | No | No | No | No | No |
| MALTA | Yes | Inspection | Licence | App. | F,L,P, | Licence |
| MAURITANIA | Yes | Inspection + Monit | Inspection | App. | I,F,M, Level | Database |
| MOLDOVA | Yes | Mesures | Law | App. | F,M,A,L,P Tx | Licence |
| MONACO | Yes | Inspection | Systematic visit | App. | F,D,P | Licence |
| MOROCCO | Yes | Inspection | Decentralization | App. | P,L,P,A | Licence |
| NETHERLANDS | No (exception) | NR | NR | NR | NR | NR |
| NICARAGUA | Yes | NR | NR | NR | NR | NR |

| Country | Station Inspection | a) | b) | c) | d) | e) |
| --- | --- | --- | --- | --- | --- | --- |
| NIGER | No | NR | NR | NR | NR | NR |
| PANAMA | Yes | Inspection | Programme | App | F,L,I,N | Licence |
| PAPUA NEW GUINEA | Yes | Inspection | Law | App | F,P,L,Tx | Tests |
| PERU | Yes | Mes | Inspection | App | P,F | Database |
| POLAND | Yes | Mes/ Licences | No | App | P,F,Tx | Licence |
| PORTUGAL | Yes | Licences | Law | App | Tx parameters | Licences |
| QATAR | Yes | Inspection | Inspection | App | P,F | Licence |
| ROMANIA | NR | NR | NR | NR | NR | NR |
| RWANDA | NR | NR | NR | NR | NR | NR |
| SAMOA | Yes | NR | NR | NR | NR | NR |
| SENEGAL | Yes | Inspection | Inspection | App | P,F,L | Database |
| SLOVENIA | Yes | Checks | Interference | App | I,M,F,D,P | F,P,M |
| SPAIN | Yes | Licence | NR | App | P,Tx, Spectrum | Licence |
| SRI LANKA | Yes | Monit (L,P) | Inspection | App | F,L,P | Place, Equipment |
| SURINAME | Yes | T parameters | Law | App | F,L | Place |
| SWAZILAND | Yes | Licence | No | NR | NR | NR |
| SWITZERLAND | Yes | Monit | Illegal | App | Best Pratices | Database |
| SYRIA | NR | NR | NR | NR | NR | NR |
| TAJIKISTAN | Yes | Mes/ Licences | Laws | App | Technical parameters | Licences |
| THAILAND | Yes | Case by case | Reports | App | I,F,G,M | Licences |
| TURKEY | Yes | Mes | Inspection | App | P,I,F,L,D | Licences |
| UGANDA | Yes | NR | Regulatory | App. | PAR,L,P | Licences |
| UKRAINE | Yes | T parameters | NR | App | P,F,I | Licences |
| UNITED ARAB EMIRATES | NR | NR | NR | NR | NR | NR |
| UNITED KINGDOM | Yes | Technical parameters | Work program | App | F,P,M Emission | No |
| UZBEKISTAN | Yes | Checks | Inspection | App | F,P,T, ------ | Licence |
| VENEZUELA | Yes | T parameters | Laws | App | F,P,L,I | Licences |

ANNEX  2-N

Responses concerning handbooks and reports (Question 17)
SECTION 1
Response by country

| List of countries | A National Spectrum Management 1995 version | B Spectrum Monitoring 2002 version | C Computer-aided Techniques for Spectrum Management 1999 version | D Report SM.2012-1, Economic Aspects of Spectrum Management 2000 version |
| --- | --- | --- | --- | --- |
| Albania | N | N | N | N |
| Bahamas | Y | N | N | N |
| Antigua and Barbuda | Y | N | N | N |
| Armenia | Y | N | N | N |
| Bahrain | Y | Y | Y | Y |
| Bhutan | Y | N | Y | N |
| Bosnia and Herzegovina | Y | – | Y | Y |
| Botswana | Y | Y | N | Y |
| Burkina Faso | Y | N | N | Y |
| Burundi | Y | N | Y | Y |
| Cameroon | Y | N | Y | Y |
| Canada | Y | Y | Y | Y |
| Central African Rep. | Y | Y | Y | Y |
| Chile | N | N | N | N |
| China | – | – | – | – |
| Colombia | Y | N | Y | N |
| Comoros | N | N | N | N |
| Costa Rica | – | – | – | – |
| Côte d’Ivoire | Y | N | N | Y |
| Croatia | Y | Y | N | Y |
| Cuba | – | – | – | – |
| Cyprus | N | N | N | N |
| Czech Rep. | Y | Y | N | N |
| Egypt | N | Y | Y | Y |
| El Salvador | Y | Y | N | N |

| List of countries | A National Spectrum Management 1995 version | B Spectrum Monitoring 2002 version | C Computer-aided Techniques for Spectrum Management 1999 version | D Report SM.2012-1, Economic Aspects of Spectrum Management 2000 version |
| --- | --- | --- | --- | --- |
| Eritrea | N | N | N | N |
| Estonia | Y | Y | N | N |
| Ethiopia | – | – | – | – |
| Finland | N | Y | N | Y |
| France | Y | Y | N | Y |
| Gabon | – | – | – | – |
| Greece | Y | N | Y | N |
| Guatemala | Y | N | N | N |
| Iran | Y | Y | Y | Y |
| Ireland | Y | N | Y | Y |
| Jordan | – | – | – | – |
| Latvia | Y | Y | Y | Y |
| Lebanon | Y | – | N | Y |
| Lesotho | Y | N | N | Y |
| Liechtenstein | – | – | – | – |
| Lithuania | N | N | N | N |
| Madagascar | N | N | N | N |
| Mali | Y | – | – | Y |
| Malta | Y | N | Y | N |
| Mauritania | – | – | – | – |
| Moldova | Y | Y | – | – |
| Monaco | – | – | – | – |
| Morocco | Y | N | N | Y |
| Netherlands | Y | Y | Y | Y |
| Nicaragua | Y | Y | Y | Y |
| Niger | Y | N | N | N |
| Panama | Y | N | N | – |
| Papua New Guinea | – | – | – | – |
| Philippines | Y | – | Y | – |
| Poland | Y | N | Y | N |
| Portugal | Y | Y | Y | Y |
| Qatar | Y | Y | Y | Y |
| Romania | – | – | – | – |

| List of countries | A National Spectrum Management 1995 version | B Spectrum Monitoring 2002 version | C Computer-aided Techniques for Spectrum Management 1999 version | D Report SM.2012-1, Economic Aspects of Spectrum Management 2000 version |
| --- | --- | --- | --- | --- |
| Rwanda | Y | Y | Y | N |
| Samoa | N | N | N | N |
| Saudi Arabia | – | – | – | – |
| Senegal | Y | Y | Y | Y |
| Slovenia | N | N | N | N |
| Spain | – | – | – | – |
| Sri Lanka | Y | Y | N | Y |
| Suriname | Y | Y | Y | N |
| Swaziland | N | N | N | N |
| Switzerland | Y | Y | Y | Y |
| Syria | Y | N | N | N |
| Tajikistan | Y | – | – | – |
| Thailand | N | N | N | N |
| Turkey | Y | Y | – | Y |
| Uganda | Y | Y | N | Y |
| Ukraine | Y | N | N | N |
| United Arab Emirates | N | N | N | N |
| United Kingdom | – | – | – | – |
| Uzbekistan | Y | Y | Y | Y |
| Venezuela | Y | N | N | Y |

ANNEX  2-N  –  SECTION  2

Breakdown of answers

|  | A National Spectrum, Management 1995 version | B Spectrum Monitoring 2002 version | C Computer-aided Techniques for Spectrum Management 1999 version | D Report SM.2012-1, Economic Aspects of Spectrum Management 2000 version |
| --- | --- | --- | --- | --- |
| OVERALL TOTAL OF RESPONSES | 64 | 59 | 60 | 60 |
| ANSWER | Y | N | Y | N | Y | N | Y | Y |
| TOTAL, EACH ANSWER | 50 | 14 | 26 | 33 | 25 | 35 | 31 | 29 |
| PERCENTAGE, EACH ANSWER | 78.125 | 21.875 | 44.06 | 55.93 | 41.66 | 58.33 | 51.66 | 48.33 |

ANNEX  2-O

Responses concerning the identification of problems experienced
in national spectrum management (Question 18)

| Question 1 | Legal and regulatory texts |
| --- | --- |
| Antigua and Barbuda | Assistance with the drafting of legislation |
| Columbia | Notification of terrestrial services |
| Comores | Texts governing spectrum management have not been signed |
| Latvia | the necessity for adjustment of legislation, the development of secondary legislation in telecommunications |
| Monaco | Reform of legal framework |
| Papua New Guinea | The legal expertise required for the development of legislation pertinent to spectrum management and telecommunications in general is inadequate. The ITU could develop a template legislation that could be used as the basis for the development of corresponding national legislations |
| Peru | Any modification of the legislation should be in keeping with the technological environment |

| Question 2 | Regulations and procedures |
| --- | --- |
| Antigua and Barbuda | Assistance with the drafting of such legal texts or regulations |
| Central Africa | ITU assistance required in the area of tariffs |
| Papua New Guinea | The legislation is publicly available i.e. anybody can purchase a copy however it is not posted on a website. Regulations and procedures for spectrum management that are developed by the regulator can also be made available to the public. The problem here is that such procedures are usually not fully developed in a form that may readily be distributed. Like in Q.1 above the ITU could develop model templates for such procedures/rules and regulations for countries to adjust and adopt. |

| Question 3 | National radio-frequency spectrum allocation table |
| --- | --- |
| Antigua and Barbuda | Assistance with the provision of such a table after a database is established |
| Central Africa | Training on frequency management software |
| Papua New Guinea | The ITU Table of Frequency Allocations could be made available on the Internet or as a soft copy that administrations can use to add their specific allocations and notes. This would save time in retyping and correcting errors, ensure all tables are standardized and free from typing errors. |
| Uganda | Experienced delay in formulation of a national table of frequency allocations. |

| Question 4 | Equipment – technical requirements and standards |
| --- | --- |
| Antigua and Barbuda | Assistance with such technical characteristics specifications |
| Papua New Guinea | Because of insufficient expertise developing countries usually adopt technical specifications from developed countries. Locating a specification can also be a problem. It would be useful if the ITU maintains a register of specifications that can be used as the first point of reference. |
| Peru | Efforts need to be made in the interests of having our own technical standards |
| Uganda | Assistance to develop capacity on equipment standards. |

| Question 5 | Spectrum redeployment |
| --- | --- |
| Antigua and Barbuda | Assistance with development of suitable method |
| Armenia | Materials concerning other Administration’s experiences |
| Botswana | Spectrum migration strategy required to align the users with the National frequency Allocation Plan |
| Papua New Guinea | A model of cost benefit analysis is required. How is the total cost to be established and what are the options available to meet this cost? |

| Question 6 | Spectrum management costs |
| --- | --- |
| Antigua and Barbuda | Assistance with setting up the requirements of such a function with equipment and staff together with cost estimate |
| Armenia | Materials concerning other Administration’s experiences |
| Malta | Increased funding would be welcome to augment the number of staff available for frequency management and for participation in International fora. |
| Papua New Guinea | What is the minimum structure required for complete spectrum management? What is the optimum ratio between core and support staff? What is the reasonable cost of spectrum management in relation to the size of the telecommunications market? |
| Uganda | Spectrum Management functions not adequately funded. |

| Question 7 | Data Base Management System |
| --- | --- |
| Albania | Problems caused by lack of computerized system to keep and maintain records national frequency assignments. |
| Antigua and Barbuda | Assistance with the establishment of such a database |
| Malta | Lack of a computerized frequency management system. |
| Samoa | The FREQMAN Data Base for Spectrum Management Allocation not supported few of technical components for isolation the intermodulation interference. Our Ministry is looking forward to replace the old system to WINBASM software has more advance in managing the Frequency Spectrum |
| Uganda | Lack of automated spectrum management system. |

| Question 8 | Coordination of frequency assignments with other countries |
| --- | --- |
| Antigua and Barbuda | Assistance with the establishment of such a system |
| Armenia | Coordination of frequency assignments to BT stations with other countries, because Armenian Administration isn’t member of ST-61 |
| Malta | We experience difficulty in carrying out terrestrial/space frequency coordination requests |
| Papua New Guinea | There is a need to develop a template for a frequency coordination agreements in border areas. |
| Uganda |  |

| Question 9 | Notification of frequency assignments to ITU |
| --- | --- |
| Antigua and Barbuda | This function will be better performed when a suitable database is in place |
| France | Difficulties have been encountered in the process of notifying assignments to the IFIC, mainly involving updates of some BR products (TeRraSys, BR IFIC, PC Capture, Preface to the International Frequency List, TO2, for terrestrial digital television). |
| Malta | Lack of human resources |
| Papua New Guinea | It would be useful if notification could be possible over the Internet. |
| Peru | There needs to be updated coordination in order to notify frequencies |
| Venezuela | The register has not been updated but work on this is under way |

| Question 10 | Policy and planning functions |
| --- | --- |
| Antigua and Barbuda | Assistance is required in setting up such a policy |
| Sri Lanka | Bandwidth requirements for the allocation of spectrum for the individual operators in the GSM1800 Band and 3G Bands |

| Question 11 | Technical analyses of frequency assignment |
| --- | --- |
| Albania | Lack of skills in the technical analyses process of frequency assignments. |
| Antigua and Barbuda | Assistance is required in setting up such a policy |
| Armenia | New methods of the technical analysis of radio frequency and parameters of radio transmitting equipment |
| Uganda | Limited equipment to effect measurements |

| Question 12 | Radio monitoring of terrestrial radio services |
| --- | --- |
| Albania | Lack of equipment and skills on frequency monitoring process |
| Antigua and Barbuda | No equipment available. Require assistance |
| Armenia | New methods of the technical analysis of radio frequency and parameters of radio transmitting equipment |
| Botswana | Shortage of fixed monitoring equipment and direction finding equipment |
| Lesotho | Shortage of fixed monitoring equipment and direction finding equipment |
| Malta | We need improvement in our direction finding facilities. We also need an upgrade of monitoring equipment and further training in radiomonitoring techniques. |
| Mauritius | Up to now we don’t have any monitoring stations, but we like to get guidelines from the ITU in setting up of our monitoring stations |
| Uganda | Lack of radio monitoring facilities at the moment |
| Uzbekistan | Administration of the Republic of Uzbekistan would like to participate in the International Monitoring Program of ITU. |

| Question 13 | Inspection of radio stations |
| --- | --- |
| Antigua and Barbuda | No equipment available. Require assistance |
| Lesotho | Shortage of measuring equipment e.g. power meters, frequency counters, spectrum analysers, field strength meters, GPS, etc. |
| Papua New Guinea | What is the reasonable proportion of cost for inspections? Should this cost be covered across the board by the licence fees or should it be paid by the licensee in full? |
| Uganda | Few technical staff to carry out radio station inspections |

| Question 14 | Technical analyses of radio frequency interference |
| --- | --- |
| Antigua and Barbuda | No equipment available. Require assistance |
| Armenia | New methods of the technical analyses of radio frequency interference complaints. |
| Uganda | Experience some difficulties in solving some cases of interference especially those relating to broadcasting services |

| Question 15 | Use of computers for national spectrum |
| --- | --- |
| Antigua and Barbuda | Require suitable software |
| Armenia | Latest version WinBASMS for Windows 2000, Windows XP |
| Botswana | No fully automated spectrum management system |
| Burkina Faso | Difficulties working with certain ITU software products such as WinBASMS |
| Estonia | The WinBasms should be modified as soon as possible. See our comments in “k” section. |
| Malta | Lack of a computerized frequency management system. |
| Papua New Guinea | Awareness of WinBASMS needs to be propagated. How many and which countries are using it? Experience could be shared among administrations. ITU needs to hold seminars for training. Advice and support on how to convert form other systems to WinBASMS is required |
| Samoa | Need 2 computers loaded with Microsoft 2000, MS Office 2000 and WINBASM software to support our spectrum work and provides training. |
| Sri Lanka | Preparation of new spectrum fee structure for cellular and fixed services |
| Uganda | Few problems but these will be overcome after acquisition of ASMS and radio monitoring facilities |
| Uzbekistan | Administration of the Republic of Uzbekistan would like to get more information about Advanced Automated Spectrum Management System (AASMS) for studying and using this program. |

| Question 16 | Organization of spectrum management |
| --- | --- |
| Antigua and Barbuda | Department requires expansion to include equipment and personnel |
| Botswana | Shortage of skilled trained personnel |
| Lesotho | Shortage of trained personnel |
| Malta | Lack of human resources in Frequency Management Section |
| Uganda | Require additional staff |

| Question 17 | Use of ITU-R Handbooks and Reports |
| --- | --- |
| Albania | Lack of ITU literatures on managing and monitoring of frequency spectrum |
| Antigua and Barbuda | Department Requires additional ITU-R Handbooks |
| Armenia | Latest publication of the Recommendations ITU-R (Russian version) |
| Papua New Guinea | Greater awareness is needed about these tools. |

Remarks of a more general nature

| Country | Remarks |
| --- | --- |
| Burkina Faso | • Difficulties with acquisition of monitoring equipment (fixed and mobile) suitable for new radio technologies • Difficulties setting up an appropriate radio fee structure to take into account some new radio technologies • Difficulties with re-planning the VHF/UHF bands for national utilization. • Difficulties with access to two/three-week training courses for spectrum management executives. • Difficulties handling certain types of international frequency coordination requests • Difficulties elaborating texts for the procedure to be used in responding to interference complaints |
| Cameroon | • Spectrum engineering • Site management and controlled-transmission areas • Acquisition of an interactive spectrum management and monitoring system • Radio fee recovery • Dealing with unauthorized transmissions • Elaboration of a calculation model for spectrum utilization fees • Measurement of propagation • Coordination with other countries in the framework of modification of the plans of Appendices 30 and 30 A |
| Columbia | • Notification of terrestrial services • Notification of space services • Coordination • Appendix 7 |

| Country | Remarks |
| --- | --- |
|  | • Appendix 8 • Appendix 30 • Appendix 30A • Services in shared bands |
| Comores | • Texts governing spectrum management have not been signed • Lack of appropriate spectrum management training • Need for WinBASMS user training • Administrative inertia and obstacles • Outdated computer • Computer shared by several managers • Limited computer access • Limited Internet access • Information provided by ITU is insufficient • Computer memory approaching saturation • Requirement for Internet computer exclusively for spectrum management purposes • Impossible to do research in certain databases (BRIFIC) • Lack of suitable software being used for spectrum management • Lack of monitoring and measuring equipment • Lack of working documents and references (ITU handbooks) • Lack of contacts • Impossibility of dealing with every issue |
| Costa Rica | • The need for software to create a computerized database • The need for programs to manage the National Radio Control budget • Guidance on the purchase of fixed monitoring stations • Guidance on the purchase of mobile monitoring stations • Guidance on the purchase of portable monitoring stations • Programs for station monitoring • Guidance of the purchase of appropriate equipment • Guidance on the purchase of the computer and engineering system • Support and financing for the purchase of equipment needed to perform proper spectrum management and monitoring |
| Eritrea | • We are just waiting for a concrete and practical reply out put for the above request under this question ------- Development of spectrum fee models where Morocco and Eritrea were the prime movers of the request for such models in Istanbul at the WTDC-02. We hope we will get a useful out put soon possibly within a year. |

| Country | Remarks |
| --- | --- |
| Estonia | • Principles of coordination of maritime stations (procedure, criteria, method of calculation) • Inter-relationship between coordination and notification process (for all services except broadcasting) |
| Mauritania | • Lack of reliable information from spectrum users • Skill in using recently acquired measuring and spectrum analysis equipment • Lack of technical resources for monitoring radio equipment compliance with ITU standards • Staff training • Participation in sub-regional seminars for sharing experience |
| Mauritius | • We also want to know if there is a specific band available for the migration of frequency bands for certain services |
| Niger | • Lack of IT resources Need for training on computerized spectrum management • No-automatic management system • Lack of fixed and mobile monitoring stations • Lack of transportable monitoring stations • Absence of a national policy on frequency management • We wish to request the assistance of ITU in setting up a national frequency management policy and an independent frequency management body. • We wish to request the assistance of ITU for hosting a monitoring station and setting up a calibration laboratory for radio equipment • Training is necessary • Free availability of WinBASMS offers advantages, as a training resource if nothing else. |
| Qatar | • Anomalous propagation effect (possibly due to duct formation over the sea) causes severe seasonal cross-border interference problems from and to the neighbouring countries, primarily in VHF/UHF bands. The phenomenon is required to be studied in depth for a lasting solution. ITU-R may like to look into the matter. Radar interference to the radiocommunication services by naval ships sailing in Arabian gulf is a major problem for the telecommunication systems of this region. The matter requires to be studied for remedial actions |

| Country | Remarks |
| --- | --- |
| Senegal | • HR shortage • Training • Equipment • Users’ non-compliance with regulations • Inflexible procedures • Tariff guide • Ignorance of the regulations among the general public |
| Tajikistan | • The methods of frequency fee calculation are obsolete & do not consider the technical characteristics of modern radio equipment. Could you send us the last methods & recommendations on frequency fee calculation? • The single methods of adding frequency fee for all the users do not provide the users separation, using the frequency in commercial & non commercial activities. Could you send us the recommendations on adding frequency fee to different users. • The lack of automatic system of spectrum management & electronic map complicates the work of spectrum management & analysis of electromagnetic compatibility of the users. Could you send us the single software on calculation of EMC for broadcasting service, frequency spectrum management & electronic map of Central Asia? • The lack of means for raising the level of skill, working in the field of frequency spectrum management reduces the productivity of labour in the field of frequency spectrum management. • The lack of means does not allow in proper time to get the documents provided by ITU. • The lack of skilled technical translators complicates the translation of technical documentations sent by ITU. • The lack of modern fast-acting computers does not allow to solve required tasks. • It is necessary to organize different training courses for the specialists on various kinds of services, as well as the work with software, which is important for the calculating electromagnetic compatibility, database management & frequency spectrum. |
| United Arab Emirates | • Interference calculation • Fees calculation |

_____________

REPORT  ON  RESOLUTION  9  (REV.  ISTANBUL,  2002)
AND  QUESTION  21/2  –  PART  III

# 1	Introduction

ITU-D Question 21/2 (see Annex 1), adopted by the World Telecommunication Development Conference (Istanbul, March 2002), aims to respond to one of the most pressing concerns of the majority of developing countries, particularly LDCs, which are experiencing difficulties in establishing a national frequency fee calculation model.

The Question was entrusted to the Joint Group on Resolution 9 (ITU-D Study Group 2 and ITU-R Study Group 1) in order to benefit from the experience it had acquired during the period 1998-2002 in mobilizing ITU-D and ITU-R expertise. It will lead inter alia to the establishment of a document structure bringing together the calculation formulas and frequency fee amounts applied by the countries for radiocommunication usages in the various frequency bands.

A questionnaire (Administrative Circular CA/12) was thus sent to administrations in order to collect the necessary data, which were analysed in depth. The responses submitted by the administrations were processed in several stages, in the course of which they were classified by region and by type and quality of response. They were then subjected to more in-depth analysis (where the content of the responses permitted it), which was used to draft this report and set up a database that the countries can query via the ITU website.

Generally speaking, Report ITU-R SM.2012-1, while it does not go into detail about the situation in each country, does describe several possible methods of administrative spectrum pricing and mentions the variables likely to be used to calculate frequency fees, in addition to the Spectrum Management Handbook.

These two documents also consider the systems of assignment by public tender and of transferable rights to use the spectrum, in both of which frequency prices are set by the market.

Question 21/2 thus carries on from Report ITU-R SM.2012-1 and the Spectrum Management Handbook, and the results of the work done under this Question will provide information on the real conditions in which frequency fees are implemented in all the countries that participated, along with the values used.

# 2	Questionnaire responses

Fewer countries than expected sent in a response to Part III of the questionnaire, relating to the calculation of fees for frequency use.

The modest number of survey participants is shown in the following table, which also gives an indication of the incompleteness of some of the responses received. The results and graphs in the following have been elaborated on the basis of those responses which were received, which are available on the ITU-D website and on a CD-ROM distributed by BDT.

| Countries that did not respond to Part III (CD) | Countries that did not respond to Part III (website) |
| --- | --- |
| BHUTAN(1) | ANGOLA |
| BOSNIA AND HERZEGOVINA | BHUTAN(1) |
| CANADA(1) | BOSNIA AND HERZEGOVINA |
| CEPT | CANADA(1) |
| CHILE(1) | CEPT |
| CHINA(1) | COSTA RICA |
| COMOROS(1) | CUBA |
| COSTA RICA(1) | CYPRUS |
| CUBA(2) | ETHIOPIA(1) |
| ETHIOPIA(1) | GABON |
| GABON | IRAN |
| IRAN | IRELAND |
| IRELAND | JORDAN |
| JORDAN(1) | LATVIA |
| LATVIA | LITHUANIA(1) |
| LITHUANIA(1) | NETHERLANDS |
| MEXICO | NICARAGUA |
| NICARAGUA | PANAMA(1) |
| PANAMA(1) | PERU(1) |
| PERU(1) | POLAND |
| POLAND | QATAR(1) |
| QATAR(1) | ROMANIA |
| ROMANIA | RWANDA(1) |
| RWANDA(1) | SAMOA |
| SAMOA | SAUDI ARABIA |
| SAUDI ARABIA | SURINAME(1) |
| SURINAME | UZBEKISTAN(1) |
| SWAZILAND(1) | VENEZUELA(1) |
| UZBEKISTAN(1) |  |
| VENEZUELA(1) |  |
| VIET NAM(1) |  |
| (1)  Countries that responded to the questions in Part III, but not to the charts. (2)  Countries that responded to the charts in Part III, but not to the questions. |

The variables and scales/formulas received are contained in the specially set up database; a large number of responses would help by enriching the database, increasing its usefulness to all administrations.

Since the database is intended to be renewed periodically, administrations are encouraged to respond to the questionnaire or add to their previous response.

The analysis and statistics in the present report refer to geographical regions, defined as follows:

(	Africa: region 1

(	Americas: region 2

(	Asia and Pacific: region 3

(	Europe and Asia minor: region 4

(	Arab States: region 5.

Number and type of response, by region: the graphs below give a breakdown of the responses received, broken down as follows:

(	number of countries that provided a full response to all of Part III of the questionnaire;

(	number of countries that did not respond to Part III of the questionnaire;

(	number of countries that responded to Part III of the questionnaire but not to questions Q.1-Q.9;

(	number of countries that responded to Part III of the questionnaire but not to charts A-E.

| Region | Number of countries that responded to the whole questionnaire | Number of countries that responded to Part III | Number of countries that did not respond to Part III | Number of countries that did not respond to the questions in Part III | Number of countries that did not respond to the charts in Part III |
| --- | --- | --- | --- | --- | --- |
| 1 | 20 | 17 | 1 | 0 | 2 |
| 2 | 13 | 6 | 1 | 1 | 5 |
| 3 | 6 | 5 | 0 | 0 | 1 |
| 4 | 25 | 20 | 1 | 0 | 4 |
| 5 | 8 | 6 | 0 | 0 | 2 |
| Total | 72 | 54 | 3 | 1 | 14 |

NUMBER  OF  RESPONSES,  BY  REGION

# 3	Analysis of responses

The responses received from administrations have been integrated in their entirety into the database created for the purpose (see § 6), by country and region. Their size precludes full reproduction in this report.

Some administrations provided full and detailed answers to all parts of the questionnaire, while others left out some or all of the questions and the five charts relating to variables used to calculate fees. In some cases there were discrepancies between the answers given to the questions and the charts, in others there were evident mistakes, which were left out of the analysis. Administrations are free to correct any erroneous data they find in their database entries.

## 3.1	General questions (Q.1 to Q.5)

3.1.1	Question Q.1: Are there any legal texts on the establishment of frequency fees?

The responses are summarized in the following table:

| Existing texts | Yes | No | No answer provided | Number of responses | Texts in progress |
| --- | --- | --- | --- | --- | --- |
| Africa | 13 | 5 | 0 | 18 | 2 |
| Americas | 10 | 2 | 0 | 12 | – |
| Asia-Pacific | 6 | 0 | 0 | 6 | – |
| Europe and Asia minor | 22 | 2 | 1 | 25 | 1 |
| Arab States | 6 | 1 | 1 | 8 | – |
| Column total | 57 | 10 | 2 | 69 | 3 |

A large majority of countries has legal texts governing the establishment of fees. Among the ten countries which do not, three indicated that work was being pursued to develop such texts.

3.1.2	Question Q.2: What procedure (regulatory, legislative, etc.) is used to review and update your system for setting frequency fees? Are reviews conducted at pre-established regular intervals? Does recourse to market mechanisms (auctions, calls for tenders) to screen applicants for spectrum access require that parliament enact legislation, that the government make a decision, or any other measure?

The responses relating to the existence of a legislative or regulatory procedure are summarized in the following table:

|  | Yes | No | No answer provided | Number of responses | Texts in progress |
| --- | --- | --- | --- | --- | --- |
| Africa | 15 | 2 | 1 | 18 | 1 |
| Americas | 9 | 1 | 2 | 12 | – |
| Asia-Pacific | 6 | 0 | 0 | 6 | – |
| Europe and Asia Minor | 23 | 0 | 2 | 25 | – |
| Arab States | 5 | 0 | 3 | 8 | – |
| Column total | 58 | 3 | 8 | 69 | 1 |

A large number of countries (58 out of 69) has legislative or regulatory procedure for reviewing and updating the fee system.

The responses relating to the interval for fee reviews are summarized in the following table:

|  | Yes | No | No answer provided | Number of responses | Texts in progress |
| --- | --- | --- | --- | --- | --- |
| Africa | 1 | 12 | 5 | 18 | 1 |
| Americas | 4 | 6 | 2 | 12 | – |
| Asia-Pacific | 0 | 6 | 0 | 6 | – |
| Europe and Asia minor | 6 | 15 | 4 | 25 | – |
| Arab States | 0 | 6 | 2 | 8 | – |
| Column total | 11 | 45 | 13 | 69 | 1 |

For the vast majority of the countries which submitted a response to this question, fees are not reviewed at regular intervals.

Responses concerning the need for a legislative or regulatory act to have recourse to the market are summarized in the following table:

|  | Yes | No answer provided | No act required, or no need foreseen | Number of responses |
| --- | --- | --- | --- | --- |
| Africa | 8 | 3 | 7 | 18 |
| Americas | 9 | 2 | 1 | 12 |
| Asia-Pacific | 5 | 1 | 0 | 6 |
| Europe and Asia minor | 17 | 3 | 5 | 25 |
| Arab States | 4 | 2 | 2 | 8 |
| Column total | 43 | 11 | 15 | 69 |

In the majority of cases having recourse to the market requires a legislative or regulatory act.

3.1.3	Question Q.3: Are the same approaches and principles used to set frequency fees for all users?

The responses concerning the similarity of methods used to determine fees for all users are summarized in the following table:

|  | Yes | No | No answer provided | Number of responses |
| --- | --- | --- | --- | --- |
| Africa | 8 | 9 | 1 | 18 |
| Americas | 5 | 5 | 2 | 12 |
| Asia-Pacific | 3 | 3 | 0 | 6 |
| Europe and Asia minor | 16 | 7 | 2 | 25 |
| Arab States | 4 | 3 | 1 | 8 |
| Column total | 36 | 27 | 6 | 69 |

The responses received do not show any clear preference, suggesting that the question may have been interpreted differently by the various administrations.

3.1.4	Question Q.4: In addition to direct frequency fees, certain administrations require the payment of additional spectrum-related charges (for example, for spectrum access, spectrum replanning, management of equipment using the frequencies, etc.). Does your administration require such payments?

The responses concerning the use of additional charges are summarized in the following table:

|  | Yes | No | No answer provided | Number of responses |
| --- | --- | --- | --- | --- |
| Africa | 4 | 12 | 2 | 18 |
| Americas | 3 | 7 | 2 | 12 |
| Asia-Pacific | 3 | 3 | 0 | 6 |
| Europe and Asia minor | 8 | 16 | 1 | 25 |
| Arab States | 1 | 5 | 2 | 8 |
| Column total | 19 | 43 | 7 | 69 |

A majority of the countries indicated that they did not use additional charges.

3.1.5	Question Q.5: To which institution(s) are the frequency fees and any additional charges collected paid?

The answers concerning the institution(s) to which fees are paid are summarized in the following table:

|  | State (or ministry) budget | National regulatory authority (or independent body responsible for spectrum management) | No answer provided | Number of countries submitting responses |
| --- | --- | --- | --- | --- |
| Africa | 4 (+ 1) | 13 | 2 | 18 |
| Americas | 7 (+ 1) | 2 | 4 | 12 |
| Asia-Pacific | 4 | 2 | 0 | 6 |
| Europe and Asia minor | 14 (+ 5) | 15 | 1 | 25 |
| Arab States | 4 | 2 | 2 | 8 |
| Column total | 33 (+7)* | 34 | 9 | 69 |
| * (+ 7) means that in total, fees are paid both to the regulatory authority and the State in 7 countries. |

The responses show that the proportion of cases in which the State (or ministry) budget is the beneficiary is comparable with those in which it is an independent body, frequently the one in charge of spectrum management.

Financing spectrum management expenditure

The answers to Q.5 may be put in the context of those received in response to Q.6, Part II (spectrum management costs and how they are funded).

The responses show that spectrum management bodies are funded in one of three ways:

a)	through spectrum use fees collected directly by the spectrum management body;

b)	through public budget funding; or

c)	by some combination of collected fees and public funding.

For countries in group a), the annual total of fees collected from spectrum users should thus correspond to the cost of spectrum management at the national level given in Q.6, Part II.

## 3.2	Exemption from payment of frequency fees

This section relates to the questions Q.6 and Q.7 in Part III of the questionnaire, which read:

Q.6: Are any applications partially or completely exempted from the payment of frequency fees?

Q.7: Are any users partially or wholly exempted from the payment of frequency fees?

Examination of the responses received to these two questions concerning exemptions from frequency use fees granted by administrations shows that, for applications, generally fully or partly exempted, there are applications operating in certain predetermined frequency bands, generally not requiring an assignment procedure on the part of the administration.

The various applications that have an exemption or discount are illustrated below, with the percentage corresponding to the three regions.

| Application | Region | No. of countries | Total |
| --- | --- | --- | --- |
| SRD | 1 | 7 | 25 |
|  | 2 | 3 |  |
|  | 3 | 3 |  |
|  | 4 | 9 |  |
|  | 5 | 3 |  |
| Citizen’s Band (CB) | 1 | 3 | 7 |
|  | 2 | 0 |  |
|  | 3 | 1 |  |
|  | 4 | 3 |  |
|  | 5 | 0 |  |
| ISM | 1 | 1 | 4 |
|  | 2 | 0 |  |
|  | 3 | 1 |  |
|  | 4 | 2 |  |
|  | 5 | 0 |  |
| Telemetry | 1 | 0 | 2 |
|  | 2 | 1 |  |
|  | 3 | 1 |  |
|  | 4 | 0 |  |
|  | 5 | 0 |  |

| Application | Region | No. of countries | Total |
| --- | --- | --- | --- |
| Cellular telephony | 1 | 0 | 1 |
|  | 2 | 0 |  |
|  | 3 | 1 |  |
|  | 4 | 0 |  |
|  | 5 | 0 |  |
| Bands forbidden in Radio Regulations | 1 | 0 | 1 |
|  | 2 | 0 |  |
|  | 3 | 0 |  |
|  | 4 | 1 |  |
|  | 5 | 0 |  |
| Sources of interference | 1 | 0 | 1 |
|  | 2 | 0 |  |
|  | 3 | 0 |  |
|  | 4 | 1 |  |
|  | 5 | 0 |  |
| Simplified professional radio (PMR)-446 | 1 | 0 | 3 |
|  | 2 | 0 |  |
|  | 3 | 0 |  |
|  | 4 | 3 |  |
|  | 5 | 0 |  |
| Radiolocation | 1 | 0 | 1 |
|  | 2 | 0 |  |
|  | 3 | 0 |  |
|  | 4 | 1 |  |
|  | 5 | 0 |  |
| EESS | 1 | 0 | 1 |
|  | 2 | 0 |  |
|  | 3 | 0 |  |
|  | 4 | 1 |  |
|  | 5 | 0 |  |

Furthermore, a number of administrations grant exemptions or discounts for frequency user fees collected from the public sector (ministries, departments, etc.), humanitarian organizations, safety departments and so on.

The organizations that benefit from an exemption or discount are shown below, with the percentage corresponding to the three regions.

| Users | Region | No. of countries |
| --- | --- | --- |
| Rail | 1 | 1 |
|  | 2 | 0 |
|  | 3 | 0 |
|  | 4 | 0 |
|  | 5 | 0 |
| Maritime | 1 | 1 |
|  | 2 | 2 |
|  | 3 | 2 |
|  | 4 | 3 |
|  | 5 | 1 |

| Users | Region | No. of countries |
| --- | --- | --- |
| Air | 1 | 3 |
|  | 2 | 2 |
|  | 3 | 3 |
|  | 4 | 3 |
|  | 5 | 1 |
| Security/defence | 1 | 9 |
|  | 2 | 5 |
|  | 3 | 5 |
|  | 4 | 12 |
|  | 5 | 4 |
| Research bodies | 1 | 1 |
|  | 2 | 0 |
|  | 3 | 0 |
|  | 4 | 0 |
|  | 5 | 0 |
| Amateur | 1 | 2 |
|  | 2 | 1 |
|  | 3 | 2 |
|  | 4 | 3 |
|  | 5 | 1 |
| Religious | 1 | 1 |
|  | 2 | 1 |
|  | 3 | 0 |
|  | 4 | 0 |
|  | 5 | 0 |
| United Nations | 1 | 1 |
|  | 2 | 0 |
|  | 3 | 2 |
|  | 4 | 0 |
|  | 5 | 0 |
| Embassies | 1 | 3 |
|  | 2 | 1 |
|  | 3 | 2 |
|  | 4 | 5 |
|  | 5 | 1 |

## 3.3	The application of frequency fees

### 3.3.1	Methods used by administrations

Charts A to E, with information provided by administrations, allow an analysis of the variables which administrations have decided should make up the fees.

In determining the amounts of fees, administrations use formulas, scales or some combination of both.

Section 5 below examines the results with respect to the use of variables by administrations.

### 3.3.2	Explanations, grounds and objectives

Few administrations gave an answer to this part of the questionnaire. Their answers are found in the database. They may be summarized briefly as follows.

Frequency use fees make it possible to:

(	finance spectrum management;

(	create incentives for more efficient spectrum utilization; and

(	make the most of the spectrum, as a public good, in the public interest.

The table below lists some of the explanations and objectives given for the variables, as expressed in the responses.

| Variable | Explanation and ground, desired objectives |
| --- | --- |
| Bandwidth | Occupation of common spectrum. Incentive for economic spectrum use. |
| Centre frequency, band position in spectrum | Propagation characteristics are not constant throughout spectrum. Incentive to make use of uncongested portions. |
| Exclusive/shared use | Occupation of common spectrum. Incentive for efficient spectrum use. |
| Allocated area, distance between transmitter and receiver | Geographic possibilities for others to reuse frequencies, based on area and distance. For commercial frequency use, the potential turnover is a function of the allocated area. |
| Number of transmitting stations | Occupation of public lands and spectrum. |
| Duration of authorization | Length of period during which the common spectrum is occupied. |
| Population covered | For commercial frequency use, the potential turnover is a function of the population that is covered. |
| Geographic location | Conditions of propagation (and therefore network cost), spectrum congestion and potential turnover are all related to the geographic location. Important for land-use planning in particular. |
| Operator turnover | The operator enjoys a position advantage by virtue of access to a common resource. Objective: redress any imbalance. |

### 3.3.3	Recourse to market mechanisms

Administrations were invited to indicate any applications for which they employed market mechanisms (auction, call for tenders or comparative selection).

The tables below give the number of countries that did so for various applications.

Wireless local loop

|  | Africa | Americas | Asia-Pacific | Europe and Asia minor | Arab States | No. of responses |
| --- | --- | --- | --- | --- | --- | --- |
| e | 0 | 0 | 0 | 3 | 0 | 3 |
| scp | 0 | 0 | 0 | 0 | 1 | 1 |
| sc | 0 | 0 | 0 | 2 | 0 | 2 |
| Column total | 0 | 0 | 0 | 5 | 1 | 6 |
| e: auction scp: call for tenders sc: comparative selection |

2G mobile systems

|  | Africa | Americas | Asia-Pacific | Europe and Asia minor | Arab States | No. of responses |
| --- | --- | --- | --- | --- | --- | --- |
| e | 0 | 0 | 0 | 1 | 0 | 1 |
| scp | 0 | 0 | 0 | 3 | 1 | 4 |
| sc | 0 | 0 | 0 | 5 | 0 | 5 |
| Column total | 0 | 0 | 0 | 9 | 1 | 10 |
| e: auctions scp: call for tenders sc: comparative selection |

3G mobile systems

|  | Africa | Americas | Asia-Pacific | Europe and Asia minor | Arab States | No. of responses |
| --- | --- | --- | --- | --- | --- | --- |
| e | 0 | 0 | 0 | 3 | 0 | 3 |
| scp | 0 | 0 | 0 | 0 | 0 | 0 |
| sc | 0 | 0 | 0 | 3 | 0 | 3 |
| Column total | 0 | 0 | 0 | 6 | 0 | 6 |
| e: auctions scp: call for tenders sc: comparative selection |

Analogue terrestrial radio

|  | Africa | Americas | Asia-Pacific | Europe and Asia minor | Arab States | No. of responses |
| --- | --- | --- | --- | --- | --- | --- |
| e | 0 | 0 | 0 | 0 | 0 | 0 |
| scp | 0 | 0 | 0 | 0 | 0 | 0 |
| sc | 0 | 0 | 0 | 3 | 0 | 3 |
| Column total | 0 | 0 | 0 | 3 | 0 | 3 |
| e: auctions scp: call for tenders sc: comparative selection |

Digital terrestrial radio

|  | Africa | Americas | Asia-Pacific | Europe and Asia minor | Arab States | No. of responses |
| --- | --- | --- | --- | --- | --- | --- |
| e | 0 | 0 | 0 | 0 | 0 | 0 |
| scp | 0 | 0 | 0 | 0 | 0 | 0 |
| sc | 0 | 0 | 0 | 2 | 0 | 2 |
| Column total | 0 | 0 | 0 | 2 | 0 | 2 |
| e: auctions scp: call for tenders sc: comparative selection |

Digital terrestrial television broadcasting

|  | Africa | Americas | Asia-Pacific | Europe and Asia minor | Arab States | No. of responses |
| --- | --- | --- | --- | --- | --- | --- |
| e | 0 | 0 | 0 | 0 | 0 | 0 |
| scp | 0 | 0 | 0 | 0 | 0 | 0 |
| sc | 0 | 0 | 0 | 4 | 0 | 4 |
| Column total | 0 | 0 | 0 | 4 | 0 | 4 |
| e: auctions scp: call for tenders sc: comparative selection |

Furthermore, it may be observed that one of the Arab States has conducted:

(	an sc to select independent trunk operators; and

(	an scp to select VSAT network operators.

For the most part, market mechanisms are called upon only for applications involving access to the end-user or, in the case of broadcasting, access to the general public.

For broadcasting applications, only comparative selection is used.

For other applications, the two main mechanisms, calls for tenders (e and scp) and “beauty contest”-type comparative selection tenders (sc), are roughly equally popular.

# 4	Updating the report and database

## 4.1	Updating the report

Question Q.9: How often would you consider it most appropriate to update the report and the database: every 2 years, 3 years, 4 years, ...?

The responses received on the subject of updating the report are summarized below.

| Update interval | 2 years | 3 years | 4 years | Number of responses |
| --- | --- | --- | --- | --- |
| Africa | 6 | 4 | 2 | 12 |
| Americas | 2 | 3 | 3 | 8 |
| Asia and Pacific | 2 | 2 | 0 | 4 |
| Europe and Asia minor | 6 | 7 | 6 | 19 |
| Arab States | 0 | 3 | 1 | 4 |
| Column total | 16 | 19 | 12 | 47 |

One country proposed an update every five years.

It is proposed that the Study Groups in question state their preference for the report updating interval.

## 4.2	Updating the database

It is proposed that the Study Groups in question state their preference for the manner of updating the database.

# 5	Analysis of results

## 5.1	Variables used to determine fees

### 5.1.1	Variables and applications identified in questionnaire

The questionnaire considers 19 variables to characterize the elements used by administrations in establishing the fees charged for frequency usage.

The variables are given in the table below.

| Categories | Variables |
| --- | --- |
| Spectrum-related variables | bandwidth |
|  | number of channels |
|  | centre frequency, or band position in the spectrum |
|  | exclusive/shared use |
| Variables relating to geographic coverage | surface area allocated |
|  | distance between transmitter and receiver |

| Categories | Variables |
| --- | --- |
| Variables relating to equipment and infrastructure | transmitter power |
|  | antenna diameter |
|  | bit rate or capacity |
|  | transmitting beam angle |
|  | number of transmitting stations |
|  | number of receiving stations |
|  | degressivity |
| Socio-economic variables | duration of authorization/licence |
|  | population density |
|  | total population covered |
|  | geographic location |
|  | operator’s turnover |
|  | gross domestic product |

The questionnaire also identified 30 applications, grouped in five categories concerning the fixed, mobile, satellite and broadcasting service and one called “other applications”.

For any given application, administrations were asked to respond with a “Yes” or “No” for each of the listed variables in charts A to E of the questionnaire, to indicate whether they used that variable in calculating the amount of the fee.

### 5.1.2	Processing of responses from administrations

All of the responses from administrations relating to the five charts, A to E, have been transcribed verbatim into the database. The quality of the statistical information extracted thus depends entirely on the manner in which administrations have filled in those charts.

The database has been designed to provide, for any of the 30 applications and for a given variable, information about which countries use the variable, and the number (and proportion) of countries in each of the five regions and worldwide which use it.

The annex contains, by way of example, the statistics for the variables used for fixed service applications worldwide.

### 5.1.3	Analysis of variables used

Variables are used more or less commonly depending on the application being considered.

#### 5.1.3.1	Most commonly used variables

Apart from “duration of authorization/licence”, the most common variables are:

(	number of transmitting stations;

(	bandwidth; and

(	transmitter power.

The tables below give the worldwide percentage for utilization (number of countries which use the variable/total replies + no-answers) on the basis of the current database contents.

Fixed service

| Radio-relay | Local radio loop | Links between fixed stations | Local radio networks |
| --- | --- | --- | --- |
| number of transmitting stations (65%) | bandwidth (56%) | number of transmitting stations (62%) | bandwidth (40%) |

Mobile service

| 2G mobile systems | 3G mobile systems | Radio-messaging | Private independent networks | Operated independent networks |
| --- | --- | --- | --- | --- |
| bandwidth (57%) | bandwidth (28%) | bandwidth (37%) | number of transmitting stations (51%) | bandwidth (40%) |

Satellite service

| VSAT | Earth stations | Satellite video reporting | Mobile-satellite service |
| --- | --- | --- | --- |
| bandwidth (47%) | bandwidth (53%) | bandwidth (27%) number of transmitting stations (27%) | bandwidth (41%) |

Terrestrial broadcasting service

| Analogue sound broadcasting | Digital sound broadcasting | Analogue television broadcasting | Digital television broadcasting |
| --- | --- | --- | --- |
| transmitter power (36%) | number of transmitting stations (21%) | transmitter power (33%) | number of transmitting stations (20%) |

Other applications

| Radio amateur | Experimental networks | Low-range, low-power devices | Radionavigation |
| --- | --- | --- | --- |
| number of transmitting stations (24%) | number of transmitting stations (21%) | number of transmitting stations (14%) | number of transmitting stations (21%) |

Remark: For some applications, the relatively low percentage of utilization indicated after the variable signifies that few countries apply fees for those applications.

#### 5.1.3.2	Rating of most commonly used variables

Given the wide range of responses, such a rating is only possible application by application. By way of an example, the table below rates the variables (with the exception of "duration of authorization") for radio-relays and 2G mobile systems.

It will be observed that socio-economic variables are not in wide use.

Radio-relays

| Variable | % use |
| --- | --- |
| number of transmitting stations | 65% |
| bandwidth | 60% |
| centre frequency or band position | 47% |
| number of channels | 44% |
| bit rate or capacity | 25% |
| number of receiving stations | 23% |
| transmitter power | 23% |
| exclusive/shared use | 22% |
| surface area allocated | 18% |
| distance between transmitter and receiver | 13% |
| degressivity | 10% |
| geographic location | 10% |
| transmitting beam angle | 7% |
| antenna height | 6% |
| gross domestic product | 1% |

2G mobile systems

| Variable | % use |
| --- | --- |
| bandwidth | 57% |
| number of transmitting stations | 27% |
| centre frequency or band position | 27% |
| surface area allocated | 24% |

| Variable | % use |
| --- | --- |
| exclusive/shared use | 19% |
| geographic location | 12% |
| number of receiving stations | 10% |
| bit rate or capacity | 9% |
| population density | 7% |
| total population covered | 7% |
| operator’s turnover | 6% |
| degressivity | 4% |
| gross domestic product | 1% |

## 5.2	Fee size

Few administrations indicated the size of their fees.

Some administrations gave detailed information on the calculation algorithms or scales, making it possible to determine the size of the fee for a given application. This information may be found in the database.

As indicated in § 3.1.5, in some countries the fee total is determined in such a way as to cover the costs of spectrum management.

## 5.3	Recourse to market mechanisms

As § 3.3.3 shows, to date few administrations have made use of market mechanisms. The total number in any one application never exceeds ten.

## 5.4	Advantages and disadvantages of each approach

Question Q.8: What are the advantages and disadvantages of the approaches currently used by your administration to establish the amount of frequency fees and any additional charges?

Twenty-four administrations responded to this question. Their answers, which may be viewed in the database, are summarized in the table below, broken down according to the spectrum pricing methodology (discussed in Chapter 2 of the report ITU-R SM.2012) and with an additional category of “other advantages and disadvantages”.

None of the administrations cited opportunity cost as the basis for pricing.

In general, each administration listed a number of advantages and disadvantages. The columns headed “advantages” and “disadvantages” provide a synopsis of the responses of the administrations concerning their spectrum pricing system and their view of the problem. This explains why apparently contradictory remarks may be found in that table (their sources are different administrations).

The number of responses given for each of the advantages and disadvantages is indicated in parentheses.

Seven administrations also indicated that studies were planned or in progress to evaluate or revise their pricing system.

| Spectrum pricing: | Advantages | Disadvantages |
| --- | --- | --- |
| by means of auctions or calls for tenders | – spectrum prices determined by the market (1). – theoretically provides for optimum spectrum utilization (1). | – market may overestimate the actual value of spectrum (1). – spectrum overpricing may inhibit the development of services (1). – price charged is fixed and cannot be revised to take account of changing economic conditions (1). |
| by means of comparative selection (“beauty contests”) | – fees can be revised to take account of changing economic conditions (1). – does not inhibit the development of services (1). | – risk of fees being priced too low by comparison with the market value of spectrum (1). |
| on the basis of the cost of spectrum management | – low administrative overhead (1). – contributes to developing spectrum management and monitoring (1). | – the real value of spectrum resource is not known or determined (2). – difficulties with detailed breakdown of fees (1). – does not address the objectives of scarcity management and spectrum reaccommodation (1). – small users may find themselves paying high fees (1). |
| on the basis of spectrum users’ income | – fees are a function of user size (1). | – inhibits user growth (1). |
| on the basis of an incentive formula | – incentive for spectrum utilization (1). – encourages higher-frequency use (2). – encourages efficient spectrum utilization (5). – encourages use of new technologies (1). – encourages research and development in radio field (1). – promotes telecommunication development in rural areas (1). – attractive for foreign investment (1). | – numerous variables and formulas are used (1). – actual spectrum occupancy in the affected geographical area is not taken into account (1). |

| Spectrum pricing: | Advantages | Disadvantages |
| --- | --- | --- |
| Other advantages and disadvantages which administrations associate with their pricing system | general advantages of fee system: – system makes it possible to reach the public authority's objectives in terms of socio-economic spectrum management (3). specific advantages of system: – fee calculation is simple to apply and readily understandable (9). – fee system is transparent (1). – fee system is stable (1). – differentiates between commercial and non-commercial activities (2). – all services are billed (2). suitable fees: – reasonable fees that are in line with market demand (1). – low fees (1). | incomplete system: – system doesn’t cover all applications (2). – important parameters left out (2). – efficiency of spectrum utilization not taken into account (1). – digital equipment is not taken into account properly (1). – duration of use is not taken into account (1). system imperfections: – does not differentiate between commercial and non-commercial activities (1). – fee tables or system too rigid (2). – inconsistency of the system (1). – fees not under control (1). – emergency services billed (1). – inadequate substantiation to motivate user compliance (1). practical difficulties: – calculation method too complicated (2). – scales difficult to apply (2). – difficulties assessing the real number of mobile and portable stations (2). fees not suitable: – fees too low (1). – fees too high (1). – fees too high for non-commercial activities (1). – fees lower than management costs (1). |

# 6	Database

The BDT secretariat has created a database for Question 21/2 in order to analyse the information provided by administrations in response to the questionnaire.

The database, which can be accessed from the website, contains all of the responses received by BDT to date.

The database was designed by BDT in consultation with the Joint Group on Resolution 9. It allows for viewing of the variables used in establishing frequency usage rights and the scales and formulas used. It is complemented by this report, which provides an analysis and the statistics for the responses received from administrations.

Section 7 below explains how to use the database.

The database may be freely accessed at the URL http://www.itu.int/ITU-D/study_groups/SGP_2002-2006/SF-Database/index.asp for purposes of consulting and displaying the information it contains.

However, modification and update rights for the data relating to any given country are restricted to the administration of that country. No administration can modify data belonging to any other administration.

To this end, BDT will provide a password for use by each administration, which can then be changed. Administrations will be asked to provide BDT with a contact to whom the password can be sent.

# 7	Using the database

The database allows the data relating to calculation of frequency usage fees to be viewed. The database contains the responses to the questionnaire on implementation of Resolution 9 of the World Telecommunication Development Conference (CA/12 and CA/120).

The homepage has four columns:

1)	The first column is for viewing the responses to the general questions (Q.1 to Q.9) in Part III of the questionnaire by:

(	region;

(	country;

(	chart (radio service);

(	application; and

(	variable.

A scroll button is used to make one or more choices, before clicking on “Display”.

2)	The second column is for viewing the data relating to calculation of frequency usage fees by:

(	region;

(	country;

(	chart (radio service);

(	application; and

(	variable.

A scroll button is used to make one or more choices, before clicking on “Display”.

3)	The third column (“scales/formulas”) is used for viewing the calculation formulas or scales that are applied, by:

(	region;

(	country;

(	chart (radio service).

A scroll button is used to make one or more choices, before clicking on “Display”.

4)	The fourth column is for:

(	obtaining the “cross-variable count”, i.e. the number of countries using a particular variable (chosen from a drop-down list) for a given application (chosen in the same way); and

(	displaying statistics and diagrams showing the rate of use of variables broken down by region, radio service and applications.

A scroll button is used to make one or more choices, before clicking on “Statistics on Chart/Region”.

5)	Modification and update of data by administration:

To do this, the user (who needs to have a password, as explained in § 6 of this report) clicks on the “Identification page” button at the bottom of the homepage.

This will take the user to a new page where the name of the country and the password must be entered. If a password has not yet been assigned for the administration, the user clicks on the appropriate link.

ANNEX  1

Definition of Question 21/2

Question 21/2: Calculation of frequency fees

# 1	Statement of the situation or problem

The draft new Question dealt with here responds to one of the most pressing concerns of numerous developing countries, particularly LDCs, which are experiencing difficulties in elaborating a national frequency fee calculation model.

Furthermore, several regulatory frameworks place the frequency resource within the State domain. As a result, its use, which may well not be equitably distributed, must be properly remunerated as part of the rational management of public property. Techniques for sharing, segmentation, access to new frequencies and reorganization of the spectrum no longer suffice to guarantee effective management. The frequency spectrum therefore has to be optimized. This effort should, however, take into account the nature of the service to be provided, the band in question and the end user (consumer activities, etc.).

The optimization effort must be adapted to the new trends in the area of spectrum usage and sharing and must reflect the socioeconomic features of each country. It is particularly urgent when it comes to evaluating bands which are in high demand or may come to be so in the light of emerging technologies, as is the case with IMT-2000 systems in the 2 GHz band.

It should be borne in mind that the economic aspects of spectrum management are addressed in the ITU-D handbook on the economic, administrative and regulatory aspects of national spectrum management, as well as in Report ITU-R SM.2012, which describes, inter alia, the three main approaches to financing national spectrum management and the corresponding main advantages and disadvantages (financing from the national budget, through the collection of fees or charges for use of the spectrum, and by public tender). The report also presents the economic approaches used to promote national spectrum management (assignment through comparative assessment procedures; random assignment; assignment by public tender; transferable, flexible rights to use the spectrum; incentive pricing and concessionary charges, etc.).

Thus, the elaboration of a national frequency fee calculation model is a very complex matter and is the source of major difficulties for numerous developing countries and particularly LDCs for which the need is extremely urgent. The proposed Question will help to meet those concerns.

# 2	Question or issue proposed for study

The proposed study relates to the methods for calculating the various charges, fees, etc. that are levied on spectrum users. The points to be considered within the framework of this new Question are as follows:

a)	Establishment in electronic format of a document structure bringing together the calculation formulas and frequency fee amounts applied by different countries for different radiocommunication usages in the various frequency bands. This database will be made available to the ITU Member States and will require periodic updating.

b)	Preparation of a report dealing with the following points:

•	Analysis of the various methods, formulas and approaches currently applied by different countries for calculating frequency fees, accompanied by a comparative study clearly highlighting:

(	approaches and principles relating to the calculation of frequency charges;

(	the justifications and reasoning for each approach;

(	how each approach contributes to fostering spectrum management and the effectiveness thereof;

(	advantages and drawbacks of each approach (socioeconomic, technical and other considerations).

•	Basic factors that may be taken into account when elaborating new formulas or reviewing existing ones.

•	How to bring about consistency and complementarity between spectrum rearrangement processes and economic optimization of frequencies.

# 3	Expected outputs

An electronic document structure and links enabling users to have easy access to data on frequency fee calculation formulas for the users of the radio-frequency spectrum in different countries. BDT is requested to coordinate participation with those countries who do not have access to the Web, providing them a hard copy upon request.

A report on the various frequency fee calculation formulas currently applied in different countries.

# 4	Required timing of the expected output

An initial version of the output is requested by mid-2003.

A regular update should subsequently be carried out.

# 5	Proposers/sponsors

This Question was submitted to WTDC-02 and has been recognized as being very important for the developing countries and LDCs, and as being urgent.

# 6	Source of required inputs

(	Inputs are expected from spectrum managers (administrations, regulators), relating to:

(	the structure of the information to be made available and the questionnaire(s) to be circulated to the Member States in order to gather the information to be entered into the database;

(	analysis of the replies and of the report.

(	Inputs are also expected from spectrum users (operators, etc.) that are subject to the fees in question, for analysis of the replies and of the report.

(	Member States’ replies to the questionnaire(s).

# 7	Target audience for the output

a)	Indicate the target audience for the output in the following table:

|  | Developed countries | Developing countries | LDCs |
| --- | --- | --- | --- |
| Telecom policy-makers | X | X | X |
| Telecom regulators | X | X | X |
| Service providers (operators) | X | X | – |
| Manufacturers | – | – | – |

b)	Target audience for the study – who specifically will use the output?

The output could be particularly useful to frequency spectrum managers when it comes to identifying the basic elements to be taken into account in elaborating a national frequency fee calculation model for the various users of the radio-frequency spectrum in the different frequency bands.

c)	Proposed methods for implementing the output

The output will be made available to all Member States free of charge (documents on paper, on the Web and on CD-ROM). An ITU circular letter should be sent out informing the Member States of the results of this study and inviting them to use that output when elaborating their national model for optimizing the frequency spectrum.

# 8	Proposed method of handling this Question

Given that this Question, which is very important and urgent for the developing countries and particularly LDCs, touches also on the field of radiocommunications, and that ITU-R Study Group 1 has already accumulated expert experience on the matter, it is proposed that it be dealt with by the joint working group already set up for the implementation of Resolution 9 (ITU-D Study Group 2/ITU-R Study Group 1).

Meetings dealing specifically with this Question should be programmed by the joint working group during the period 2002-2003.

# 9	Coordination requirements for the study

Coordination between ITU-D and ITU-R is required and should be carried out within the framework of the joint working group on Resolution 9.

In addition, coordination with ITU-D Study Group 1 is necessary (Question 12/1).

ANNEX 2

Spectrum Fees Database statistics for all countries

CHART A: FIXED SERVICE

_____________

# Footnotes

1	A revision of the ITU-R National Spectrum Management Handbook will be completed in 2005.

2	The Radio and Telecommunications Terminal Equipment Directive of the countries of the European Union. This Directive provides procedures to replace the need for national type approval (the new procedures include the use of manufacturer’s declaration of compliance).

3	CIS: Commonwealth of Independent States

5	Récepteur

6	Emetteur

# Text boxes

X

1