| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0526 |
|  | English only |
| WG(s):1, 6 | 4th FG IPTV meeting: Bled, Slovenia, 7-11 May 07 |
| CONTRIBUTION |
| Source: | Cisco Systems, Inc. |
| Title: | Container Option for Server Configuration |

Introduction

In some DHCP service deployments, it is desirable to pass configuration options from a DHCP server in one administrative domain to another DHCP server in a different administrative domain.  In one example of such a deployment, an IPTV Service Provider (SP) may need to provide certain SP domain-specific information to IPTV device(s) located in the consumer domain.  This information is sent from the IPTV SP DHCP server to the Delivery Network Gateway (DNG) DHCP server (through the DNG DHCP client) which can then be passed along to ITF device(s) in the consumer network.  This contribution describes how the delivery of this information can be achieved.

The following companion Cisco contributions refer to and make use of this Container Option contribution:

“DNG Network Attachment”

“ITF Network Attachment”

“IPTV Device Attachment and Initialization process for Core IPTV and NGN Architectures

Discussion

Proposal

It is proposed that the Container Option concept be adopted by WG1 and 6 in the context of the DNG and ITF initialization in an IPTV environment.   The Container Option concept is referred to in the other Cisco companion contributions (DNG Network Attachment, ITF Network Attachment and IPTV Device Attachment and Initialization process for Core IPTV and NGN IPTV Architectures).