| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0536 |
|  | Original: English |
| WG(s): | 1 | 4th FG IPTV meeting: Bled, 7-11 May 2007 |
| CONTRIBUTION |
| Source: | Korea (Republic of) |
| Title: | Proposed Architecture for 3rd Party Value-Added IPTV Services |

# Scope

This contribution identifies and defines new functional components and interfaces for 3rd party value-added services.

# Reference

[1]	ITU-T Recommendation Y.2012 (2006), Architecture and Requirement of the NGN

[2] 	ITU-T Recommendation Y.2011 (2006), General principles and general reference model for NGN

[3] 	FG IPTV-DOC-0062, Working Document: IPTV Architecture

# Abbreviation

This contribution document uses the following abbreviations.

ANI				Application Network Interface

IPTV				Internet Protocol TV

NGN				Next Generation Network

IMS				IP Multimedia Subsystem

OSA				Open Service Architecture

ASF&SSF 	Application Support Functions and Service Support Functions

APL-SCM-FE 	Application Service Coordination Manager Functional Entity

APL-GW-FE 	Application Gateway Functional Entity

AS-FE 		Application Support Functional Entity

SS-FE Service 	Switching Functional Entity

# Introduction

Unfortunately, there are no explicit components and interfaces for OSA in the current working document: IPTV architecture.

This contribution aims at:

- adding a new architectural component and an interface to existing IPTV architecture defined in Working Document: IPTV Architecture (FG IPTV-DOC-0062)

- proposing a new NGN-based IPTV architecture for service provider and network provider to deploy 3rd party value-added service using open interface (e.g., Telecom Web Services) for 3rd party applications.

# Proposed Architecture for 3rd Party Value-Added IPTV Services using Open Interface

Figure 1 shows an overview of the NGN functional architecture that allows the support of the release 1 services. The NGN functions are divided into service stratum functions and transport stratum functions according to Y.2011 [1]. The NGN supports a reference point to the applications functional group called application network interface (ANI), which provides a channel for interactions and exchanges between applications and NGN elements. The ANI offers capabilities and resources needed for realization of applications.

Figure 1: NGN architecture overview

Application Support Functions and Service Support Functions (ASF&SSF) shown in Figure 1 is comprised of Application support Functional Entity (AS-FE), Application Gateway Function Entity (APL-GW-FE), Application Service Coordination Manager Functional Entity (APL-SCM-FE), and Service Switching Functional Entity (SS-FE). Among these entities, APL-GW-FE provides a secure open interface for the applications to use the capabilities and resources of the NGN. The Applications connected to APL-GW-FE are usually realized by OSA application servers. Therefore, for creating 3rd party IPTV services, functional entity APL-GW-FE in the NGN architecture is required for IPTV architecture.

Figure 2: Application/service support functions

The current IPTV architecture [3] can be classified by 3 approaches such as NGN and IMS based architecture, NGN and Non-IMS based architecture, and Non-NGN based architecture. The “NGN-based” architecture implies that the IPTV architecture should be harmonized with [Y.2012] for providing IPTV services. Consequently, it is reasonable to accommodate the NGN functional component APL-GW-FE in current “NGN based” IPTV architecture if IPTV architecture is based on NGN architecture. Unfortunately, there is no service component which could be mapped to APL-GW-FE in the current NGN based IPTV architecture.

If the NGN component APL-GW-FE is added to the existing NGN-based IPTV architecture, innovative 3rd party IPTV application services are easily created by using open interface (e.g., Parlay X Web Service). Someone may assume that common NGN components are hidden in the current NGN because they are common components for all “NGN based” architecture including the IPTV architecture. However, there is no explicit component for APL-GW-FE in the current NGN based IPTV architecture. In the following section, we will add a new component, namely Application Gateway Functions which can be mapped to APL-GW-FE and interfaces to the existing architecture for 3rd party IPTV services using open interface.

## NGN-based with Non-IMS Session Control Architecture Extension for 3rd Party value-added services

## NGN-based with IMS Session Control Architecture Extension for 3rd Party value-added services