| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0642 |
|  | English only |
| WG(s): 6 | 5th FG IPTV meeting: Geneva, 23-31 July 2007 |
| CONTRIBUTION |
| Source: | China Netcom Group, P.R.China |
| Title: | Proposal on the requirements of EPG and service navigation system |

1.  Introduction

There are so many requirements of EPG and service navigation system so far. We analysis  these requirements,and classify them as three kind of requirements as following:

- Pure technical requirements.

For example, Based on HTML/XML mechanism etc.

- Basic functionality and performance requirements of the system

For example, Real-time,Smart retrieval, Interactive,Distributed of the system etc.

- Others

Such as individuality application requirements etc.

# 2. Proposal

Because we work on a technical standard/specification, so,it is suggested only to put the Pure technical requirements and Basic functionality and performance requirements of the system into the working document:service navigation system.

It is proposed to add the following condensed requirements into Clause 5.2.1 of DOC-0098e besides that already listed in the document:

(5) Navigation system should be Real-time,Smart retrieval,Interactive,Distributed

(6) Navigation system  should support to select,search service/content and service descriptions

(7) The IPTV Middleware can optionally support assignment of  human useable shortcut identifier to a service.

And delete the apostrophe there.

It is proposed to add the following condensed requirements into Clause 5.2.2 of DOC-0098e besides that already listed in the document:

(7)  Service and content should be sorted or filtered or both by time or other criteria

(8)  Navigation page is recommended to be presentable without any consideration on the type of terminal and is recommended to be able to adapt on it.

(9) Navigation page can have customized capabilities including on-demand feeding, transforming, filtering, and gathering function.

And delete the apostrophe there.

_________________