| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0695 |
|  | English only |
| WG(s): 3 | 5th FG IPTV meeting: Geneva, 23-31 July 2007 |
| CONTRIBUTION |
| Source: | China Telecom, Huawei |
| Title: | Proposal Procedures of Service Authorization |

# 1. Introduction

Service authorization is important function in the IPTV service architecture, especially to the service carriers and service providers. It is the main function to guarantee the security of IPTV services. In this contribution, we discuss the procedures of service authorization and propose to add them to related working document.

# 2. Discussion

Service authorization is the right or permission to use a system resource and the process of granting access. In a telecom service system, the result of service authorization should be the reference data of the accounting function. Service authorization procedure should be comprised of the subscriber, IPTV service control function, the transport control functions and transport functions in linear TV service.

In some cases, if user and subscription info changes between the rights info transferring and the request of accessing resource, the Transport Functions could not detect the change. This situation will appear in services that need real-time authorization in LTV service.

In these cases, the Transport Function requests the authorization information from IPTV Application via IPTV Service Control Function in real time when receives requests for a specific channel from user. The authorization procedure should be the figure as below.

Figure 1

In IPTV environment, services and applications would be miscellaneous and flexible. Therefore, it is necessary to provide a real-time service authorization method.

# 3. Proposal

we propose to add the procedures shown in figure 1 into chapter 10.2.2, working document of WG3.

Contributor List

| Name | Company | Tel. | Email |
| --- | --- | --- | --- |
| Jianting Meng | China Telecom | +86 21 58755057 | mengjt@sttri.com.cn |
| Jincheng Li | Huawei | +86 29 87674145 | lijincheng@huawei.com |
| Haining Yan | China Telecom | +86 21 28970207 | yanhn@sttri.com.cn |
| Li Jiang | China Telecom | +86 21 58750441 | jiangli@sttri.com.cn |

____________