| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-DOC-0172 |
|  | English only |
| WG(s): 2 | 6th FG IPTV meeting: Tokyo, Japan, 15-19 October 2007 |
| OUTPUT DOCUMENT |
| Source: | Acting Editor |
| Title: | Living List - Traffic management for IPTV |

The following information has been agreed by WG2 to be under further consideration by WG2 prior to inclusion in formal output documents.

### Item 1 (Busan Meeting)

Source: FG IPTV-C-0123, Huawei, “Traffic management of IPTV multicast services”

### Item 2 (Busan Meeting)

Source: FG IPTV-C-0198, ETRI, “A proposal for bandwidth management architecture in access network for IPTV service”

Item 3 (Mountain View Meeting)

Source: FG IPTV-C-0317, Huawei Technologies “ Proposal for traffic management admission control”

## Admission Control

Admission control and resource reservation strategy is necessary to support QoS assurance for IPTV services on a managed network. IPTV Services supported by admission control will satisfy unicast and multicast service demand for subscribers. Unicast admission control satisfies IPTV unicast services, such as VOD, Time Shifted TV etc. Multicast admission control satisfies multicast services, such as BTV, NVOD etc.  In order to realize multicast admission control, subscribers first join a multicast group to request multicast services. The multicast admission control function allocates and reserves resource for subscribers. When the multicast admission control function allocates and successfully reserves resources for subscribers, the multicast replication function will forward IPTV multicast streaming service to subscribers.

Editor’s Note: The italicized text is the relevant material that is for further study (FFS).

Item 4  (Mountain View Meeting)

Source: FG IPTV-IL-0033, DSL Forum, TR-101 “Migration to Ethernet-Based DSL Aggregation”

________