| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-DOC-0194 |
|  | English only |
| WG(s): 6 | 7th FG IPTV meeting: Qawra, St. Paul’s Bay, Malta, 11-18 December 2007 |
| OUTPUT DOCUMENT |
| Source: | Editor |
| Title: | IPTV Middleware, Applications and Content Platforms |

Summary

This document identifies and defines middleware platforms, including applications, content formats, and their uses, that facilitate effective and interoperable use of an IPTV system for presenting and interacting with IPTV services. This document is a general document for IPTV middleware, application and content platforms. It describes content provisioning, service discovery, channel and content identification and location resolution, and profiling. This document refers to text on middleware, content coding, metadata, which can be found in other documents.

Keywords

IPTV, middleware, applications

Current status

Since the scope of this document is very broad there are still some clauses, especially on Profiling that need more text. This document is currently about 80% complete.

Dependency or relationship to other FG IPTV documents

- Toolbox for content coding [FG IPTV-DOC-0195]

- IPTV Middleware [FG IPTV-DOC-0196]

- IPTV Metadata [FG IPTV-DOC-0197]

- Standards for IPTV Multimedia Application Platforms [FG IPTV-DOC-0198]

CONTENTS

1	Scope	3

2	References	3

3	Definitions	4

3.1	This working document uses the following terms defined elsewhere:	4

3.2	This working document defines the following terms:	6

4	Abbreviations and acronyms	7

5	Content provisioning	9

5.1	Introduction	9

5.2	Interface between content/metadata providers and service providers	9

5.3	Gap analysis for content and metadata provisioning	10

6	Service Discovery	11

7	Channel Identification and location resolution	13

8	Profiling	13

9	Events	14

9.1	Input events	14

9.2	Other events	14

10	Service navigation systems	14

Appendix I: Profiling	15

Appendix II: Input events	19

Appendix III:  Example of assignment of input events	20

Appendix IV: Services navigation systems	21

IPTV MIDDLEWARE, APPLICATION AND CONTENT PLATFORMS

Scope

This document identifies and defines middleware platforms, including applications, content formats, and their uses, that facilitate effective and interoperable use of an IPTV system for presenting and interacting with IPTV services.

Figure 1-1: Scope of this document

For practical reasons the following topics are included in other documents

- Toolbox for content coding [FG IPTV-DOC-0195]

- IPTV Middleware [FG IPTV-DOC-0196]

- IPTV Metadata [FG IPTV-DOC-0197]

- Standards for IPTV Multimedia Application Platforms [FG IPTV-DOC-0198]

References

The following ITU-T Recommendations and other references contain provisions, which, through reference in this text, constitute provisions of this working document. At the time of publication, the editions indicated were valid. All Recommendations and other references are subject to revision; users of this working document are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations and other references listed below. A list of the currently valid ITU-T Recommendations is regularly published.

The reference to a document within this working document does not give it, as a stand-alone document, the status of a Recommendation.

[ITU-T F.700]	ITU-T Recommendation T.700 (2000), Framework Recommendation for multimedia services

[ITU-T H.222AM1]	ITU-T Recommendation H.222.0 Amd 1(2002), Information technology – Generic coding of moving pictures and associated audio information: Systems Amendment 1: Carriage of metadata over ITU-T Rec. H.222.0 | ISO/IEC 13818-1 streams

[ITU-T J.90]	ITU-T Recommendation J.90 (2000), Electronic programme guides for delivery by digital cable television and similar methods - Reference operating scenario and requirements

[ITU-T J.94 AM1]	ITU-t Recommendation J.94 Amendment 1 (1998), Annex B - Service information delivered out of band for digital cable television systems

[ITU-T J.98]	ITU-T Recommendation J.98 (2003), Metadata requirements for video-on-demand in cable networks

[ITU-T J.148]	ITU-T Recommendation J.148 (2003), Requirements for an objective perceptual multimedia quality model

[ITU-T J.190]	ITU-T Recommendation J.190 (2002), Architecture of MediaHomeNet that supports cable-based services

[ITU-T J.200]	ITU-T Recommendation J.200 (2001), Worldwide common core ( Application environment for digital interactive television services

[ITU-T Q.1702]	ITU-T Recommendation Q.1702 (2002), Long-term vision of network aspects for systems beyond IMT-2000

[ITU-T T.171]	ITU-T Recommendation T.171 (1996), Protocols for interactive audiovisual services: Coded representation of multimedia and hypermedia objects

[ITU-T T.174]	ITU-T Recommendation T.174 (1996), Application programming interface (API) for MHEG-1

[ITU-T Y.101]	ITU-T Recommendation Y.101 (2000), Global Information Infrastructure terminology: Terms and definitions

[ISO/IEC 13818-2] 	ISO/IEC 13818-2 (2000), Information technology -- Generic coding of moving pictures and associated audio information: Video

[ISO/IEC 14496-12] 	ISO/IEC 14496-12 (2005), Information technology -- Coding of audio-visual objects -- Part 12: ISO base media file format

[ETSI EN 300 468]	ETSI EN 300 468 V1.8.1 (2007), Digital Video Broadcasting (DVB); Specification for Service Information (SI) in DVB systems

[ETSI TS 102 323]	ETSI TS 102 323 V1.2.1 (2005), Digital Video Broadcasting (DVB); Carriage and signalling of TV-Anytime information in DVB transport streams

[ATIS-0800002]	ATIS standard ATIS-0800002(2006), IPTV Architecture Requirements

Definitions

## This working document uses the following terms defined elsewhere:

- Application [ITU-T Y.101]: A functional implementation realized as software running in one or spread over several interplaying hardware entities.

Application manager [ITU-T J.200]: The entity that is responsible for managing the lifecycle of the applications. It manages applications running in both the Presentation engine and Execution engine if both are present.

Application Programming Interface (API) [ITU-T J.200]: Consists of software libraries that provide uniform access to system services. [ITU-T J.200]

Note: In the case of middleware, it is an interface between application layer and middleware service which encapsulates the services offered by the middleware and enable application developer to develop new application.

Character [ITU-T J.200]: A specific "letter" or other identifiable symbol, e.g. "A".

Character encoding [ITU-T J.200]: Mapping between an integer input value, and the textual character that is represented by this mapping, e.g. in ASCII value 65 (decimal) is character "A", or shift-JIS for Japanese characters.

Content [ITU-T T.174]: Encoded generic value, media or non-media data

EPG provider [ITU-T J.90]: The entity that collects, collates and assembles the elements of information that constitute the EPG database.

Execution engine (EE) [ITU-T J.200]: instructions and associated data and media content. An execution engine may be implemented with an operating system, computer language compilers, interpreters, and Application Interfaces (APIs), which a procedural application may use to present audiovisual content, interact with a user, or execute other tasks, which are not evident to the user. A common example of an execution engine is the JavaTV software environment, using the Java programming language and byte code interpreter, JavaTV APIs, and a Java Virtual Machine for program execution.

Home network (HN) [ITU-T J.190]: Short-range communications system designed for the residential environment, in which two or more devices exchange information under some sort of standard control.

Metadata format [ITU-T H.222AMD1]: Identifies the coding format of metadata.

Metadata service [ITU-T H.222AMD1]: Coherent set of metadata of the same format delivered to a receiver for a specific purpose.

Multimedia [ITU-T J.148]: The combination of multiple forms of media such as audio, video, text, graphics, fax, and telephony in the communication of information.

Multimedia application [ITU-T T.174]: An application which involves the presentation of multimedia information to the user.

Multimedia service [ITU-T Q.1702]: A service in which the interchanged information consists of more than one type, such as text, graphics, sound, image and video.

Multimedia representation [ITU-T T.171]: The property of handling several types of representation media.

Presentation [ITU-T T.411]: The operation of rendering the content of a document in a form perceptible to a human being.

Presentation engine [ITU-T J.200]: A subsystem in a receiver that evaluates and presents declarative applications consisting of content, such as audio, video, graphics, and text primarily based on presentation rules defined in the presentation engine. A presentation engine also responds to formatting information, or "mark-up", associated with the content, to user inputs, and to script statements, which control presentation behaviour and initiate other processes in response to user input and other events. A common example of a presentation engine is an HTML browser, capable of displaying text and graphic content formatted in HTML, with interactive behaviour programmed in ECMA script.

Service [ITU-T Y.101]: A structure set of capabilities intended to support applications.

Stream [ITU-T J.200]: A unidirectional continuous flow of content.

Telecommunication service [ITU-T F.700]: Set of telecommunication capabilities that work in a complementary and cooperative way in order to let users perform applications.

User device [ATIS-0800002]:  Also known as Home Network End-Device (HNED), Home Network Device (HND), Consumer Equipment (CE), terminal and physical device. A piece of hardware equipment running its software and attached to a Home Network and being identified by a GUID, e.g. a MAC address. A single Device can be used by one or more users.

This working document defines the following terms:

Application instance: An occurrence of an application

- Broadcast TV: One-way transmission of TV signals from one point to two or more other points.

- Character set:  See character encoding.

- Content protection: Act of preventing unauthorized use of any content.

- Electronic Content Guide (ECG): A service navigation interface used especially for content streaming and download.

Note: It is sometimes used synonymously with EPG.

- Electronic Program Guide (EPG): A service navigation interface which is used especially for programs.

Note: in some traditional Broadcast Services, EPG is defined as an on-screen guide used to display information on scheduled live broadcast television programs, allowing a viewer to navigate, select, and discover programs by time, title, channel, genre. This traditional definition does not cover “catalogues” for on-demand and download services (sometimes called ECG) and bi-directional interactive service (sometimes called IPG) for end-user interaction with a server or head-end.

Some EPGs utilize web-pages, or teletext to realize this function.

- Electronic Service Guide (ESG): A service navigation interface used especially for available services and contents.

- Extended channel: Means to organise different operation content together, including live channel, TVOD, information service, EPG and so on. For each extended channel, there is a related channel number. [0062]

- Globally Executable MHP (GEM): A terminal specification based on MHP that enables applications to interoperate across OCAP, MHP and other GEM based platforms.

- IPTV Terminal Function (ITF)*: The functionality within the home network that is responsible for terminating the IP signal, and converting the content into a renderable [i.e. enabling to be seen and/or heard] format, e.g. a STB.

*: Based on [ATIS-0800002] with modification

- Interactive Program Guide (IPG): A service navigation interface used especially for bi-directional interactive service with a server or head-end.

Note: It is sometimes used synonymously with EPG.

- Interactive Television (iTV): A service in which the user can send requests, within a browser environment, to the service provider in order to obtain additional information. This capability requires channels to have what is known as a 'return path'.

- Lifetime/Lifecycle of an application: Characterizes the time from which the application is loaded to the time the application is destroyed.

- Metadata: Structured, encoded data that describe characteristics of information-bearing entities to aid in the identification, discovery, assessment, and management of the described entities.

Note: EPG metadata has many applications and may vary in depth from merely identifying the content package title or information to populate an EPG to providing a complete index of different scenes in a movie or providing business rules detailing how the content package may be displayed, copied, or sold.

- Middleware: A layer of software between applications and resources, which consists of a set of service enablers that allow multiple functionalities running on one or more devices in an IPTV system to interact across a network.

- Segmentation: Division of content into different parts, e.g. scenes and chapters.

- Service Navigation: The presentation of information that allows the end-user to discover, select and consume services.

- Service Navigation Interface: A user interface which is intended to provide information on available services, including content that may be accessed by end-users for service navigation.

- Set-top box (STB): A device that contains demodulator, de-multiplexer, decoder, other functionalities and interfaces related to signal reception and presentation of the distributed programme at the subscriber's site.

- Time shifting: A function which allows playback of content after its initial transmission.

- Time-shifted TV: A TV program that has been time shifted.

- User Interface (UI): Also known as UI, a user interface is the sensory and behavioural aspects of a program that are presented to a user. The term is generally used to denote the menuing and navigational constructs of a program.

- Video-on-Demand (VoD): A service in which the subscriber can view video content whenever desired. The operating assumption is that the content is stored on the provider’s VoD server. Subscriber accesses the movie from a library directory which may include search engine that accesses movie description and rating.  Subscribers typically have the ability to pause, play, rewind, fast forward the content, or even stop viewing it and return to it at a later time when using this service.

Abbreviations and acronyms

This document uses the following abbreviations and acronyms.

API	Application Programming Interface

AV	Audio Video

DVB	Digital Video Broadcasting

EPG	Electronic Program Guide

ESG	Electronic Service Guide

ETSI	European Telecommunications Standards Institute

GEM	Globally Executable MHP

GIF	Graphics Interchange Format

GUI	Graphical User Interface

HN	Home Network

HTML	Hyper Text Mark-up Language

HTTP	Hyper Text Transport Protocol

I/O	Input / Output

ID	IDentifier

IETF	Internet Engineering Task Force

IHDN	In Home Digital Network

IP	Internet Protocol

IPR	Intellectual Property Rights

ISDN	Integrated Services Digital Network

ISO	International Organization for Standardization

ITU	International Telecommunication Union

ITV	Interactive Television

JDK	Java Development Kit

JFIF	JPEG File Interchange Format

JPEG	Joint Picture Expert Group

LMDS	Local Multipoint Distribution System

MAC	Media Access Control

MHP	Multimedia Home Platform

MIME	multipurpose internet mail extensions

MMDS	Multipoint Microwave Distribution System

MPEG	Moving Picture Experts Group

NTSC	National Television Systems Committee

NVOD	Near-Video-On-Demand

OCAP	OpenCable Application Platform

OS	Operating System

OSD	On Screen Display

PFR	Portable Font Resource

PNG	Portable Network Graphics

PSI	Program Specific Information

PSIP	Program and System Information Protocol

RAM	Random Access Memory

ROM	Read Only Memory

SI	Service Information

TCP	Transmission Control Protocol

TS	Transport Stream

UDP	User Datagram Protocol

UI	User Interface

URL	Uniform Resource Locator

UTF8	Universal Transformation Format 8

VM	Virtual Machine

WAN	Wide Area Network

XML	eXtensible Markup Language

Content provisioning

Introduction

Content provisioning in IPTV is the activity of providing TV channels, programs, movies, music and other contents between content providers and service providers. Service providers may sign contracts with content and metadata providers, import contents and metadata from content/metadata providers.

To protect content rights, content provider may encrypt the content before delivery to service provider.

In this clause we focus on the interface between content/metadata providers and service providers and not on the content/metadata processes inside the service provider domain.

Interface between content/metadata providers and service providers

Content providers can provide audiovisual channels, contents and metadata together or separately.

Pure metadata providers also exist.

In the case of broadcast retransmission, broadcast service platforms such as terrestrial, cable, or satellite digital broadcasting can provide audiovisual channels, metadata and contents for interactive services to IPTV Service platforms for retransmission.

Figure 5-1: Relations between content providers & service providers

"Streams" stands for single programme streams and for multiple programme streams.

For content provisioning, a set of interfaces is needed and identified:

- Contract exchange (not to be standardised)

- Content & metadata provisioning interface

- Consumption reporting

Standards are needed for the content & metadata provisioning interface.

The metadata elements for provisioning are recommended to be as common as possible with the metadata elements made available to the end-user, however with elements specific to the relation between "content provider" and "service provider" (such as distribution conditions).

Gap analysis for content and metadata provisioning

Table 5-1: Content provisioning standards

| Content provisioning method | Identified standards |
| --- | --- |
| File format for content provisioning | [ISO/IEC 14496-12] |
| File format for metadata provisioning | [SMPTE-380M] |
| File format for combined content & metadata provisioning | [ISO/IEC 14496-12] (need to be extended) |
| Stream format for channel/content provisioning | [ISO/IEC 13818-2] |
| Content provisioning transport protocol | [ISO/IEC 13818-2], [IETF RFC3550], [IETF RFC768], etc. |
| Stream format for combined channel/content & metadata provisioning | [ETSI EN 300 468] & [ETSI TS 102 323] |

Service Discovery

There are different IPTV configurations to be considered, such as:

- Configuration with only one IPTV service provider on the network

- Configuration with multiple IPTV service providers on the network with preconfigured specific IPTV service provider

- Configuration with multiple IPTV service providers on the network without preconfigured specific IPTV service provider

In the case where there is only one IPTV service provider on the network or when there is a preconfigured service provider, here are the different steps in the service discovery:

- step 1: discovery of IPTV service provider entry point

- step 2: acquisition of the description of the IPTV services offered by the service provider and IPTV Service Selection

Figure 6-1: Service discovery with configuration of several IPTV service providers on the network

In the case where there are several service providers and there is no preconfigured service provider (see above figure), here are the different steps in the service discovery:

- step 1: discovery of the IPTV service provider description provider entry point

- step 2: acquisition of the description of the IPTV service providers and IPTV service provider selection

- step 3: acquisition of the description of the IPTV services provided by the selected service provider and IPTV service selection

Step 1 is always the discovery of the starting entry point and this is dealt with in the document "IPTV Network Control Aspects" [FG IPTV-DOC-0189]

The starting entry point might be:

- An IPTV service provider description provider entry point (when there are several IPTV service providers on the network and no specific service provider entry point is provided in the terminal device configuration data)

- An IPTV service provider entry point (when there is only one IPTV service provider on the network or when a specific service provider entry point is provided in the terminal device configuration data). The IPTV service provider maybe running a web-based solution, a metadata-based one or a mixture of them.

Here are two examples showing how descriptions of available IPTV service providers can be acquired by terminal devices, when the entry point is an IPTV service provider description provider entry point, the first one making of HTTP or S-HTTP protocols and the second making use of the IGMP protocol

Figure 6-2: HTTP or S-HTTP request to get the description of the available IPTV service providers

In this case the service provider description provider may answer with a set of metadata containing the description of the available service providers.

Figure 6-3: IGMP join request to receive the description of the available IPTV service providers

In this case the service provider description provider sends periodically the set of metadata containing the description of the available service providers.

The metadata related to the description of the available IPTV service providers can be found in the IPTV metadata document [FG IPTV-DOC-0198].

Here are two examples showing how descriptions of IPTV services offered by an IPTV service provider can be acquired by IPTV terminal devices, when the entry point is an IPTV service provider entry point, the first one making of HTTP or S-HTTP protocols and the second making use of the IGMP protocol

Figure 6-4: HTTP or S-HTTP request for description of the IPTV services offered by a service provider

Figure 6-5: IGMP join request to receive the description of the IPTV services offered by a service provider

Channel Identification and location resolution

Domain names (DNS) could be used to identify destination multicast addresses of channels in EPG. These domain names would be registered on DNS servers with their corresponding multicast addresses. When end users try to access multicast channels in the EPG, their IPTV terminal devices resolve the domain names with DNS servers. When they get the multicast addresses for the domain names, they issue out group membership reports to join the multicast groups, and receive contents from the multicast channels.

Profiling

Appropriate information can be found in Appendix I.

Events

Input events

Appropriate information can be found in Appendix II.

Other events

For further study.

Service navigation systems

Appropriate information can be found in Appendix III.

Appendix I: Profiling

(This Appendix does not form an integral part of this document)

This appendix includes material for discussion on profiling. Although the IPTV FG did not have time to discuss it, it was felt valuable to keep it to be the basis for further discussion in the IPTV GSI.

I. 	Profiling Process for IPTV Service

I.1. 	Overview

The “IPTV service scenarios” and “IPTV service requirements” documents define IPTV services and requirements for IPTV network.  The IPTV network should satisfy all the requirements identified.  But it is difficult to develop the complete IPTV specifications satisfying all the requirements in single step.  In this document, the IPTV standardization process is classified into three profiles.

In classifying profiles, the following principles are considered.

- Market urgency – the services that are widely deployed in the market should be standardized with high priority.

- Technical difficulty - the level of standardization effort should be considered.

- Consistency – the results of each profile should be aligned with the results of other profiles.

- Compatibility – as a result of profiling process, there will be end devices and networks having different capability sets.  The end device is expected to be used in the network with different capability set.  Thus, the capability set of latter profile should include all the capabilities of previous profiles.

I.2. 	Description of each profile

Table I-1shows the characteristics of each profile on user perspectives. In profile 1, users may recognize the IPTV service as terrestrial/cable/satellite digital TV service providing CoD service.   In profile 2, users may recognize the IPTV service as internet service enabled TV.  Users access web applications and internet content with IPTV end devices.  Complete set of IPTV service that satisfying all the requirements are provided in profile 3.

Table I-1: Profiles on User Perspectives

|  | Profile 1 | Profile 2 | Profile 3 |
| --- | --- | --- | --- |
|  | TV/CoD over IP Network | Internet Service Enabled TV | Complete IPTV on NGN |
| Service Category | Linear/Broadcast TV Content On Demand | Web Services Interactive Data Services | Telephony Services Converged Service Mobile IPTV Service |
| Content Diversity | SP Provisioned Content | 3rd Party Content Internet Content User Created Content |  |
| Interactivity | Content Selection/View (Play/Pause) | Various Content Manipulation (Search, Save, Copy, Transfer, …) Internet Services | Telephony |

End devices are classified into five profiles on their service capability.  End devices will be implemented with different profiles.  Thus, compatibility between different profiles is required.

Table I-2:  End Device Profile

|  | Profile 1 | Profile 2 | Profile 3 |
| --- | --- | --- | --- |
|  | Minimal 1 | Minimal 2 | Basic | Enhanced | Full |
| Channel | X |  | X | X | X |
| CoD |  | X | X | X | X |
| Interactive Data and /or Storage |  |  |  | X | X |
| Telephony |  |  |  |  | X |

Table I-3 lists the deliverable services for each profile.

Table I-3: Services for each Profile

| 1st Level | 2nd Level | Profile 1 | Profile 2 | Profile 3 |
| --- | --- | --- | --- | --- |
| Content | Channel | Linear/Broadcast TV and Audio Broadcast Ad. | Trick Mode PPV NPVR Multi-angle PVR Content Sharing User Created Channel 3rd Party Channel | Mobile IPTV Targeted Ads |
|  | On Demand | Real/Near Content on Demand | Push Content on Demand User Created Content 3rd Party Content | Mobile IPTV |
|  | Content Navigation | EPG Content Advisory | IPG IPTV/Internet Portal |  |
| Interactive Data |  | Internet Access E-mail Chat Presence Interactive Ad. T-Information(news, weather, transportation, government) T-Entertainment(game) T-Commerce(banking, shopping, ticketing,) | Location-based Service |
| Telephony-based |  |  | SMS Caller ID Voice Call/conference Video call/conference Converged Service |

Table I-4 summarizes the target environment and required functionalities for each profile.

[Note] Interfaces and signalling protocols between each domain are not classified here.  Priorities and capabilities on interfaces and signalling protocols are needed for describing architectural aspects.

Table I-4: Target Environment and Required Functionalities

|  | Profile 1 | Profile 2 | Profile 3 |
| --- | --- | --- | --- |
| Target End Device | STB without storage | PC / STB with storage | PC/STB/Mobile device with storage |
| Target Network Infrastructure | Wired IP network | Wired/wireless IP network | NGN including mobile network |
| Target Network QoS Model | Best-effort or Diffserv | SLA-based QoS control | NGN QoS control |
| Security Aspects | Content security(select/view only) Service security | Content security(various manipulations) End device security | Network security |
| QoS/Performance Aspects | Dedicated/Provisioned QoS | Dynamic QoS | Dynamic QoS on NGN QoE/Performance monitoring |
| Middleware Aspects | Content metadata | Content delivery/ licensing metadata Content provisioning | User metadata |
| End System Aspects | A/V format Terminal management | Remote management Home networking |  |
| Network Control Aspects | Identification Stream control Transport packet format | Content distribution Session control | Multicast network control |

Appendix II: Input events

(This Appendix does not form an integral part of this document)

This appendix includes material for further consideration by the IPTV-GSI.

A number of input events have been identified and can be found in some specifications as follows:

In GEM 1.0.2 specification, clause G.5, “Input events”, in Annex G specifies that the minimum set of input events which shall be available to the applications if they are interested in receiving them. The defined minimum set of input events by inclusion of the clause G.5 of MHP 1.0.3 specification are as follows;

VK_0 to VK_9

VK_UP

VK_DOWN

VK_LEFT

VK_RIGHT

VK_ENTER

VK_TELETEXT

VK_COLORED_KEY_0

VK_COLORED_KEY_1

VK_COLORED_KEY_2

VK_COLORED_KEY_3

Among these input events, GEM based terminal specifications are allowed to make optional the VK_TELETEXT and VL_COLORED_KEY_3 input events.

This can be found in clause G.5, “Input events”, in Annex G of ARIB STD-B23 with following text;

This clause conforms to GEM1.0 “G.5 Inputs events”, Note that VK_TEKETEXT shall not be used. Form mapping of actual buttons to remote controller and so on, it shall be specified in operational guideline.

In Addition, similar definition for support of a user input events can be found in clause 5.4.13.4 of ARIB STD-B24, Vol.2 that defines a declarative content format and its middleware.

However no agreement was possible on the proposed minimum set of input events listed in the following table.

Table II-1: Proposed minimum set of input events

Input event

Digit from 0 to 9 Direction of up, down, left and right Determination of a choice (ENTER) 3 special buttons (Colored buttons)

Appendix III:  Example of assignment of input events

For information, Table A.1 shows relationship between minimum set of input events listed in Table 1 and middleware for procedural and declarative content format. GEM is chosen for procedural content format case and BML for declarative one as examples.

Table III-1: Example of assignment of input events

| Input event | GEM | BML |
| --- | --- | --- |
| Digit from 0 to 9 | VK_0 to VK_9 | “numeric-tuning” keygroup of used-key-list attribute. |
| Direction of up, down, left and right | VK_UP VK_DOWN VK_LEFT VK_RIGHT | “basic” keygroup of used-key-list attribute. |
| Determination of a choice (ENTER) | VK_ENTER | “basic” keygroup of used-key-list attribute. |
| special buttons (Colored buttons) | VK_COLORED_KEY_0 VK_COLORED_KEY_1 VK_COLORED_KEY_2 VK_COLORED_KEY_3 | “data-button” keygroup of used-key-list attribute. |

Note 1: GEM-based terminal specifications are allowed to make optional the VK_COLORED_KEY_3 input event.

Note 2: BML defines used-key-list attribute that is a part of CSS properties to request input event available for interactive content.

Appendix IV: Services navigation systems

(This Appendix does not form an integral part of this document)

This appendix includes material for discussion on service navigation systems. Although the IPTV FG did not have time to reach an agreement, it was felt valuable to keep it to be the basis for further discussion in the IPTV GSI.

The material in this appendix may be a candidate to be incorporated in the main body of this document or be considered to form an independent document after further work.

______________________