## Slide 1: Interoperability Issues in Public Safety Trunking Mobile Networks
R.K. Siddhartha,
Addl. Director, DCPW
Ministry of Home Affairs
INDIA

## Slide 2: Outline
Public Safety Mobile Networks
Deployment Scenarios and Case Study
Standards and interoperability
Proposal

## Slide 3: Public Safety Trunking Mobile Networks
Radio communications used by responsible agencies and organizations dealing with maintenance of law and order, protection of life and property, and emergency situations.
-Complex Features and Functionalities need to be provided by a Public Safety Trunking Mobile Network

## Slide 4: Public Safety Trunking Mobile Networks-2
- Group management,
- Dynamic Group Number Assignment,
Emergency,
- DMO
- Pre-emptive Priority,
- Enable/Disable Handset,
- End-to-End Encryption,
- Air Interface Encryption (Static, Derived & Group Cipher Keys )
Resulting in-
Complexity adds development cost
Magnified by the limited market

## Slide 5: ITU in Public Safety Network Standardization
-ITU-R : Radio Sector
Rep. M.2014 lists a number of
technologies, and their RF parameters
e.g. TETRA/APCO/DMR etc.
-ITU-T : Standardization Sector
Standards/Recommendations?

## Slide 6: Deployment Scenarios in Developing Countries
Deployment of Trunking Radio Mobile Network in a Phased manner
2. Interconnection of Different networks
is required for Mission Criticality of
operations
3. Integration with Existing Radio
Network systems

## Slide 7: Case Study- 1 Public Safety Trunking Mobile Network based on Standard
A Trunking Radio Public safety Network based on an Open standard, was deployed in a City(INDIA)
An expansion of deployed Network was required after about two year time to extend the coverage to adjacent City/Suburban Areas
The Incumbent Equipment Vendor quoted very
unreasonably hefty cost
(there was a catch)
The second vendor was chosen for expanding deployed network/coverage. The vendor deployed the network within a reasonable cost.
(again there was a catch)

## Slide 8: Non Implementation of Interface for interconnection
GW
The catch was
First vendor knew, that expansion of the network can only be carried out with his own equipment!
The second vendor was also in the know that two networks cannot interconnect ! (later passed on blame)
Inter Network Interface of Standard not implemented by vendors

## Slide 9: Case Study-2 Interconnection on IP
An integration of
Standards based
(Same Technology)
Public Safety mobile networks
Of Different Vendors was
Envisaged by Connecting
them on Core IP.
-Even a Basic Individual Voice Call
from One Vendor Network to another not compatible
Reason being Use of incompatible payload type
X

## Slide 10: Interoperability in Public Safety Mobile Networks?
Currently makeshift arrangement is used for interoperability between two or more incompatible Radio Systems.
Analogue Patching Between Networks:
This functionality is required when terminals from one network need basic group call communications with terminals operating on another network.
This solution has already been deployed using a Generic 4-Wire Interface (G4WIF) between consoles from each of the different networks

## Slide 11: Case example – Bespoke Solutions for a Standardized Interface
The TETRA standard is a suite of standards -
Air interfaces,
Network interfaces,
Mission critical functions, services and facilities
Standardization began in 1990s, TETRA Inter-
System Interface (ISI) is rarely implemented
Bespoke solutions for connecting equipments from
different vendors whilst avoiding the need for a
full ISI (Interservice Interface)

## Slide 12: Standards are for Interoperability
Do they in the abstract deliver the benefits of
compatibility, modularity and interoperability?
Greater interoperability is an important
benefit of standards
Interoperability comes from conforming standards
but if standards are not implemented there is no
conformance
Proprietary Networks could have given the
same scenario as absence of Interoperability

## Slide 13
Risks with Proprietary solutions
vendor lock-in
discontinued product Lines
ongoing licensing costs
Systems with high interoperability have
lower equipment costs
lower transactions costs
higher competition between equipment
suppliers higher productivity through
automation
more innovation of technology and
applications
Standards are for Interoperability -2

## Slide 14: Defining Compatibility Levels in Standards
DYNAMIC BEHAVIOUR |  |  |  |  |  | INTERCHANGEABLE
APPLICATION FUNCTIONALITY |  |  |  |  | INTEROPERABLE | 
PARAMETER SEMANTICS |  |  |  |  |  | 
DATA TYPE |  |  |  | INTER WORKABLE |  | 
DATA ACCESS |  |  | INTER CONNECTABLE |  |  | 
COMMUNICATION INTERFACE |  |  |  |  |  | 
COMMUNICATION PROTOCOL |  | CO- EXISTENCE |  |  |  | 
source: IEC TC 65/290/DC

## Slide 15: Defining Compatibility Levels-2
Incompatibility : Inability of two or more devices to work together in the same application
Coexistence: Ability of two or more devices operate independently of one another in the same communication network
Interworkability: Ability of two or more devices to support transfer of device parameters
Interoperability: Ability of two or more devices to work together in one or more application
Interchangeability :Ability of two or more devices to replace each other in working together in one or more applications

## Slide 16: Difficulties in Conforming to Standards
  Misinterpretations
  Various implementation options
  Over specification/Under-specification
  Flexibility - for consensus
  Not comprehensive - cross references

## Slide 17: Feedback Mechanism from Interoperability Testing
IMPLEMENTAIONS
STANDARDS
INTEROPERABILITY
TESTING
FEEDBACK FLOW
Standard Framing must be a Dynamic and Living process for achieving Interoperability

## Slide 18: Proposal
To fulfill deployment needs of developing countries
Standards for facilitating Interoperability in Public
Safety Mobile networks be framed within the
ambit of ITU-T
A collaborative approach of standardization
with Radio Sector of ITU can be envisaged for
Radio networks

## Slide 19: Thank you for your kind attention! rksiddhartha@dcpw.gov.in