RECOMMENDATION  ITU-R  BT.1124-1

REFERENCE  SIGNALS  FOR  GHOST  CANCELLING  IN  TELEVISION

(Question ITU-R 55/11)

(1994-1995)

Rec. ITU-R BT.1124-1

The ITU Radiocommunication Assembly,

considering

a)	that a ghost cancelling system using a ghost cancelling reference (GCR) signal is one of the most effective countermeasures for ghost images in individual and collective antenna reception of television signals;

b)	that the system should be effective for cancelling multiple and long delayed ghost images as well as short delayed ghost images and it should be also effective for leading ghosts and waveform equalization of video signals;

c)	that the GCR signals can be inserted into the lines in the vertical blanking intervals;

d)	that for each television system an appropriate GCR signal can be defined;

e)	that for each country the appropriate GCR signal can be used to suit the various propagation conditions and the types of transmission media;

f)	that the ghost canceller using the GCR signals can be manufactured at a reasonable cost,

recommends

1	that the GCR signal should be a dedicated reference signal optimized for ghost cancelling;

2	that the GCR signal should allow the rapid determination of the channel response even under poor signal-to-noise conditions;

3	that the GCR signal must be able to provide a flat amplitude and linear group delay response versus frequency over the entire passband of each system;

4	that the GCR signal should make efficient use of the vertical interval resources;

5	that for conventional television systems, a broadcaster wishing to integrate a GCR signal should use a GCR signal complying with the specifications given in Annex 1 for:

–	System A,

–	System B,

–	System C;

6	that for advanced television systems, a broadcaster wishing to integrate a GCR signal should use a GCR signal complying with the specifications given in Annex 2 for:

–	HD-MAC, D-MAC and D2-MAC;

–	MUSE.

ANNEX  1

GCR signal specifications for conventional TV systems

1	Introduction

System A has been standardized, and used extensively in Japan since 1989.

System B is undergoing trial transmission and will become a standard for NTSC in Korea in January 1994.

System C is an ATSC standard for NTSC in the United States of America and is being adopted as a standard in Canada. It is in use in both these countries. Standardization is being evaluated for PAL, SECAM 625-line systems in Europe and in Australia and New Zealand.

1.1	System A

Requirements for the GCR signal relevant to the NTSC system are specified in Tables 1 and 5 and Figs. 1 to 3.

TABLE  1

Specifications of GCR waveform

| Specifications (output point of the GCR signal inserter) |
| --- |
| Notes, other information |
| Reference values | Tolerance values |
|  | 1 | Amplitude | 70% | ± 2% | Difference between the set-up level in the effective horizontal scan period and the central point level of the bar width of the GCR waveform. |
| 2 | Set-up | 0% | ± 2% | Difference between the pedestal level in the horizontal blanking line period and the effective horizontal scan line period. |
| 3 | Width | 160 sc (44.7 ms) | ± 1.0 sc (± 0.28 ms) | Time from the 50% point of the GCR waveform rising edge to the 50% point of its trailing edge. |
| 4 | Position | 60 sc (16.76 ms) | ± 1.5 sc (± 0.42 ms) | Time from the 50% point of the horizontal synchronous pulse trailing edge to the 50% point of the GCR waveform rising edge. |
| 5 | Rising edge characteristics |

(as shown in Fig. 3)

The waveform integrated by one clock at the  sample after

| the pulse is multiplied by the window function. |
| --- |
| 6 | Trailing edge characteristics | 0.25 ms (2T bar) | ± 0.05 ms | Time from the 10% point to the 90% point of the trailing edge (2T characteristics for the slope). |
| 7 | Phase against colour burst | 0°(1) | ± 40° | Phase relationship between the 50% point of the GCR waveform trailing point and the colour sub-carrier synchronous to the colour burst. |

sc:	sub-carrier cycles

(1) Specified at the output point of the GCR signal generator. Not specified at the output point of the GCR inserter unless necessary.

FIGURE 1/BT.1124-1...[D01] = 3 CM

TABLE  2

Specifications of zero-pedestal waveform

| Items | Specifications (output point of the GCR signal inserter) |
| --- | --- |
| Notes, other information |
|  | Reference values | Tolerance values |
|  | Set-up | 0% | ± 2% | Difference between the pedestal level in the horizontal blanking line period and the set-up level of the effective horizontal scan line period. The difference with the set-up level of the GCR waveform is 0.5 IRE or less. |

FIGURE 2/BT.1124-1...[D02] = 3 CM

FIGURE 3/BT.1124-1...[D03] = 3 CM

TABLE  3

Insertion line

| Insertion line numbers | 18 and 281 |
| --- | --- |

TABLE  4

Constraints of previous line

| Field numbers |
| --- |
|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| A | B | C | D | A | B | C | D |
| A, B, C, D: same or different fixed waveform |

TABLE  5

Field-to-field sequence

| Field numbers | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Waveform(1) | GCR | 0 | GCR | 0 | 0 | GCR | 0 | GCR |
| (1) GCR: GCR waveform 0: zero-pedestal waveform |

1.2	System B

The GCR signal is the ternary sequence (TS) of length 366 and consists of two GCR signal waveforms of opposite polarity. They are derived from a low-pass filtered sequence of length 366 with an appropriate cutoff frequency, each riding on a pedestal of 30 IRE units. To eliminate the effects of the colour bursts, synchronizing signals and the preceding and following VBI line signals, the signal is transmitted in a four-field sequence consisting of two pairs of pairwise identical waveforms.

Requirements for the GCR signal are specified in Tables 6 to 8 and Figs. 4 and 5.

TABLE  6

Ternary sequence of length 366

| 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | -1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | -1 | 0 | 1 | 0 | 0 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 |
| -1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 |
| 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 |
| 1 | 0 | -1 | 0 | -1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | -1 |
| 0 | 1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| -1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 |
| -1 | 0 | 0 | 0 | -1 | 0 | 0 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 |
| 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 |
| -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 |
| -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 1 |
| 0 | -1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 |
| -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 0 | 0 | -1 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | -1 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 |
| 1 | 0 | 0 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 |
| 0 | -1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 |
| 1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 |
| 0 | -1 | 0 | -1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |
| -1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 | 1 | 0 | -1 | 0 | -1 |
| 0 | 1 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | -1 | 0 | -1 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 | 0 |

TABLE  7

Transmission sequence of GCR signal

| Signal waveform | S1 | S2 | S3 | S4 |
| --- | --- | --- | --- | --- |
| Field number | 1 | 2 | 3 | 4 |
| Colour burst phase | + | - | - | + |
| GCR signal polarity | - | + | - | + |

TABLE  8

Procedure for channel characterization at the receiver

| Step | Processing algorithm |
| --- | --- |
| 1 | SDATA = (-S1 + S2 - S3 + S4) / 4 |
| 2 | SDATA* TS |
| 3 | Channel characterization result |

S1 to S4:	received signal waveforms

TS:	ternary sequence

*: correlation

FIGURE 4/BT.1124-1...[D04] = 3 CM

FIGURE 5/BT.1124-1...[D05] = 3 CM

1.3	System C

Requirements for the ghost cancelling reference (GCR) signal are described below. Specific parameters for 525- and 625-line NTSC, PAL and SECAM television systems (see Note 1) are set out in Table 9.

NOTE 1 – Correct operation of the motion adaptive colour plus (MACP) process used by the PALplus system relies on the fact that points separated by 312 lines within a frame have a precise phase relationship. In order to avoid disturbing this relationship, any changes to the equalization of the signal applied by a ghost canceller located in either the transmission or reception chain should preferably be made during the period of lines 624 to 22.

The GCR signal is placed on a single line in the vertical blanking interval, on one line per field in 525-line systems, and on one line per frame (two fields) in 625-line systems.

The GCR signal has a flat spectrum and high energy up to the frequency f1 and has low energy beyond the frequency f2. The values of f1 and f2 are shown in Table 9. Figure 6 shows the spectrum of the GCR signal. The normalized GCR signal as a function of time is shown in Fig. 7.

In 525-line systems, the GCR signal is placed on line 19 (and the corresponding line in the following field). In 625-line systems, the GCR signal is preferably placed on line 318, with the preceding line 317 containing no time-varying information. For both 625- and 525-line systems the line immediately preceding the GCR line should preferably not contain time varying information to avoid constraining the performance of ghost cancellers.

To provide efficient cancellation of 625-(525)-line systems requiring post ghost cancellation ranges greater than approximately 38 (31) m

# Comments

Page: 15
Attention, le format § des énumérations suivantes a été réduite à Before 2pt pour une meilleure MEP.