RECOMMENDATION  ITU-R  P.839-1

RAIN  HEIGHT  MODEL  FOR  PREDICTION  METHODS

(Question ITU-R 201/3)

(1992-1997)

Rec. ITU-R P.839-1

The ITU Radiocommunication Assembly,

considering

a)	that knowledge of the height of the 0° C isotherm during rainy conditions is required in several prediction models used in the design of space telecommunication systems,

recommends

1	that the following model be used for the global estimation of h0 (mean 0° C isotherm height):

| h0 = |  |
| --- | --- |

for	j  >  –23	Northern Hemisphere

for   —0  £	j  £  –23	Northern Hemisphere

for   —0  ³	j  ³  –21	Southern Hemisphere

for   –71  £	j  <  –21	Southern Hemisphere

for j < –71 Southern Hemisphere

where h0 is in km above mean sea level and j is the latitude in degrees;

2	that for North America and Europe west of 60° E longitude the following model be used for the estimation of hFR (mean 0° C isotherm height during rainy conditions):

hFR  =  3.2  –  0.075 (j  –  35)               for       35  £  j  £  70

where hFR is in km above ground;

3	that for other areas in the world, where no further information is available, hFR be equated to h0.

NOTE 1 – hFR, in general, is different from h0. The sign and magnitude of the difference is dependent on climatic conditions.