RECOMMENDATION  ITU-R  S.1715

Guidelines developed in response to the studies requested
in Resolution 140 (WRC-03)

(2005)

The ITU Radiocommunication Assembly,

considering

a)	that Article 22 of the Radio Regulations (RR) contains epfd( limits on non-GSO FSS systems which, if met, protect GSO FSS networks from unacceptable interference;

b)	that in the development of RR Article 22 epfd( limits for the 20 GHz FSS band, different considerations were made for the lower portion of the band (17.8-18.6 GHz) as compared to the upper portion (i.e. 19.7-20.2 GHz) of the band;

c)	that the temporal characteristics of the interference caused to GSO FSS networks by certain types of non-GSO FSS systems may be significantly different than those caused by other types of non-GSO FSS systems;

d)	that any non-GSO FSS use of the band 19.7-20.2 GHz is subject to RR No. 5.484A;

e)	that protection of GSO FSS networks in the band 19.7-20.2 GHz from unacceptable interference may be able to be provided by a certain type of non-GSO FSS1 system that does not meet the epfd( limits in RR No. 22.5C (Table 22-1C) subject to the agreement of the affected administration(s) under RR No. 22.5CA;

f)	that Resolution 140 (WRC-03) invited ITU-R to develop “criteria which would protect GSO FSS networks in the band 19.7-20.2 GHz from unacceptable interference by HEO FSS systems taking account of the combined effect of interference into downlinks of the GSO FSS networks from HEO FSS systems and other non-GSO FSS systems”;

g)	that Resolution 140 (WRC-03) invited administrations “to consider using the relevant ITU-R Recommendations regarding the protection of GSO FSS satellite networks from interference by non-GSO FSS systems as a guideline for consultation between administrations, to fulfil their obligations under RR No. 22.2 in the band 19.7-20.2 GHz, and in the case where an administration responsible for a non-GSO FSS system requests the application of RR No. 22.5CA”,

noting

a)	that GSO FSS networks with specific receive earth stations having very large antennas and non-GSO FSS systems operating in the 19.7-20.2 GHz frequency band are subject to coordination under RR No. 9.7A and No. 9.7B, as specified in Table 5-1 of RR Appendix 5;

b)	that in order to provide the required protection to GSO FSS networks, the long-term portion of the epfd( limits in RR Article 22 in the 19.7-20.2 GHz band is about 15 dB more stringent than the corresponding limit in the 17.8-18.6 GHz band;

c)	that the effect on co-frequency sharing between non-GSO FSS systems of having some non-GSO FSS systems meet the RR Article 22 epfd limits and having other systems meet the levels included in this Recommendation has not yet been evaluated,

recommends

1	that the following guidelines could be applied in the event that an administration planning a certain type of non-GSO FSS system for operation in the 19.7-20.2 GHz band, which system does not meet the epfd( limits specified in RR No. 22.5C (Table 22-1C) for this band, requests the application of RR No. 22.5CA in connection with Resolution 140 (WRC-03) with respect to its system:

–	that any such system should provide protection to GSO FSS networks equivalent to that provided by the single entry epfd( limits specified in Table 22-1C of RR No. 22.5C for this band;

–	that the set of epfd( masks shown in Table 1, which has been derived for a certain type of non-GSO FSS system that does not otherwise meet the epfd( limits in the 19.7-20.2 GHz band based on the objective of providing, to GSO FSS networks, protection equivalent to that provided by the epfd( masks contained in RR No. 22.5C (Table 22-1C), may be taken into consideration by an administration receiving such a request for application of RR No. 22.5CA, subject to its agreement, in any discussions concerning the possible application of RR No. 22.5CA;

2	that administrations take note that, if they agree to permit a non-GSO FSS system to operate at the epfd( levels of Table 1 on their territory, they are also agreeing (see Note 1), under resolves 2 of Resolution 76 (WRC-2000), to a level of aggregate epfd( on their territory caused by all non-GSO systems (including those indicated in recommends 1) that is higher than the corresponding level in Table 1C of Resolution 76 (WRC-2000) by an amount which accommodates the higher epfd( levels in Table 1 in addition to the epfd( caused by systems operating in compliance with the single entry epfd( limits in Table 22-1C of RR No. 22.5C;

3	that the following Notes be considered as part of this Recommendation.

NOTE 1 – The single entry epfd( levels in Table 1 are higher than the aggregate long-term limits in Table 1C of Resolution 76 (WRC-03).

NOTE 2 – This alternative Table is not meant to be considered in conjunction with the epfd( limits of RR Article 22, but instead is to be used on its own in situations where a non-GSO FSS system does not meet the epfd( limits and application of RR No. 22.5CA is requested.

NOTE 3 – Administrations operating or planning to operate non-GSO FSS systems that would rely on RR No. 22.5CA and this Recommendation for use of the 19.7-20.2 GHz band should not request protection or accommodation in intersystem coordination with other co-frequency non-GSO FSS systems that do not rely on RR No. 22.5CA at levels beyond those which a system that meets the applicable limits could request.

TABLE 1

An illustrative example of the single-entry epfd( radiated by a certain type 
of non-GSO satellite system in the FSS
in the frequency band 19.7-20.2 GHz

| Frequency band (GHz) | epfd( (dB(W/m2)) | Percentage of time during which epfd( may not be exceeded | Reference bandwidth (kHz) | Reference antenna diameter and reference radiation pattern (1) |
| --- | --- | --- | --- | --- |
| 19.7-20.2 | –172.4 | 100 | 40 | 70 cm Recommendation ITU-R S.1428 |
|  | –158.4 | 100 | 1 000 |  |
|  | –174.0 | 100 | 40 | 90 cm Recommendation ITU-R S.1428 |
|  | –160.0 | 100 | 1 000 |  |
|  | –182.8 | 100 | 40 | 2.5 m Recommendation ITU-R S.1428 |
|  | –168.8 | 100 | 1 000 |  |
|  | –187.6 | 100 | 40 | 5 m Recommendation ITU-R S.1428 |
|  | –173.6 | 100 | 1 000 |  |
| (1) For this Table, reference patterns of Recommendation ITU-R S.1428 should be used only for the calculation of interference from non-GSO satellite systems in the FSS into GSO satellite networks in the FSS. |

# Footnotes

1	Non-GSO FSS systems with an inclination between 35° and 145°, an apogee greater than 18 000 km, operating in a limited active arc, and not meeting the epfd( limits in RR No. 22.5C (Table 22-1C).