|  | INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- | --- |
|  | RADIOCOMMUNICATION STUDY GROUPS | Document 4/49(Rev.1)-E |
|  |  | 2 November 2004 |
|  |  | Original: English |

Source:	Documents 4A/78 (Annex 22) and 4A/TEMP/40(Rev.2)

Working Party 4A

REVISION of RECOMMENDATION ITU-R S.731

Reference earth-station cross-polarized radiation pattern
for use in frequency coordination and interference assessment
in the frequency range from 2 to about 30 GHz

(1992)

The ITU Radiocommunication Assembly,

considering

a)	that, for coordination studies and for the assessment of mutual interference between radiocommunication-satellite systems and between earth stations of such systems and stations of other services sharing the same frequency band, it may be useful to use a cross-polarized radiation pattern for the earth-station antenna;

b)	that, for the determination of coordination distance and for the assessment of interference between earth and terrestrial stations, a cross-polarized radiation pattern based on the level exceeded by a small percentage of the side-lobe peaks may be appropriate;

c)	that, a reference earth-station co-polarized radiation pattern for use in frequency coordination and interference assessment is contained in Recommendation ITU-R S.465;

d)	that some measurements have been made of the cross-polarized off-axis gain performance of earth stations and radiation patterns have been developed which are quantitively similar;

e)	that a single cross-polarized off-axis reference pattern can be used which includes those contained in Annex 1;

f)	that the use of antennas with the best achievable radiation patterns will lead to the most efficient use of the radio-frequency spectrum and the geostationary-satellite orbit,

recognizing

1	that further measured information on cross-polarization performance is desirable;

2	that the measured off-axis gain performance of earth-station antennas contains the cross-polarization emission from the source antenna;

3	that the cross-polarized radiation patterns are measured in the main beam of the source antenna,

recommends

1	that, in the absence of particular information concerning the cross-polarized radiation pattern of the antenna for the earth station involved, a single reference radiation pattern may be used for:

1.1	frequency coordination studies and interference assessment between earth stations in the fixed-satellite services and stations of other services sharing the same frequency band;

1.2	coordination studies and interference assessment between networks in the fixed-satellite service;

2	that the following cross-polarized radiation pattern may be used on an interim basis for angles between the directions considered and the axis of the main beam, for frequencies in the range 2-30 GHz:

Gx()  =  23  –  20 log 	dBi	for  r	      7°

Gx()  =  20.2  –  16.7 log 	dBi	for  7°	      26.3°

Gx()  =  32  –  25 log 	dBi	for          48°

Gx()  =  –10	dBi	for  	      180°

r is equal to 1° or 100 /D, whichever is greater;

3	that the following Notes should be regarded as a part of this Recommendation.

NOTE 1 – The reference cross-polarized radiation pattern should be assumed to be rotationally symmetrical.

NOTE 2 – The reference cross-polarized pattern should be used for cases involving opposite polarizations.

NOTE 3 – Other cross-polarized radiation patterns of earth stations may be used by mutual agreement between the administrations concerned.

NOTE 4 – The reference radiation pattern should be used with caution over the range of angles for which the particular feed system may give rise to relatively high levels of spill-over and for antennas with D/λ less than 50.

NOTE 5 – This cross-polarized radiation pattern complements the co-polarized pattern of Recommendation ITU-R S.465.

NOTE 6 – Annex 1 contains several cross-polarized off-axis radiation patterns corresponding to the envelopes of the peaks of the measured gain characteristics of various antennas, in support of recommends 2.

ANNEX  1

Modelling of earth-station antenna cross-polar characteristics

This Annex presents background information used to develop cross-polarized patterns obtained for theoretical and measured patterns. Pattern measurements were obtained for different antenna diameters (1.2 m, 1.8 m, 2.4 m, 3.5 m at 12.625 GHz, and 3.7 m at 10.7 GHz). For each antenna diameter, the relative measured and envelope patterns are described. Equations are then derived which describe the relative cross-polarized envelopes for antennas with D/  100 and D/  100. A single function is developed which can be used to describe the off-axis cross-polarized pattern for all antennas.

Calculated co-polarized and cross-polarized patterns for single offset feed antennas are shown in Figs. 1 and 2 along with the respective envelope functions. The effects of feed supports for axisymmetric arrangements are shown in Fig. 3.

In order to estimate the worst-case polarization discrimination (factor of polarization isolation), the relative co-polarized G//(φ) and cross-polarized G+(φ) envelopes have been obtained.

a)	The relative co-polarized envelope used in this Annex is assumed as follows:

For systems with D/λ ≤ 100,

G//(φ) 	= 52 – 10 log (D/λ) – 25 log φ – G0		dBi 	for  (100 λ/D)° ≤ φ ≤ 48°

= 10 – 10 log (D/λ) – G0 			dBi	for  48° 	 < φ ≤ 180°

For systems with D/λ > 100,

G//(φ) 	= 32 – 25 log φ – G0				dBi 	for  1°		 ≤ φ ≤ 48°

= –10 – G0					dBi	for  48° 	 < φ ≤ 180°

b)	The cross-polarization level is such that G+(φ) = G// (φ1') (with φ1' = 2.2φ1 for small antennas, and φ1' = 1.8φ1 for large antennas) for 0° < φ < φ1.

Finally, the relative cross-polarized envelopes could have the following envelopes:

# 1	Small antennas (D  100)

G0 =	 maximum co-polarized gain of antenna  (dBi)

G(φ) =	 52 – 10 log (D/λ) – 25 log φ – G0 (dBi)

φ1 = 	100 λ/D (degrees)

φ1' = 	2.2 φ1 (degrees)

φ2 = 	25.1º

φISO =   (degrees)

for 0 < φ ≤ φ1,

(1)

for φ1 < φ ≤ φ2,

(2)

if φ > φISO,

(3)

for φ2 < φ ≤ 180º,

G+(φ) = 10 – 10 log (D/λ) – G0	(4)

The patterns shown in Figs. 4 and 6 are calculated for stations with antenna diameters of 1.20 m and 1.80 m operating at a centre frequency of 12.625 GHz. The patterns measured for these types of antennas are shown in Figs. 5, 7 and 8. In each case one example of the measured co- and cross-polarized pattern is given, but the envelopes shown are averages from measurements on several antennas of the same type.

FIGURE 4

1.2 m antenna, f = 12.625 GHz, relative co- and cross-polar calculated patterns

FIGURE 5

1.2 m antenna, f = 12.625 GHz, relative co- and cross-polar measured patterns

FIGURE 6

1.8 m antenna, f = 12.625 GHz, relative co- and cross-polar calculated patterns

FIGURE 7

1.8 m antenna, f = 12.625 GHz, relative co-polar measured pattern

FIGURE 8

1.8 m antenna, f = 12.625 GHz, relative cross-polar measured pattern

# 2	Large antennas (D  100)

G0 = maximum co-polarized gain of antenna (dBi)

G(φ) = 29 – 25 log φ – G0 (dBi)

φ1 = 1º

φ1' = 1.8 φ1 (degrees)

φ2 = 20º

φ3 = 33.1º

φISO = = 14.45º

for 0 < φ ≤ φ1,

(5)

for φ1 < φ ≤ φ2,

(6)

for φ2 < φ ≤ φ3,

G+(() = 32 – 25 log ( – G0	(7)

for φ3 < φ ≤ 180º,

(8)

The patterns shown in the Figures below are calculated for stations with the following antenna diameters and frequencies: 2.40 m and 3.50 m at 12.625 GHz, and 3.70 m at 10.70 GHz. The patterns measured for these types of antennas are shown in Figs. 10, 11, 13, 14, 16 and 17. In each case, one example of the co- and cross-polarized measurements is shown, but the envelopes given were derived from the average of several antennas of the same type.

The functions given above for D  100 and D  100 can be expressed in terms of absolute gain. The functions given for D  100 can be normalized to a (32 – 25 log ( co-polar function by letting (52–10 log  equal 32. Evaluation of these functions as absolute gain for various values of D/ is as follows:

Gx()	=  22.70  +  0.29   –  25 log 	dBi	for  D    25	(9)

=  22.69  +  0.37   –  25 log 	dBi	for  D  =  50	(10)

=  22.87  +  0.42   –  25 log 	dBi	for  D    75	(11)

=  22.15  +  0.47   –  25 log 	dBi	for  D    100	(12)

The angles at which these gain functions are equal to a co-polar envelope gain of (32 – 25 log ( are   21.4° and 20.8° respectively. Additional functions which have been developed are:

Gx()	=  20  –  21 log 	dBi		(13)

Gx()	=  23.6  –  20 log 	dBi		(14)

Gx()	=  22  –  25 log 	dBi		(15)

Equation (15) is based on a requirement that the cross-polar gain be 10 dB less than the co-polar gain out to 7°

These functions are plotted in Fig. 18. From this Figure, a single function which adequately covers all the above functions is:

G()	=  23  –  20 log 	dBi	for  r	      

=  20.2  –  16.7 log 	dBi	for  	      

=  32  –  25 log 	dBi	for          

=  –10	dBi	for  	      

r is equal to 1° or 100 /D, whichever is greater.

FIGURE 9

2.4 m antenna, f = 12.625 GHz, relative co- and cross-polar calculated patterns

FIGURE 10

2.4 m antenna, f = 12.625 GHz, relative co-polar measured pattern

FIGURE 11

2.4 m antenna, f = 12.625 GHz, relative cross-polar measured pattern

FIGURE 12

3.5 m antenna, f = 12.625 GHz, relative co- and cross-polar calculated patterns

FIGURE 13

3.5 m antenna, f = 12.625 GHz, relative co-polar measured pattern

FIGURE 14

3.5 m antenna, f = 12.625 GHz, relative cross-polar measured pattern

FIGURE 15

3.7 m antenna, f = 10.7 GHz, relative co- and cross-polar calculated patterns

FIGURE 16

3.7 m antenna, f = 10.7 GHz, relative co-polar measured pattern

FIGURE 17

3.7 m antenna, f = 10.7 GHz, relative cross-polar measured pattern

FIGURE 18

Absolute cross-polar side-lobe antenna gain pattern

G1(φ)	=	22.70 + 0.29φ – 25 log φ	(for D/λ = 25)

G2(φ)	=	22.69 + 0.37φ – 25 log φ	(for D/λ = 50)

G3(φ)	=	22.87 + 0.42φ – 25 log φ	(for D/λ = 75)

G4(φ)	=	22.15 + 0.47φ – 25 log φ	(for D/λ = 100)

G5(φ)	=	20.0 – 21 log φ

G6(φ)	=	23.6 – 20 log φ

G7(φ)	=	22.0 – 25 log φ

G8(φ)	=	23.0 – 20 log φ 	for φr 	 ≤ φ ≤ 7°

=	20.2 – 16.7 log φ	for 7° 	 < φ ≤ 26.3°

=	32.0 – 25 log φ	for 26.3° < φ ≤ 48°

G9(φ)	=	32 – 25 log φ

______________