RECOMMENDATION  486-1*

REFERENCE  OF  PRECISELY  CONTROLLED  FREQUENCY  GENERATORS
AND  EMISSIONS  TO  THE  INTERNATIONAL  ATOMIC  TIME  SCALE

(Question 3/7)

(1974-1978)

Rec. 486-1

The CCIR,

CONSIDERING

(a)	that, for a user, data concerning the error of a standard-frequency and time-signal emission are of great importance;

(b)	that the International Atomic Time scale (TAI) has considerable importance as a reference for time and frequency comparisons;

(c)	that, in many cases, it is technically possible to adjust a radiated standard frequency so that the variations of phase with respect to TAI or Coordinated Universal Time (UTC) remain within a narrow tolerance ± Dt, which is small compared to the period of the carrier frequency;

(d)	that the TAI frequency and the UTC frequency are identical;

(e)	that equipment is available which is capable of receiving several nearly synchronous emissions, thereby providing alternative operation in case of transmitter interruption;

(f)	that there is a need for universally accepted reference frequencies for use in electronic systems;

(g)	that there is an ever-increasing need for frequencies of high stability, particularly with regard to data transmission;

(h)	that many new precisely controlled electronic systems (e.g. those controlled by atomic frequency generators) are now coming into use;

(j)	that these systems can be better coordinated if they use a common frequency reference,

UNANIMOUSLY  RECOMMENDS

1.	that the UTC frequency (Ref. Recommendation 460) should be used as the ultimate reference for standard-frequency emissions;

2.	that data concerning the accuracy of the standard frequency, with reference to the UTC frequency, should be an average of the relative frequency difference over 10 days or more;

3.	that the range ± Dt over which the phase of the standard frequency can vary with reference to UTC should be specified for each LF and VLF emission and the values published by the Administrations responsible for the standard time and frequency services;

4.	that the UTC frequency should also be used as the ultimate reference for other electronic systems.

# Footnotes

*	The Director, CCIR is requested to bring this Recommendation to the attention of the CCITT.