## Slide 1: ITU Workshop on the Efficient Use of the Spectrum/Orbit Resource, 14-16 April 2014 The Evolution of Mobile Satellite Applications

## Slide 2: Outline
Evolution of Mobile Satellite Services
Aeronautical applications
Maritime applications
Emergency relief applications
Conclusion

## Slide 3: Evolution of Mobile Satellite Services
Began with MARISAT GSO network (UHF, VSATs operating in L-band)
Big-LEOs (L- and S-band) and Little-LEOs (VHF)
Earth Stations on Vessels and Aeronautical MSS (C-/Ku-band)
Soon Ka-band MSS networks …
Examples of all of these types still operate
Services have evolved from simple (analogue) voice carriers to flexible data / IP channels
Terminals now range from low-rate low-power devices (size of a pack of cards) to multi-megabit high-cost mobile VSATs
Very large multitude of applications…

## Slide 4: Explosion in Applications
Low-rate data:
  Tsunami detection buoys
  Container tracking modules
  Hiker’s safety alert
High-rate data:
  Video/audio streaming
  Internet connectivity
Real-time voice:
  AMS(R)S cockpit comms
  Remote worker safety
  Disaster relief comms

## Slide 5: Iridium NEXT
Iridium operating since 1999, the only satellite network to cover 100% of the earth – from pole to pole
Markets include maritime, aviation, emergency services, oil and gas exploration, forestry, mining, journalism ...
Iridium investing over $2.1bn in their NEXT program
Iridium NEXT will renew the entire satellite network, beginning 2015
NEXT state-of-the-art design will further extend capabilities

## Slide 6
Intersatellite Crosslink
Iridium System
Satellites
Iridium Gateway
Subscriber (Service) Links
Feeder Links
Aircraft users
Handheld users
Terrestrial Phone &
Data Network
Maritime users

## Slide 7: Aeronautical applications
Satellite networks already serve the commercial aeronautical industry:
  Passenger voice and data connectivity
  Machine-to-Machine (M2M) applications for aircraft system monitoring
New applications will include:
  Integrated air-traffic control (AMS(R)S) functionality – reliable cockpit comms beyond reach of VHF
  Satellite ADS-B (Automatic Dependent Surveillance-Broadcast) – extending the tracking of commercial aircraft, for safety and efficiency

## Slide 8: Space-based ADS-B
North America, Europe and elsewhere moving to ADS-B system of aircraft tracking
  Higher degree of accuracy than traditional radar
  Fewer dead spots
  Information received by neighbouring aircraft, as well as ATC
  But reliant on a network of terrestrial receivers …
Aireon is placing ADS-B receivers on Iridium satellites
  Collects the same signals from aircraft (no new aircraft equipment)
  Provides 100% global coverage – including oceans and poles
  Safety: Extends benefits of ADS-B to inter-continental routes
  Efficiency: Environmental benefits from more direct routing
Aireon is a partnership of air navigation service providers, equipment manufacturer/integrators and Iridium – commercial service to begin in 2016

## Slide 9: Maritime applications
First MSS networks developed for the maritime market - initially limited to analogue voice!
Now a wide variety of terminals, for all sizes of vessel:
  Small emergency tracking and alerting units
  Installed voice/data units
  Broadband internet connectivity
New and pending developments
  Long Range Tracking and Identification (LRIT) – permits tracking of commercial shipping vessels by maritime authorities
  Ship Security and Alerting System (SSAS) – transmission of security alerts, to help combat terrorism and piracy
  Expansion of GMDSS – maritime safety system will be expanded to accommodate multiple satellite systems

## Slide 10: GMDSS
Global Maritime Distress and Safety System (GMDSS): series of safety communications systems that large commercial vessels must carry to ensure safety of life
Includes emergency locator beacons and various (optional) communications equipments
Intergovernmental organisation INMARSAT were originally the only satellite provider in the GMDSS
Iridium has applied to become part of the GMDSS, offering improved coverage and extension to the polar regions (which GSO systems cannot serve)

## Slide 11: Emergency Relief Applications
Disaster Early Warning
Damage assessment reporting
  Mobility required
Relief supply logistics support
  Ordering relief supplies
  Supply movement tracking and redirection
Coordination of search and rescue efforts
  Injury/death reporting
  Request for medical team support
  Coordination of evacuations
Facilitating communications between first responders / relief workers and survivors and family members

## Slide 12: Conclusion
MSS has evolved extensively from roots in Marisat
Huge increase in satellite applications, driven by smaller and cheaper terminal types
Increasing demand for broadband services, but still a strong demand for cost-effective narrow-band services
Aeronautical and maritime industries have specific needs for all forms of satellite comms, and continue to drive some of the safety-critical applications like AMS(R)S, ADS-B and GMDSS

## Slide 13
Thank you.