## Slide 1: Security by Design in Smart Grids A Need to Rethink ICT in Power System Controls
Carsten Strunge,
Senior Development Engineer, Energinet.dk
cas@energinet.dk
ITU Workshop on “ICT Security Standardization for Developing Countries”
(Geneva, Switzerland, 15-16 September 2014)

## Slide 2: The Challenge of Balancing Wind Power and Electricity Consumption
2012
2035
Approx. 30 pct. of classic demand
Approx. 75 pct. of classic demand
Approx. 140 pct. of classic demand
2050 (scale 1:1)

## Slide 3: The Challenge to Utilization Renewabel Power
50,0 Hz
49,5 Hz
50,5 Hz
Power production
Consumption
New paradigm:  More load must follow production.
Not just locally, but cross boarder
* Local balancing should only be for congestion management.

## Slide 4: The Challenge of the Changing Power System
SC
HVDC
NO/SE
HVDC
NL
HVAC
DE
HVAC
SE
400 kV
10 kV
0,4 kV
SVC
150 kV
60 kV

## Slide 5: The Generalized Stakeholder and Domain Model (from NIST)

## Slide 6: What is the problem?
Internet is chosen as carrier of data (economy)
Internet does no longer offer secure communication
But it can be secured by:
  Ensuring authenticitet (”user identification”)
  Securing data in motion (by encription)
  Securing data at rest (on devices level)
  Building security into control processes
And it is necessary to continuously monitor the entire system (both Electric Power and ICT)

## Slide 7: What is Security by Design in Smart Grid?
Security and robustness in data exchange
  X.509, PKI
  RBAC, IEC61850 and SecureMMS, CIM and “SecureCIM”
Secure and robust data storage
  Access to data at the source
  Roll Based Access Controls (RBAC) at source
Secure and robust data processing
  Semi-offline controls though exchange of schedules
  Distributed controls with clear client-server relations
Secure and robust fall-back schemes
  Detection of abnormal behavior
  Segmentation and isolation of “infected” processes and ICT-networks
  Fall-back concepts
To have information security thought into the power system control concepts.

## Slide 8: Basic Elements in the Smart Grid Control Loop and Client-Server Relation
Control1
(Client agent)
Communication
Communication
Control2
(Other clients)
Control box w. RBAC
(Agent or Gateway)
Sensor
Actuator
(Server)
Power System
Status for availibility
Control and information
data
data

## Slide 9: Elements in the Smart Grid Control Loop - Prosumer Relation
DSO Voltage and
Emergency controls (SCADA)
Communication
(Fiber, PLC, GPRS, ?)
Communication
(Internet)
Market Aktor
Commercial Operation
(Aggregator)
Control box w. RBAC
(Agent or Gateway)
Sensor
Meter
Actuator
DER, CHP
HP, EV
etc.
Power System
Status for availibility
Control and information
Energy og
online power
E.g. via AMR/AMI
data
data

## Slide 10: Local Technical VPP and Commercial VPP in Smart Grid
Control
TekniskVPP
(Agent)
Market actor A
ComVPP
Market actor B
ComVPP
10/0,4 kV
Communication
(Internet)
AMI/AMR
Tech + ComA + ComB
Tech + ComA
Tech + ComA + ComB
Tech + ComA

## Slide 11: Proof of Concept Demonstration
CHPCOM
project
Combined Heat and Power Communication
CHPCOM
Secure IEC 61850 based Information Exchange in a Danish Context

## Slide 12: CHPCOM– is testing standards to make assets Smart Grid Ready
DSO/DNO
Balance responsible
Flexibility Market Aggregator
Technical control
Generator
CHP plant
Control
Power
sale
Power buy

~


Internet
Accumulator
Electric Boiler
Power Market
TSO
Data
Measurement
Measurement
International data exchange standard IEC 61850
Secured according to IEC 62351
Supply of services
Local resources to balance the local grid
Market control
Measurement
Data
Measurement
New
District heat
Solar heat
See: www.chpcom.dk (not yet available in English)

## Slide 13: CHPCOM – Role Based Access Control
CHPCOM RBAC unit
incl. IP-Firewall
Internet
IEC62351-4 SecureMMS from SISCO
IEC62351-8 RBAC from EURISCO

## Slide 14: RBAC structure in IEC 62351-8 - Whitelisting, Roles and Rights
Subject
Person/system whitelisted and identified by X.509 based certificate, whishes access to a resource
Example
Roles
Rights
Operations
Objects
Roles define basic user rights
Rights defines access to specific functions
Functions can conduct specific actions at resource
Resource read or write data
DCIP1.EngCtl.ctlVal
Start engine #1
Write
Egon Olsen
BRP Operator
IEC TS 62351-8
IEC 62351-8 also applies to IEC TC57 CIM-standards

## Slide 15: The CHPCOM data flow
RBAC
s/MMS
s/MMS
61850 GW
61850 DB
SCADA DB
RTU
MMS
SCADA
s/MMS
SecureMMS
Gateway
SCADA
SCADA frontend
MMS
INTERNET
Firewall
PKI
Components

## Slide 16: CHPCOM Information Security Activities
Implementation of
  PKI-elements
  X.509 certificates with encoded roles
  Automated certificate handling
  SecureMMS
  IEC 62351-8 RBAC gateway
Security Analysis
  PKI policies.
  Clients and Servers policies for installation and secure management.
Standardisation
  Feedback to basic X.509 standard (ITU-T SG17) with specific Smart Grid requirements;
  Feedback to IEC 62351 (TC57 WG15) on SecureMMS and RBAC implementation
Identify legislative needs
  Identify the legislative requirements in Denmark.
  Dialog with key stakeholders.

## Slide 17: Conclusions and Recommendations What we found Smart Grid needs from ITU-T
Automated machine2machine solutions e.g. for certificate renewal
Local certificate whitelists
Strong processes for initial certificate “bootstraping”
Multiple associated parallel PKI
  E.g. Smart Grid-PKI, Smart Meter-PKI, EV-PKI, etc.
And not least a good cooperation between ITU-T and IEC TC57.