## Slide 1: Standardization activities on optical access transport systems in ITU-T SG15
Hiroshi OTA
Study Group Engineer, ITU/TSB hiroshi.ota@itu.int
Workshop on “Monitoring Quality of
Service and Quality of Experience of Multimedia Services in Broadband/Internet Networks”
(Maputo, Mozambique, 14-16 April 2014)

## Slide 2: Overview

## Slide 3: ITU consists of three sectors and General Secretariat
ITU-T
develops ICT standards
ITU-R manages radio spectrum and satellite orbits
ITU-D promotes ICT development
General Secretariat coordinates work of ITU

## Slide 4: ITU-T Study Groups (SGs)
SG2: Operational aspects of service provision and telecommunications management
SG3: Tariff and accounting principles including related telecommunication economic and policy issues
SG5: Environment and climate change
SG9: Television and sound transmission and integrated broadband cable networks
SG11: Signalling requirements, protocols and test specifications
SG12: Performance, QoS and QoE
SG13: Future networks including cloud computing, mobile and next-generation networks
SG15: Networks, technologies and infrastructures for transport, access and home
SG16: Multimedia coding, systems and applications
SG17: Security
TSAG: Telecommunication Standardization Advisory Group

## Slide 5: SG15: Networks, Technologies and Infrastructures for Transport, Access and Home
Optical transport networks and access network infrastructures
Optical and other infrastructures, systems, equipment, fibres, control plane technologies
Customer premises, access, metropolitan and long haul
Lead SG for:
  access network transport
  optical technology
  optical transport networks
  smart grid
Details are at http://www.itu.int/en/ITU-T/studygroups/2013-2016/15

## Slide 6: Questions under SG15
Q1:Coordination of access and Home Network Transport standards
Q2: Optical systems for fibre access networks
Q3: General characteristics of transport networks
Q4: Broadband access over metallic conductors
Q5: Characteristics and test methods of optical fibres and cables
Q6: Characteristics of optical systems for terrestrial transport networks
Q7: Characteristics of optical components and subsystems
Q8: Characteristics of optical fibre submarine cable systems
Q9: Transport network protection/restoration
Q10: Interfaces, Interworking, OAM and Equipment specifications for Packet based Transport Networks
Q11: Signal structures, interfaces, equipment functions, and interworking for transport networks
Q12: Transport network architectures
Q13: Network synchronization and time distribution performance
Q14: Management and control of transport systems and equipment
Q15: Communications for Smart Grid
Q16: Outside plant and related indoor installation
Q17: Maintenance and operation of optical fibre cable networks
Q18: Broadband in-premises networking

## Slide 7: From recent development
G.fast (Fast Access to Subscriber Terminals) (Q4/15 and Q16/15)
  FTTdp (Fibre to the distribution point)
  G.fast transceiver aspects are under development by Q4/15
  G.fast infrastructural aspects of FTTdp deployment is under study by Q16/15
PON (Passive optical networks) (Q2/15) and optical fibres for FTTH (Q5/15)
  Major technology for FTTH (Fiber to the home)

## Slide 8: G.Fast - Fast Access to Subscriber Terminals (Q4/15)

## Slide 9: What is FTTdp ?
A broadband access solution taking fibre to a distribution point (FTTdp) very close to the customers premises, with total wire length to the customers’ transceiver up to 250m.
  It is expected that the bulk of the loop lengths may be in the order 30 to 50m. On 30 m loops, aggregate data rates up to at least 500 Mb/s should be supported on a single pair.

## Slide 10: FTTdp/G.fast “raison d’être”
To provide the best aspects of ‘Fibre to the home’ and ‘ADSL’:
  Fibre to the home bit-rates
  customer self-installation like ADSL

## Slide 11: Applications
Next-generation IPTV service at well over 100 Mb/s
Access to small and medium business sites at well over 100 Mb/s
Backhaul for very small wireless cell sites, including HetNet
Backhaul for WiFi hot spots

## Slide 12: Service rate performance targets
500-1000 Mb/s for FTTB deployments @<100m, straight loops
500 Mb/s at 100m
200 Mb/s at 200m
150 Mb/s at 250m
Aggregate service rates ≥500 Mb/s with start frequency of 23 MHz and VHF and DAB bands notches

## Slide 13: Migration example
Coexistence with xDSL: VDSL2 to G.fast migration

## Slide 14: Standards time-line
September 2010: Broadband Forum (BBF) Service Provider Action Council (SPAC) agreed to develop a white paper capturing network operators’ potential requirements.
January 2011: At request of BBF, ITU-T Q4/15 agreed to study the transceiver aspects of FTTdp, and issued a call for papers.
February 2011: Q4/15 opened G.fast project and assigned an Associate Rapporteur/Editor
June 2011: Q4/15 agreed to develop a new Recommendation
Recommendation ITU-T G.9700 (Power spectral density specification), approved in March, 2014
Recommendation ITU-T G.9701 (Physical layer specification) – consented in December 2013

## Slide 15: Standards body cooperation
Close cooperation between standards groups is needed:
  ITU-T Q4/15 for G.fast transceiver aspects
  ITU-T Q2/15 for PON related aspects
  Broadband Forum (FAN and E2E Architecture WGs) for architectural aspects
  Broadband Forum addresses certification and interoperability testing of equipment based on ITU-T G-PON and DSL Recommendations, and
  ETSI TM6 for reverse power feeding aspects

## Slide 16: PON (Passive Optical Networks) (Q2/15) and optical fibres for FTTH (Q5/15)

## Slide 17: PON Evolution
G-PON (Gigabit-capable PON)
NG-PON1 = XG-PON (10Gbit-capablePON)
NG-PON2 = TWDM-PON (40Gbit-capable PON)

## Slide 18: Capacity Trend for PON
1994
TPON
1999
A-PON
B-PON
2009
NG-PON1
XG-PON
10GEPON
2014
NG-PON2
TWDM-PON
Generation
Bandwidth
0.05G
2.5G
40G
10G
2004
G-PON
GEPON
0.6G
0.15G
Downstream
Upstream
10G
40G
100G
2020+
NG-PON3
?
250G
40G
100G
250G

## Slide 19: G-PON: Widely deployed
G-PON: Gigabit-capable passive optical networks
System defined in the Recommendation ITU-T G.984 series
  Recommendation ITU-T G.984.1: System requirements
  Recommendation ITU-T G.984.2: PMD specifications
  Recommendation ITU-T G.984.3: TC specifications
  Recommendation ITU-T G.984.4: OMCI - Subsumed by Recommendation ITU-T G.988
    Now used for all ITU PONs and P2P systems
  Recommendation ITU-T G.984.5: WDM matters for the future
  Recommendation ITU-T G.984.6: Reach extension
  Recommendation ITU-T G.984.7: Long reach
  Plus supplements…
Standards considered stable and mature
Minor optional enhancements continue even now

## Slide 20: XG-PON
XG-PON: 10-Gigabit-capable passive optical networks
System defined in the Recommendation ITU-T G.987 series
  Recommendation ITU-T G.987: Definitions, abbreviations and acronyms
  Recommendation ITU-T G.987.1: General requirements
  Recommendation ITU-T G.987.2: Physical media dependent (PMD) layer specification
  Recommendation ITU-T G.987.3: Transmission convergence (TC) layer specification
  Recommendation ITU-T G.987.4: Reach extension

## Slide 21: XG-PON system (ITU-T G.987 series) coexisting with G-PON
GPON
OLT
MAC
Logic
WDM
OLT Tx
1490nm
OLT Rx
1310nm
NNI
Data
I/O
GPON
ONU
MAC
Logic
WDM
ONU Rx
1490nm
ONU Tx
1310nm
UNI
Data
I/O
XGPON
ONU
MAC
Logic
WDM
ONU Rx
1577nm
ONU Tx
1270nm
UNI
Data
I/O
GPON OLT
GPON ONU
XG-PON ONU
XGPON
OLT
MAC
Logic
WDM
OLT Tx
1577nm
OLT Rx
1270nm
NNI
Data
I/O
XG-PON OLT
WDM1
1490nm
1577nm
1310nm
1270nm

## Slide 22: NG-PON2
NG-PON2: 40-Gigabit-capable passive optical networks
System defined in the Recommendation ITU-T G.989 series
  Recommendation ITU-T G.989 : Definitions and conventions
  Recommendation ITU-T G.989.1: General requirements
  Recommendation ITU-T G.989.2: Physical media dependent (PMD) layer specification (Consented in December 2013 – under approval process)
  Recommendation ITU-T G.989.3: Transmission convergence (TC) layer specification (draft in progress)
    Based on G.987.3, with wavelength control and 10G upstream added
  Recommendation ITU-T G.multi = Wavelength control layer (draft in progress)
    Meant as a general framework for TWDM-systems, of which G.989 is one
  Recommendation ITU-T G.984.5 = Wavelength coexistence (Consented April 2014 – under approval process)
  Recommendation ITU-T G.988 = ONU management and control interface
    Standard in force, can be easily reused for TWDM

## Slide 23: NG-PON2 Wavelength Plans (ITU-T G.989.2 – under approval progress)
Wavelength Compatible Systems | TWDM |  | PtP WDM PON
 | Downstream | Upstream | Upstream/Downstream
GPON, RF Video, XG-PON1 | 1596-1603 nm | Wide Range 1524-1544 nm Reduced Range 1528-1540 nm Narrow Range 1532-1540 nm | Shared Spectrum 1603-1625 nm Expanded Spectrum 1524-1625 nm

## Slide 24: Evolution in the recommendation for Recommendation ITU-T G.652 fibers
Existing Recommendation ITU-T G.652.D category is already optimized to be used with G-PON and XG-PON systems, with the necessity to define attenuation attribute in the range of interest (1260 nm - 1650 nm)
A new category has been proposed with enhanced behavior in attenuation and bending loss for both transport and access networks applications
Proposals under evaluation:
  to reduce the existing MFD range in order to improve the compatibility with other single mode categories (e.g. Recommendation ITU-T G.657)
  to improve the geometrical requirements in order to enable the use of low cost connectors or splicing machines in access network
  necessity to define attenuation attribute in the range of interest in access network: 1260 nm e 1650 nm

## Slide 25: Evolution in the recommendation for Recommendation ITU-T G.657 fibers
Optimization of B2/B3 categories (not necessary compliant with Recommendation ITU-T G.652) has been developed:
  improved compatibility with other Recommendation ITU-T G.657 categories and with Recommendation ITU-T G.652 with the reduction of MFD range (Minimum typical MFD was modified from 6.3 mm to 8.6 mm)
Definition of methods to measure MPI in Recommendation ITU-T G.650.1
Proposals under evaluation:
  Proposal to reduce existing MFD range also for A1/A2 subcategories in order to improve the compatibility with other single mode categories (e.g. Recommendation ITU-T G.652) and to harmonize with Cenelec standards on connectors. That would result in an improvement in OTDR unidirectional measurements interpretation (this measurement could be necessary to be used on PON networks where bidirectional test is not usable to localize faults).
  Necessity to go deep in the study of mechanical reliability related to the FTTH installation conditions

## Slide 26: Thank you!
hiroshi.ota@itu.int