## Slide 1: QoE and QoS Monitoring / Measuring in Broadband Internet Networks
Seppo Lohikko
Principal Consultant, Omnitele Ltd seppo.lohikko@omnitele.com
Workshop on “Monitoring Quality of
Service and Quality of Experience of Multimedia Services in Broadband/Internet Networks”
(Maputo, Mozambique, 14-16 April 2014)

## Slide 2
Omnitele
Introduction to QoS and QoE
QoS / QoE Monitoring and Management
Omnitele approach to measure end-user QoS / QoE
Summary
topics discussed

## Slide 3
COMPETITIVE NETWORK BENCHMARK | SWEDEN | 2014
www.omnitele.com
why we exist
Network strategy, design and quality management for maximised customer experience and minimised network cost.
track record
Founded in 1988 to set up world’s first GSM network. 1000+ projects in 80+ countries.
independent
Privately owned by telecom background Finnish shareholders, independent of all international operators and network infrastructure vendors.
omnitele way
Being Straightforward, Trusted and Intelligent ensures excellent Omnitele Experience.

## Slide 4
Business Development Ongoing
Projects Completed
In total Omnitele has completed over 50 projects in Africa since 2007.
Omnitele footprint in Africa

## Slide 5
Omnitele
Introduction to QoS and QoE
QoS / QoE Monitoring and Management
Omnitele approach to measure end-user QoS / QoE
Summary
topics discussed

## Slide 6: Quality of Service / Quality of Experience / voice
User
User
Equipment
Access
Network
Core
Network
Access
Network
User
Equipment
User
”MOS”

## Slide 7: Quality of Service / Quality of Experience / data
User
User
Equipment
Access
Network
Core
Network
Internet
IP Trans
port
Network
performance
Network
performance
Network
performance
Network
performance
Network
performance
Total network performance
Quality of Service
Technical component of Quality of Experience

## Slide 8: Paradigm Shift Required in QoS Measurements
Throughput & Coverage measurements are obviously insufficient to capture the End-user QoS
Two services: CS & PS
Few KPIs to capture overall QoS: Call Completion Rate, Bitrate
   NETWORK CENTRIC QOS REQUIREMENTS
Yesterday
A Generic PS service does not exist anymore
Instead WWW, Video, IM, VoIP…
   APPLICATION SPECIFIC QOS REQUIREMENTS
Today
Notes: Game has changed: bitrate is no longer the only bottleneck of the end-user QoS. Different apps have different bottlenecks. Bitrate is important but it does not give the whole picture.

## Slide 9: Application Performance is the Make It or Break It
 focus on the services – not the networks
END-USERS MIND SERVICE QUALITY, NOT NW PERFORMANCE
They consume VoIP, video, news, social networking, etc
They don’t consume average throughput

## Slide 10
Balls are so expensive...
I want it to go easily into the goal…
We just want a ball!
We just want a ball!
Any ball is good!
If we cannot define the QoE of a soccer ball, how can we approach something as complex as a Telecom Service?
QoE of a soccer ball?
I want it with iPod dock and blue LEDs

## Slide 11
QOE DEPENDS ON…
expectations
branding
socio-economic background
price
customer care
provisioning
end-user QoS
network
service
device
QoE
brand
price
QoS
expectations
our focus
what are QoS and QoE?

## Slide 12: Diverging Promise, Delivery and Expectation
Promise | Operators are marketing with headline speeds
Delivery | End-user bitrate only fraction of the headline
Expectation | 10Mbit/s MBB = 10Mbit/s DSL
Chart: 
| 7.2 HSPA R6 | 14 HSPA R6 | 21 HSPA+ R7 | 42 HSPA+ R8 | 100 LTE R8
Headline | 7.2 | 14 | 21 | 42 | 100
Reality | 4.1 | 4.92 | 5.166 | 10.8486 | 28.2064
*Based on Omnitele network simulations and analysis of real operator networks
Frustration guaranteed!
Notes: There are so many different bitrates, that nobody can be sure of nothing. The gap between the promise and the delivery is widening. Regulators should counteract the development.

## Slide 13
QoE, QoS and network performance quantified
  QUALITY OF EXPERIENCE
  How well service quality meets expectations?
  overall Satisfaction, e.g. 1-5 ”stars”
  Highly market dependent and user segment specific
  QUALITY OF SERVICE
  How well does a service perform
  Measured application/service KPIs
  product of one or more network performance factors
  NETWORK PERFORMANCE
  Technical measurements of the network
  e.g., delay, jitter, packet loss, throughput...
RSCP
Ec
/N0 latency jitter packet loss RSRP RLC throughput RSRQ
RAB setup success rate modulation coding TX power G
-
factor Channel C/I
Timing Advance Mobile TX Power Voice Codec Usage Handover Success Rate
MCS Usage Distribution Time Slot Utilization Block Error Ratio Active Set
Size SHO Success Rate ISHO Success Rate CQI E
-
DPDCH Throughput PDSCH
modulation MAC DL BLER MAC UL BLER MAC UL Retransmission Rate

## Slide 14
The contour shape is universal
Steep QoE decrease right after X1
The actual values vary with respect to markets, services, segments, devices, price plans...
No ”one size fits all” exists – remember the soccer ball!
Source: A Generic Quantitative Relationship between Quality of Experience and Quality of Service. (Fiedler, Hossfeld, Tran-Gia)
Generic relation of Qos and QoE

## Slide 15
common operator challenge: “How is the business?”
need to find right targets for acceptable QoE!
“The network is excellent. RSCP, Ec/No, BLER aligned with targets”
“Churn is high, customers not satisfied, competitor has higher quality”
???

## Slide 16: introduction | problem setting
Technical organisation can easily measure and impact network performance but end-user’s care about QoE
Improved End-user Satisfaction, Network Efficiency and Return on Investment
Need to find the right KPI target values giving sufficient QoE and optimise the network accordingly
…In essence, this is what CEM is in technical context!
1|
2|
3|

## Slide 17
Omnitele
Introduction to QoS and QoE
QoS / QoE Monitoring and Management
Omnitele approach to measure end-user QoS / QoE
Summary
topics discussed

## Slide 18: Let’s explore briefly some typical QoS / QoE tooling frameworks…

## Slide 19
Mobile operators’ CEM strategies: the market reality | telecoms intelligence survey report | Nov2013
Typical operator challenges

## Slide 20
Straightforward implementation, but not necessarily sufficiently detailed level of data
Complex integration to other BI systems (CDR, CRM)
Limited location accuracy: ~20% of cell radius
Cross-correlation to any QoE polls difficult
Cost efficient & easy rollout
Network statistics & probes
Notes: CDR = CRM, customer relationship managent

## Slide 21
Accurate user, device, time, location and service context
QoE polls implemented with the agent software
QoE & QoS from same source: straightforward cross correlation
…CHALLENGING ROLLOUT (deployment cost, user sensitivity)
Detailed data in high “resolution”, but rollout challenges expected
Smartphone QoS/QoE agents

## Slide 22
QoE Server
QoE Client
Manage QoE client pool
Control QoS measurements and QoE queries
Data aggregation, KPI trending, QoE vs. QoS X-correlation
QoS “agent” monitoring end-user behaviour and QoS
User interface for QoE polls and end-user feedback
Send KPI values and QoE poll answers to QoE server
QoS
QoE
Meta
Config.
QoE?
Example system with smartphone agent

## Slide 23
HOW ABOUT A HYBRID SOLUTION?
QoE–QoS modelling with smartphone agents in limited user group
Apply model in probe data to obtain network wide exposure to QoE
PROBLEM SETTING:
Smartphone agents: sufficient detail but rollout challenges
NW probes: straightforward rollout but lack of detail
Hybrid solution

## Slide 24
Automatic Service
Assurance Monitoring
Benchmark & Quality
Measurements
Customer Experience
Platform
Present QoS Results
End-user Qos
Measurements
QoE model
Apply QoE model to measured QoS results
Calculated
MOS score
Tune QoE
model based on
controlled
CE Measurement
International
Benchmarks
QoE Modelling Surveys
Probes & statistics
Example hybrid solution overview

## Slide 25
Omnitele
Introduction to QoS and QoE
QoS / QoE Monitoring and Management
Omnitele approach to measure end-user QoS / QoE
Summary
topics discussed

## Slide 26: Basics | QoS Framework Suggested by ETSI
Conclusion | Need to define the corresponding ”reference levels” for all relevant L4 services and killer apps.
Network Availability
Network Accessibility
Service Accessibility
Service Retainability
Service Integrity
Web
Radio
WWW
SMS
Email
VoIP
FTP
MMS
Y
Video
CS
Voice
X
Z
L1
L2
L3
L4
*TS 102 250-2
Accessibility
Retainability
Integrity
The probability that a user can access a service when network is available
E.g. Call Setup Success Rate, Data session setup success rate
Probability that the service is not interrupted during the connection
E.g. Call drop rate, PDP context cut-off ratio
The service quality when service is in use, up and running
E.g. bitrate, voice quality, call setup time

## Slide 27: From KPIs to End-user QoS…
Network Availability
Network Accessibility
Service Accessibility
Service Integrity
Service Retainability
=
[Total Problems ] / [All attempts] = End-user QoS
Coverage Problems
Network Access Problems
Service Access Problems
Service Drops
Service Quality Problems
+
+
+
+
Total Problems
Omnitele QoS Framework following ETSI TS 102 250-2

## Slide 28: WWW & Video dominate usage!
Chart: 
| General Browsing | Video Streaming | P2P | Gaming | VoIP | M2M
Subscribers using (%) | 0.72 | 0.2 | 0.07 | 0.05 | 0.05
Share of data volume (%) | 0.2 | 0.705 | 0.033 | 0.011 | 0.003 | 0.047
MOBILE DATA USE CASE POPULARITY AND DATA VOLUME
Source: Allot MobileTrends Report Q2/2013, CISCO VNI 2012
Which applications to measure

## Slide 29: Bitrate impact on Web Browsing QoS
End-user QoS mainly defined by
  webpage waiting time and
  streaming video buffering time
Bitrate is important but its impact is highly non-linear
The higher the bitrate, the less important it becomes
Chart: WWW Page Download Time [s] vs. Bitrate [kbit/s]
| 1 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 4500 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
 | 8001.157 | 81.157 | 41.157 | 27.8237 | 21.157 | 17.157 | 14.4903 | 12.5856 | 11.157 | 10.0459 | 9.157 | 6.4903 | 5.157 | 4.357 | 3.8237 | 3.4427 | 3.157 | 2.9348 | 2.757 | 2.4903 | 2.2999 | 2.157 | 2.0459 | 1.957
“Frustration”
“As good as it can get”
“Acceptable”
Shape of the curve differs between networks  Bitrate measurements do not show the truth. Waiting time and buffering time do!
Notes: The importance of bitrate improvement decreases while the bitrate increases. Instead of comparing the operators by bitrates, the benchmarks should measure more meaningful attributes, e.g. WWW page waiting time. WWW page waiting time is something that everyone understands, hence benchmarking it enables apples to apples comparison.

## Slide 30: Let’s take a dive into WWW browsing Quality of Experience…
OPERATOR CASE: QoE FOR WWW BROWSING

## Slide 31
2. QoS targets: measure QoE & QoS and cross-correlate to define the relation
3. NW performance targets: Link QoS with NW performance to find right network performance KPI targets
1. QoE targets: define the desired WWW QoE level
OBJECTIVE | sufficient web browsing experience for high value customers

## Slide 32
QoE defined in 1 – 5 SCALE
Captured with end-user queries: “On 1-5 scale, what is your WWW browsing experience?”
rating | QoE | Impairment
5 | Excellent | Imperceptible
4 | Good | Perceptible but not annoying
3 | Fair | Slightly Annoying
2 | Poor | Annoying
1 | Bad | Very Annoying
1. QoE TARGET | define the desired WWW QoE
SUFFICIENT
QoE TARGET
90% of customers ≥ 4

## Slide 33
unsatisfactory region
(MOS < 4)
Chart: Web Browsing QoS and QoE
Average(s) | 1 | 2 | 3 | 4 | 5
2. QoS TARGET | correlate QoS with QoE
QoS target: WWW download time < 3s
QoE target ≥ 4

## Slide 34
accepted region
(www download time < 3s)
unsatisfactory region
(www download time > 3s)
Chart: 1000KB WWW Page Waiting Time vs. Bitrate
| 1 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 4500 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 15000 | 20000 | 25000 | 30000 | 35000 | 40000
HSPA | 8001.2 | 81.2 | 41.2 | 27.8667 | 21.2 | 17.2 | 14.5333 | 12.6286 | 11.2 | 10.0889 | 9.2 | 6.5333 | 5.2 | 4.4 | 3.8667 | 3.4857 | 3.2 | 2.9778 | 2.8 | 2.5333 | 2.3429 | 2.2 | 2.0889 | 2 | 1.7333 | 1.6 | 1.52 | 1.4667 | 1.4286 | 1.4
3. CTO TARGETS | find required NW performance to deliver desired QoE
90% of subs get > 4,5 Mbit/s
CTO’s NW Performance Target:
Duly noted!
Notes: Technology agnostic, device specific delays not taken into account

## Slide 35
Omnitele
Introduction to QoS and QoE
QoS / QoE Monitoring and Management
Omnitele approach to measure end-user QoS / QoE
Summary
topics discussed

## Slide 36: Session conclusions & key messages
Challenge: CMO and CTO talk different language
NW DEVELOPMENT SHOULD BE DRIVEN BY QoE
CMO team to set QoS/QoE targets based on demand & strategy (…and regulation?)
CTO team to deliver sufficient NW performance
1|
2|
3|
Proper CEM is imperative for securing good enough QoE
Need to define the corresponding reference levels for all relevant L4 services and killer apps.

## Slide 37: End-User Quality Surveys
Periodic QoS measurement process is required to follow the quality trends
A proper methodology involves truly end-user centric approach: measure WWW, VoIP, video…not network
A holistic QoS process involves KPIs that really matter from customer perspective
Wake up!

## Slide 38: End of Session …
Questions?

## Slide 39: Any further enquiries:
Mr. Seppo Lohikko Principal Consultant
Omnitele Ltd. Mobile: +358 44 2793811 seppo.lohikko@omnitele.com www.omnitele.com
Follow us at www.linkedin.com/company/omnitele
http://www.youtube.com/channel/UCyMeM3j2L9MQoB0qeDCev3g