## Slide 1: Defending Vehicle ECUs from Malicious Attacks and Intrusions Using Hardware Security Modules (HSM)
Seigo Kotani, Ph. D.
Principal Expert, Mobility IoT Business Unit, Fujitsu Ltd.
TCG* Board of Director, Co-Chair of Embedded Systems WG and Vehicle Services Subgroup
ITU/TTC Workshop on
How Communications will Change Vehicles and Transport
July 4, 2016
*

## Slide 2
Agenda
Fujitsu’s activities for vehicle securities
Proposal based on HSM, typically TPM*
Introduction of TCG and TPM 2.0 Automotive Thin
Feasibility study to Remote Firmware Update for Vehicle ECU with TPM
*Trusted Platform Module

## Slide 3
Fujitsu’s Mobility IoT Business Unit from Feb. 2016
■ We’ll aim at a global servicer in the Mobility business by providing service application and integration system.
Concept : Mobility as a Service（MaaS） Mobility IoT Platform
■ We’ll support safety, relief and comfortableness of human’s mobility with sensor and AI technologies. Concept : Human Centric Mobility
+
Category | Products/ Service | Description
Mobility as a Service | BigData utilization services | Services to business which related to mobility
Mobility IoT Platform | Cloud Platform | Cloud platform for mobility business
 | Dynamic Map Database | Dynamic Map data management system
 | AI Platform (IoT/Cloud) | Deep Learning Unit (DLU)
 | Security (IoT/Cloud) | Cyberattack protection
Human Centric Mobility | Driver Sensing | Contactless vital sensing (Iris, Pulse, etc.)
BigData
IoT Devices
Cloud
Mobility IoT
Solution
Mobility as a Service
Sensor Technology
Human Centric Technology
Cloud platform
Functions utilizing BigData
Insurance
Police/Security
Logistics/
Transportation
Infrastructure
etc.
Mobility IoT Platform
Human Centric Mobility
(Target businesses)
Services to business
which related to mobility

## Slide 4
Demo Overview in Fujitsu Forum Tokyo 2016
G/W
Cloud (Mobility IoT Platform)
Internet
Hacker
First
wall
Second wall
Third wall
Multi-layered defenses effective in protecting the system as a whole from the risk of hacking
Sending
unauthorized
messages
Eavesdropping
Data falsification
Virus infection
Unauthorized
access
Hacking
In-vehicle service 1
In-vehicle service 3
In-vehicle service 2
Security library
Security middleware/ library
Security service
Design/ development phase
Management phase
Planning phase
Security consulting
Drafting security policies
↓
Security threat analysis
↓
Proposing defense measures
Providing security products
Device authentication (first wall)
Filtering (second wall)
Message authentication (third wall)
Configuration management
Key management
Remote maintenance
Service solutions
Key management system
Configuration management system
Falsification detection system
Maintenance service
Life cycle management

## Slide 5
Proposal
Methods for Defending Vehicle ECUs from Malicious Attacks and Intrusions
Using Hardware Security Modules (HSM)
global industry standards, supportive of a hardware-based root of trust, for interoperable trusted computing platforms.
Protocol
Interface
Function
Algorithm
IP Core
Package
(Application)
TPM (Trusted Platform Module)
Define in the international standards
Protocol
Interface
Function
Algorithm
IP Core
Package
(Application)
Conventional HSM
Proprietary product
Assure a behavior by using TCG testbed
Define in the TCG specifications

## Slide 6
Why TPM?
Require critical functionality for remote maintenance of vehicle
  Secure communications to remotely verify current situation
  Confirm installation completion and success or failure
  Record and retain certifiable audit logs
TPM (ISO11889) /TNC* (IETF RFC5792/5793) technologies could satisfy these requirements with reasonable costs
ECU
TPM
Log
Induction
Support independent third-party verification
⇒Satisfy transparency and fairness
Create & deliver by using open technologies
⇒ Guarantee the verifiability of audit logs
*Trusted Network Connect

## Slide 7
TCG: Mission and History
The Trusted Computing Group (TCG) is a not-for-profit organization formed to develop, define and promote open, vendor-neutral, global industry standards, supportive of a hardware-based root of trust, for interoperable trusted computing platforms.
  Work based on hardware root of trust
  Over 10 years of creating widely used and highly vetted industry specifications
  Some specifications are international standards
  Specifications embodied in more than 2 billion products today
Standards Drive Adoption

## Slide 8
TCG: Membership
Total Membership including Commercial, Liaison, Academic, Invited Experts and Government participants: 130+Members:
Vehicle, Chips, Cloud, Embedded, IoT, Mobile, PC
Promoters:
Contributors:

## Slide 9
TCG Working Groups
Embedded Systems
– 4 Subgroups: Vehicle Services, IoT, Network Equipment, RTM*
Infrastructure
Mobile
PC Client
Server
Storage
TCG Software Stack
Trusted Mobility Solutions
Trusted Multi-tenant Infrastructure
Trusted Platform Module
Virtualized Platform
…
Virtualized Platform
Mobile Phones
Applications
Storage
Infrastructure
Servers
Desktops & Notebooks
Security
Hardware
Authentication
Embedded
Systems
June 2011
Established
Network
Security
*Root of Trust Measurement

## Slide 10
Standardization
Trusted Computing Technologies
  Trusted Platform Module (TPM) – hardware root-of-trust & key storage
  Trusted Network Connect (TNC) – access control & endpoint compliance
  Self-Encrypting Drive (SED) – hardware encryption & fine-grained locking
  Automotive, PC Client, Mobile – Profiles of TPM 2.0 Library Spec
Trusted Computing Platforms
  Interfaces across multiple platforms for trusted data, devices, and networks
  Automotive, Embedded Systems, Internet of Things, Cloud/SDN, Virtual Machines, Servers, Desktops, Laptops, Tablets, Mobile Phones, and more
Formal Liaisons, Collaborators/Partners
  ETSI, Global Platform, Industrial Internet Consortium (IIC), Mobey Forum, ISO, IEEE, IETF, OASIS, and more
TCG TPM 2.0 Automotive Thin Profile Family “2.0” Level 00 Version 1.0 Published: March 16, 2015
http://www.trustedcomputinggroup.org/wp-content/uploads/TCG-TPM-2.0-Automotive-Thin Profile_v1.0.pdf

## Slide 11
TPM2.0 Automotive Thin Profile
Features
  For sensors, actuators, and controllers implemented as digital ECUs with limited resources (slow CPU with limited ROM, RAM and NVRAM)
  For deployment in ECUs to support their integrity and attestation for secure boot, normal operation, and remote maintenance services
  ECU measures firmware into TPM PCR*, uses TPM to create an integrity digest and sign the digest, and sends digest to maintenance center
  ECU receives the appropriate firmware update, installs the update, and sends confirmation of the successful installation
*Platform Configuration Registers

## Slide 12
Auto-Rich
Installed
Auto-Thin
Installed
Update Data
FW
Digest
FW
Digest
Update Data
TNC
Remote Center
Recognize a status of the vehicle by surveying FW Digest
Select & send a suitable update data
“TPM 2.0 for Automotive Thin” installed in ECU
Measure ECU FW to create a digest & sign to the digest
“TPM 2.0 for Automotive Rich” installed in Head unit
Work as “TPM 2.0 for whole vehicle”; furthermore
Gateway between the Remote Center and ECU
Head Unit / Gateway
HW
1~2 core
RAM
OS
Others
Applications
TPM
ECU
HW
1 core
RAM
Others
Application
TPM
Message Flow for Remote Maintenance

## Slide 13
Reference: Auto Thin Resources
Auto Thin Profile – TPM 2.0 Mandatory Resources
  Authorization Sessions
    Minimum of 3 sessions
  Cryptographic Algorithms
    • At least one of RSA 2048 or ECC P256. Additional asymmetric algorithms and key sizes are allowed.
    • At least one symmetric algorithm. AES 128 is recommended, others are allowed.
    • SHA-256. Other hash algorithms are allowed.
  Platform Configuration Registers (PCRs)
    PCR0 is required – only reset by TPM2_Startup().
    Support for other PCR is optional.

## Slide 14
Remote Firmware Update for Vehicle ECU with TPM
CAN or
other
Remote Maintenance
Center
Vehicle
Cloud
In-Vehicle HMI on Tablet PC
ECU2: LED
Motor
TCG published TPM 2.0 Automotive Thin Profile v1.0
TrustCube concept is built-in
Connecting Center, In-vehicle Server and ECUs, files downloaded from Center enable ”ECUs update” with TCG’s TPM authentication procedure.
ECU1: Actuator
3G LTE
or other
Wi-Fi
In-Vehicle Server
®
2016/2 RSA Conf. SF,
2016/4 SAE World Cong. Detroit

## Slide 15: Fujitsu: TrustCube concept
®
®
Input as
specifications
Who
Identify operator
by ID/PW, Biometrics
What
Current platform
identify, Registered ID,
PKI Certificate
How
Current environment of
platform: software version,
hardware model
3D analysis using trust factors
to determine the level comm. &
actions to be authorized
Record and retain certifiable audit logs
with “who agreed”, “for what platform,”
“why accepted remote maintenance,” etc.

## Slide 16: Thank you, Questions?
Please contact
Seigo Kotani
skotani@jp.fujitsu.com
Join us!
TCG
http://www.trustedcomputinggroup.org/
Embedded Systems WG
http://www.trustedcomputinggroup.org/developers/embedded_systems
If you are interested in the following applications;
Standardization for
Automotive
IoT
Hardcopy devices
Mobile communication devices
Household applications (TV/Settop box, etc)
Industrial control and machinery
Financial transaction terminals
Medical equipment
Smart Grid/Smart meter
Sensor network/Monitor cameras …