INTERNATIONAL TELECOMMUNICATION UNION

TELECOMMUNICATION
STANDARDIZATION SECTOR

STUDY PERIOD 1997 - 2000

COM 11-R 67-E

October 1997

Original: English

Question: 15/11

E

STUDY GROUP 11 – REPORT R 67

SOURCE*:	STUDY GROUP 11

TITLE:	REPORT OF THE MEETING HELD IN GENEVA FROM 1-19 SEPTEMBER 1997 - PART I - IMPLEMENTORS' GUIDE (VERSION 9/97) FOR Q.2110 (7/94)

________

The reports of the meeting of Study Group 11 and its Working Parties are published in the documents listed in COM 11-R 60.

NOTE - This text was approved by Study Group 11 at its Plenary on 19 September 1997. This text is also available from ITUDOC.

1	Introduction

1.1	References

[1]	ITU-T Recommendation Q.2110 - July 1994 - B-ISDN ATM Adaptation Layer - Service Specific Connection Oriented Protocol (SSCOP).

1.2	Background

This guide is a compilation of reported defects, their resolutions and minor upgrades to the 1994 edition of ITU-T Recommendation Q.2110 [1]. It includes all approved corrigenda and is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

1.3	Scope of the guide

This guide records the resolutions of defects in the following categories:

•	editorial errors;

•	technical errors, such as omissions, inconsistencies, etc.; and

•	ambiguities.

In addition, this guide records minor enhancements to the Recommendation in the following categories:

•	increased interoperability; and

•	deployment possibility in new environments.

1.4	Contacts

Rapporteur Q.15/11:	Dr. Pietro Schicker		Tel:	+4101093801555
					Swiss Telecom PTT		Fax:	+4101093801557
					Scientific Consulting 		Email:	schicker@scicon.ch
					Oberhöhe
					CH-8340 Ringwil
					Switzerland

Former Rapporteur:	 	G. Ratta			Tel:	+1 732 332 5174
					Lucent Technologies		Fax:	+1 732 949 1196
					101 Crawfords Corner Road	Email:	gratta@lucent.com
					Holmdel, NJ 07733-3030
					United States

1.5	Document history

| Version | Summary | Version | Summary |
| --- | --- | --- | --- |
| 9/97 | New Implementors' Guide | 1997-09-19 | Subclause 2.1 added |

2	Editorial errors

2.1	Correct connector label in the SDL diagrams

Synopsis:

In the printed version of Q.2110 [1], the connector at the bottom of part 38 of 51 should contain the label "B".

Mod. a):

In the SDL diagram (Figure 20/Q.2110), replace the actions towards the bottom of part 38 of 51 with the definition as shown in Figure 2.1 below.

Figure 2.1

3	Technical errors

None.

4	Ambiguities

4.1	Use of SSCOP in conjunction with SSCF

Mod. a):

Add the following sentence at the end of § 1:

In particular, an SSCOP entity can only be used in conjunction with the requirements specified by a particular SSCOP user, e.g., a particular SSCF Recommendation, and as a peer entity to the corresponding SSCOP entity, operating in conjunction with the requirements specified by same SSCOP user, e.g., the same SSCOP Recommendation.

5.	Increased interoperability

5.1	Increased robustness during power-up connection establishment

Synopsis:

An option is introduced to allow the SSCOP entity to accept a BGN PDU in state IDLE irrespective of the values of N(SQ) in the BGN PDU and the state variable VR(SQ).

Mod. a):

In the SDL diagram (Figure 20/Q.2110), replace the actions after receipt of a "BGN PDU" in state "Idle" with the definition as shown in Figure 5.1 below.

Figure 5.1

Mod. b):

In § B.5.3, add a further row to the table as follows:

| ITEM # | Protocol Feature | Status | References | Support |
| --- | --- | --- | --- | --- |
| SP11 | Is power-up robustness implemented | O | SDL | Yes:___ No:___ X:___ |

6	Deployment possibility in new environments

None.

__________