INTERNATIONAL TELECOMMUNICATION UNION

TELECOMMUNICATION
STANDARDIZATION SECTOR

STUDY PERIOD 1997 - 2000

COM 11-R 69-E

October 1997

Original: English

Question: 16/11

E

STUDY GROUP 11 – REPORT R 69

SOURCE*:	STUDY GROUP 11

TITLE:	REPORT OF THE MEETING HELD IN GENEVA FROM 1-19 SEPTEMBER 1997: PART 1 - IMPLEMENTORS' GUIDE (VERSION 09/97) FOR Q.705 (03/93)

________

The reports of the meeting of Study Group 11 and its Working Parties are published in the documents listed in COM 11-R 60.

1	Introduction

1.1	References

[1]	ITU-T Recommendation Q.705 (03/93)

1.2	Background

This guide is a compilation of amendments to the 1993 edition of the ITU-T Recommendation Q.705[1]. It includes all approved corrigenda and is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

1.3	Scope of the guide

This guide records the resolutions of defects in the following categories:

•	editorial errors;

•	technical errors, such as omissions, inconsistencies, etc.; and

•	ambiguities.

1.4	Contacts

Editor:	Klaus D. Gradischnig
	Siemens AG
	OEN SN SE 51	Tel:	+49 89 722 63197
	Hofmannstr. 51	Fax:	+49 89 722 48212
	D-81359 Munich	Email:	Klaus.Gradischnig@oen.siemens.de

1.5	Document history

| Version | Summary |
| --- | --- |
| 09/97 | New Implementors' Guide |

2	Editorial errors

None.

3	Technical errors

3.1	Inhibit/allow STP access by a combination of designated outgoing linksets to designated DPCs

Synopsis

§ 8.2 ii) describes a screening option by the combination of outgoing linksets and destination point code. Use of this option in a non-trivial manner (i.e. not either of the two possibilities of allowing or of inhibiting STP access for all outgoing linksets of the route to the DPC in question) would result in an unpredictable discarding of MSUs by the STP.

Mod. a):	Delete ii)	To inhibit/allow STP access by a combination of designated outgoing linksets to designated DPCs from § 8.2 of Q.705.

4	Ambiguities

None.

_____________________