|  | INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2001 - 2004 | COM 11-R 46-E March 2002 Original: English |

E

STUDY GROUP 11 - REPORT R 46

SOURCE*:	STUDY GROUP 11

TITLE:	IMPLEMENTORS' GUIDE (03/2002) FOR RECOMMENDATION Q.773 (06/1997)

________

# 1	Introduction

## 1.1	References

[1]	ITU-T Recommendation Q.773 (06/97): Transaction Capabilities formats and encoding

## 1.2	Background

This guide is a compilation of reported defects, their resolutions and minor upgrades to the 2000 edition of the ITU-T Recommendation Q.773[1]. It includes all approved corrigenda and is intended to be an additional authoritative source of information for implementors to be read in conjunction with the Recommendation itself.

## 1.3	Scope of the guide

This guide records the resolutions of defects in the following categories:

•	editorial errors;

•	technical errors, such as omissions, inconsistencies, etc.;

•	ambiguities.

In addition, this guide records minor enhancements to the Recommendation in the following categories:

•	increased interoperability;

•	deployment possibility in new environments.

## 1.4	Contacts

Rapporteur Q.13/11:	Dr. Pietro Schicker	Tel:	+41 1 938 1555
					Swiscom Ltd	Fax:	+41 1 938 1557
					Switzerland	Email:	schicker@scicon.ch

## 1.5	Document History

| Version | Summary |
| --- | --- |
| 2002-03-01 | New Implementors' Guide |

# 2	Editorial Errors

## 2.1	Syntactical Error in ASN.1

Synopsis

In Annex A, the definition of Component {OPERATION : Invokable, OPERATION: Returnable}contains a syntactical error.

Modification 1)

Replace the definition of {OPERATION : Invokable, OPERATION: Returnable} towards the end of Annex A with the following definition:

Component {OPERATION : Invokable, OPERATION: Returnable} ::= CHOICE

{

basicROS	ROS {TCInvokeldSet, {Invokable}, {Returnable}},

returnResultNotLast	[7] returnResult < ROS {{},{},{Returnable}}

}

TCInvokeldSet INTEGER ::= {-128..127}

END – TCAPMessages

NOTE - The definition of TCInvokeldSet is equivalent to the following definition:

TCInvokeldSet ::= INTEGER (-128..127)

# 3	Technical Errors

None.

# 4	Ambiguities

None.

# 5	Increased Interoperability

None.

# 6	Deployment Possibility in New Environments

None.

______________________