|  | INTERNATIONAL TELECOMMUNICATION UNION |
| --- | --- |
| ITU-T | G.7713/Y.1704 Implementers’ Guide |
| TELECOMMUNICATION STANDARDIZATION SECTOR OF ITU | (27 May 2005) |
|  | SERIES G: TRANSMISSION SYSTEMS AND MEDIA, DIGITAL SYSTEMS AND NETWORKS |
|  | Implementers’ Guide for ITU-T Rec. G.7713/Y.1704 (12/2001) Distributed call and connection management (DCM) |

Summary

This document is an Implementers' Guide for ITU-T Recommendation of G.7713/Y.1704 (12/2001).

Source

This document was agreed by ITU-T Study Group 15 on 27 May 2005.

(  ITU  2005

All rights reserved. No part of this publication may be reproduced, by any means whatsoever, without the prior written permission of ITU.

Table of Contents

1.0	Introduction	1

2.0	Terms to be removed from Rec. G.7713/Y.1704 and Amendment 1 to G.7713/Y.1704	1

2.1	Terms to be removed from Rec. G.7713/Y.1704	1

2.2	Terms to be removed from Amendment 1 to Rec. G.7713/Y.1704	3

Implementers’ Guide for Recommendation G.7713/Y.1704 
(Distributed call and connection management (DCM))

Implementers’ Guide for definitions and terms found in Rec. G.7713/Y.1704

Abstract

SG15/WP3 has approved terminology Recommendations for Synchronous Digital Hierarchy (SDH) (Rec. G.780/Y.1351), Optical Transport Networks (OTN) (Rec. G.870/Y.1352) and Automatically Switched Optical Networks (ASON) (Rec. G.8081/Y.1353).

This Implementers’ Guide identifies terms originally listed in Rec. G.7713/Y.1704, which can now be removed from that Rec. and replaced with text pointing to the appropriate Terminology Rec. for the definition.  This Implementers’ Guide should remain in force until such time as Rec. G.7713/Y.1704 is revised and reissued.

# 1.0	Introduction

Study Group 15 has agreed to the development of a single source Recommendation for definitions currently found in Working Party 3 SDH/OTN/ASON Recommendations.  However, not all affected Recommendations are currently in process for revision.  To facilitate this transition, this Implementers’ Guide identifies the terms which can be removed and replaced when the initial source Recommendation is revised and reissued.  This Implementers’ Guide should remain in force until such time as Rec. G.7713/Y.1704 is revised and reissued.

# 2.0	Terms to be removed from Rec. G.7713/Y.1704 and Amendment 1 to G.7713/Y.1704

The following tables identify the target term, with appropriate replacement definition text for the Recommendation identified in the title of this Implementers’ Guide.

## 2.1	Terms to be removed from Rec. G.7713/Y.1704

| Original Term | Replacement text |
| --- | --- |
| 3 Terms and Definitions The following terms are defined in ITU-T Rec. G.805: – Administrative domain – Layer network – Link connection – Management domain – Subnetwork – Subnetwork connection The following term is defined in ITU-T Rec. G.806: – Management Information (MI) signal The following terms are defined in ITU-T Rec. G.8080/Y.1304: – Agent – Component – Subnetwork controller – Call controller – Connection controller – Connection admission control – Route controller – Neighbour discovery – Link resource manager – Policy – Protocol controller – Subnetwork point – Subnetwork point pool | 3 Terms and Definitions The following terms are defined in ITU-T Rec. G.805: – Administrative domain – Layer network – Link connection – Management domain – Subnetwork – Subnetwork connection The following term is defined in ITU-T Rec. G.806: – Management Information (MI) signal The following terms are defined in ITU-T Rec. G.8081/Y.1353: – Agent – Call controller Component Connection admission control Connection controller – Neighbour discovery – Policy Protocol controller Route controller Soft permanent connection Subnetwork controller Subnetwork point Subnetwork point pool Switched connection The following term is described in ITU-T Rec. G.8080/Y.1304: - Link resource manager |
| The following terms are defined in ITU-T Rec. G.807/Y.1301: – Soft permanent connection – Switched connection | (to delete this part of the text ) |
| The following terms are defined in ITU-T Recs G.852.2 and G.853.1: – Connection termination point. (Examples of connection termination points for technology specific instances may be found in ITU-T Rec. G.784 (for SDH) and ITU-T Rec. G.874 (for OTN).) – Trail termination point. (Examples of connection termination points for technology specific instances may be found in ITU-T Rec. G.784 (for SDH) and ITU-T Rec. G.874 (for OTN).) | The following terms are defined in ITU-T Recs G.852.2 and G.853.1: – Connection termination point. (Examples of connection termination points for technology specific instances may be found in ITU-T Rec. G.784 (for SDH) and ITU-T Rec. G.874 (for OTN).) – Trail termination point. (Examples of connection termination points for technology specific instances may be found in ITU-T Rec. G.784 (for SDH) and ITU-T Rec. G.874 (for OTN).) |

## 2.2	Terms to be removed from Amendment 1 to Rec. G.7713/Y.1704

The following table identifies the target term, with appropriate replacement definition text for the Recommendation identified in the title of this Implementers’ Guide.

| Original Term | Replacement text |
| --- | --- |
| 3 Terms and Definitions Add the following definitions to G.7713/Y.1704: Domain – See Recommendation G.8080/Y.1304. Access Group Container – See Recommendation G.8080/Y.1304. Call Segment - An association between two call control entities (as per Q.2982, which is equivalent to G.8080 call controllers), using a telecommunication service to concatenate a call. Signalling controller – A signalling controller contains the functions of connection control and/or call control. | 3 Terms and Definitions The following terms are defined in ITU-T G. 8081/Y.1353: - Domain - Access Group Container Call Segment - An association between two call control entities (as per Q.2982, which is equivalent to G.8080 call controllers), using a telecommunication service to concatenate a call. Signalling controller – A signalling controller contains the functions of connection control and/or call control. |
| The following terms are defined in ITU-T G.783: - TPmode/PortMode | The following terms are defined in ITU-T G.783: - TPmode/PortMode |

_____________________________