## Slide 1: ENUM Call Flow Scenarios
Steven D. Lind AT&T +1 973 236 6787 sdlind@att.com
Workshop Document: WS ENUM-8-E
Original: English

## Slide 2: ITU Telecommunication Standardization Bureau Document No. 8-E Study Group 2
Tutorial Workshop on ENUM
Geneva, 8 February 2002
SOURCE: Steven D. Lind
TITLE: ENUM Call Flow Scenarios

## Slide 3: Overview
Cover 3 “call” scenarios
  IP-based to IP-based
  CSN to IP-based
  IP-based to CSN
  IP-based origination of global services is a special case
Based on certain assumptions
Applications are only examples; others possible

## Slide 4: Communication between IP-based terminals
1. End user enters E.164 Number: 1-973-236-6787 (e.g., in to: field)
DNS
IP-based Network
2. Application client formats number into FQDN (e.g., 7.8.7.6.6.3.2.3.7.9.1.e164.arpa) and looks up name in DNS
3. DNS returns all NAPTR records associated with
FQDN
4. Application selects appropriate NAPTR record (e.g., mailto:sdlind@att.com) and completes processing

## Slide 5: Call from CSN to IP-based Networks
DNS
Gateway
CSN
IP-based Network
SIP Client
SIP Server
1. End User dials E.164 Number: 1-973-236-6787
2. CSN Provider forwards to appropriate
Gateway
3a. G/W formats FQDN 7.8.7.6.6.3.2.3.8.9.1. e164.arpa; looks up FQDN in DNS
3b. DNS returns NAPTR recs, eg: sip:sdl@sip.att.net
4a. G/W looks up host name for sip.att.net in DNS
4b. DNS returns IP address of host (sip.att.net)
5. Call is routed to designated IP address
6. Call is completed to port of designated user

## Slide 6: Call from IP-based to CSN Networks
DNS
Gateway
CSN
IP-based Network
SIP Client
SIP Server
1. End user dials E.164 Number: 1-973-236-6787
2a. SIP Client formats number into FQDN and looks up in DNS
2b. DNS returns NAPTR recs, eg: tel:+19732366787
3. SIP Client initiates INVITE
LS
4a. SIP Server looks up G/W address in Location Server
4b. Location Server returns IP address of G/W
5. SIP Server routes call to appropriate G/W
6. Gateway completes call through CSN

## Slide 7: Summary
ENUM can be used on application specific basis
  Each application looks for a specific NAPTR record (or discreet set of records) that it can process
Potential for communication control application
  Takes in all NAPTR records and uses application and priority information to make communication between two parties efficient
  Subscriber can exert some control within the parameters of the defined NAPTR record