| INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- |
|  | WRC-2000 | WORLD RADIOCOMMUNICATION CONFERENCE | Document DT/87-E |
|  |  |  | 22 May 2000 |
|  |  |  | Original: English |
| ISTANBUL, 8 MAY – 2 JUNE 2000 |  |
| Chairperson, Sub-Working Party 4A-6 |
| REFINEMENT OF COORDINATION PROCEDURE |
| REPORT TO WORKING GROUP 4A |

SWG 4A-6 met on Saturday to revisit the proposed changes to S11.44 (Terms of Reference 2), and to consider S9 changes related to coordination of BSS earth stations (Terms of reference 8).

# 1	Article S11.44 - Deadline for notification

The group had a further extensive discussion on this topic and sought advice from BR on their interpretation of the problem. As a result, the group agreed that there was a deficiency in the Radio Regulations that needed to be fixed. The proposals shown below were agreed as being suitable to fix this problem.

It was also noted that the existing ROP for Article S11.44 needs to be clarified to align with the changes proposed below. Further it was noted that Resolution 51 covers transitional arrangements for networks subject to the pre-WRC-97, nine-year rule. However, should Resolution 51 be modified, or another transitional Resolution be prepared, consideration should be made for transitional arrangements for filings that have a nine year life.

MOD

S11.44		The notified date16 of bringing into use of any assignment to a space station of a satellite network shall be no later than five years following the date of receipt by the Bureau of the relevant information under No. S9.1. The notified date of bringing into use may be extended at the request of the notifying administration by not more than two years, only under the conditions specified under Nos. S11.44B to S11.44I. Any frequency assignment not brought into use within the required period shall be cancelled by the Bureau after having informed the administration at least three months before the expiry of this period.

ADD

_______________

16	S11.44.1	In the case of satellite assignments that are brought into use prior to the completion of the coordination process, and for which the Resolution 49 (WRC-97) data has been submitted to the Bureau, the network assignment shall continue to be taken into consideration for a maximum period of seven years from the date of receipt of the relevant information under No. S9.1. If the assignments have not been notified by the end of this seven-year period, and the provisions of S11.32A and/or S11.41 have not been sought, the relevant assignment shall be cancelled by the Bureau after having informed the administration at least three months before the expiry of this period.

# 2	Modifications to Article S9

The group decided that these items referred to SWG 4A-6 relating to Article S9, should be referred to GT PLEN for their advice, as they deal with BSS matters in general before final decision. Accordingly, WG 4A should consider referring the proposed modifications to Article S9 as contained in DT/41, to GT PLEN-1 for their advice. SWG 4A-6 did propose changes to Article S9.17, relating to the lower frequency of applicability contained in S9.17, to bring it into alignment with the proposed revisions of Appendix S7, and to note that a sharing scenario for broadcasting-satellite earth station and typical earth station parameters can be found in the new proposed Appendix S7.

It was stressed by two administrations, that the issue of coordination of BSS earth stations with FS services, was an extremely sensitive issue and required careful consideration before any regulatory changes are made.

Accordingly, all text in this proposal is in parentheses for the advice of GT PLEN-1.

## MOD

S9.17	[f)13	for any specific earth station, typical mobile earth station or typical earth station in the broadcasting-satellite service with parameters shown in Appendix S7, in frequency bands above 100 MHz allocated with equal rights to space and terrestrial services, in respect of terrestrial stations, where the coordination area of the earth station includes the territory of another country, with the exception of the coordination under No. S9.15 [and Article 4 of Appendix S30A and the coordination of earth stations in the broadcasting-satellite service which are subject to the Appendix S30 Plans];]

____________