NOC	IAP/5/104

ARTICLE  5

220-335.4 MHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
|  | 220-225 |  |
| 223-230 BROADCASTING Fixed Mobile | AMATEUR FIXED MOBILE Radiolocation 5.241 | 223-230 FIXED MOBILE BROADCASTING |
|  | 225-235 FIXED MOBILE | AERONAUTICAL RADIONAVIGATION Radiolocation |
| 5.243 5.246 5.247 |  | 5.250 |
| 230-235 FIXED MOBILE |  | 230-235 FIXED MOBILE AERONAUTICAL RADIONAVIGATION |
| 5.247 5.251 5.252 |  | 5.250 |
| 235-267 FIXED MOBILE 5.111 5.199 5.252 5.254 5.256 |
| 267-272 FIXED MOBILE Space operation (space-to-Earth) 5.254 5.257 |
| 272-273 SPACE OPERATION (space-to-Earth) FIXED MOBILE 5.254 |
| 273-312 FIXED MOBILE 5.254 |

312-315 FIXED MOBILE Mobile-satellite (Earth-to-space) 5.254 5.255

315-322 FIXED MOBILE 5.254

322-328.6 FIXED MOBILE RADIO ASTRONOMY 5.149

328.6-335.4 AERONAUTICAL RADIONAVIGATION 5.258 5.259