NOC	IAP/5/181

# 2	Limits to the change in the overall equivalent protection margin for frequency assignments in conformity with the Region 2 Plan

With respect to § 4.2.3 c) of Article 4, an administration in Region 2 shall be considered as being affected if the overall equivalent protection margin17 corresponding to a test point of its entry in the Region 2 Plan, including the cumulative effect of any previous modification to that Plan or any previous agreement, falls more than 0.25 dB below 0 dB, or, if already negative, more than 0.25 dB below the value resulting from:

–	the Region 2 Plan as established by the 1983 Conference; or

–	a modification of the assignment in accordance with this Appendix; or

–	a new entry in the Region 2 Plan under Article 4; or

–	any agreement reached in accordance with this Appendix.

Reasons:	There was a consensus among Region 2 administrations participating in the ITU-R studies, that the current methodology cited in Section 2 of Annex 1 (i.e. OEPM degradation) and associated limits were appropriate and should be maintained.

# Footnotes

17 	For the definition of the overall equivalent protection margin, see § 1.11 of Annex 5.