NOC	IAP/5/183

# 4	Limits to the power flux-density to protect the terrestrial services of other administrations18, 19, 20

With respect to § 4.1.1 d) of Article 4, an administration in Region 1, 2 or 3 shall be considered as being affected if the consequence of the proposed modified assignment in the Regions 1 and 3 List is to increase the power flux-density arriving on any part of the territory of that administration by more than 0.25 dB over that resulting from that frequency assignment in the Plan or List for Regions 1 and 3 as established by WRC-2000. The same administration shall be considered as not being affected if the value of the power flux-density anywhere in its territory does not exceed the limits expressed below.

With respect to § 4.2.3 d) of Article 4, an administration in Region 1, 2 or 3 shall be considered as being affected if the consequence of the proposed modification to an existing assignment in the Region 2 Plan is to increase the power flux-density arriving on any part of the territory of that administration by more than 0.25 dB over that resulting from that frequency assignment in the Region 2 Plan at the time of entry into force of the Final Acts of the 1985 Conference. The same administration shall be considered as not being affected if the value of the power flux-density anywhere in its territory does not exceed the limits expressed below.

With respect to § 4.1.1 d) or § 4.2.3 d) of Article 4, an administration in Region 1, 2 or 3 shall be considered as being affected if the proposed new assignment in the Regions 1 and 3 List, or if the proposed new frequency assignment in the Region 2 Plan, would result in exceeding a power flux-density, for any angle of arrival, at any point on its territory, of:

–148     dB(W/(m2 ( 4 kHz))	for	(  (  5°

–148  +  0.5 (( – 5)     dB(W(m2 ( 4 kHz)	for     5°	<	(  (  25°

–138     dB(W/(m2 ( 4 kHz))	for     25°	<	(  (  90°

where represents the angle of arrival.

# Footnotes

18 	See § 3.18 of Annex 5.

19 	In the band 12.5-12.7 GHz in Region 1, these limits are applicable only to the territory of administrations mentioned in Nos. 5.494 and 5.496.

20 	See Resolution 34.