ADD	EUR/13A12/17

DRAFT  Resolution  [EUR/13A12-1]  [XXX]  (WRC-03)

Use of the frequency band 36-37 GHz

The World Radiocommunication Conference (Geneva, 2003),

considering

a)	that the frequency band 36-37 GHz is allocated to the Earth exploration-satellite (passive) service and to the space research service (passive) on a primary basis;

b)	that the frequency band 36-37 GHz is allocated to the fixed service and to the mobile service on a primary basis;

c)	that the Earth exploration-satellite (passive) service protection criteria are contained in Recommendation ITU-R SA.1029;

d)	that Recommendation ITU-R F.758-2 (Considerations in the development of criteria for sharing between the terrestrial fixed service and other services) provides characteristics of fixed service point-to-multipoint systems operating in the band 36-37 GHz, but does not provide information on characteristics of fixed service point-to-point systems operating in this band;

e)	that the band 36-37 GHz is not available for high-density applications in the fixed service (see No. 5.547);

f)	that EESS (passive) operating in the band 36-37 GHz may be interfered by the emissions of systems of active services,

recognizing

a)	that EESS (passive) systems may experience harmful interference if a high density of fixed stations is deployed in the band 36-37 GHz;

b)	that sharing criteria between EESS (passive) and fixed service systems need to be defined in the band 36-37 GHz,

resolves

1	to invite ITU-R to conduct sharing analysis between passive services and the fixed and mobile services in the band 36-37 GHz to define appropriate sharing criteria;

2	to recommend that WRC-07 review the results of studies and consider the inclusion of the sharing criteria within the RR,

urges administrations

1	to provide characteristics of active systems (fixed and mobile) operating in the band 36-37 GHz;

2	to avoid deploying a high density of active service stations in the band 36-37 GHz.

Reasons:	ITU-R studies could not be completed because of a lack of data about fixed or mobile service systems in this band. This Resolution therefore asks administrations to provide such characteristics and, in the meantime, to avoid any deployment of high density fixed service or mobile service systems in the 36-37 GHz band in order to limit the interference to EESS passive sensors in this band.