MOD	EUR/13A27/1

ARTICLE  6     (WRC-2000)

Coordination, notification and recording in the Master International
Frequency Register of frequency assignments to terrestrial stations
or to earth stations in the fixed-satellite service (Earth-to-space)
affecting frequency assignments to broadcasting-satellite stations
in the bands 11.7-12.2 GHz (in Region 3), 11.7-12.5 GHz
(in Region 1) and 12.2-12.7 GHz (in Region 2)10

6.1	The provisions of No. 9.19 and the associated provisions under Articles 9 and 11 are applicable in respect of frequency assignments to broadcasting-satellite stations in the bands 11.7-12.5 GHz in Region 1, 12.2-12.7 GHz in Region 2 and 11.7-12.2 GHz in Region 3:

a)	to transmitting terrestrial stations in the band 11.7-12.7 GHz in all Regions;

b)	to transmitting earth stations in the fixed-satellite service in the band 12.5-12.7 GHz (in Region 1).

6.2	In applying the procedures referred to in § 6.1, the provisions of Appendix 5 are replaced by the following:

6.2.1	These procedures are to be applied in respect of administrations whose territory is included within the service area associated with:

a)	assignments in conformity with the appropriate Regional Plan in Appendix 30;

b)	assignments included in the Regions 1 and 3 List;

c)	assignments for which the procedure of Article 4 has been initiated, as from the date of receipt of the complete Appendix 4 information under § 4.1 or 4.2.

6.2.2	The criteria to be applied are those given in Appendix 7.

Reasons:	To replace Annex 3 of Appendix 30 by Appendix 7 with appropriate BSS parameters to be included in Table 8 of Annex 7 of this Appendix.

ANNEX  1     (WRC-2000)

Limits for determining whether a service of an administration is affected
by a proposed modification to the Region 2 Plan or by a proposed
new or modified assignment in the Regions 1 and 3 List
or when it is necessary under this Appendix to seek
the agreement of any other administration14

(See Article 4)

# Footnotes

10	These procedures do not replace the procedures prescribed for terrestrial stations in Articles 9 and 11.

14 	With respect to this Annex, except for Section 2, the limits relate to the power flux-density which would be obtained assuming free-space propagation conditions.

With respect to Section 2 of this Annex, the limit specified relates to the overall equivalent protection margin calculated in accordance with § 2.2.4 of Annex 5.