MOD	EUR/13A27/15

# 2	Threshold values for determining when coordination is required between transmitting feeder-link earth stations in the fixed-satellite service in Region 2 and a receiving space station in the Regions 1 and 3 feeder-link Plan or List or a proposed new or modified receiving space station in the List in the frequency band 17.8-18.1 GHz

With respect to § 7.1, Article 7, coordination of a transmitting feeder-link earth station in the fixed-satellite service with a receiving space station in a broadcasting-satellite feeder link in the Regions 1 and 3 feeder-link Plan or List or a proposed new or modified receiving space station in the List is required when the power flux-density arriving at the receiving space station of a broadcasting-satellite service feeder link of another administration would cause an increase in the noise temperature of the feeder-link space station which exceeds a threshold value of T/T corresponding to 6%, where T/T is calculated in accordance with the method given in Appendix 8, except that the maximum power densities per hertz averaged over the worst 1 MHz are replaced by power densities per hertz averaged over the necessary bandwidth of the feeder-link carriers.

Reasons:	Harmonization of the inter-Regional criteria with a common T/T value of 6%.

APPENDIX  5  (WRC-2000)

Identification of administrations with which coordination is to be effected or 
agreement sought under the provisions of Article 9