ADD	EUR/13A30/30

11.44K		In the case of launch delays which are beyond the control of the notifying administration, the notified date of bringing into use will be extended by the Bureau in accordance with No. 11.44 from the date on which the delay of the launching was made known if due diligence information required by Resolution 49 (WRC-97)* is provided for the satellite network; if the procedure for effecting coordination in accordance with Section II of Article 9, where applicable, has commenced; and if suitable evidence of the launch delays are provided by the notifying administration.

Sub-Part 30K – Application of the coordination arc

# 1	Introduction

## 1.1	Application of the Rules of Procedure relating to the use of the coordination arc

As an answer to the decision of Council in Resolution 1182 on the backlog in the processing of satellite network filings, the RRB adopted a provisional revision to the Rules of Procedure for No. 9.36 by extending the application of the coordination arc to the unplanned BSS bands as well as other bands for the FSS. This provisional Rule is to be applied until the matter is considered by WRC-03. The CPM considered the RRB’s Rules and included in its report in Section 3.4.1 suggested changes to Table 5-1 of Appendix 5 to reflect these Rules.

Europe proposes that WRC-03 adopt the following changes to Appendix 5, which are based on the CPM text.

## 1.2	Extension of the application of the coordination arc to services other than FSS and BSS and to the bands for which there is no allocation to either FSS or BSS

The coordination arc was first introduced for the geostationary FSS networks, in a limited range of frequency bands above 3.4 GHz, at WRC-2000. Since that date the use of the coordination arc has been extended to other frequency bands not subject to a plan for the FSS and BSS, by a Rule of Procedure adopted by the RRB in response to Council Resolution 1182. In the extension of the application of the coordination arc to other frequency bands, the lower frequency limit has been maintained at 3.4 GHz.

Given the potential advantages offered by the coordination arc concept, consideration should be given to extending its use to more geostationary-satellite networks, subject to Section II of Article 9 and operating in frequency bands above 3.4 GHz that are not subject to a plan.

The coordination arc method for determining affected GSO networks has many advantages over the use of the Appendix 8 procedures used by the Bureau, including:

–	allowing the notifying administration to identify the potentially affected networks and start the coordination process at the beginning of the five-year period rather than wait until the Bureau has completed the Appendix 8 analysis – which may be two to three years into the five-year time limit when taking into account the processing delays; and

–	substantially reducing the volume of data required under Appendix 4 as the link noise temperature data in Section D of Annex 2 is not needed for the coordination arc procedure.

Recognizing that the method may not be universally applicable and may have drawbacks if applied to certain systems or between services involving “inhomogeneous” parameters (e.g. significant variations in antenna gains and beam sizes), Europe considers that extension of the coordination arc beyond the proposal in § 1.1 needs to be studied on a case-by-case basis.

To date ITU-R has only undertaken studies for sharing involving the FSS and BSS. Studies into the applicability of the coordination arc and the possible quantification of the precise orbital arc separation to be used for intra-service sharing between satellite services other than the FSS and all inter-service sharing cases, have not been completed. It is therefore proposed to invite ITU-R to complete the relevant studies into the applicability and appropriate value of orbital arc separation for each group of frequency bands and space services as a matter of urgency. A report on the study findings should be submitted to the Director as soon as possible.

# 2	Proposals

APPENDIX  5  (WRC-2000)

Identification of administrations with which coordination is to be effected or 
agreement sought under the provisions of Article 9