ADD	EUR/13A42/3

DRAFT  Resolution  [EUR/13A42-2]  (WRC-03)

Sharing conditions between Earth exploration-satellite service (passive) and
 the other active services (fixed, mobile) in the band 10.6-10.68 GHz

The World Radiocommunication Conference (Geneva, 2003),

considering

a)	that the frequency band 10.6-10.68 GHz is allocated to the Earth exploration-satellite service (EESS) (passive), radio astronomy and space research (passive) services on a primary basis;

b)	that the frequency band 10.6-10.68 GHz is allocated to the mobile and the fixed services on a primary basis;

c)	that the EESS (passive) protection criteria are contained in Recommendation ITU-R SA.1029;

d)	that Recommendation ITU-R F.758-2 provides characteristics of fixed service systems operating in the band 10.6-10.68 GHz;

e)	that footnote No. 5.482 specifies that “in the band 10.6-10.68 GHz, stations of the fixed and mobile, except aeronautical mobile, services shall be limited to a maximum equivalent isotropically radiated power of 40 dBW and the power delivered to the antenna shall not exceed 
–3 dBW”;

f)	that the limits specified in No. 5.482 may be exceeded subject to agreement obtained under No. 9.21 and are not applicable in Saudi Arabia, Armenia, Azerbaijan, Bahrain, Bangladesh, Belarus, China, the United Arab Emirates, Georgia, India, Indonesia, Iran (Islamic Republic of), Iraq, Japan, Kazakhstan, Kuwait, Latvia, Lebanon, Moldova, Nigeria, Uzbekistan, Pakistan, the Philippines, Qatar, Syria, Kyrgyzstan, Russia, Tajikistan, Turkmenistan and Ukraine;

g)	that EESS (passive) operating in the band 10.6-10.68 GHz may be interfered by the emissions of systems of active services;

h)	that the band 10.6-10.7 GHz is of primary interest to measure rain, snow, sea state and ocean wind,

recognizing

1	that the provisions given in No. 5.482 may not be sufficient to ensure the protection of the EESS (passive),

2	that sharing criteria between EESS (passive) and active services systems need to be reviewed in the band 10.6-10.68 GHz,

resolves

1	to invite ITU-R to conduct sharing analyses between EESS (passive) and the fixed and mobile services in the band 10.6-10.68 GHz in order to define appropriate sharing criteria;

2	to recommend that WRC-07 review the results of the studies and consider the inclusion of the sharing criteria within the Radio Regulations,

urges administrations

1	to provide the relevant characteristics of active systems (fixed and mobile services) operating in the band 10.6-10.68 GHz;

2	to contribute to the sharing studies between active services and EESS (passive) in the band 10.6-10.68 GHz.