ADD	EUR/13A8/11

5.XX2	In order to avoid unacceptable interference to the Earth exploration-satellite (passive) service in the band 52.6-54.25 GHz, the unwanted emissions power delivered to the antenna of any station in the fixed service operating in the band 51.4-52.6 GHz shall be limited to –33 dBW in a 100 MHz reference bandwidth in the band 52.6-54.25 GHz.