ADD	ASP/25/129

Resolution  [ASP/1.12/EESS]  (WRC-03)

Use of the frequency band 36-37 GHz

The World Radiocommunication Conference (Geneva, 2003),

considering

a)	that the frequency band 36-37 GHz is allocated to the Earth exploration-satellite service (EESS) (passive) and to the space research service (passive) on a primary basis;

b)	that the frequency band 36-37 GHz is allocated to the fixed service and to the mobile service on a primary basis;

c)	that the EESS (passive) protection criteria are contained in Recommendation ITU-R SA.1029;

d)	that Recommendation ITU-R F.758-2 provides characteristics of fixed service point-to-multipoint systems operating in the band 36-37 GHz, but does not provide information on characteristics of fixed service point-to-point systems operating in this band;

e)	that the band 36-37 GHz is not available for high-density applications in the fixed service (see No. 5.547);

f)	that the EESS (passive) operating in the band 36-37 GHz may be interfered by the emissions of systems of active services,

recognizing

a)	that EESS (passive) systems may experience harmful interference if a high density of fixed-service stations is deployed in the band 36-37 GHz;

b)	that sharing criteria between EESS (passive) and fixed-service systems need to be defined in the band 36-37 GHz,

resolves

1	to invite ITU-R to conduct sharing analyses between passive services and the fixed and mobile services in the band 36-37 GHz in order to define appropriate sharing criteria;

2	to recommend that WRC-07 review the results of the studies and consider the inclusion of the sharing criteria within the Radio Regulations,

urges administrations

1	to participate actively in the aforementioned studies by submitting contributions to ITU-R, including provision of characteristics of active systems (fixed and mobile services) operating in the band 36-37 GHz;

2	to take into account that EESS (passive) systems may experience harmful interference, if the band 36-37 GHz is heavily used by the fixed- and mobile-service stations, prior to the establishment of the sharing criteria.

Reasons:	In order to protect the operation of EESS (passive) and space research service (passive) systems, it is important to establish sharing criteria between passive services and active terrestrial services in the band 36-37 GHz. For this purpose, it is useful to develop a resolution which promotes ITU-R to conduct the sharing analysis mentioned above, and administrations to take the interference problems into account.