MOD	RUS/30/5

TABLE  10

Predetermined coordination distances

| Frequency sharing situation | Coordination distance (in sharing situations involving services allocated with equal rights) (km) |
| --- | --- |
| Type of earth station | Type of terrestrial station |  |
| Ground-based in the bands below 1 GHz to which No. 9.11A applies. Ground-based mobile in the bands within the range 1-3 GHz to which No. 9.11A applies | Mobile (aircraft) | 500 |
| Earth stations in the space research and space operations services in the 258-261 MHz band | Mobile (aircraft) | 400 |
| Aircraft (mobile) (all bands) | Ground-based | 500 |
| ... |  |  |

Reasons:	To ensure adequate protection for the existing services, it is proposed to set the predetermined coordination distance in Appendix 7 of the Radio Regulations at 400 km, based on a sharing scenario involving systems of the aeronautical mobile service.