ADD	IRN/32/91

5.311bis	The use of the band 620-790 MHz by geostationary-satellite systems for television stations using frequency modulation for which the corresponding assignments were notified and brought into use, in accordance with the Radio Regulations, after 4 July 2003 shall be under the condition that it does not cause harmful interference to, nor claim protection from terrestrial television broadcasting systems operating in Region 1 as well as the concerned neighbouring countries in Region 3 in accordance with the corresponding regional Plan and its revisions.

Reasons:	Limit the use of this band to GSO BSS satellite systems to protect the 2005 revised ST 61 and GE 89 Plans plus those of neighbouring countries.