ADD	F/36/1

1.x	to consider the practical experience of protection of radiodetermination services in the 5 GHz band from wireless access systems including RLANs, and take appropriate action

Background/reasons

Agenda item 1.5 of WRC-03 addresses, amongst other issues, an allocation to the mobile service in the bands 5 150-5 350 MHz and 5 470-5 725 MHz for the implementation of wireless access systems (WAS) including RLANs in accordance with Resolution 736 (WRC-2000).

Considering that the bands 5 250-5 350 MHz and 5 470-5 725 MHz are allocated to the radiodetermination service (radiolocation and maritime radionavigation), studies have been carried out within ITU-R on the sharing in these bands between WAS including RLANs and radars.

As indicated in the final Report from the CPM to WRC-03, mitigation techniques, such as Dynamic Frequency Selection (DFS), are required for the WAS including RLANs to enable co-existence in these bands between these systems and radars. The new Recommendation ITU-R M.[8A-9B/RLAN-DFS [Doc. 8/152]] describes this mitigation technique and provides, in its Annex 1, detection, operational and response requirements, which should be fulfilled to ensure the protection of systems in the radiodetermination service.

The determination of these requirements has been based on extensive theoretical studies.

It is expected that WRC-03 will decide to include these requirements in the Radio Regulations on a mandatory basis.

Additional studies, based on testing and practical experience, are planned in the next ITU-R study period (2003-2007) and should enable to confirm whether the values of the DFS requirements stated in the new Recommendation ITU-R M.[8A-9B/RLAN-DFS [Doc. 8/152]] are appropriate.

Should these studies conclude that, in order to provide adequate protection for the radiodetermination service, there is a need to modify the mandatory requirements included in the Radio Regulations, WRC-07 would also need to review this topic.