ADD	CME/42/4

5.XXX	Use of the bands 5 150-5 350 and 5 470-5 725 MHz by the mobile service is limited to those applications described in Recommendation ITU-R M.1450-1 for wireless access systems, including RLANs. Such systems must employ interference mitigation techniques to protect existing services complying with the relevant ITU-R recommendations. Wireless access systems, including RLANs, must neither cause harmful interference to, nor claim protection from, nor otherwise impose constraints on operation or development of the existing services.

Reasons:	Results of ITU-R studies have demonstrated the feasibility of sharing between wireless access systems in the mobile service and the other services having a primary allocation in the bands 5 150-5 350 MHz and 5 470-5 725 MHz.