MOD	CME/42/5

5.328A	Additional allocation: the band 1 164-1 215 MHz is also allocated to the radionavigation-satellite service (space-to-Earth) (space-to-space) on a primary basis. Stations in the radionavigation-satellite service in the band 1 164-1 215 MHz shall operate in accordance with the provisions of Resolution [RNSS 1.2.1-1] (WRC-03) and shall not claim protection from stations in the aeronautical-radionavigation service. No. 5.43A does not apply. Use of the band 1 164-1 215 MHz by the radionavigation-satellite service is subject to the application of the provisions of Nos. 9.12, 9.12A, and 9.13. The provisions of No. 21.18 apply.

ARTICLE  21

Terrestrial and space services sharing frequency bands above 1 GHz