ADD	J/58A6/3

TABLE 1C11, 2

Alternative limits on aggregate epfd( radiated by non-GSO FSS systems having certain 
specified types of orbit in the frequency band 19.7-20.2 GHz

| Frequency band (GHz) | epfd( (dB(W/m2)) | Percentage of time during which epfd( may not be exceeded | Reference bandwidth (kHz) | Reference antenna diameter, and reference radiation pattern3 |
| --- | --- | --- | --- | --- |
| 19.7-20.2 | –166.9 | 0-100 | 40 | 70 cm Recommendation ITU-R S.1428 |
|  | –152.9 | 0-100 | 1 000 |  |
|  | –168.5 | 0-100 | 40 | 90 cm Recommendation ITU-R S.1428 |
|  | –154.5 | 0-100 | 1 000 |  |
|  | –177.3 | 0-100 | 40 | 2.5 m Recommendation ITU-R S.1428 |
|  | –163.3 | 0-100 | 1 000 |  |
|  | –182.1 | 0-100 | 40 | 5 m Recommendation ITU-R S.1428 |
|  | –168.1 | 0-100 | 1 000 |  |
| 1 For certain GSO FSS receive earth stations, see also Nos. 9.7A and 9.7B. 2 The limits shown in this Table may be used as an alternative to the limits shown in Table 1C. A non-GSO system shall meet the limits of this Table in both the 40 kHz and the 1 MHz reference bandwidths. 3 For this Table, reference patterns in Recommendation ITU-R S.1428 shall be used only for the calculation of interference from non-GSO FSS systems into GSO FSS systems. |

Reasons:	Addition of this Table is required to reflect the study results in ITU-R regarding an alternative set of epfd( limits which are appropriate to non-GSO systems having certain specified types of orbit in the fixed-satellite service in the frequency band 19.7-20.2 GHz.