ADD	J/58A6/4

22.5CB		3)	The limits given in Table 22-1C1 are alternative limits to those given in Table 22-1C which are applicable to non-geostationary-satellite systems having a certain specified types of orbit in the fixed-satellite service in the 19.7-20.2 GHz frequency band. These systems shall meet either all the limits in Table 22-1C or all the limits given in Table 22-1C1. Certain specified types orbit mentioned in this Table is either of the following orbits:

–	an orbit with an eccentricity at least 0.05, an inclination between 35º and 145º, an apogee of at least 18 000 km, and a period that is the geosynchronous period (23 h, 56 min) multiplied by m/n where m and n are integers (the ratio m/n may be less than, equal to, or greater than one);

–	a circular orbit (with an eccentricity of at most 0.005), with the geosynchronous period (23 h, 56 min) and an inclination between 35º and 145º.

Reasons:	This addition is necessary to make clear the relationship between the limits given in Table 22-1C and the alternative limits.