ADD	INS/61/4

5.ZZZ	The band 1 429-1 432 MHz is also allocated on a primary basis to the mobile-satellite service (space-to-Earth), limited to feeder links for non-geostationary systems in the mobile-satellite service with service links below 1 GHz. In order to protect the radio astronomy service in the 1 400-1 427 MHz band, the aggregate power flux-density radiated by all space stations within any feeder link in a non-geostationary system shall not exceed the level of –180 dB(W/m2) in the 1 400-1 427 MHz band and a level of –196 dB(W/(m2 · 20 kHz)) in any 20 kHz portion of the 1 400-1 427 MHz band, at the site of any radio astronomy station for more than 2% of the time. The use of the band 1 429-1 432 MHz by the mobile-satellite service is subject to coordination under No. 9.11A.

Reasons:	To provide additional allocations for non-GSO MSS feeder links (space-to-Earth) to support existing non-GSO MSS allocations below 1 GHz, and protect the radio astronomy service in the 1 400-1 427 MHz band.