MOD	KOR/109A12/6

TABLE  5-1 (continued)

| Reference of Article 9 | Case | Frequency bands (and Region) of the service for which coordination is sought | Threshold/condition | Calculation method | Remarks |
| --- | --- | --- | --- | --- | --- |
| No. 9.11 GSO, non-GSO/ terrestrial | A space station in the broadcasting-satellite service (BSS) in any band shared on an equal primary basis with terrestrial services and where the BSS is not subject to a Plan, in respect of terrestrial services | 620-790 MHz 1 452-1 492 MHz 2 310-2 360 MHz 2 520-2 655 MHz 2 655-2 670 MHz 12.5-12.75 GHz (Region 3) 17.3-17.8 GHz (Region 2) 21.4-22 GHz (Region 1 and 3) 74-76 GHz | Bandwidths overlap; and – for non-GSO satellite system in accordance with No. 5.418 of the Radio Regulations, the pfd at the Earth’s surface produced by emissions from a space station for all conditions and for all methods of modulation under assumed free-space propagation conditions exceeds: (128 dB(W/(m2 · MHz)) 0°  θ < 5° (128 + 0.6 (5) dB(W/(m2 · MHz)) 5°  θ < 25° (116 dB(W/(m2 · MHz)) 25°  θ < 35° (116 + 1.5 (35) dB(W/(m2 · MHz)) 35°  θ < 37° (113 dB(W/(m2 · MHz)) 37°  θ < 90° where θ is the angle of arrival of the incident wave above the horizontal plane, in degrees. | Check by using the assigned frequencies and bandwidths |  |
| . . . |  |  |  |  |  |

Reasons:	Resolution 539 (WRC-539) could be suppressed at WRC-03.