ADD	USA/172/3

Draft  RESOLUTION  [5 GHz]  (WRC-03)

Consideration by 2007 World Radiocommunication Conference use of the band 5 091-5 150 MHz for new aeronautical applications

The World Radiocommunication Conference (Geneva, 2003),

considering

a)	that two current aviation safety objectives (i.e. to provide more information to the pilot/cockpit, and to reduce runway incursions) could be met by systems such as the airport network and location equipment in the band 5 091-5 150 MHz;

b)	that the band 5 091-5 150 MHz also may be suitable to support data links that carry critical aeronautical data from systems such as air traffic control radars, wind shear radars, remote maintenance monitoring systems, runway lighting, low-level wind shear alert systems, automated weather surface observing systems, or automatic weather observation systems;

c)	that the band is allocated to the aeronautical radionavigation service, the fixed-satellite service (Earth-to-space) in accordance with No. 5.444A, and the aeronautical mobile-satellite (route) service in accordance with No. 5.367;

d)	that the band 5 000-5 150 MHz is used for the operation of the international standard system (microwave landing system) and that the requirements of this system shall take precedence over other uses of this band (No. 5.444);

e)	that compatibility between new aeronautical systems and the microwave landing system will be ensured by ICAO;

f)	that the proposed new aeronautical systems are conceptual, thus studies need to be performed to determine the compatibility of these systems with MSS feeder links;

g)	that there is a need for continued operation of non-GSO FSS systems used for feeder links in the mobile-satellite service (Earth-to-space) in this band,

recognizing

a)	that the appropriate ITU-R Study Group may need to adopt a draft new Question on compatibility of new aeronautical systems with existing systems in the band;

b)	that it is not feasible to introduce these new aviation applications in other aeronautical bands used for safety communications, radionavigation and surveillance due to the incompatibility and spectrum congestion;

c)	that bands used for non-aviation applications would not be suitable, because the bands would not provide the integrity, availability and reliability needed to support safety systems, and would constrain the use and development of existing users;

d)	that it is important to protect the existing primary services in the band,

invites the ITU-R

–	to study, in advance of WRC-07, and to report the results of such studies of the spectrum requirements and technical characteristics of the aviation systems described in considering a) and b);

–	to study, in advance of WRC-07, and to report the results of such studies of the technical and operational issues related to the potential use of the 5 091-5 150 MHz band by the aviation systems described in considering a) and b) and the sharing conditions between such new services and the allocated services in the band;

–	to conduct, and complete compatibility studies between new aeronautical systems and existing systems in time for WRC-07,

further invites

ICAO to participate in these studies,

resolves

that WRC-07 consider allocation and regulatory provisions concerning the use of the band 5 091-5 150 MHz for new aeronautical applications.